## Slide 1: Depolarization (hardware)
J. Wenninger
With input from the BE RF colleagues
W. Hoefle, D. Valuch, L. Arnaudon

## Slide 2: Depolarization process
The depolarization process itself was never studied in detail at LEP.
Some ‘magic’ depolarization settings were established and kept for the entire LEP life-cycle.
It is not unrealistic to assume that as a starting point one can consider similar depolarization settings for FCC-ee and LEP.
  Scale the time scales for the ~4 times longer revolution period.
  More issues with decoherence of the spin vectors during depolarization process at FCC-ee ?!?

## Slide 3: LEP kicker
Magnetic kicker with max field of ~ 0.4x10-3 Tm.
Kicker pulse: ~1 ms FWMH. One pulse per revolution.
Standard field strength for depolarization ~ 0.2x10-3 Tm.
  orbit kick of 1.2 mrad, spin rotation of 140 mrad.
~ 1 ms
L. Arnaudon, S. Myers and R. Olsen, Commissioning of the LEP transverse feedback system, Proc. IEEE Particle accelerator Conf. EPAC90 (Nice, 1990 )

## Slide 4: LEP depolarization
Depolarization sweeps were typically 22 Hz wide to provide an energy within 0.44 MeV.
  More precise frequency determinations were possible, usually not used because the standard accuracy was adequate and more accurate scans could be time consuming.
In the first set of measurements Qs was modified to confirm that the depolarization did not happen on a Qs sideband, and the energy was varied using the RF frequency to determine if the depolarization scan corresponded to ns or 1-ns.
  From them on it was usually possible to track the energy.

## Slide 5: LHC transverse feedback system
Four kickers per beam, per plane, located in RF zone (UX451) at point 4
  Electrostatic kicker, length 1.5 m.
  Providing a kick of ~2 mrad @ 450 GeV (all 4 units combined).
  Useful bandwidth ~1 kHz – 20 MHz.
ADT kickers and power amplifiers at point 4

## Slide 6: LHC TF digital processing
Impulse response of “standard bandwidth” and “enhanced bandwidth” operation of the LHC TF.
Almost bunch-by-bunch kicker for LHC 25 ns bunch spacing.
  More or less what would be nice to have for FCC-ee depolarization.

## Slide 7: LHC ->FCC-ee
The LHC TF system would provide a transverse kick of up to ~20 mrad at the Z peak with ~10 MHz bandwidth. This is 10x more than what we may need  OK !
For a LEP like kick of ~1 mrad there is a factor 4-5 margin wrt DA. AM arrangement of 2 kickers with adequate phase advance to enhance the deflection may be used to overcome DA issues.