## Slide 1: FCC-hh impedances and instabilities
O. Boine-Frankenheim (for EuroCirCol Task 2.4)
S. Arsenyev, L. Mether, B. Salvant, D. Schulte (CERN)
D. Astapovych, U. Niedermayer (TU Darmstadt)
V. Kornilov (GSI)
B. Riemann (TU Dortmund)

## Slide 2: Task 2.4 Single Beam Stability
e-
Electron clouds:
created by residual gas or wall emission.
beam pipe
Bunch
Wakefields and impedances:
2D and 3D simulation codes
Image current
Beam-beam interaction:
Not part of this work package
(but, electron lenses for LD are)
Instabilty thesholds (Landau damping):
Dispersion relations and tracking studies
Compare with LHC observations
and simulations as much as possible.
-> Scaling with beam energy,…

## Slide 3: 2D impedance code in frequency space
U. Niedermayer et al., Space charge and resistive wall impedance computation in the frequency domain using the finite element method, Phys. Rev. ST-AB 18, 032001, 2015
BeamImpedance2D (PYTHON): https://bitbucket.org/uniederm/beamimpedance2d.git
Open source package FEniCS (A. Logg, K. Mardal, G. Wells et al.)
Mesh from GMSH (C. Geuzaine, J. Remacle)
Nodal functions
Nedelec edge functions

## Slide 4: Impedance of the FCC-hh beam screen
“frog”-shape
FCC
LHC
Boundaries and parameters for impedance calculations with BeamImpedance2D

## Slide 5: Coupled bunch instability: FCC vs. LHC
b=0.014 m
b=0.02 m
(Thick) resistive wall impedance
growth time at 3.3 TeV:
approx. 200 turns
at 50 TeV:
approx. 1000 turns
(LHC at 7 TeV: 2000 turns)
Growth rate:
FCC
LHC
(Sacherer 1974)
Transverse impedances (only real part)

## Slide 6: Dispersion relation and Landau damping
(action)
(coherent tune shift)
(octupoles)
(incoherent tune spread)
(for stability)
see V. Kornilov
Example stability plot for LHC (7 TeV)
Possible strategy: Active dampers for k=0, octupoles for k>0.
LHC (7 TeV) vs FCC-hh (50 TeV):
Undesired effects: Reduction of dynamic aperture,…

## Slide 7: Landau damping: Possible alternative schemes
Shiltsev et al PRL (2017)
Tune spread induced by a
counter-propagating electron beam:
Electron lenses
FCC-hh: Active feedback for k=0 modes, Landau damping for k>1.
Still, additional Landau damping concepts are helpful !
Grudiev PRAB 2014
Schenk et al, IPAC17
Radio-Frequency
Quadrupole (RFQ)
No local spread (in z) !
Dispersion relation and Landau damping ?
(longitudinal action)
Detailed particle tracking studies are ongoing (see also V. Kornilov).
Shiltsev et al
PRL 2017
LHC: 10 x larger stability area then with octupoles

## Slide 8: Option: HTS coated screen
P. Krkotic,
U. Niedermayer
“depinning frequency“
B=16T
Hybrid coating
Hybrid coating (HTS stripes):
Possible reduction of the resistive wall instability growth rates by factor 5-6.
Possible reduced TMCI thresholds.

## Slide 9: Electron cloud studies
openEcloud : https://github.com/openecloud
e.g. F. Petrov, O. Boine-Frankenheim, O. Haas, PRAB (2014)
Fast 2D Poisson solver, PIC solver, SEY model, interfaces to PATRIC/pyORBIT (to do)
FCC
LHC
D. Astapovych
B=0
B=1 T
25 ns bunch
spacing

## Slide 10: Electron cloud studies: Buildup
See also L. Mether
Photoelectrons without mitigation would dominate the buildup (L. Mether, 2016)
FCC beam pipe design: Photoelectrons stay in antechamber (first approximation)
Saturated electron cloud
density depends on pipe radius
Lower electron energies
for smaller
Differences between different
simulation models and codes:
SEY model
Pipe geometry and mesh
Particle pusher and field solver
…..
Next step: (residual) photoelectrons
D. Astapovych
25 ns bunch spacing
SEY
LHC: B=1 T
FCC: B=1 T
SEY threshold for buildup

## Slide 11: Electron cloud: instability thresholds
Rumolo et al. PRL (2008): Electron cloud induced instability
stronger at higher energies because of smaller beams.
(focusing strength for electrons
in the bunch potential)
Electron cloud density thresholds
(K. Ohmi et al, IPAC2015)
3 TeV: ne,th = 4.4 x 1010 m-3
50 TeV: ne,th = 5.7 x 1011 m-3
-> Next step: Detailed simulations
to determine instability threshold densities
(and required SEY for FCC) !
If the the FCC screen will be a-C coated
(with SEY lower/equal 1) and the chosen
screen design avoids photoelectron entering
in the pipe, electron could induced instabilities
should be absent in the FCC.
Simulation for LHC (drifts), B-F., Petrov (PRAB 2012/2015)

## Slide 12: Status and Plans (EuroCirCol WP 2.4)
Impedances studies:
Screen and coatings (HTS and laser): HTS for impedance, Laser for SEY
Warm parts (see B. Riemann)
Collimators: Important at top energy
Impedance library (see S. Arsenyev)
Impedance budgets -> from instability thresholds (!) or tolerable head loads.
Screen/Collimators: Coupled bunch damped by Octupoles (k>=0) and Feedback
TMCI (might be an issue with laser coating and collimators)
Other Landau damping mechanisms and combinations (see V. Kornilov)
Ecloud buildup and instability thresholds:
Estimates for buildup (see L. Mether)
Required SEY for instability supression.

## Slide 13
Backup

## Slide 14: FCC beam screen and impedance
High-frequency parts and coatings treated separately.
Beam pipe | 
Material | Cu, SS
Cu thickness [μm] | 300
Laser/a-C coating [μm] | 1-10
Betatron side-bands
are at 1-2 kHz
Resistive wall instability: