## Slide 1
Yuri Alexahin (on behalf of FNAL – NIU team)
EuroCirCol meeting
9 October 2017
Energy collimation studies

## Slide 2: The Team
N. Mokhov & M. Syphers (NIU) – leaders,
E. Gianfelice-Wendt – optics design
Y. Alexahin – optics & collimation arrangement design
I. Tropin – MARS simulations & collimation arrangement design
A. Narayanan (NIU PhD student) – G4beamline and MARS simulations

## Slide 3: Optics Modifications
Left: The starting optics is Collider dev/fcc hh dev.seq as found back in June 2017
Right: Eliana’s optics modification – the merit factor Dx2/x increased by 7 times
- 43km
IPF @ 44.6km
- 43km

## Slide 4: Quadrupole Strength Modification

## Slide 5: Optics Functions @ Collimators
Eliana’s design
Original design

## Slide 6: Warm Section Optics
Optics functions in warm section (from bpm.6l3.b1 to bpmwc.6r3.b1) and trajectories of particles scattered in the primary collimator by 10rad

## Slide 7: Collimators for Preliminary Study
Important Note:
Generally the contribution to the transverse impedance goes as x,y/gap3, so for horizontal momentum collimator Zx ~ x /Dx3, while for the vertical Zy ~ 1/y1/2.
In Eliana’s design both contributions are smaller!
name | collim. plane | length (m) | position from warm start (m) | jaw distance (mm) from centerline | jaw angle (rad) w.r.t. centerline
TCP | h | 2.5 | 43.75 | 10 | -72.75
TSCH1 | h | 2.5 | 343.0 | 5 | 0
TSCV | v | 2.0 | 545.47 | 3.6 | 0
TSCH2 | h | 2.5 | 732.82 | 9 | 0
TTV | v | 1.5 | 888.65 | 2.5 | 0

## Slide 8: G4beamline* Simulations
The goal of the study was to see if it is possible to eliminate protons with relative momentum deviation p larger (by absolute value) than max=0.0015 not allowing scattered protons with transverse amplitudes larger than 12 at 50 TeV to escape.
A G4BL input file was built that includes warm magnets and collimators as described on slides 2-3 which act on dp/p < 0 part of the halo. The gaps were calculated for max=0.0015
Three values of dp/p were chosen: -0.0016, -0.0015 and -0.0014
For each dp/p value an ensemble of 104 particles was built based on MADX values of optics functions at the warm section entrance as
where the initial phases x,y were randomly distributed in the interval (0, 2), while action variables Ix,y were distributed according to the exponential law with the average =4.1*10-11m and truncation at 5 amplitude (Ix,y =12.5).
Protons that reached the end of the warm section were analysed.
*) T. Roberts, http://g4beamline.muonsinc.com

## Slide 9: G4BL Tracking Results (30k protons total)
Distribution in the transverse amplitudes of surviving particles at the warm end, none survived of those with  = -0.0016

## Slide 10: Next steps
Limitations:
Present shape and dimensions of collimators and magnets are too simplistic.
Magnets work as “black holes”: kill all particles entering iron.
No beamline enclosure, instead some disc absorbers put to kill off particles with large amplitudes.
Only 50 TeV case considered
To-do list with G4BL
More realistic configuration of collimators (may be shorter C + metallic?)
More realistic sizes of the magnet iron yokes (w/o “kill” option)
Additional absorbes for secondaries and low energy protons
Energy deposition in collimators and magnets (“totalEnergy” command)
Injection energy case
Draft of the report
MARS model and simulations

## Slide 11: MARS Unleashed!
Lattice file for warm section was created and checked by tracking protons with original collimators (?)
Proton trajectories in horizontal (left) and vertical (right) plane. MARS notations differ from conventional x  y

## Slide 12: TSCV (the right half) used in G4BL simulations
Since there is no elliptic apertures in G4beamline I had to invent something that would produce smaller impedance and collimate particles with large |dp/p| tighter:
Schematic view of the cross-section of the right half of the TSCV collimator acting on protons with p < 0. The red star shows the beam center while the teal ellipse shows the 12 envelope for p = ‑0.0015.
beam center