## Slide 1: New Triplet and EIR Optics
Léon van Riesen-Haupt
on behalf of the JAI FCC team

## Slide 2: Before Berlin
Alternative Triplet before Berlin
Designed using ‘triplet optimisation code’
2-3-2 configuration
  Identical magnets
  15 m long
  Varied shielding
  Protected from debris (see J Abelleira)
Integrated into lattice
  Includes a flat optics

## Slide 3: 40 m
First iteration triplet design with ‘optimisation code’
  Split to maximum 15 m
  2-4-2 configuration
  Q2 magnets shorter than Q1 and Q3 magnets
  Same shielding maintained

## Slide 4: Next Iteration
This design was not followed up because
  Magnets are not identical
    This was a key benefit of the 45 m design
  Optimisation code does not include splitting
    This might not be optimal solution once splitted
  Very similar to baseline
    Similar design already explored by Roman
Instead take the 45 m triplet and move it forward 5 m
  Slight re-matching needed to re-optimise x and y focal points

## Slide 5: Re-Matching
Quadrupole | Sub Quads | Length | Coil Radius | Shielding | k | Gradient | Aperture
Q1 | 2 | 15 m | 98.3 mm | 44.2 mm | 0.000637 | 106 T/m | 43 mm
Q2 | 3 | 15 m | 98.3 mm | 33.2 mm | -0.000664 | 111 T/m | 54 mm
Q3 | 2 | 15 m | 98.3 mm | 24.2 mm | 0.000581 | 97 T/m | 63 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding |  | Gradient | Aperture
Q1 | 2 | 15 m | 98.3 mm | 44.2 mm | 0.000637 | 106 T/m | 43 mm
Q2 | 3 | 15 m | 98.3 mm | 33.2 mm | -0.000664 | 111 T/m | 54 mm
Q3 | 2 | 15 m | 98.3 mm | 24.2 mm | 0.000581 | 97 T/m | 63 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding | k | Gradient | Aperture
Q1 | 2 | 15 m | 96.5 mm | 44.2 mm | 0.000647 | 108 T/m | 41 mm
Q2 | 3 | 15 m | 96.5 mm | 33.2 mm | -0.000674 | 112 T/m | 52 mm
Q3 | 2 | 15 m | 96.5 mm | 24.2 mm | 0.000590 | 95 T/m | 61 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding |  | Gradient | Aperture
Q1 | 2 | 15 m | 96.5 mm | 44.2 mm | 0.000647 | 108 T/m | 41 mm
Q2 | 3 | 15 m | 96.5 mm | 33.2 mm | -0.000674 | 112 T/m | 52 mm
Q3 | 2 | 15 m | 96.5 mm | 24.2 mm | 0.000590 | 95 T/m | 61 mm

## Slide 6: Moved Triplet
Same benefits as previous triplet
  7 Identical magnets
  Same shielding as before
Slightly decreased aperture due to larger strength
Enough BSC for and round optics
reachable with compromises
Optics for flat(ter) optics
  See J Abelleira’s talk for details
Created injection optics for completeness

## Slide 11: Injection Optics @ 3.3TeV

## Slide 12: Summary and Outlook
triplet moved forward 5 m
Achieve similar optics as before
  Can reach round optics comfortably
  New flat optics
  Injection optics
Still identical magnets and ‘short’ design
Enough debris protection (see J Abelleira)
New flat optics
Integrated into most recent IR of R Martin
Integration into ring ongoing (A Chance)
  Can perform chromaticity studies
  Also interesting for flat beam-beam