## Slide 2: Assembly and Test Activities for the Cryogenic System of DarkSide-20k at CERN CERN Cryolab Infrastructure
T. Koettig, L. Mapelli, J. Bremer

## Slide 3: Content
Requirements for the cryogenic system
Upgraded supply systems
LN2 transfer line to building 159

## Slide 4: Requirements
Assembly and test activities for the cryogenic system of DarkSide-20k at CERN Cryolab.
Fluids | Quantities
LN2 during cool down | 100 l/hr or 80 kg/hr
LN2 during normal operation | 20 l/hr or 16 kg/hr
LAr (max level of impurity will be apecified) | 2 t
Compressed air | Small consumption operating valves
Table 1 Consumables for the commissioning and tests
Electrical power | 20 kW
Crane Fork Lift | 250 kg 1 ton
4 m
4 m
5 m

## Slide 5: Infrastructure already upgraded or in place
Experimental space of 4 x 5 m2 with 4 m height
Upgrade of the electrical supply and pressurized air 6 barg
Network and wifi connection
Crane capabilities in the area 250 kg (maybe need an increase in height 3.5 m => 4.5 m)

## Slide 6: Routing of the new to be installed LN2 transfer line
Buffer
600 l
Phase
separator
Cryolab 165

## Slide 7: Routing of the new to be installed LN2 transfer line
Buffer
500 l
Phase
separator
Cryolab 165
DS 20k experimental space
in Bldg. 159
LN2 tank
VB
Buffer
500 l

## Slide 8: PID of the new to be installed LN2 transfer line

## Slide 9: Conclusions
Experimental space is ready
Supply of electricity, pressurized air ready
LAr can be purchased via CERN gas group
LN2 transfer line is under study, price inquiry started
Thank you for your attention