## Slide 1: PS Impedance Model Status
SPS Injection Losses Review: 30/11/17
B. Popovic
Acknowledgements: C. Vollinger, A. Lasheen, H. Damerau

## Slide 2: Overview: Sources of Emittance Blow Up
Large impedances at low frequencies
  Coupled bunch instabilities
  Especially the cavities
Broadband impedance sources
  Loss of Landau damping
Large impedance sources at high frequencies
  Microwave instabilities
From A. Lasheen Talk: PS beam injected into SPS : measurements & simulations

## Slide 3: Introduction to PS Impedance Model
Necessary to continue to build & maintain a longitudinal impedance model of the PS machine
Build CST models for Wakefield & Eigenmode simulations
  From CATIA files (when available), otherwise 2D drawings
Confirm Wakefield & Eigenmode simulations with measurement (when possible and required)
  RF measurements
  Beam based impedance measurements
Provide confirmed results for BLonD code
Identify objects whose impedance can be reduced

## Slide 4: Overview of Model Elements so Far
40 & 80 MHz Cavities
  CST Models of the bare cavities created
    No feedback system effects
    No HOM couplers or frequency tuners
10 MHz Cavity Model developed by G. Favia
Transmission Line Kickers
  CST Models of the KFA13, KFA21, KFA45, KFA71 & KFA79 created
    Compare longitudinal impedances to previous CST models (S. Persichelli, Transverse)
    Ferrite material from previous CST models (S. Persichelli, Transverse)
Baseline Magnet Unit Section
  CST models of the most common pumping manifold & bellows types
UHV Gate Valves
  10 Valves in the PS
  CST model (including internal mechanisms) created
    Model confirmed via EM measurements
PS Dump
  CST model of the two identical dumps currently in the machine
  Working with EN-STI on the replacement dump design to reduce its impedance*
*IWG #14 : https://indico.cern.ch/event/671318/

## Slide 5: 40/80 MHz Bare* Cavities: CST Models
*Note that the actual impedance seen by the beam is much lower, due to feedback systems
40 MHz cavity | Eigenmode | Measured
Res. Freq | 39.03 MHz | 40.06 MHz
Q | 25,795 | 13,352
R/Q | 33.7 | -
80 MHz cavity | Eigenmode | Measured
Res. Freq | 79.96 MHz | 80.11 MHz
Q | 37,246 | 19,300
R/Q | 57.4 | -
Source of :
Uncontrolled Emittance Blow Up
Notes: 40 MHz Cavity Measured by us on 040417
80 MHz Measured by CV (???) for tuner

## Slide 6: 40/80 MHz Cavities: Model Summary
Impedance performance is dominated by feedback systems
  Necessary to incorporate the effect of feedback systems
  CST Model is just one small part of the model
Options proposed for dealing with the feedback
  Model cavity together with feedback loops as was done with the PS 10 MHz cavity (presented by H. Damerau today)
  Obtain impedance of 80 MHz cavity using measurements of gap voltage instead of modeling the feedback loops
Geometry is starting point for the model
Shape of mechanical short is included
  Separate model of the mechanical short has been analyzed
Does not include tuners that adjust frequency
Does not include HOM dampers
  Explore how to implement this in Wakefield Simulations
Notes: Impedance seen is defined by feedbacks around cavities NOT GEOMETRICAL STRUCTURE
Feedback systems are narrow band, around 80 MHz

## Slide 7: Transmission Line Kickers
CST models built from old drawings and CATIA
KFA13, 21, 71 & 79 all contain identical modules
  KFA13 & KFA21 are identical units
Important step would be to measure at least one module to benchmark simulations
8C11 Ferrite
  Using ABP provided definition*
  Ferrite sample to be characterized
Module
*https://impedance.web.cern.ch/impedance/PS.htm

## Slide 8: Transmission Line Kicker Models
KFA79
KFA13 & KFA21
KFA71
KFA45

## Slide 9: KFA45: Models
Previous Impedance Model
New Longitudinal Impedance Model

## Slide 10: KFA45: Comparing Wakefield Simulation Results
Source of :
Loss of Landau Damping
Probable Source of Emittance Blow Up
Notes: Show abs or (real & imaginary)…check with Alex

## Slide 11: Vacuum Elements of MU Sections (100 Total)
Downstream Assembly
Upstream Assembly Types (99):
Standard (67)
Enlarged (25)
‘Exotic’ Variations (7)
  Wide, special, etc.
Pumping Manifold Slot (99):
Pickup Assembly
  Standard (40)
  Large (12)
Group Pumping Coupling (8)
Actuator of SEM Grid Detector (3)
Cover/Empty (36)
Pumping Manifold: Internal Downstream Assy. (29)
Pumping Manifold Types (100):
Internal (29) & External (37)
Enlarged Internal (10) & External (8)
Remainder (16) are ‘exotic’ variations
  Wide, Narrow etc.
Standard Upstream Assembly (67)
Beam
Top View of MU 49
Equipment Owner to Confirm/Provide:
Accuracy of models (number of bellow convolutions, etc.)
Complete/detailed models (integration model only)
Number of elements (vacuum report)
Notes: Std. Upstream Assembly (P-0m0401 / ST0371940)
Std. Int. Downstream Assy (P-00407 / ST0371891)
MSG 48-52-54 (ST0520401_01 ) Actuator of SEM Grid Detector
*MU62 Has an Enamelled Upstream Flange DN273 instead of a Upstream Assy. (bellow)
•MU41 has no slot for pickup ( Downstream Compensator Assy/ ST0516001 )

## Slide 12: Impedance of Baseline MU Section
Standard Upstream Assembly (67)
Standard Internal Downstream Assy. (29)
Sources of :
Loss of Landau Damping
Possible Emittance Blow Up
Microwave Instability
Notes: Std. Upstream Assembly (P-0m0401 / ST0371940)
Std. Int. Downstream Assy (P-00407 / ST0371891)
1.6 GHz => Bunch Length of PS (ns????)
Imaginary Z /n (n=freq/revolution freq (470KHz (?))
*MU62 Has an Enamelled Upstream Flange DN273 instead of a Upstream Assy. (bellow)

## Slide 13: UHV Gate Valve: CST Models
Previous Impedance Model
New Longitudinal Impedance Model
10 Valves total
No internal model available
  Not included in previous model
  Proprietary
  Drawn using datasheet
  Measurements necessary
Source of :
Microwave Instability

## Slide 14: UHV Gate Valve: Measurement Setup
Measured using probe method
Setup closed at both ends
  Traps travelling wave modes
  TE11p
Investigated resonances at
  1.2 GHz, 1.34 GHz & 1.5 GHz
Notes: VAT UHV Gate Valve Series 108 Order No. 10844-Xe44-BIH1 DN 160 Flange X Dimensional Drawing 544734

## Slide 15: UHV Gate Valve: Comparing Measurement & Simulation Results
TE111
TE112
TE113
TE116
TE116
1345.67 MHz
Q: 1442
TE117
TE111
1207.04 MHz
Q: 2352
TE115
TE118
Cavity Mode
TM010
1504.18
Q: 1184
TE119
TE114

## Slide 16: Preliminary PS Dump Model
Installed in straight sections 47 & 48
Main problem modes are ‘Coax Cavity’-like
Simplified moveable dump
Moveable
Dump
PS
Beam Pipe
Actuator
Beam
Source of :
Emittance Blow Up
Microwave Instability
Notes: CONCERNS: LENGTH OF ACTUATOR ELECTRICAL CONNECTION

## Slide 17: ‘Coax Cavity’-like Modes
626 MHz
811 MHz
150 MHz
Eigenmode Solver: Front View
Beam
Beam
Beam

## Slide 18: Path Forward
Cavities
  Implementing the effects of the feedback systems
  HOM Couplers
  Validation with measurements
Kickers
  Measure 8C11 Sample
    Ferrite measurement script in development
    8C11 samples to be machined
  If available, attempt to measure individual kicker modules
Straight (SD) & Magnet (MU) Sections
  Begin to model beam instrumentation devices (pickups, BPMs)
  Confirm counts of passive elements
PS Dump
  Confirm length of actuator & electric connection
  Add realistic material definitions to the moveable dump
  New PS dump design is in progress (EN-STI)
    Current replacement design is a higher impedance contributor than the current design

## Slide 19: Further Elements to add
Complete survey of straight sections (SD)
20 MHz & 200 MHz Cavities
Septa
Remaining Kickers
  KFA4 & KFA28
Beam instrumentation
  Wall current monitors
  Wire scanners
  Pick-ups
Vacuum elements
  Flanges, bellows, transitions
  Vacuum report, such as in the SPS, or similar document
Notes:   Wideband PU (SD90 & SD94)
  Sensitive Pick-ups (SD83 & SD93)
  Position Sensitive Wall current monitors (PSWCM) (SD00)
  Wall Current Monitors (WCM) (SD03 & SD95)
  Wire Scanners

## Slide 20: Summary
Cavities are most obvious candidates for admittance blow up
  Large impedance values
  Reduction via feedbacks (H. Damerau talk)
Other sources of impedances
  Kickers’ resonances at low frequency
Future elements need to be impedance analyzed & reduced when possible
  Example: New beam dump design
Wideband impedance sources (Kickers)
  Reductions in Landau damping
Microwave instabilities
  Gate valves
  Pumping manifolds in magnet unit (MU) sections
Maintenance of impedance model

## Slide 21: Supplemental Slides

## Slide 22: Wakefield Simulation of the Closed Mechanical Short
Mode at 1.49 GHz
Notes: Cutoff of TM01 a=73 mm => 1.572 GHz (Simple Cav Model)
Cutoff of TM01 a=103 mm => 1.114 GHz (Simplified bellow inner Radius)
1.491 GHz, for cut off of TM01 => a =76.96 mm

## Slide 23: KFA79: Models
New Longitudinal Impedance Model
Previous Impedance Model

## Slide 24: KFA79: Comparing Wakefield Simulation Results

## Slide 25: Comparing KFA79 to KFA13
Inline modules produce a ‘forest’ of resonances (KFA13)
Inline modules seem to allow additional modes to build up along beam path
  I.E. Higher coupling between modules
KFA79
KFA13

## Slide 26: KFA71: Preliminary Wakefield Simulation Results
Preliminary Wakefield Results
  Need to run longer wakelength to further resolve peaks
Notes: 400 meter wakelength, decays down to -8.75 dB
2.370 meter long structure

## Slide 27: UHV Gate Valve: TM010 Cavity Mode in the Valve
 | Eigenmode Simulation | Wakefield Simulation | Measured
Res. Freq | 1.503 GHz | 1.496 GHz | 1.504 GHz
Q | 1294 | 1206 | 1184
R Shunt | 39.0k Ohm | 36.2k Ohm | -