## Slide 1
Assembling FGD

## Slide 2
First step: extrusion of bars
-1- the central y-hole and the reflective coating
can be part of the extrusion process
-2- the x-holes and z-holes can then be pierced
in the bars directly with precision.
Second step : cutting the cubes
-3- the cubes can then be produced by
(precision) cutting of the cubes from the bar
-4- we end up with cubes with four reflective faces,
three holes, and precise dimension in y direction.
I - Production of minicubes
-1-
-2-
-3-
-4-

## Slide 3
I - Production of overall frame and reflective sheets
the bottom carbon fiber frame has no holes
the top plate have all the future holes to feed the WLS fibers
a 60 cm steel rod is inserted in each hole
Intermediate reflective plate similarly (to be drilled all together).
They are identical and contain 200x180 =36000 holes

## Slide 4
by inserting steel rods in the holes we obtain a ‘fakir board’ with 180x2000 = 36000 pins
of adjustable length (by moving the distance between the boards).
we set them first to 1cm …..

## Slide 5
by inserting steel rods in the holes we obtain a ‘fakir board’ with 180x130 = 23400 pins
of adjustable length (by moving the distance between the boards).
we set them first to 1cm …. and
insert the first line of cubes e.g. in z
insert the WLS through the z holes
repeat over the first plane and insert the y WLS

## Slide 6
and then lay the reflective layer (aluminized mylar few 10s of microns)
Then push the rods up by 1cm and repeat the operation.

## Slide 7
Conclusions
I think we can find ways to assemble superFGD in one piece which use the ‘natural’ tolerances
by placing the cubes in such a way that the vertical direction has small errors
(few microns per cube) and cubes are held together by the top down pressure.
The tolerances of the cubes are largely sufficient to ensure that if they are aligned
plane by plane on rods, there will be no problem inserting the WLS in the horizontal plane.
The final vertical WLS will come in place from the construction principle.
The process requires fabrication of several layers of carbon fiber or reflector (mylar)
with 23000 holes in them, and the use of the same number of rods.
If we can 3D-print the detector this is obviously more practical, although the requirements
on holding «blocs» of ~10 kg (25x25x25cm^3=15.5kg) are much more severe:
the inertia of such masses can easily damage the fibers – a cube of 1 gramme cannot.