## Slide 1: High efficiency power source development activities in CERN
Jinchi Cai, Igor Syratchev
On behalf of HEIKA team

## Slide 2: Outline
HE Klystron and code ‘KlyC’
FCC Klystron development
X-box Klystron upgrade
Other collaborations

## Slide 3
9.3 M Euro
10.7 M Euro
Excessive electricity bill, M Euro
1 year
Efficiency, %
FCC e+e- at 50 Euro/MWh and 5000 hours/year:
Efficiency impact on operation cost
High efficiency! How high it could/should be!?
Pulsed, 0.7 GHz,
92 MW
37 MW, more than twice the overall RF cryogenic power needs
100 MW

## Slide 4: Mechanism and concepts
Velocity modulated
with small input power [Pin]
Density modulated
Bunch circuit
Output power ~ Pin x 103~6
Glossary: Saturation, velocity congregation, Radial stratification
CSM tube: η=78%
Input cavity
Gain cavity
Higher harmonic cavities
Penultimate cavity
Output cavity
Single cylindrical beam
coupler

## Slide 5: High Efficiency International Klystron Activity lead by CERN
COM method
CSM method
Partitioning analysis and massive optimizations are necessary!
Recommended by industry
Optimised at CERN
Kladistron
Notes: COM method:
Using core oscillation to collect the peripherals

## Slide 6: Available Simulation tools
Disk model: AJDISK,Klys4.5,Dev5,Klypwin
Discrete model: Tesla, KlyC
PIC:FCI,MAFIA,CST PIC, Magic, GDFIDL, Vorpal (+?)
Free access for the klystron community.
Efficiency, much faster (~1/100) simulation than PIC
Precision, 2D simulation are supported (‘frozen’ beam)
Diversity, possible extension to other Klystron’s topologies (Multi-gap, Multi-beam, Traveling wave structure etc…)
Flexibility, full adapted for special needs (partitioning, bunched beam generation etc.) and versatile output data interface.
Of all of them only AJDisk is a non-commercial product.
Klyc1D/2D potentials:
Notes: A tool is needed to simulate a Klystron

## Slide 7: KlyC Graphical User Interface
EM 2D
Import
Gaussian profile

## Slide 8: Eff. Optimizer in KlyC
Global: genetic algorithm
Local: pattern search
Example:125kV, 80A, S
S band, perv.=1.9
3 days for optimization
45%
67%

## Slide 9: Outline
HE Klystron and code ‘KlyC’
FCC Klystron development
X-box Klystron upgrade
Other collaborations

## Slide 10: FCC e+e-: 0.8GHz,133.9kV×12.5A×80%>1.3MW
KlyC output graphics

## Slide 11
Klystron’s Power gain curves and bandwidth (KlyC).
145 kV
134 kV
120 kV
110 kV
100 kV
In saturation
134kV
In saturation
4 MHz
Tube operation at miss-matched RF load

## Slide 12: Benchmark with PIC code
Efficiency=80%@KlyC1.5D; 80% @Magic 2D and 79% @CST 3D
Time cost=20min@KlyC1.5D; 12 h @Magic 2D and 50h @CST 3D

## Slide 13
MAGIC (0.07T) 2D, 79.4%
FCC#6. KlyC2D vs MAGIC
MAGIC (20T) 2D, 79.6%
The radial bunch ‘expansion’ in output cavity (MAGIC2D) practically does not affect efficiency. This validates KlyC2D as an attractive (and fast) tool.
Nz=256,Nr=4, =79.9%,Tcpu= 20 min
Tcpu = 4000 min (~1ooo ns)
Beam settings:
Saturation=97%
Nz=128,Nr=4
Convergent analysis

## Slide 14
Fully saturated bunch
Optimised congregation
Linear congregation
Stratified bunch with linear congregation
88.70%
90.1%
84.20%
FCC CSM tube
80.1%
Power conversion efficiency. Limiting factors.
82.6%
CST MWS
Sabre effect and Ohmic
Benchmark with CST for the same bunch quality
Notes: Mention zening’s name

## Slide 15: Outline
HE Klystron and code ‘KlyC’
FCC Klystron development
X-box Klystron upgrade
Other collaborations

## Slide 16: Toshiba E37113
FCI simulation results, test saturation efficiency~43%
Large beam aperture to accommodate large current
Efficiency upgrade to 60% by just changing the circuit design
Y. Okubo, et al. Development of an X-band 6MW Pulsed Klystron

## Slide 17: Efficiency upgrading
Recommended by industry
Optimised at CERN
Congregation study
60%?
ultimate efficiency constrained by space charge effect
Y.Okubo, et al. Status of high efficiency Klystron development in TETD (COM&BAC)
X band–relatively large beam aperture-low coupling coefficient(M~0.5)
Bunching difficulty
extraction difficulty
RF breakdown
Ohmic loss

## Slide 18: Design process
1D with ‘artificial’ output cavity(M=0.9): 73%
2D with ‘artificial’ output cavity—64%
Scale and opt.
Check
2D with real output cavity—48%
Opt.
2D with real output cavity(M=0.5): 54%
Emax>200MV/m
Enhance the efficiency while decreasing the peak electric field by multi-cell
Weak coupling so multi-modes are coupled with each other
Single mode theory can’t be used any more!

## Slide 19: Coupling mode theory implanted into KlyC
Cell1 and cell3 coupled with cell2
𝜅 matrix can be calculated by coupling adjacent cells
 | F1 | F2 | F3
Coupled theory | 11.7704+0.0406j | 12.0114+0.1308j | 12.1735+0.0364j
HFSS eig. | 11.7710+0.0377j | 12.0051+0.1325j | 12.1722+0.0378j
CST MWS | 11.77111+0.0382j | 12.00470+0.1325j | 12.17316+0.0376j
3cell structures in previous slide
mono.
congr.

## Slide 20: Design with coupled cell structure
62% efficiency design in KlyC
Eff.=
Modulation process
Velocity varation

## Slide 21: CST 3D PIC verification
Phase space movie in CST
KlyC reference
60.5% efficiency with Bz=2.5Br=0.36
~100MV/m
Benchmarked!
Field distribution
Beam dynamics
Energy distribution

## Slide 22: Performance evaluation
>50MHz
Next step to improve the performance
Sacrifice the high gain to broaden the bandwidth
Larger gap or tapered structure to decrease the maximum electric field(~100MV/m)
Sensitivity analysis to make the tube more robust and reliable
optimize Bz for the tradeoff between clearance and efficiency

## Slide 23: Outline
HE Klystron and code ‘KlyC’
FCC Klystron development
X-box Klystron upgrade
Other collaborations

## Slide 24
FCC h+h- /LHC:
0.4GHz,54kV×9A×72%~0.35MW (Pin=80W)

## Slide 25
ESS:
0.704GHz,110kV×15.272A×75%~1.3MW (Pin=90W)
Output eff.
Eff=75.8%

## Slide 26: Thales tube TH2180
comparison between KlyC measurements. Simulation have been done by company

## Slide 27: Conclusion & Outlook
The 1.5D computer code KlyC is a new and reliable tool for the klystron optimization. It is available in the public domain. Number of institutions, Labs and industries are using it now.
The new klystron bunching technologies have been developed at CERN within HEIKA collaboration. They have been successfully applied for the design of different klystrons ensuring that developed tubes have reached their ultimate performance.
Recommended by industry
Optimised at CERN
1.4
1.6
FCC Lband 1.3MW
ESS Lband 1.3MW
LHC UHF 0.35MW
Xbox Xband 8.5MW

## Slide 28
Thanks for your attention!
Acknowledgment
Authors would like to all the contributors for their feedback for the benchmark of KlyC and design results
MAGIC PIC
Scan QR code for More benchmark work done
Notes: 75% ESS tube 110kV,16.84A; 70% LHC tube 54kV,9A