## Slide 1: X-Band RF Test Stands at CERN
Jan Paszkiewicz on behalf of the Xbox group
SINAP, Shanghai, 4-8 June 2018

## Slide 2: Compact Linear Collider
Linear e+e- collider for precision particle physics measurements.
Staged implementation up to 3 TeV.
Linear due to synchrotron losses.
100 MV/m accelerating gradient for high energy with reasonable machine length.

## Slide 3: RF Accelerating Structures
X-band (11.994 GHz RF)
Traveling wave: RF pulse passes through the structure.
Accelerating gradient (energy gain of particles) = 100 MV/m
Peak surface field ≥ 200 MV/m, depends on design.
High fields require high power: 40 - 50 MW without beam.
CLIC BDR requirement: ≤ 3x10-7 bpp/m to limit losses of luminosity.
Wakefield damping due to beam dynamics requirements.

## Slide 4: Test Stands at CERN
Xbox 1: 50 MW klystron, 50 Hz, connection with CLEAR (e- linac)
Xbox 2: 50 MW klystron, 50 Hz
Xbox 3: 4x6 MW klystrons, 400 Hz, 4 structure test slots
Sbox: 43 MW klystron, 25 Hz, S-band (2.9985 GHz)

## Slide 5: Generating High RF Power
Modulators
Pulse Compressors
Klystrons

## Slide 6: Xbox 2 Block Diagram
50 MW klystron
1 kW solid state amplifier
Pulse compressor
Structure under test
RF Load
Directional couplers

## Slide 7: Xbox 3 Block Diagram
6 MW klystron
300 W solid state amplifier
Hybrid coupler
Pulse compressor
Structure under test
RF Load
Directional couplers

## Slide 8: Structure Diagnostics Overview
Device under test
RF Load
Incident Power
Reflected Power
Transmitted Power
Ion gauge readout
Ion gauge readout
60 dB directional coupler
Upstream Faraday cup signal
Downstream Faraday cup signal
RF In From Pulse Compressor
WR90 Waveguide
Input coupler
Output coupler
Beam-pipe
Beam-pipe
Radiation Monitor

## Slide 9: Structure Diagnostics Overview

## Slide 10: Breakdown
Transmitted RF Pulse
Incident RF Pulse
Beam Axis

## Slide 11: Breakdown
Incident RF Pulse
Reflected RF Pulse
Beam Axis
Breakdown
Emitted Current

## Slide 12: Breakdown Diagnostics
BD position resolved using timing of RF pulses.
Low group velocity (~0.02c), 65 ns filling time: very high time resolution not needed.
Vacuum

## Slide 13: Breakdown Phase
Change in reflected channel
Change in incident channel: indicates reflected RF has made a round trip. Phase sampled here.

## Slide 14: Conditioning Procedure
Algorithm controls power based on current BDR (based on last 360000 pulses).
Typically reach 110 MV/m accelerating gradient.
Increase pulse length in steps when gradient target reached. (50 , 100, 150, 200 ns)
Conditioning history of TD26CCN3 in Xbox 2
Conditioning algorithm
Pulse length increased when target gradient reached.
Reduction in BDR during flat run
Ramping of gradient by algorithm

## Slide 15: Conditioning of Different Structures
The conditioning curve can differ from the ‘ideal’ one due to constraints such as:
Limited available power
Vacuum level of other line
Radiation limits
Breakdowns in test stand itself (esp. pulse compressors)
Large breakdown clusters

## Slide 16: Conditioning Comparison – Normalised Gradient
BDR dependence on field in TD26CCN3 structure in Xbox 2. (Thomas Lucas)
Gradient, BDR and pulse width summarised using normalised gradient.
Based on empirical relationship between E, BDR and τ.
Higher normalised gradient = low BDR at high field and long pulse length, ie. well-conditioned.

## Slide 17: Persistence of Conditioning State
3 structures have been moved from one line to another so far to continue conditioning at higher power. During moving, the structures are exposed to air for several hours.
In each case, the structure needs some time to re-condition but it is significantly faster than the first time.
Both the PSI structures also spent some amount of time at reduced power due to external factors – normalised gradient did not increase significantly in this period.
T24 PSI 1
T24 PSI 2
TD24 SiC 2
Slow conditioning
Slow conditioning

## Slide 18: Breakdown Locations: T24 PSI 1
Xbox 3D
Xbox 2
Time

## Slide 19: Breakdown Locations: T24 PSI 1
Xbox 3D
Xbox 2
Time
Likely to be artifacts, not real structure BDs.

## Slide 20: Breakdown Locations: T24 PSI 2
Xbox 3D
Xbox 2
Time

## Slide 21: Breakdown Locations: T24 PSI 2
Xbox 3D
Xbox 2
Time
Most BDs in this phase occurred outside the structure

## Slide 22: Breakdown Locations: TD24 SiC 2
Xbox 3C
Xbox 3D
Time

## Slide 23: Breakdown Locations: TD24 SiC 2
Xbox 3C
Xbox 3D
Time
Likely to be artifacts.
Structure detuned: phase advance no longer 120 °

## Slide 24: Breakdown Clustering
T24PSI 1 in Xbox 2
Similar average slope (breakdown rate) but instantaneous BDR is either very high or very low.

## Slide 25: BDR Statistics: T24PSI1 in Xbox 2
BDR in histogram obtained using a Gaussian window with σ = 50000 pulses. BDR window for conditioning algorithm is 360000 pulses. An IIR window is essential for high dynamic range.
Gradient
Norm. Gradient
Pulse length
BDR
Each point = 30 BDs

## Slide 26: BDR Statistics: T24PSI2 in Xbox 2
Each point = 30 BDs
Gradient
Norm. Gradient
Pulse length
BDR

## Slide 27: BDR statistics: TD26CCN3
Each point = 30 BDs
Gradient
Norm. Gradient
Pulse length
BDR

## Slide 28: Conclusions
6 X-band testing slots available at CERN.
Main diagnostics are RF signals, Faraday cups, and vacuum levels.
High gradients achieved: maximum of 119 MV/m in T24 PSI 1.
Structures retain their conditioning state after venting and moving.
Breakdowns occur in the whole structure but tend to focus at the beginning towards the end of the conditioning process.
Strong clustering of BDs in time was observed in the T24 PSI 1 but not the TD26CCN3 – more analysis to be done as data becomes available.

## Slide 29: Thank you!
Questions?

## Slide 30: Comparison of BDR windows

## Slide 31: Structure Final Performance