## Slide 1: Research on wakefield suppression of two bunch operation mode in X-band disk-loaded accelerating structure
Xiaoxia Huang, Wencheng Fang
Shanghai Institute of Applied Physics, Chinese Academy of Sciences

## Slide 2: Outline
Tentative idea of two bunches
Wakefield suppression
Position analysis of the second bunch
Feasibility of several bunches

## Slide 3: Tentative idea of two bunches
Single bunch operation mode – 50Hz
Demand of Ten Beam lines
Beam Instability, Wakefield Suppression
SXFEL
Demand of 20 Beam lines - 100 Hz
Demand of 20 Beam lines
Two bunches operation mode – 50Hz

## Slide 4: Tentative idea of two bunches
Waveguide Damped Structure:
good wakefield suppression
complex Structure

## Slide 5: Tentative idea of two bunches
Gaussian detuning:
When the frequencies of the lowest two-pole field mode of the accelerating structure are Gaussian distribution, the time domain of the wakefield exhibits Gaussian attenuation.
The larger σf in frequency domain, the faster of Gaussian attenuation in time domain.
Rebound phenomenon:
Limited number of cells in accelerating structure
Two bunch:
Second bunch put in valley
Second Bunch
Detuned Structure
Similar to disk-loaded structure

## Slide 6: Tentative idea of two bunches
Disk-loaded Structure:
simple
constant-gradient
Transverse Wakefield
constant-impedance
constant-gradient
special design disk-loaded structure
realize two bunch operation mode

## Slide 7: Wakefield function vs. ABCI
L = 10.497 mm, a = 3.775 mm, b = 10.585 mm, t = 1.5 mm
Valid square:
s/L<0.15, 0.34<a/L< 0.69, 0.54<g/L< 0.89
Infinity Period
Unrelated with σ

## Slide 8: Wakefield suppression vs. Cell
Multipole fields
Similar
Example of CLIC damped structure
i=1
i=(N+1)/2
i=N

## Slide 9: Wakefield suppression vs. Frequency
Assuming that the impedance of each cell is the same with different frequency
Assuming that the Density of frequency is the Gaussian distribution
Wakefield vs. Frequency
Impedance vs. Frequency
f0 = 15.5 GHz
Bigger σf , Stronger suppression
More the number of frequency N, Rebound more late and more bunches can be placed

## Slide 10: Frequency of dipole mode
Fundamental frequency - 11424 MHz
Simulation b in the case of different a and t
Lowest frequency of dipole mode
Under the condition of the same fundamental frequency
L = 8.7475 mm, phase advance = 120 degree

## Slide 11: Model-1: Frequency vs. cells
Assuming that the number of cells is N, the frequency is Gaussian distribution

## Slide 12: Gaussian distribution - 1
N=20, Δf=0.2GHz, f0=16GHz,
σf = 60

## Slide 13: Gaussian distribution - 2

## Slide 14: Model-2: Gaussian Density
De
Cell vs. Frequency
N cells and f1 - fN :
De(fi)*(fi+1-fi) is the same
Sizes of all cells

## Slide 15: Example
σf = 500 MHz, f0 = 16.2 GHz, fmax-fmin = 2 GHz
f1 : f9 = 15.2 GHz : 0.25 GHz : 17.2 GHz
n(f1)=1, n(f2)=3, n(f3)=5, n(f4)=7, n(f5)=8, n(f6)=7, n(f7)=5, n(f8)=3, n(f9)=1 N=40

## Slide 16: Second bunch position
s = 0.284 m
s = 0.375 m
Second bunch
s = 0.4986 m = 19 λ
s ≠ int * λ

## Slide 17: Several bunches
Further Work
Second bunch
s = 0.4986 m = 19 λ
Third bunch
s = 0.9972 m = 38 λ

## Slide 18
Thanks for your attention!