## Slide 1: Injection steering studies in the PS
E.Senes, V.Forte, A.Huschauer, F.Tecker
LIU PS Beam Dynamics working group
02.11.2017
Acknowledgement: F. Asvesta, G.P. di Giovanni, A. Oeftiger

## Slide 2: Outline
Goal and methods
Emittance measurements
First simulations
Space charge contribution (?)

## Slide 3: Goal and method
Goal: understand whether the steering is a source of emittance growth at the injection in the PS
Idea: from the optimal steering situation, randomly change the injection kicker strength of KFA45 and observe the emittance growth.
Kick strength: 90% to 106% of the nominal kick (due to power converter limitations)
Beam types (only first bunch injected)
Beam | Intensity (1010 ppb) | εx / εy (mm mrad) | Brightness index
BCMS | 78 | 1.4/1.2 | 60
INDIV | 13 | 1.75/0.75 | 10.4
INDIV_HI_HE | 26 | 2.6/1.8 | 11.2
Notes: BCMS in different working points and with different coupling condition

## Slide 4: Analytitcal expectation for missteering
Injecting a beam offcenter in the phase space leads to emittance growth after the filamentation occurs
At the kicker location
The emittance blowup can be estimated using the following
V. Kain, CAS Erice

## Slide 5: Analytitcal expectation for missteering
Injecting a beam offcenter in the phase space leads to emittance growth after the filamentation occurs
At the kicker location
The emittance blowup can be estimated using the following
!
The analytic formula assumes that the two planes are completely decoupled
Notes: So working out the red formula one expects eps = eps0 + beta/2 * kick^2

## Slide 6: One word about the emittance calculation
Δp/p of the beams used is small, e.g. < 0.85e-4 (BCMS)
Dispersive component deconvolution do not impact significantly on the emittance measurement
Usual measurements setup:
  H: BWS65, V: BWS85
  C185, 15m/s
  Measured twiss parameters are used (see appendix)
  The dispersive component has not been subtracted

## Slide 7: BCMS beam
Nominal settings: linear coupling is exploited (clone of the operational beam)
Expected a parameter is β/2:
KFA45: β/2 = 11.26 (MADx model)
Notes: So good news
We are optimised in the nominal injection
Bad news:
- The model is more complicated

## Slide 8: BCMS beam
Correcting coupling: skew quads are used to compensate the linear coupling

## Slide 9: INDIV beam
Clone of the operational INDIV beam

## Slide 10: INDIV_HI_HE beam
Modified INDIV beam in the PSB with higher emittance and intensity than INDIV

## Slide 11: First simulations results
pyHeadTail have been used to simulate the injection oscillations. For the moment no coupling is implemented
Parameters: similar BCMS beam
Intensity = 80*1010 protons
εx = 1.5 *10-6 um / εy = 1.3 *10-6 um
Initial kick = 1 mrad
Filamentation takes ~100 turns

## Slide 12: First simulations results
Simulation bechmarking is still in progress
Nominal BCMS beam
Analytical expectation for decoupled motion
Measured
β/2 ~ 3.6
Analytical expectation
β/2 ~ 11.26
Simulation
β/2 ~ 18 (expected 8)
Notes: Simulation good in shape, but too steep !  under investigation

## Slide 13: Space charge induced tune shift
For all the measurements the maximum tune shift has been computed
BCMS like beams:
BCMS beams
INDIV beam
Notes: High brigthness  linear

## Slide 14: INDIV_HI_HE beam (again)
Modified INDIV beam in the PSB with higher emittance and intensity than INDIV
Tune footprint is smaller (0.07, 0.08),
Useful to disentangle the effects

## Slide 15: Summary
KFA45 was used to test the contribution of the injection missteering to the emittance blowup
For nominal operations the injection seems to be optimised in most cases
Simulation work have just been started. The next step is include coupling.
Disentangling the effects is the key point:
  Small tune footprint beams
  Measuring and simulating coupling
The precision in the emittance measurement is the key issue when it comes to talk about tune shift, the new measurement paradigm should help a lot in that sense

## Slide 16: Spares

## Slide 17: Emittance calculation
Used Guido’s dispersive component deconvolution function
The used twiss parameters are the measured one (Vincenzo’s presentation last meeting)
BCMS operational conditions
From H. Bartosik et al.
at MD days 2017

## Slide 18: BCMS changing the working point