## Slide 1
Stefan Ulmer
RIKEN
Fundamental Symmetries Lab
2018 / 01 / 15
PRECISION TRAPS

## Slide 2: Outline
Motivation and Introduction
Trapping of Charged Particles
Basic Methods
Antiproton Measurements in Penning traps
  Charge – to – Mass Ratios
  Magnetic Moments

## Slide 3: Fundamental Physics in 2018
Relativistic quantum field theories of the standard model describe a plethora of particle physics phenomena
!!! At the same time, the Standard Model is the biggest success and the greatest frustration of modern physics !!!
The Standard Model is not just a list of particles and a classification - it is a theory that makes detailed, precise quantitative predictions!
g / 2 = 1.001 159 652 180 73 (28)

## Slide 4: Beyond Standard Model Physics
Standard model is incomplete
  contains 19 free parameters which need to be tuned by experiments
observations beyond the SM
  neutrino oscillations
  dark matter
  energy content of the universe
  several fine-tuning problems
  origin of lepton helicity
  absence of antimatter in the universe:
  known Standard Model CP violation produces one baryon in 1018 photons observed CMBR density: one baryon in 109 photons
so at least we know, that we know quite a lot about almost nothing
what’s next?
how can we produce input to solve at least some of the problems?

## Slide 5: How to solve problems in physics?
Prominent and rather fruitful strategy:
  Investigate very well understood, simple systems and look of unexpected deviations.
Example: Hydrogen
Basic models
Bohr / Schroedinger
Relativistic models
Dirac
HFS – coupling and nuclear
effect
Pauli / Bloch etc.
QED effects
Asymmetric WI-effects
Bethe / Schwinger
1
10-4
10-7
10-4 to 10-11
!!! A single particle in a trap is one of the simplest systems you can think of !!!

## Slide 6: How to trap charged particles…
Maxwell equations:
Harmonic potential:
++
Earnshaw theorem: Not possible to trap particles in static electric fields.
Nobel prize in 1989
Dynamic approach: Paul Trap
Static approach: Penning Trap
Physics idea: Oscillating rf-fields drive particles back to center – time average attractive (particle ping/pong)
Physics idea: counteract the radial saddle-potential by superimposing a strong magnetic field
Natural consequence: both trap-types have stability issues…

## Slide 7: Paul Trap vs. Penning Trap
Cheap
Variable
Open access
Noisy
Micromotion
Expensive
Constrained
Closed system
STABILITY
Controlability
Reliability
Use Paul trap once you’re interested in physics properties which are defined by internal interactions in composed charged systems.
Use the Penning trap for ultra-high precision studies or experiments dealing with complex many particle systems.
Prominent in fundamental studies
Prominent in quantum information

## Slide 8: Traps in Antimatter Physics
The Penning trap is the “work-horse” of the antimatter physics community.
First paper on trapped antiprotons
Trap as a container for positrons and antiprotons to produce antihydrogen (see lectures by Testera and Yamazaki)
Trap as an instrument to study the fundamental properties of trapped antiparticles (this lecture / Smorra lecture).
This entire field of physics would likely NOT EXIST without traps!

## Slide 9: Trap Results in Antimatter Physics
Two collaborations dealing with single particles in traps – ATRAP and BASE
??? What is behind all that ???
  (A)TRAP pioneered fundamental experimental methods.
  BASE enhanced fractional precision of these experiments.

## Slide 10: Penning Trap
single particle in a trap: simplest superimposed static magnetic and static electric fields result in three fully decoupled harmonic single-particle oscillators.
Superimpose the simplest electrostatic potential you can think of
radial confinement of charged particles by a constant magnetic field
B
results in three harmonic oscillator modes
axial mode
modified cyclotron mode
magnetron mode

## Slide 11: The Invariance Theorem
The three trap frequencies can be combined to a robust invariance relation
misalignment of B-axis and E-axis cancels out
ellipticities of trap potential cancel out
tilted trap
potential
B2 and B1
image charge
image current
shift in B1
contaminants
drifts B(t)
Single particles in Penning traps give direct access to the fundamental properties of trapped particles
Precise frequency measurements in traps provide information about fundamental properties of trapped particles.

## Slide 12: Different Perspective: Fundamental Symmetries
Within the framework of classical physics, a single particle in a Penning trap is a well understood, very simple system (three harmonic oscillators).
Penning traps thus provide perfect boundary conditions to test exotic theories and search for physics beyond the Standard Model.
How would a yet undiscovered physics effect look like?
Whatever it is:
Need to ask the right questions
System 1
System 2
A precision trap is an artificial, highly modular, extremely exotic atom

## Slide 13: Interaction Potentials – Minimal SME
Physics: such interactions can e.g. be induced by CPT-odd dark matter couplings
Example: Standard Model Extension
Inspired by string theory translated to SM via effective field theory
Idea of construction: Consider all possible low dimension bi-linears within the Poincare group (useful but not fundamental).
Dirac equation
CPT-odd modifications
++
++
Pseudo-magnetic field, with different coupling between matter and antimatter
Measurements:
coefficients can be constrained by searching for diurnal variations in comagnetometer measurements.
comparisons of particle/antiparticle magnetic moments in traps

## Slide 14: Interaction Potentials – Non-Minimal SME
these types of interactions can only be uncovered by explicit measurements on antimatter
Yukawa picture:
Stationary Yukawa potential:
Effective interaction length:
Potentially sensitive to exchange bosons, exclusively coupling to antimatter.
Potentially sensitive to heavy exchange bosons at strong interaction strenghts.
Complementary approach to HEP

## Slide 15: The Penning Trap – Key Techniques

## Slide 16: Blueprint Measurements in Penning traps
Cyclotron Motion
Larmor Precession
Determinations of the q/m ratio and g-factor reduce to measurements of frequency ratios -> in principle very simple experiments –> full control, (almost) no theoretical corrections required.
g: mag. Moment in units of
nuclear magneton
S. Ulmer, A. Mooser et al. PRL 106, 253001 (2011)
S. Ulmer, A. Mooser et al. PRL 107, 103002 (2011)
simple
difficult

## Slide 17: Non Destructive Particle Detection (see Smorra lecture)
Idea: Oscillating particle induces image currents in trap electrodes.
What are we dealing with?
Image current detection:
  Requires detection systems with high sensitivity
  Non destructive – long observation times – precise information about trapped particle
  Real time observation of particle manipulation
Q=30000
10-16 A/mm
single charge

## Slide 18: Example: Resistive Cooling and Peak Detection
Power dissipated in detection resistor
Particle is cooled resistively

## Slide 19: The Continuous Stern-Gerlach Effect
Energy of magnetic dipole in magnetic field
Leading order magnetic field
correction
This term adds a spin dependent quadratic axial potential -> Axial frequency becomes function of spin state
Measurement based on continuous Stern Gerlach effect.
Frequency Measurement
Spin is detected and analyzed via an axial frequency measurement
S. Ulmer, A. Mooser et al. PRL 106, 253001 (2011)
Single Penning trap method is limited to the p.p.m. level

## Slide 20: The Penning Trap – Ingredients

## Slide 21: Some basic homework
Typical ingredients of Penning trap experiments
  Stable and homogeneous superconducting solenoid
  Precisely machined trap electrodes
  RF electronics
  Ultra stable power supplies
  Most of the high-precision experiments are operated under cryogenic conditions.
  Cryogenic operation -> good vacuum
Centre of a good magnet
Paramter | Value
dB/dt | < 10-11/h
B1 | < mT/m (NMR shimming limit)
B2 | < 0.5 T/m2 (NMR shimming limit)
HCI experiment at University of Mainz
Sturm / Blaum / Quint / Werth
Supplies-rack of CERN’s BASE experiment
Ulmer / Mooser / Smorra

## Slide 22: Cylindrical Trap Design
Degrees of freedom for defined radius:
1.) Length of ring electrode
2.) Length of correction electrode
3.) Compensation/Ring voltage
1.) C4 = 0
2.) C6 = 0
3.) orthogonality
easy to understand / simple to optimize / easy to machine

## Slide 23: Particle Loading – Matter (here protons)
In-trap creation by bombarding an appropriate target with an electron beam

## Slide 24: Particle Loading - Antiprotons
25 GeV/c protons
3.5 GeV/c antiprotons
5.3 MeV antiprotons
-> Degrader -> 1keV
Particles in the trap, what’s next?

## Slide 25: Electron Cooling / Electron Kickout
Idea: Store antiprotons and electrons in the same trap volume
Coulomb interaction -> electrons cool fast due to cyclotron radiation
Obtain a cold cloud of antiprotons
Get rid of electrons…
Cold particles in the trap, what’s next?

## Slide 26: Preparation of a Single Particle
Single particle extraction by trap potential manipulation:
C. Smorra, Int. Journ. Mass. Spec (2015)
Evaporation:

## Slide 27: Sideband Coupling/Cooling
Application of a quadrupolar drive at sum or difference frequency of two involved modes:
Rotating wave approximation
Diagonalization
important coupling
practically applied by injecting rf on segmented, rf-blocked electrodes
coupled
system
coherent TRACELESS system at complex eigenvalues

## Slide 28: Examples: Sideband Coupling
Effectively: Amplitude modulation of particle motion
Classical “Dressed states”
also useful for efficient cooling of radial modes
widely used to measure temperature of the radial modes.
practically nothing
else but
the FFT of an
amplitude
modulated signal
S. Ulmer et al. Phys. Rev. Lett 107, 130005 (2011)

## Slide 29: Temperature in Sideband Cooling
Sideband cooling -> dynamics in quantum states and cooling dynamics stops if n+,-=nz
Cooling Limit:

## Slide 30: EXPERIMENTS – Charge to Mass Ratios

## Slide 31: Results of proton/antiproton mass comparisons
Limitations of 1995 measurement and last factor of 10 improvement?
[G. Gabrielse et al., PRL 82, 3198 (1999)]
Progress ???
Historical measurements for current antimatter physics program
[J. Harrington et al., XXX XX, (201X)]<

## Slide 32
Slightly inhomogeneous magnetic field.
Offset potentials on the electrodes of the cryogenic trap.
Change of polarity leads to position shift of the particle.
Systematic uncertainties due to the particle position are large (~10-9)
For protons (polarity inversion (dV=10V)) much larger as for H- ions (dV=0.005V).
to H- ion => reduces to antiproton to proton charge-to-mass ratio
Magnetic field cancels out!
Rtheo = 1.001 089 218 754 2(2)
Why would we want to use a hydrogen ion rather than a proton

## Slide 33: Measurement
Measurement cycle is triggered by the antiproton injection into the AD
One BASE charge-to-mass ratio measurement is by 50 times faster than
achieved in previous proton/antiproton measurements.
AD cycle
First high-precision mass spectrometer which applies this fast shuttling technique

## Slide 34: BASE Measurements – Proton to Antiproton Q/M
Result of 6500 proton/antiproton Q/M comparisons:
S. Ulmer et al., Nature 524 196 (2015)
Rexp,c = 1.001 089 218 755 (64) (26)
Most precise test of CPT invariance with Baryons.
Consistent with CPT invariance
Constrain of the gravitational anomaly for antiprotons:
8.7
Our 69ppt result sets
a new upper limit of

## Slide 35: Example: Resolution Limit in BASE
Sideband based magnetic field measurements:
Sideband measurement in presence of a magnetic field inhomogeneity
Sideband measurement in homogeneous magnetic field, in presence of running accelerator
Sideband measurement using a self shielding solenoid
??? Physics understood ???
Further improvement by direct measurement methods

## Slide 36: EXPERIMENTS – Magnetic Moments

## Slide 37: Magnetic Moment Measurements
Energy of magnetic dipole in magnetic field
Leading order magnetic field
correction
This term adds a spin dependent quadratic axial potential -> Axial frequency becomes function of spin state
- Very difficult for the proton/antiproton system.
- Most extreme magnetic conditions ever applied to single particle.
Measurement based on continuous Stern Gerlach effect.
Frequency Measurement
Spin is detected and analyzed via an axial frequency measurement
S. Ulmer, A. Mooser et al. PRL 106, 253001 (2011)
Single Penning trap method is limited to the p.p.m. level

## Slide 38: 0.8 p.p.m. Measurement
single particle in the magnetic bottle
measurement
  Measure cyclotron frequency
  Measure Larmor frequency
  Measure cyclotron frequency
evaluate g-factor
repeated the scheme in total six times
co-magnetometer measurement
task: resolve these two «cut» frequencies

## Slide 39: Result and Limitations
noise driven random walk in the magnetron mode traces magnetic field.
Result
from six independent g-factor measurements
Ultimately limits g-factor measurement to the 1 p.p.m. to 0.1 p.p.m. level
250 kHz
250 Hz

## Slide 40: Can we do better ?
probably, by putting a lot of effort in we would be able to reach with the single-trap method the 0.1 p.p.m. - level.
apply alternative measurement schemes: multi-trap methods

## Slide 41: «Simplest»: The Double Penning-Trap Method
inhomogeneous magnetic field for spin state analysis
homogeneous magnetic field for frequency measurements
comparison
single-trap method
multi-trap method
!!! measured !!!
!!! measured !!!

## Slide 42: The Double Penning-Trap Method
Initialize the spin state
1.) measure cyclotron
2.) drive spin transition at
analyze the spin state
measures spin flip probability as a function of the drive frequency in the homogeneous magnetic field of the precision trap
spin flipped in PT
no spin-flip in PT
particle transport

## Slide 43: Challenges – High-Fidelity Single Spin-Flip Resolution
this is the game changer...
...where all the work is in...
SSF not resolved
SSF resolved
To conclude in which quantum state the particle leaves / returns from precision trap, the double trap method requires high-fidelity spin-state resolution
p.p.m.
p.p.b.
resolving single antiproton spin flips is a challenge

## Slide 44: Challenges – High-Fidelity Single Spin-Flip Resolution
Physics
  heating by rf at a noise density of about drive radial cyclotron quantum transitions.
  transition rates scale with the cyclotron quantum number.
cold particle (50mK)
hot particle (1K)
high-fidelity spin state resolution
fidelity at 65%, not useful for measurements
observation of antiproton spin transitions with high-fidelity requires ultra-cold particles

## Slide 45: Sub-Thermal Cooling
Cold particle is prepared by resistive cooling in the PT
thermalize particle (6 min.)
Analyze temperature using the magnetic bottle
particle below threshold -> MEASURE
particle above threshold
particles with single spin-flip resolution are in this temperature range
works (see BASE-Mainz measurements), but sub-thermal cooling is EXTREMELY time consuming
NOTE: each cyclotron frequency measurement heats the particle to about 300K
12 min.

## Slide 46: Current Time Budget of a (CERN) Double-Trap Experiment
Chart: 
| spin analysis | frequency measurements | transport | sub-thermal cooling | maintenance
measurement budget | 9.6 | 12 | 1.2 | 144 | 8
COOLING
transport
frequency measurements
spin analysis
maintenance
Cooling is a problem
requires new ideas
multi-trap multi-particle methods
This talk
Sympathetic cooling of protons and antiprotons
MOOSER

## Slide 47: BASE Two-Particle Method
Idea: divide measurement to two particles
«cold» cyclotron particle to flip and analyze the spin- eigenstate
«hot» cyclotron particle which probes the magnetic field in the precision trap
pay: measure with two particles at different mode energies
win: 60% of time usually used for sub-thermal cooling useable for measurements
challenges:
  transport without heating
  more challenging systematics

## Slide 48: The Magnetic Moment of the Antiproton
first measurement more precise for antimatter than for matter...
...so how about the proton magnetic moment?
G. Schneider et al., Science 358, 1081 (2017)
C. Smorra et al., Nature 550, 371 (2017)

## Slide 49
Thanks very much for your attention

## Slide 50: Phase Sensitive Methods I
prepare a coherent cyclotron state with well-defined phase:
Direct measurement of cyclotron frequency (more stable)
BUT: Systematic error (special relativity, B2) ~ r+2 !
wait for certain evolution time
Apply sideband pi-pulse and couple cyclotron energy to axial mode, which conserves the phase
...thus, imprints cyclotron phase to axial phase
Measure for different evolution times and unwrap phase.
D. Pritchard, J Thompson, S. Rainville, E.Cornell, E. Myers, M. Redshaw,…..many papers

## Slide 51: P’n’A - Method
Solution: Phase-conserving parametric amplification
Pulse
Nothing
Amplify
28Si13+
dΓ/ Γ ~ 4 10-11
E.g. applied in recently published most precise measurement of the electron mass.
[S. Sturm et al., PRA 87, 030501 (2013)]

## Slide 52: Phase Sensitive Axial Detection
Idea: Instead of frequency measurement – measurement of phase relative to locked drive
Measured in 1s per trial.
[S. Ulmer et al., PhD Thesis (2011)]

## Slide 53: Sympathetic Cooling
Idea:
  Laser-cool 9Be+ ion(s)
  Design a trap for resonant coupling
  Energy exchange
«Laser-cooled» antiprotons (mK-cooling within ms) !!! -> Higher precision, specifically in magnetic moment measurements.
[C. Ospelkaus Group, PTB Braunschweig]

## Slide 54: Coupled Oscillators
Two charged particles trapped in direct vicinity interact via coulomb interaction.
Effective Energy Exchange
Static
Dynamic
Resonant Coupling:
0.5s/mm3
[C. Ospelkaus Group, PTB Braunschweig]

## Slide 55: Proton Spin Quantum Transitions
A. Mooser, K. Franke, S. Ulmer et al. Phys. Rev. Lett. 723, 78 (2013)
Improvement of apparatus, trap wiring, quality of detection systems (lower noise, faster measuring cycles).
Based on Bayesian filter -> fidelity of > 90% achieved

## Slide 56: Frequency Shifts in Penning Traps
Particles in imperfect Penning traps -> Anharmonic Oscillators
This can be one of the considerable limitations in frequency ratio measurements !
e.g. a not considered offset potential (50mV) and adjustment of resonance voltage shifts ratio (p/pbar comparison) by already 30ppt!

## Slide 57: Trap Tuning
Adjust voltages of correction electrodes to make the trap harmonic.
Allows for trap tuning to mV.

## Slide 58: Additional Frequency Shifts
What else modifies the result of your precision experiment?
Effective potential of the induced image charge
  Modification of the quadrupolar potential
  Correction of the invariance theorem
Modifies cyclotron frequency at level of 1e-10
  Strong scaling with trap radius.
  Typical traps (1cm diameter) ->

## Slide 59: QUESTION
In a perfect Penning trap
- Homogeneous magnetic field
- Perfect electric quadrupole
- large trap (no image charge shift)
Any additional frequency shift?

## Slide 60: Resolution Limits
Dip measurements are limited to a certain precision
  Line width
  Signal-to-noise ratio
  Averaging time
  Voltage drifts and scatter
scatters
scatters
scatters

## Slide 61: Direct Measurements
Measurement of cyclotron frequency with cyclotron resonator
[G. Gabrielse et al., PRA 82, 3198 (1999)]
Problem: Cyclotron detectors are not very sensitive (small inductance) -> considerable frequency shifts due to large particle energy.
[J. Harrington et al., XXX XX, (201X)]<