## Slide 1: Electron Cooling
Gerard tranquille
Be-be-ea

## Slide 2: Electron Cooling (an introduction)
What
Why?
Basic theory of electron cooling
Electron cooling hardware
Diagnostics

## Slide 3: What is electron cooling?
A fast process to shrink the size, divergence and energy spread of a stored charged particle beam without the loss of intensity.
  Phase-space compression.
Proposed by G. Budker in 1966.
First demonstration on the NAP-M ring in Novosibirsk.

## Slide 4: Why electron cooling?
Loss free compression of ion beams
  Accumulation of rare species of charged particles
  Luminosity increase for colliding beam experiments
  Smaller spot sizes for fixed-target experiments
  High resolution experiments with internal targets
Compensation of beam heating effects
  Intrabeam, residual gas and internal target scattering
Electron target for precision experiments e.g. recombination

## Slide 5: Electron cooling theory
To cool a stored ion beam with electrons a monochromatic electron beam is overlapped with the ion beam in a straight section of the ring.
The velocity of the electrons is made to match the average velocity of the ion beam.
In the rest frame of the electrons the ions are seen as passing through the electron gas with a variety of velocities
The ions transfer their energy to the electrons through Coulomb scattering.
The electrons are continuously renewed -> heat exchanger

## Slide 6
Two gases of different
temperatures T1 an T2
tend to an equilibrium
temperature T3
As the electron beam is
continuously renewed, the
ion beam temperature tends
to the electron beam temperature.
The velocity spread is reduced
by a factor (m/M)1/2
Analogy with the mixing of gases

## Slide 7: The cooling force
Consider a single electron-ion collision in the electron beam rest frame.
The ion moves with a velocity Vi* and scatters from the electron at impact parameter b.
The momentum transfer is:
c being the Coulomb force

## Slide 8
As we consider times from negative to positive infinity we can neglect the longitudinal part of the force and we can replace the Coulomb force with the transverse component
The energy transferred from the ion to the electron is

## Slide 9
So far we have only considered a single electron-ion collision.
When an ion passes through a large number of electrons, we have to integrate over all possible impact parameters to obtain the energy lost as it travels a length dx through an electron cloud of density ne*.
Logarithmic ration of maximal to minimal impact parameters is called the
Coulomb logarithm

## Slide 10
Minimum impact parameter is determined by the maximum momentum transfer to the electron (head-on collision):
Using the classical electron radius we obtain:
In a system of charged particles the Coulomb field is shielded and falls off exponentially at the Debye radius
The Deybe radius is usually smaller than the electron beam radius. If not the latter is taken as the maximum impact parameter

## Slide 11
We can finally write the cooling force as:

## Slide 12: Cooling rate (time)
The rate of velocity change at which the ion is slowed down in the electron gas can be written as:
Using the following relations:
The friction rate can be expressed as:

## Slide 13
The inverse of the friction rate is defined as the cooling time.
Inserting we obtain
To get the cooling time in the laboratory frame we note that ne = gne* , hence
where h is the ratio of the cooling length to the ring circumference

## Slide 14
We have considered electrons has being stationary. However, they have a finite temperature Te and hence a velocity distribution f(Ve) which can be considered to be Maxwellian characterised by its velocity spread Δe.
To account for this we have to replace the ion velocity with the ion-electron velocity difference and average over the electron velocity distribution.
The expression for the frictional force becomes:

## Slide 15
For an electron beam with a rectangular velocity distribution the cooling force is shown below

## Slide 16
For a Maxwellian velocity distribution the cooling force has to be evaluated numerically.
However a good approximation is:

## Slide 17
Using this approximation the cooling time in the laboratory frame can be written as:
In general the electron temperature Te is independent of the beam energy and hence De is a constant of the device.
We can distinguish two domains of cooling:
Cooling of hot beams
  Cooling time is proportional to
Cooling of “warm” beams
  Cooling time practically independent of Vi* since De is constant
  t is independent of ion beam intensity

## Slide 18: Equilibrium
Ideally cooling will continue until the ion beam temperature reaches the electron beam temperature
and
Resulting in an ion divergence and momentum spread
In practice heating effects will prevent us from reaching this regime

## Slide 19: Digression on ion beam and storage ring properties
Beam emittance: The volume of phase space occupied by the beam
6-dimensional space generated by the transverse and longitudinal coordinates and their derivatives
(x,x’,y,y’,E(z),j(Dp/p))
Projections in the 3 dimensions define the transverse and longitudinal emittances.
x = be x’ = ge r = D

## Slide 20: How to build an electron cooler
Source: cathode
Beam transport: solenoids, steering magnets
Beam dump: collector
Acceleration system: electron gun
Vacuum, diagnostics

## Slide 21: The electron gun
Electrons are produced in an electron gun where they are accelerated electrostatically to the desired energy.
A thermionic cathode is heated resistively to 1000°C and electrons are emitted from the surface.
Electrons are emitted from the cathode in all directions because of their thermal energy.
Due to space-charge, an electron cloud is formed just in front of the cathode.
Electrons are extracted from this cloud and accelerated to required energy by a series of electrodes.
Cathodes are normally oxide-coated and indirectly heated by a filament.
BaO (or a mixture with SrO and CaO) is the most common used oxide due to its low work function.
Modern cathodes are also doped with chemicals or compounds of metals with a low work function which form a metal layer on the surface to emit more electrons.
The lifetime of these cathodes is determined by the purity of the cathode materials.
The heater consists of a fine wire or ribbon, made of a high resistance metal alloy like nichrome, similar to the heating element in a toaster but finer. It runs through the centre of the cathode, often being coiled on tiny insulating supports or bent into hairpin-like shapes to give enough surface area to produce the required heat. Typical heaters have a ceramic coating on the wire.

## Slide 22
The cathode is surrounded by the Pierce shield, an electrode on cathode potential shaped to produce perpendicular potential lines to the beam axis.
Special attention must be paid to the design of the subsequent accelerating electrodes to keep the field lines perpendicular.
The final electron current follows Child’s law:
r is called the perveance and is essentially determined by the ratio of the beam radius r0 and the cathode-anode distance d.
The electron gun is embedded in a longitudinal field to avoid the electrons being lost.
Transverse motion of the electrons are transformed into spirals about the magnetic lines with the cyclotron frequency and radius

## Slide 23
Two types of gun have been used on electron coolers:
  Resonant-optic gun
  Adiabatic gun
Resonant-optic guns require the magnetic field to be matched with the spiral length of the electrons i.e. the time the electrons need to pass through the acceleration column is equal to a multiple n of the inverse of the cyclotron frequency.
Resulting in the length of the accelerating column

## Slide 24
An adiabatic gun works at a fixed value of the magnetic field regardless of the electron energy.

## Slide 25
1. 14mm convex cathode
2. Control electrode (modifies density distribution and intensity)
3. Pierce electrode
4. Grid electrode (fixes the intensity)

## Slide 26: Electron beam transport
After the gun, the electrons enter a drift region where they are transported to the interaction section where the cooling of the circulating ion beam takes place.
In the drift region the electric potential lines are parallel to the electron trajectories with increasing space going from the centre to the edge of the beam. The radial behaviour of the electric field is described by the potential of a homogeneous charge distribution with sharp boundaries.
Substituting for and

## Slide 27
The change of electric potential across the electron beam has two consequences:
A radial electron velocity distribution of a parabolic form
ExB situation leading to an azimuthal drift of the electron beam with velocity:

## Slide 28
The magnetically confined electrons are bent into the interaction region with a curved solenoid or toroid.
An additional dipole field is required to compensate the centrifugal force experienced by the electrons.
The properties of the magnetic field are important to guarantee a good cooling efficiency of the ion beam and to ensure that the electron beam is not heated. In the cooling region the angle between the magnetic field lines and the ion beam should be small compared to the average transverse temperature of the electron beam.

## Slide 29
ELENA cooler magnetic system components
Main cooler solenoid
Gun solenoid
Collector solenoid
Expansion solenoid
Squeeze coil at collector
2 x Toroid section consisting of
9 racetrack coils each
Various corrector coils to
ensure good field quality
Orbit correctors
Solenoid compensators

## Slide 30
Chart: Longitudinal position (mm)
| -350 | -300 | -250 | -200 | -150 | -100 | -50 | 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350
measured | -0.58118 | 0.070344 | 0.28598 | 0.36748 | 0.3777 | 0.4134 | 0.4353 | 0.44868 | 0.42631 | 0.39448 | 0.35504 | 0.33754 | 0.38004 | 0.57763 | 1.1748
shimmed | -0.40464 | 0.022613 | 0.049936 | 0.020613 | 0.035099 | 0.035117 | 0.060528 | 0.12478 | 0.086499 | 0.065349 | 0.092895 | 0.060358 | 0.0087784 | 0.027406 | 0.30631
Chart: Longitudinal position (mm)
| -350 | -300 | -250 | -200 | -150 | -100 | -50 | 0 | 50 | 100 | 150 | 200 | 250 | 300 | 350
measured | 0.53099 | 0.55805 | 0.54959 | 0.53111 | 0.50764 | 0.4871 | 0.46406 | 0.44495 | 0.4335 | 0.43375 | 0.44026 | 0.446 | 0.45292 | 0.46519 | 0.47962
shimmed | 0.2855 | 0.29487 | 0.30889 | 0.31384 | 0.33527 | 0.35243 | 0.34424 | 0.33488 | 0.32478 | 0.33279 | 0.35858 | 0.34496 | 0.33733 | 0.29873 | 0.25328

## Slide 31: The cooling section
Have to match velocities, position and angle

## Slide 32: Electron beam collector
Reduce the power of the electron beam to the lowest possible value.
Capture the electrons with maximum efficiency.
Electrons are decelerated in the collector. The remaining power is dissipated on the collector surface.
Deceleration is done in two steps to avoid the formation of a virtual cathode at the collector entrance
Secondary electrons emitted from the collector surface or reflected electrons can bounce back and forth between the gun and collector and be lost on the vacuum chamber. Careful design and the use of the magnetic field can improve the collection efficiency

## Slide 33
Suppressor electrode slows down the primary electrons at the collector entrance.
Magnetic field is reduced to spread out the electrons on the collector surface.
Surface on which the electrons are collected is water cooled.

## Slide 35: Vacuum system
Electron coolers operate under ultra-high vacuum conditions (<10-10 Torr).
Main outgassing comes from:
  Hot cathode
  Collector
  Electron loss on the vacuum chamber
Cooler must be bakeable.
Differential pumping system between gun/collector and cooling section.
Careful choice of vacuum chamber material (316LN stainless steel, avoid trapped volumes).
NEG coating of the vacuum chamber for increased pumping.

## Slide 37: Additional effects to improve cooling
Flattened electron beam distribution
  After acceleration in the gun the longitudinal velocity spread is compressed giving a smaller longitudinal temperature
Magnetised electron cooling
  Electrons make many rotations enhancing the exchange of energy
Beam expansion
  Reduction of the electron transverse temperature
Electrostatic bend in the toroids
  ExB field for full compensation of the excitation of reflected electrons in the vertical B field of the toroid

## Slide 38: Electrostatic bend
Electrons experience a centrifugal force in the toroid.
This drift can be compensated by an additional magnetic field in the opposite direction.
Reflected and secondary electrons however are excited by this field and can oscillate between the gun and collector before being lost.
Complete compensation is obtained by superimposing an electric field on the magnetic field

## Slide 39: Beam expansion
Needed for:
  Adapting the electron beam size to the injected beam size for optimum cooling.
  Reducing the magnetic field in the toroids, thus reducing the closed orbit distortion.
  Reducing the transverse thermal temperature of the electron beam.
Bo=0.235T, B=0.075T, ro=14mm => r=24.8mm
Bo=0.235T, B=0.075T, Eo=100meV => E=32meV

## Slide 40: Effects of the cooler on the circulating beam
Deflection of the circulating beam due to the vertical field in the toroid.
Tune shift due to the focusing effect of the electron beam.
The solenoidal field of the cooler twists the ion beam by an angle:
Effect is negligible unless working close to a resonance

## Slide 44: Electron coolers at CERN
LEIR
Ee up to 6.5 keV
Ie = 600 mA
k = 3, r = 14 to 25mm
B (in cooling section) = 750 G

## Slide 45
AD
Ee up to 35 keV
Ie = 2.5 A
B = 600 G
40 years old!

## Slide 46
ELENA
Compact cooler
Ee up to 355 eV
Ie = 5m A
k = 10, r = 8 to 25mm
B (in cooling section) = 100 G
Being commissioned