## Slide 1: Beam diagnostics (Non-destructive methods)

## Slide 2: Demand for beam diagnostics
Essential for any accelerator
‘Organ of sense’
Deal with real beam with imperfections
Three categories
  Reliable, quick measurements for general functionality, e.g. current transformer
  For a daily check of performance and stability, e.g. profile determination
  Complex instrumentation, e.g. Emittance measurement
P. Forck, Lecture Notes on Beam Instrumentation and Diagnostics, Joint University Accelerator School, January – March 2012
Notes: Reliable, quick measurements to determine the basic parameters of a machine setting used as a fast check of the general functionality
Instrumentation built for a daily check of performance and stability, or for the control of wanted parameter changes in the accelerator setting.
Complex instrumentation for the commissioning of a new accelerator component, for the
development of higher performance and for solving more serious problems in case of a malfunction.

## Slide 3: Beam Position Monitoring

## Slide 4: Electrostatic BPM
-
-
-
-
-
+
+
+
+
+
-
+
+
+
-
-
+
-
+
+
-
-
+
-
-
+
+
-
+
-
-
-
-
-
-
-
+
+
+
+
-
+
+
+
-
-
+
-
+
+
-
-
+
-
+
-
-
-
-
-
-
-
+
+
+
+
-
+
+
+
-
-
+
-
+
+
-
-
+
-
-
+
+
-
+
-
V
-
-
-
-
-
-
-
-
+
+
+
+
+
-
-
+
-
+
-
+
-
+
-
-
-
-
+
+
+
-
+
+
-
+
-
-
+
-
+
-
-
-
-
-
+
+
+
-
+
+
-
-
+
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
courtesy O.R. Jones
R

## Slide 5: Beam Position Monitor Principle
d
The BPM principle is based on symmetry
  The beam displacement d is detected by a pair of symmetrical arrange electrodes
  BUT: Hoops, wait a minute, not so fast… What happens if the beam / bunch intensity changes?!
    The -signal still contains beam intensity information!
    Need to “normalize” the -signal
courtesy O.R. Jones
=
–

## Slide 6: “Shoe-box” BPM
ground guards
without
with
Split-plane (“shoe-box”) BPM with ground-guards
  Improved sensitivity and reduced cross-talk
  Improved linearity
courtesy P. Kowina

## Slide 7: Spit-Plane BPM
Pros
  Linear position response
    No correction for non-linearities required, simple analog read-out electronics without post-processing
  high transfer impedance at low frequencies
    Good match for long bunches, low-β beam
    High signal levels, allows operation at low frequencies with high load impedance
Cons
  Complicated mechanics, requires sufficient real-estate
  High capacitive source impedance, reflective
  Eigenmodes at low frequencies, high beam coupling impedance
    Limited to low frequency operation, typically <300 MHz

## Slide 8: Button BPM Equivalent Circuit
Increase | Effect
Radiusbutton (larger area & Cbutton) | Higher signal level Lower resolution
Thicknessbutton (larger volume) | Lower wake impedance Lower resolution, higher weight
Widthgap (more trapped modes) | Higher resolution Higher wake impedance
typically 50 Ω
courtesy M. Wendt

## Slide 9: Button BPM
Pros
  Robust simple construction, cost effective, minimum real-estate
    RF UHV feedthrough and button is a single element
Cons
  High-pass characteristic with high cut-off frequency
    Typically >= 500 MHz,
    bad match to operate with long bunches, or at low frequencies
  Capacitive source impedance, reflective
LHC Button BPM (CERN)

## Slide 10: Stripline or Directional Coupler BPM
+
+
+
+
+
Upstream Port (term.)
Downstream Port (term.)
Up
Down

## Slide 11: Stripline BPM
Pros
  Well defined, and high transfer impedance function
    For striplines with l >> w, TEM operation
    Can be “tuned” to match a dominant beam frequency
      Optimizing the length of the stripline
  Matched characteristic impedance with 50 Ω source
    Only for terminated ports
      Shorted downstream port: 0 Ω source, no directivity
    Reduced reflection effects between generator (stripline BPM) and read-out electronics!
  Directivity
    Separate beam position measurement of counter-rotating beams
      e.g. near the IP in a ring collider
Cons
  Complicated, fragile mechanics, high costs, requires sufficient real-estate
    More RF feedthroughts required, impedance control of the stripline, strip-electrode may require a support structure
Stripline BPM LHC (CERN)
Stripline BPM FLASH (DESY)

## Slide 12: Electro-Optic Beam Position Monitors
courtesy S. Gibson

## Slide 13: Beam Current Monitoring

## Slide 14: Current measurement
What is the beam current?
  In an accelerator the current is formed by N particles of charge state q per unit of time t or unit of length l and velocity β = v/c.
Measurement methods
  Faraday cup
  Wall current monitor
  Current transformer
  Cryogenic Current Comparator (CCC)
We can measure the beam through the electric and magnetic fields created by the beam.

## Slide 15: Beam transformer
Courtecy: W. Blokland

## Slide 16: Current Monitor Limitations

## Slide 17: Wall-Current Monitors
The image current accompany the beam current.
A voltage proportional to beam current can be measured across the resistors
Also the noise issue will limiting the resolution

## Slide 18: Cryogenic Current Comparator (CCC)
Non-destructive measurement device for low intensity beams (between 1 nA an 10 μA)
The CCC consists of:
  Cryogenic device
  SC pickup coil,
  High efficient SC shield,
  High performance SQUID
  measurement system.

## Slide 19: Beam profile Monitoring

## Slide 20: Measure the beam profile
Intercepting methods
  Scintillating screen
  Optical transition radiation (OTR)
  Wire scanner
  Scraper
Non intercepting methods
  Synchrotron radiation
  Laser wire
  Rest gas ionisation
  Beam induced fluorescence
  Gas jet beam profile monitor

## Slide 21: Synchrotron radiation
Charged particles emit electromagnetic radiation when accelerated
Synchrotron radiation: change of direction
Light is radiated only in the forward direction, tangent to the beam’s instantaneous circular path through a bend.
Credit: U. Iriso and F. P´erez, ALBA

## Slide 22: Synchrotron radiation
Synchrotron radiation is broad band.
Visible wavelength
  Optical component is easy to implement.
  diffraction limits the resolution at longer wavelengths when the beam is small
X-ray
  Better resolution
  Hard to form an image
    Pinhole camera
    Zone plates

## Slide 23: Laser wire
First ionization potential for H‐ ions is 0.75eV.
Photons with λ<1500nm can separate H‐ ion into free electron and neutral H.
The H‐ ion has no excited states so the electron is removed into the continuum.
Laser can be used to mark a portion of beam by neutralization.
Once a porton of the beam is marked, measurements can be made on the neutral beam, the removed electrons, or the reduced beam current with beam current transformer or BPM stripline.
T. Shea, Laser Diagnostics for H- beams, , Accelerator Beam diagnostics, USPAS 2009

## Slide 24: Laser wire scanner station @ SNS
Q‐switched Nd:YAG laser
l = 1.06 mm
frep = 30 Hz, Tw = 7 ns
Ep = 50 – 200 mJ
T. Shea, laser diagnostics, USPAS 2009

## Slide 25: Residual gas based Ionization Profile Monitor
Credit: P. Fork, GSI

## Slide 26: Residual gas image of a electron beam
E-Beam direction
Give you a one dimensional profile!
Secondary ions or electrons are collected.
Magnetic field are used to compensate the profile distortion by self space charge force or wake fields.
Secondary particles are collected by electronics or optical (scintillator plus MCP)

## Slide 27: Beam induced fluorescence (BIF)
Schematic drawing of the BIF-monitor as installed at GSI UNILAC. *
BIF detection principle - How the beam induced fluorescence light is imaged, intensified and detected.*
*Credit: GSI, http://www-bd.gsi.de/dokuwiki/doku.php

## Slide 28: IPM and BIF
The cross section for impact ionization and fluorescence dependent on the beam energy, residual gas species, and certain fluorescent wavelength.
BIF has longer integration time due to lower cross section and viewed at certain solid angle.
Might need gas injection using a leaking valve to increase the local pressure.
Normally N2 has higher cross section, other gases such as Ne, Ar has been used.
Using Supersonic gas jet！

## Slide 29: Motivation to use gas jet
Low temperature
High directional jet
Non-invasive or minimum-invasive
Not dependent on beam species, energy and intensity
No damage threshold
Not affect the vacuum very much

## Slide 30: Gas jet profile monitor in Cockcroft institute

## Slide 31: Gas jet beam profile monitor
Estimated jet property
Parameter | Value
Density | 2.5*1016 particle/m3
Thickness | 0.5 mm
Vertical size | 5 mm
Estimated integration time = 1 ms
MCP
Phosphor screen
Ionization
Ions extraction
Visible light

## Slide 32: Typical results at CI
size | Value
Xrms | 0.42
Yrms | 1.23
Xrms from residual | 1.01
Setting | Value
Energy | 3.75 keV
Current | ~5.0 mA
External field | 7.5 kV/m
Exposure | 70 ms

## Slide 33: Beam halo Monitoring

## Slide 34: Halo Formation and Negative Effects
Beam Halo has many negative effects
  Nuclear Activation of The Transport Channel
  Emittance Growth
  Emission of Secondary Electrons
  Increasing Noise in The Detectors
Causes of Beam Halo
Nonlinear forces due to space charge
Parametric resonances
Scattered Laser Light in Photo-cathodes:
Misalignment, Magnet error, noise
Notes: Beam halo is group of particles outside the beam core.
Beam halo can be caused by parametric resonances or nonlinear forces due to space charge [2], as well as field emission, light scattered on photo-cathodes, or by numerous other phenomena
It brings many negative effects such as emittance growth, emission of sencondary electrons and so on. Because of this negative effects, we want to avoid halo by study the phenomenon.
Experimentally, the challenge to measure faint halos is we need a method with high dynamic range about 10_5 or 10_6. people using image system to detect the halo using coronagraphy method, the mask usually is not adaptive when the beam core shape changes.
Today, we will introduce an adaptive mask method to measure halo using a device call DMD().

## Slide 35: Halo measurements with coronagraph
A coronagraph is a telescopic attachment designed specifically to block out the direct light from a star, so that nearby objects can be resolved without burning out the telescope's optics. Most coronagraphs are intended to view the corona of the Sun, The coronagraph was introduced in 1930 by the astronomer Bernard Lyot.
The simplest possible coronagraph is a simple lens or pinhole camera behind an appropriately aligned occulting disk that blocks direct sunlight; during a solar eclipse, the Moon acts as an occulting disk and any camera in the eclipse path may be operated as a coronagraph until the eclipse is over.
http://en.wikipedia.org/wiki/Coronagraph

## Slide 36: Coronagraph
*T. Mitsuhashi, EPAC 2004 and Faraday Cup Award presentation 2004
OSR halo monitor at KEK employing Lyot Coronograph*
LHC coronagraph
T.M. Mitsuhashi et al., IPAC’17, Copenhagen, Denmark
What if the beam core don’t have a regular shape?

## Slide 37: Digital Micro-mirror Device
Micro-mirror architecture:
120
*DLPTM Texas Instruments Inc.
Segment of DMD:
13.68 um

## Slide 38: Optics System and Image process
180 Frames
32 mm
900 Frames
32 mm
C.P. Welsch et al.,
Proc. SPIE (2007)
J. Egberts, et al.,
JINST 5P04010 (2010)
H. Zhang, et al.,
Phys. Rev. STAB 15 (2012)
B. Lomberg, et al.
Proc. IBIC (2013)

## Slide 39: Demonstration of Adaptive Masking on UMER
70
280
x
y
(a)
(b)
IQ
640
660
250
45
45
60
82.9%IQ
66.3%IQ
49.7%IQ
Quadrupole Current
32mm
Different Beam / Different Mask Shape
6mA beam

## Slide 40: Thank you for your attention

## Slide 41: Reference
Workshops, conference and schools
  BIW, IBIC
  DITANET, OPAC, USPAS, JUAS, JAS, CAS
J. Harasimowicz et al., Rev. Sci. Instr. 81 (10), 2010
H. Koziol, BEAM DIAGNOSTICS FOR ACCELERATORS
P. Forck, Lecture Notes on Beam Instrumentation and Diagnostics, Joint University Accelerator School, January – March 2012
U. Raich, Accelerator Beam Diagnostics, USPAS, Albuquerque NM, June 23-26, 2009
H. Zhang, PhD thesis, university of Maryland, 2014
E. Bravin, Transverse Profile Measurements, CAS on Beam Instrumentation 2018, Tuusula, Finland
C. Welsch, Beam Diagnostics, CIPAS, 2015
J. Harasimowicz, et al., PRSTAB, 15, 122801 (2012)
A. Peter, Intensity Measurements, CAS on Beam Instrumentation 2018, Tuusula, Finland
W. Blokland, beam current monitor, Accelerator Beam diagnostics, USPAS 2009
T. Shea, Laser Diagnostics for H- beams, , Accelerator Beam diagnostics, USPAS 2009
S. Gibson, Application of lasers in beam instrumentation, CAS on Beam Instrumentation 2018, Tuusula, Finland