## Slide 1
N-Tof Winter school
Zermatt, January 2018
Xavier Doligez
Institut de physique nucléaire d’Orsay
doligez@ipno.in2p3.fr
Nuclear Data &
Fission Nuclear Energy
From nuclear physic to energy prospective

## Slide 2
Introduction : preliminary remarks
Let’s be a little bit provocative !
« ADS : a solution to the waste problem »
« The advantage of the Th/U fuel cycle is the availability of Th (3 times more than U) »

## Slide 3
Introduction : preliminary remarks
Only two actinides present on earth : uranium and thorium
   Only one fissile material : 235U  UOx : 238U + 235U
  Only two options for nuclear fuel  MOx : 238U + Pu
N-Tof measurements  for uranium saving or waste management

## Slide 4
Outline:
Nuclear reactor physics 101
  Chain reaction and criticality
  Nuclear reactor technology
  Fuel evolution
Nuclear reactor models
  Neutron transport equation
  A two steps calculation
  Model precisions
Nuclear data Uncertainty Analysis
  Total Monte Carlo (TMC) Methods
  Perturbation theory
Natural uranium resources and waste production
  Radiotoxicity
  Waste management
  Uranium saving
Waste transmutation
  Fission products
  Minor actinides

## Slide 5
Nuclear reactor physics 101
Fission = between 2 and 3 neutrons + 200 MeV + 2 Fission Fragments
A nuclear reactor core = a place where a chain reaction take place
Mean generation time:
L~10-6 s

## Slide 6
Nuclear reactor physics 101
capture
capture
“Sterile” absorption
Leakage
“Sterile” absorption
Leakage
Mean generation time
L~10-6 s
Power release is constant over time
A critical chain reaction

## Slide 7
Nuclear reactor physics 101
The neutron multiplication factor : a way to quantify the chain reaction
Neutron reaction rate + neutron leakage
Neutron fission rate x number of neutron by fission
From neutron reaction cross section to reaction rate
neutron
Material :
Interaction probability on dx :
For neutrons per , the number of interaction over is :
: neutron flux
Reaction rate :
In reactor physics, the neutron flux is a volume quantity
   is not a current

## Slide 8
Nuclear reactor physics 101
The neutron multiplication factor : a way to quantify the chain reaction
Some obvious remarks :
 The criticality is not a function of the neutron flux (neither the reactor power)
The criticality is a time dependent quantity
 The criticality is a global quantity
There is no such thing as “Local criticality”
Characterization of materials ()
Characterization of the reactor geometry

## Slide 9
Criticality – slowing down and uranium enrichment
For neutrons, it’s a competition between fission and (capture + leakage)
Neutron cross section are obviously function of the kinematic energy

## Slide 10
Criticality – slowing down and uranium enrichment
Fission spectrum
No critical system are possible with uranium 238 !
Cross section ratio more favorable for criticality

## Slide 11
Slowing down by neutron moderation
Slowing down process is assured by scattering on light nucleus !

## Slide 12
Criticality – slowing down and uranium enrichment
Neutron cross section are obviously function of the kinematic energy

## Slide 13
Reactor technology
A compromise between the fuel fabrication and the reactor fabrication
  uranium enrichment technology vs reactor technolgy
Coolant | Gaz (Air, CO2) | Light water | Heavy (light) water | Light Water
Moderator | Graphite | Graphite | Heavy water | Light Water
Fuel | Natural uranium | Enriched uranium | Natural uranium | Enriched uranium
GEN I
Time
GEN II (PWR, BWR, CANDU)
EPR, AP1000, CANDU6
~ 2010
~ 1975
~ 1960
Based on the use of 235U
   Moderator = coolant

## Slide 14
Reactor presentation
81 % of the reactors in the world are Light Water Reactors (435 operational reactors )
  (Boiling Water Reactors or Pressurized Water Reactors)
205 fuel assemblies
xy side cut
xy side cut
264 fuel pins

## Slide 15
Reactor technology : towards future technology
  What about future reactors ?
   A sustainable use of the resources :
Coolant | Liquid sodium | Liquid lead | Gaz | Molten salts
Moderator |  |  |  | 
Fuel | Uranium + plutonium | Uranium + plutonium | Uranium + plutonium (ceramic) | Thorium + uranium (molten salt)
238U+n 239U 239Np 239Pu
Fertile
Fissile
232Th+n 233Th 233Pa 233U
Fertile
Fissile
Safer
Optimised waste production
Optimized resources consumption
As cheap as possible
Non proliferant
Paper reactors !
  No more moderation ! (see later)

## Slide 16
Neutron spectrum
Neutron spectrum is very dependent on reactor technology (and fuel ! )
Reaction rates :
Fuel evolution depends on the neutron spectrum

## Slide 17
Fuel evolution
Bateman’s equation
Again, Criticality (and neutron spectrum) does not depend on the neutron flux !
  The reactor thermal power gives you the neutron flux
PWR UOX @ 3.5%
Evolution of the criticality

## Slide 18
Fuel evolution
Bateman’s equation
Criticality (and neutron spectrum) does not depend on the neutron flux !
  The reactor thermal power gives you the neutron flux
Chart: Year of operation
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4
 | 1.2027 | 1.143 | 1.1195 | 1.0938 | 1.0718 | 1.0505 | 1.0299 | 1.0135 | 0.9946 | 0.97848 | 0.96197 | 0.94462 | 0.9295 | 0.91562 | 0.90099 | 0.88726 | 0.87394 | 0.86032 | 0.85025 | 0.83764 | 0.82645
Chart: Year of operation
| 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.6 | 1.8 | 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4
 | 1.2027 | 1.143 | 1.1195 | 1.0938 | 1.0718 | 1.0505 | 1.0299 | 1.0135 | 0.9946 | 0.97848 | 0.96197 | 0.94462 | 0.9295 | 0.91562 | 0.90099 | 0.88726 | 0.87394 | 0.86032 | 0.85025 | 0.83764 | 0.82645
 | 1.0843 | 1.0518 | 1.0313 | 1.0122 | 0.994 | 1.0843 | 1.0518 | 1.0313 | 1.0122 | 0.994 | 1.0843 | 1.0518 | 1.0313 | 1.0122 | 0.994 | 1.0843 | 1.0518 | 1.0313 | 1.0122
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0.8 | 1.3
 | 0.8 | 1.3
 | 0.8 | 1.3
Evolution of the criticality
Partial refueling allow a better use of the fuel

## Slide 19
Nuclear wastes
Heavy nuclei =
Uranium + Plutonium + Minor actinides
Fission products
At the beginning of operation there are only uranium and oxygen in the fuel
At the end of cycle (EOC), there are :
  fission products (function of the produced energy)
  Heavy nuclei (function of the good use of the fuel)
The more the fuel produces energy, the more it is radioactive !
 The cooling should be efficient especially on rector shut down phases

## Slide 20
Outline :
Take home messages :
  There is a compromise between the reactor technology and the fuel cycle technology
    Reactors fueled with natural uranium are possible
    No critical systems are possible with 238U only
      There is a need of fissile material
  During reactor operation, !
    The criticality is tuned constantly with neutron poison
PART II : Reactor models
  Neutron transport equation
  Deterministic vs stochastic methods
  Model precisions
Two main objectives :
- Prediction of the power deposit
- Prediction of reactions rates for fuel evolution
 Prediction of the neutron flux

## Slide 21
Boltzmann’s equation
3 variables for space
2 variables for direction
1 variable for energy
1 variable for time
7 dimensions ()
 introducing the neutron current
Main goal : predict the power deposit
   Predict the neutron flux as a function of space, direction and energy

## Slide 22
Boltzmann’s equation
7 dimensions ()
Main goal : predict the power deposit
   Predict the neutron flux as a function of space, direction and energy
 any neutron reaction induces a change for the neutron
3 variables for space
2 variables for direction
1 variable for energy
1 variable for time

## Slide 23
Boltzmann’s equation
3 variables for space
2 variables for direction
1 variable for energy
1 variable for time
7 dimensions ()
 scattering = a change in the angle, or in the energy
fission = production of new neutrons

## Slide 24
Boltzmann’s equation
3 variables for space
2 variables for direction
1 variable for energy
1 variable for time
7 dimensions ()
Slowing down
Fission production
Transport
External sources + Neutron decays from FF

## Slide 25
Stationary equation
No external sources
Adjustment of the fission production for steady state
Eigen value problem :
   If is a solution, is also a solution
   No relation between criticality and power
Few order of magnitude :
- Neutron energy range : from 25 meV to 20 MeV
> 20 000 bins
- Neutron mean free path : ~cm
- Reactor fuel pin : ~ 1 cm
- Reactor fuel assembly : ~ 20 cm
- Reactor core typical dimension : ~m
>109 bins for space (103 in each direction)
> 1000 bins for angle
Finite element method may solve this equation

## Slide 26
Boltzmann’s equation resolution : the stochastic way
With the use of Monte-Carlo methods, there are no approximations (almost…)
  - MCNP ; SERPENT
Source neutrons
Neutron range
Interaction (nucleus + reaction)
Fission : sample the number of emitted neutrons, their energy,…
Simulate the particle histories, a great number of time
No geometry discretization
No energy discretization
Question : In a critical system, when does the story ends ?
 Fissions end the story !
Initial neutron source :
(energy, position, direction)
Source propagation : recording fission location
Tallies are scored
Inactive cycles
Active cycles
Stories are not completely independent

## Slide 27
Boltzmann’s equation resolution : the stochastic way
With the use of Monte-Carlo methods, there are no approximations
Dumonteil E., Malvagi F., Zoia A., Mazzolo A., Artusio D., Dieudonné C., De Mulatier C., Particle clustering in Monte Carlo criticality simulations, Annals of Nuclear Energy, Volume 63, January 2014, Pages 612-618
z
N independant simulations
It is impossible to simulate a full core
At reasonable computer power
With the use of Monte-Carlo methods, there are no approximations (almost…)
  - MCNP ; SERPENT

## Slide 28
Cell calculation
Resolution of the time independant Boltzmann’s equation on a single assembly with reflective conditions
Core calculation
Diffusion equation resolution on a full core
Angle
Diffusion approximation
S
Energy
homogeneization
condensation
A two step simulations

## Slide 29
Multigroup Flux :
Multigroup cross section
Neutron spectrum
Microscopique cross-section
The condensation process
Hem… ? is unknown

## Slide 30
Reaction rate conservation
For each group g :
Same issue : is solution of the diffusion calculation
Approximation : ~
Cell calculation
Core calculation
The homogenization process

## Slide 31
Precision on reactor models : examples
How it is done in « real industrial life » ?
  Hundreds of calculations are needed at each fuel refueling
  Tens of years of industrial knowledge
    Two groups cross-sections libraries fitted
    Precision on
PWR
Fuel composition ?
Operation time = 1 years !
How it is done in « real research life » ?
  0 power mock-up reactors
    MCNP calculations with deterministic code comparison for nuclear uncertainty analysis
    Precision on
Prediction of the criticality of the first superPHENIX core = 2/360
Prediction of the criticality of the first VENUS-F core = 9/87

## Slide 32
Outline:
Take home messages :
  Resolving the transport equation is still a challenge
    No easy calculation scheme, even for the static resolution ( calculations)
    The evaluated nuclear data is strongly tuned to fit industrial feedback
  For industrial use, hundreds of calculations are needed at each refueling for
    Criticality
    Cycle length
    Safety coefficients
  Model approximations can lead to strong uncertainties
    - In evolution, the end of cycle composition is up to 10% biaised
PART III : Nuclear data uncertainties
  TMC method
  Perturbation theory
  Fuel evolution

## Slide 33
Total Monte Carlo method
A. Koning, D. Rockman, ANE 2008
Creation of a serie of evaluation
 Code TALYS (NRG)
Sampling among all those evaluations
N ENDF Files
N MCNP calculations
239Pu(n,f)
Chart: 
| 1.15246 | 1.1527293333333333 | 1.1529986666666665 | 1.1532679999999997 | 1.1535373333333341 | 1.1538066666666662 | 1.1540760000000001 | 1.154345333333336 | 1.1546146666666661 | 1.1548839999999991 | 1.1551533333333341 | 1.155422666666666
 | 2 | 2 | 2 | 4 | 7 | 8 | 12 | 10 | 16 | 15 | 11 | 4
k
Example : analysis of 239Pu nuclear data on SFR assembly calculations
ND
1,294.10-2
100 calculations

## Slide 34
Total Monte Carlo method
An other example : A PWR assembly with thorium fuel
ND Th-232 | ND U-233
1,05.10-2 | 6,12.10-2
uncertainty of approximately few %
Parameters are sampled to build different evaluations
  Each one is different from the other ()
  Not easy to understand
  Calculation needs are consequent

## Slide 35
Perturbation theory : a smart way to study uncertainties
Boltzmann’s equation
Adjoint equation
Picture taken from : Dos Santos N, Optimisation de l’approche de représentativité et de
transposition pour la conception neutronique de programmes expérimentaux dans les maquettes critiques, PhD thesis
On a physical point of view, the adjoint flux represents the total contribution in the neutron balance of a new neutron at position , energy and direction

## Slide 36
Coherence between perturbations and TMC
With all the different evaluation from TALYS, it is possible to built the correlation matrixes
Chart: Th-232 (capture)
 | Th-233 | U-233
Capture only | 0.0105 | 0.0045
Fission only | 0.0012 | 0.0544
Capture + fission | 0.012 | 0.0599
TMC | 0.01 | 0.06
Fission
Capture
Fission
Capture
Energy
Good agreement with the Total Monte Carlo only if the number of group is high enough !
 Low computational requirements

## Slide 37
Extended perturbation theory
Aufiero M., Bidaud A., Kotlyar D., Leppänen J., Palmiotti G., Salvatores M., Sen S., Shwageraus E., Fratoni M., New Approaches and Applications for Monte Carlo Perturbation Theory, M&C 2017, Jeju, Korea, April 16-20, 2017
Recent developments allows perturbation based on continuous energy functions
   computed with NJOY (with the ERRORR module)

## Slide 38
Evolution
During evolution, the coupling between neutron transport equation and Bateman’s equation is too strong to expect an easy application of the perturbation theory
TMC application : 1 fuel evolution calculation for each random cross section
Reminder :
  All other reaction rates are correlated to fission cross section

## Slide 39
Outline :
Take home messages :
  Tools exist to quantify the impact on new measurements on precisions
    Typical uncertainty for criticality induced to nuclear data ~ few %
      Much higher than model uncertainties
    Typical uncertainty for fuel evolution induced to nuclear data ~5%
       Lower (or same order of magnitude) than model uncertainties
PART III : Waste production and natural uranium consumption
  Waste definition
  Plutonium valorization
  For the following, a 10% uncertainty on inventory at reactor discharge is fully acceptable !

## Slide 40
Nuclear wastes vs valuable matter
“96 % of the nuclear spent fuel is reusable”
Wastes : « Radioactive wastes are radioactive matter which NO further utilization is planed » European legislation (2006)
U nat
U enr
-Fission Product
-100% U et Pu
-100% Np, Am, Cm
Open cycle : ex USA
U nat
U enr
-Fission Product
-0,1% U et Pu
-100% Np, Am, Cm
« Closed » cycle : ex France
Pu monorecycling
U & Pu
BOC
EOC

## Slide 41
Radiotoxicity : a way to quantify the impact of nuclear wastes
Time in year
Radiotoxicity (u.a.)
Spent UOx after 5 years of cooling
The Sievert is a unit built to quantify the damages of radiations on the human body

## Slide 42
The use of Pu in current reactor to decrease radiotoxicity
Time (year)
Radiotoxicité (u.a.)
Open cycle
Mox fuel aims to save natural uranium (see next part)
   Will recycling Plutonium improve the radiotoxicity ?
7 Uox spent fuel are needed for 1 Mox assembly !
Spent MOX fuel contains Pu  It is not a waste…
It is temporally stored for further use… (if there are uranium tension)
MOX
UOX
Uenr
UOX
Uenr
UOX
Uenr
UOX
Uenr
UOX
Uenr
UOX
Uenr
Pu

## Slide 43
The long-term storage
Two types of long lived wastes
- High activities
- medium activities
Is it safe ?
Exemple : actinides diffusion after 500 000 years ~ 15 m
Maximum doses at the surface induced by the storage
Only one solution so far : geological disposal
  Granit (USA, Sweeden)
  Clay (France, Belgium)
  Salt mine (Germany)
Clay is adapted for actinides
the risk comes from fission products

## Slide 44
Plutonium valorization and natural uranium comsumption
Based on the use of 235U (0,7% of natural uraniuml)
- 1 ton of fission
- 27 tons of enriched uranium
- 200 tons of natural uranium
- Improve the enrichment process
- Uranium recycling
- Plutonium recycling
PWR
1 GWe.y
> 130 tons of Unat/GWe.y
Neutron balance :
Neutron production | Neutron consumption
neutrons by fission | 1 n for fission + n for capture on fissile + neutrons on the fertile
Neutron production | Neutron consumption
fissile nuclei are disappearing for chain reaction
Production of fissile should be at each fission
1 ton/Gwe.y

## Slide 45
Breeding reactors
For breeding, the number of available neutrons
Breeding capability depends (at first order) only on the fissile nucleus

## Slide 46
50 years of PWR operation
One Fast reactor initial inventory

12 t
of Pu

Nucléaire durable : les réacteurs rapides
Fissile inventory issue
235U –fission
235U –capture
238U –capture
Fast neutron reactors do not value U-238
- In France, there are 200 000 tons of depleted uranium available (30 000 tons of Th)
Those reactors needs an initial fissile inventory ; and then, can be operated indefinitely
With fast reactors, the enrichment should be higher : 10 to 12%
With thermal reactors, cross sections impose a uranium enrichment between 3 and 4%

## Slide 47
Sodium cooled - Fast Neutron Reactor
Why liquid sodium as coolant :
  Cheap element
  Good thermal properties (compact reactors)
  Sodium is unstable neither with water nor with air
  Positive void coefficient
Such reactors are developed to face a potential uranium lack on a world wide scale
  What are the uranium resources ?

## Slide 48
Economic viability
Natural uranium price ($)
Electricity price ($)
PWR-type
Investment for the reactor construction
Breeder
“Maximum” natural price that defines the ultimate resources

## Slide 49
Economic viability, with error bars !
Natural uranium price ($)
Electricity price ($)
PWR-type
Breeder
“Maximum” natural :
From 130 $/kg until > 1000$/kg
Today : 285 Gwe (Full power equivalent)
60 000 tons of natural uranium/years
Estimated resources 10 – 23 millions of tons

## Slide 50
Natural uranium consumption
Nuclear power
400 $/kg
200t/(GWe.an)
130t/(GWe.an)
Cumulated ressources consumption
Year
Year
50 years of PWR production
Initial SFR-Na inventory

12 t
ofPu

Exemple : French fleet of 60 GWe (100% SFR-Na) : ≈ 1200 tonnes de Pu
In 2015 : 350 tons of Pu «available» = 30% of the needed Pu
It’s a long term choice with a huge uncertainty
Pu = valuable matter
A drastic increase of nuclear production before the end of the century

## Slide 51
Outline:
PART IV : Transmutation
- Fission products
- Minor actinides
Take home messages :
  Plutonium can be either the most painful waste, either a valuable matter
    Its definition would considerably change the game of waste management
    The valorization of plutonium into Mox fuel make sense if and only if there a development of GEN-IV reactors
  An urgent need of GEN-IV reactors implies a huge increase of nuclear power !
    Drastically means more than a factor 4
  If the plutonium is a valuable matter, what can be done for other radiotoxic elements
Time in year
Radiotoxicity (u.a.)

## Slide 52
Transmutation
The transmutation = recycling nuclei in reactors to make them disappear by nuclear reactions
    99Tc (210 000 y) + n 100Tc 100Ru (stable)
    135Cs (2.3 .106 y) +n 136Cs 136Ba (stable)
    133Cs (stable) + 2 n 135Cs (2.3 .106 y)
β- (15s)
β-
 A look on the evolution
At reactor level
At fleet level

## Slide 53
Transmutation
Principle contributors for radioactive pollution :
Isotope | Quantities produced in PWR (kg/Twhe) | Radio-active decay (years) | Cross section (barns) |  | (years) | 
 |  |  | Fast spectrum | thermal spectrum | Fast spectrum | Thermal spectrum
79 Se | 0.02 | 6.5 .104 | 0.03 | 0.1 | 730 | 2200
99 Tc | 2.9 | 1.5 .106 | 0.2 | 4.3 | 110 | 51
129 I | 0.66 | 1.6 .107 | 0.14 | 4.3 | 160 | 51
135 Cs | 1.4 | 2.3 .106 | 0.07 | 0.07 | 310 | 170
Isotope | Quantities produced in PWR (kg/Twhe) | Radio-active decay (years) |  |  |  | 
 |  |  | Fast spectrum | thermal spectrum | Fast spectrum | Thermal spectrum
79 Se | 0.02 | 6.5 .104 | 0.03 | 0.1 | 730 | 2200
99 Tc | 2.9 | 1.5 .106 | 0.2 | 4.3 | 110 | 51
129 I | 0.66 | 1.6 .107 | 0.14 | 4.3 | 160 | 51
135 Cs | 1.4 | 2.3 .106 | 0.07 | 0.07 | 310 | 170
  Only I and Tc transmutation is possible
The solution is to recycle fission products in dedicated target (with a special neutron moderation) in a high neutron flux available in fast reactors
No material that could contain iodine that may suffer irradiation have been found

## Slide 54
Transmutation
239Pu
240Pu
241Pu
242Pu
241Am
238Pu
242Am
242Am
*
242Cm
243Cm
244Cm
245Cm
Fission
Capture
243Pu
Decay
243Am
244Am
Actinide transmutation = fission after one or several neutron capture on the given actinide
Fission and capture cross section of minor actinides impose a fast spectrum for transmutation
 The reduction of safety coefficient is too important in current PWR
Two strategies are possible :
U, Pu, MA
SFR
U, Pu
SFR or PWR
MA
AM + Pu
 Single strata scenario
 Double strata scenario
All fuel assemblies are contaminated with MA
MA are concentrated

## Slide 55
Double strata imposes ADS
Fission Yields of different actinides
Delayed neutron

## Slide 56
Double strata imposes ADS
Fission Yields of different actinides
Delayed neutrons represent only a small fraction of the neutron production ()
They are essential for reactor operation

## Slide 57
Double strata imposes ADS
Critical reactor
Dr = +0.01
ADS k=0,97
Dr = +0.01
P = +50%
Critical reactor
Dr = +0.001
ADS k=0,97
Dr = +0.001
P = +3%
Simple quasi-static kinetic equation for a critical reactor :
fraction of delayed neutron
 allowed keff range for power increase is only ]1;1+b[
In a ADS, the physics is completely different

## Slide 58
Double strata imposes ADS
A European prototype for ADS
Safer than critical reactor ?

## Slide 59
Waste compared to the in-cycle inventory
1000 years of operation will produce the same radiotoxicity of matter needed to the reactor fleet
Needs of “end of game” studies that would reduce the global inventory of plutonium and minor actinides
A small recall :
  Plutonium is very radiotoxic
  A SFR needs a lot of Pu to operate
X 1000

## Slide 60
The impossible choice of transmutation
The wastes produced before the deployment of Fast Reactors dominates the total wastes
No transmutation
Imediate transmutation
« delayed
transmutation
Quantity of wastes
Time of operation
Minor actinides inside glasses
2038 : beginning of transmutation
In 2150, the gain due to transmutation is low
Production
Transmutation term

Transmutation efficiency function of:
 Flux (consequently the power)
 Irradiation time

## Slide 61
Outline :
Take home messages :
  Transmutation is a pro-nuclear option
    It implies that plutonium is a valuable matter handled inside the fuel cycle
    Only minor actinides (even americium) are considered
      Curium and higher elements would imply neutron and gamma doses unacceptable in different facilities
      “The nuclear paradox”
Trust in next generations |  | Yes | No
Pro-nuclear | GEN-IV reactors | x | 
 | Transmutation |  | x
Anti-nuclear | GEN-IV reactors |  | x
 | Transmutations | x | 

## Slide 62
Time importance for nuclear reactors transitions
Time constant that have to be combined with a 14 year decay constant
The global nuclear power evolution is the key hypothesis for future nuclear studies
REP
EPR
RNR
Plutonium decay constant is not compatible with such times
   Ice cream effect (eat it quickly or get dirty)
Study of flexible strategies
year
% power
A mature reactor technology in 2040 implies urgent improvement on nuclear data and reactor modeling !
Thank you for your attention !