## Slide 1
ALEGRO 2018 workshop at Oxford
Positron Acceleration in Plasma Introduction, Status and Objectives
Sébastien Corde and Spencer Gessner
WG8 coordinators
March 26, 2018

## Slide 2
Outline
Introduction of the scientific context for positron acceleration in plasma
    Motivation and relationship with LWFA-PWFA WG4 and 5
    Difficulties for positron acceleration in plasma
    No self-consistent scheme for simultaneously achieving high efficiency, low preserved emittance and transverse instability mitigation
Paths identified so far (all have major problems for linear colliders)
  Quasi-linear plasma wakefield
  Nonlinear plasma wakefield
  Hollow plasma channels
WG8 Status and Objectives
          WG8 CERN mini-workshop
          WG8 sessions at ALEGRO 2018 workshop
          Identify path forward, potential issues, and R&D priorities

## Slide 3
Introduction to Positron acceleration in Plasma

## Slide 4
Plasmas are asymmetric accelerators
Plasma acceleration schemes (both LWFA and PWFA) are promising candidates for an advanced linear collider. But plasmas are asymmetric accelerators: there are profound difference between electron and positron acceleration in plasmas.
The plasma electrons are mobile but the ions are not.
The symmetry of the accelerating mechanism is broken.
mi >> me
e-
e+
Exception
Linear plasma waves are symmetrical.

## Slide 5
Plasmas are asymmetric accelerators
Positron acceleration has very similar difficulties in both LWFA and PWFA. It would be beneficial to tackle the problem across the fields of LWFA and PWFA.
Laser Direction
LWFA laser driver
PWFA particle beam driver
WG8 Positron acceleration is a joint sub-WG to LWFA-PWFA WG4 and 5

## Slide 6
Where can positrons be accelerated and focused in a non-linear plasma wakefield?
The field is accelerating behind the pinch in the first bubble.
But the field is defocusing in this region.
Electron-driven or laser-driven nonlinear blowout wakes:
Plasmas are asymmetric accelerators

## Slide 7
Tiny volume where it’s simultaneously accelerating and focusing. But Ez varies rapidly in this volume, both transversely and longitudinally.
Plasmas are asymmetric accelerators
Tiny volume for positrons
Electron-driven or laser-driven nonlinear blowout wakes:

## Slide 8
Transverse force is highly nonlinear in r
 emittance growth
Plasmas are asymmetric accelerators
Tiny volume for positrons
Electron-driven or laser-driven nonlinear blowout wakes:

## Slide 9
Major problems:
Efficiency is low
Stable propagation of a witness positron bunch requires either high emittance or very low charge; otherwise it collapses and drives nonlinear wakefield.
Linear plasma wakes (any driver):
Driver
Challenges of Positron acceleration in Plasma

## Slide 10
Major problem:
Transverse instability
Hollow plasma channels:
Challenges of Positron acceleration in Plasma

## Slide 11
Challenges of Positron acceleration in Plasma
Plasma acceleration is being considered for an advanced linear collider, where positrons are strongly desired.
Positron is half the equation we have to deal with!
Yet very little research on how to accelerate positrons in plasmas.
Mostly due to the lack of facilities delivering positrons for plasma acceleration research.
« The most outstanding problem is the acceleration of positrons with bunch brightness, required for a linear collider » [Lebedev et al., World Sci. (2016)].

## Slide 12
As of now, no self-consistent scheme for accelerating positrons in plasma that can simultaneously provide:
    High energy efficiency
    Extremely low preserved emittance
    Mitigation of transverse instabilities
Plasma-based particle accelerators face a major challenge:
Deserve serious attention
The positron problem
Challenges of Positron acceleration in Plasma
It’s all about beam quality and efficiency

## Slide 13
Identified paths for positron acceleration in plasma

## Slide 14
Nonlinear plasma wakefield

## Slide 15
  Unexpected result: a large number of positrons are accelerated. Not just a tiny volume being accelerating and focusing for positrons.
  Accelerated positrons form a spectrally-distinct peak with an energy gain of 5 GeV.
  Energy spread can be as low as 1.8% (r.m.s.).
  Energy extraction efficiency of about 30% is deduced.
Experimental results in 1.3 m plasma
Positron acceleration in nonlinear plasma wakefield:
Nonlinear plasma wakefield
S. Corde et al., Nature 524, 442 (2015)

## Slide 16
Nonlinear plasma wakefield
Transverse force is nonlinear in r, and is slice dependent.  emittance growth
P. Muggli et al., Phys. Rev. Lett 101, 055001 (2008)
P. Muggli | ALEGRO Positron Acceleration in Plasma Mini-Workshop, CERN | February 9 2018
Halo formation

## Slide 17
Nonlinear plasma wakefield
“Weird” bunch shape for radial equilibrium  no emittance growth
K. Lotov, Phys. Plasmas 24, 023119 (2017) K. Lotov | ALEGRO Positron Acceleration in Plasma Mini-Workshop, CERN | February 9 2018
If initially Gaussian, the bunch evolves with emittance growth until equilibrium (quasi-steady state) is reached, after which emittance is preserved.
Single-stage plasma accelerator to avoid emittance growth in multiple stages

## Slide 18
Nonlinear plasma wakefield
Plasma wake shaping using e.g. doughnut-shaped drivers  linear focusing force
J. Vieira et al Proceedings of AAC (2014); N. Jain et al arXiv (2015)
Jorge Vieira | ALEGRO Positron Acceleration in Plasma Mini-Workshop, CERN | February 9 2018
Potential for high efficiency and preserved emittance in nonlinear plasma wakefield

## Slide 19
Nonlinear plasma wakefield
Potential for high efficiency and preserved emittance in nonlinear plasma wakefield
Plasma wake shaping using e.g. doughnut-shaped drivers  linear focusing force
J. Vieira et al Proceedings of AAC (2014); N. Jain et al arXiv (2015)
Jorge Vieira | ALEGRO Positron Acceleration in Plasma Mini-Workshop, CERN | February 9 2018

## Slide 20
Quasi-linear plasma wakefield

## Slide 21
A. Doche et al., Scientific Reports 7, 14180 (2017)
Quasi-linear plasma wakefield
Drive charge: 460 pC
Trailing charge: 260 pC
Plasma density: 1 × 1016 cm-3
1.65 m upstream of the plasma entrance
Emittance without Ti: 100 um x 10 um
With Ti 300 um : 270 um x 60 um

## Slide 22
Acceleration of a distinct positron bunch in a plasma
A. Doche et al., Scientific Reports 7, 14180 (2017)
By varying incoming emittance, experiment spans nonlinear to quasi-linear regime
Quasi-linear plasma wakefield

## Slide 23
Quasi-linear plasma wakefield
Weiming An | ALEGRO Positron Acceleration in Plasma Mini-Workshop, CERN | February 9 2018
Stable propagation for trailing positron bunch requires high emittance or low charge.
Without stable propagation, the trailing positron bunch collapses and a nonlinear wavefield is generated
 same problems as discussed for nonlinear plasma wakefield

## Slide 24
Low emittance implies low charge, and therefore low efficiency per bunch.
“True” quasi-linear regime therefore requires multi-pulse/multi-bunch and/or energy recovery, to accommodate for the low efficiency per bunch and to reach good overall efficiency.
S. Hooker et al., J. Phys. B: At. Mol. Opt. Phys. 47, 234003 (2014); J. Cowley et al., Phys. Rev. Lett. 119, 044802 (2017)
Quasi-linear plasma wakefield

## Slide 25
Hollow plasma channels

## Slide 26
Hollow plasma channels
  The Hollow Plasma Channel is a structure that symmetrizes the response of the plasma to electron and positron beams. There is no plasma on-axis, and therefore no focusing/defocusing force from plasma ions.
Plasma Wall
Plasma Wall

## Slide 27
Hollow plasma channels

## Slide 28
We measure changes to the beam as the beam is translated in the transverse directions x and y. The beam size increases when the beam interacts with the plasma channel.
Both the Kick Map and Beam Area Measurement (Volcano Plot) are consistent with an annular plasma channel.
S. Gessner et al., Nat. Commun. 7, 11785 (2016)
Hollow plasma channels

## Slide 29
At a bunch separation of 400 microns, the trailing bunch gains about 20 MeV on average, while the drive beam loses about 11 MeV.
Hollow plasma channel with two beams:
Hollow plasma channels

## Slide 30
Hollow plasma channels
Experimental measurement [C. Lindstrøm et al., 2018] of transverse wakefield in hollow plasma channel largely agrees with theoretical model [C. Schroeder et al., Phys. Rev. Lett. 82, 1177 (1999)].
Need mitigation mechanisms for transverse instability in hollow plasma channels.
C. Lindstrøm et al., Phys. Rev. Lett 120, 124802 (2018)

## Slide 31
WG8 Status and Objectives

## Slide 32
Working Group 8 sessions
ALEGRO WG8 mini-workshop at CERN (February 9, 2018)
Talks:
  Review results from previous experiments
  Get a common understanding of the challenges and proposed solutions
  Look ahead to future experiments
Discussion:
  What are the major obstacles to accelerating high-quality positron beams in plasma?
  There are many proposed solutions. What are their advantages and drawbacks?
  There aren’t many facilities of positron PWFA/LWFA research. Is there anything we can do about it?
  What about novel sources of positron beams for plasma acceleration experiments?

## Slide 33
Working Group 8 sessions
There is only one facility that produces positron beams for plasma acceleration experiments.
Increasing access to positron beams will accelerate positron PWFA/LWFA research.
In this session we examine existing and novel technologies for producing positron beams in the context of a PWFA/LWFA research facility.
Looking ahead, the LC community would benefit from compact, low-emittance positron sources if they can replace expensive damping ring complexes.
WG8 session on novel positron sources: Tuesday @10:30

## Slide 34
Working Group 8 sessions
Positron Source Topics
Compact Damping Rings
V. Yakimenko, FACET-II TDR, SLAC-R-1072
In-Situ Positron Generation
X. Wang, PRL 101, 124801 (2008)
Positron Beams from Electro-static Traps
J. Danielson, Rev. Mod. Phys., Vol. 87, 2015
Laser Generated Positron Beams
G. Sarri, Nat. Comm., 6747, 2015

## Slide 35
Working Group 8 sessions
Detailed report on ALEGRO WG8 mini-workshop at CERN
Hollow channels for positron acceleration in LWFAs
Discussion on positron acceleration in LWFA schemes
WG8 joint session with LWFA WG4: Tuesday @15:30
WG8 joint session with PWFA WG5: Wednesday @10:30
Prospects and challenges for positron acceleration in the quasi-linear regime
Transverse wakefields in hollow plasma channels
Discussion on most viable paths moving forward for positron acceleration

## Slide 36
Objectives
Survey existing work in LWFA/PWFA positron acceleration
Provide input by identifying most promising path and highlighting their potential limitations
Prioritize R&D on solving the most important problems and on exploring new promising ideas
Emphasize need for facilities for positron LWFA/PWFA research
Our goals
Quasi-linear plasma wakefield
How to accelerate low emittance beams with high efficiency?
Multi-pulse, energy recovery.
Hollow plasma channels
How to mitigate transverse instabilities?
Nonlinear plasma wakefield
How to preserve emittance?
Doughnut-shaped wakes, weird trailing bunch shaping, single-stage accelerator.
Position trailing bunch at zero-crossing of transverse wakefield, look for damping mechanisms.
It’s all about beam quality and efficiency
Positron problem deserves serious attention