## Slide 1: Future Accelerators for Particle Physics
Roger Ruber
FREIA Laboratory
Dept. of Physics and Astronomy
Uppsala University
30 October 2018

## Slide 2: Accelerator History for Particle Physics
Different options
what to collide: lepton vs hadron
how to collide:
  fixed target or colliding beams
  linear vs circular
  acceleration technology
    DC, RF, wakefield
Project ideas
linear electron collider: SC or NC
circular electron or proton collider
circular electron – proton collider
But also
non-HEP use of accelerators

## Slide 3: Lepton versus Hadron Collisions
Leptons
for precision physics
well defined CM energy
polarization possible
Hadrons
at the frontier of physics
huge QCD background
not all nucleon energy available in collision
p
p
e+
e-

## Slide 4: Particle Collisions
Fixed Target
Collider

## Slide 5: Linear versus Circular
source
main linac
N
S
N
S
accelerating cavities
Circular Collider many magnets, few cavities → need strong field for smaller ring
multi-pass → high bunch repetition rate for high luminosity
ring → synchrotron radiation losses
Linear Collider few magnets, many cavities → need efficient RF power production
single pass → need higher gradient for shorter linac
single pass → need small cross-section for high luminosity:
(exceptional beam quality, alignment and stabilization)

## Slide 6: Linear versus Circular: Cost
Linear Collider
E ~ L
cost ~ aL
Circular Collider
ΔEturn ~ (q2E4/m4R)
cost ~ aR + b ΔE
optimization: R~E2 → cost ~ cE2
examples:
  LEP200: ΔE ~ 3%; 3640 MV/turn
  LHC: Bmag limited
cost
energy
Circular
Collider
Linear
Collider

## Slide 7: Projects for Future Accelerators
 | Electrons Linear | Circular | Hadrons Linear | Circular
Particle Physics | ILC |  | LBNF / PIP-II | 
 | CLIC |  | ESSnuSB | 
 |  | FCC-ee |  | FCC-hh
 |  | CepC |  | SppC
Material Science | LCLS-II |  | ESS | 
 | ERL Berlin |  | IFMIF (Japan) | 
 | ERL Cornell |  | CSNS (China) | 
Nuclear Energy |  |  | MYRRHA | 
 |  |  | C-ADS | 

## Slide 8: European Strategy 2013 → Update in 2019
Approved by CERN council (May 2013), ESFRI roadmap
Identified four highest priorities:
Highest priority is exploitation of the LHC including luminosity upgrades
  HiLumi LHC upgrade project
Europe should be able to propose (by 2018-2019) an ambitious project at CERN after the LHC
  circular proton collider (FCC-hh) → high-field magnets
  linear electron collider (CLIC) → high-gradient acceleration
Europe welcomes Japan to make a proposal to host ILC
Long baseline neutrino facility

## Slide 9: Circular Colliders

## Slide 10: High Luminosity LHC Upgrade Project
Increase the LHC luminosity with a factory 5
  peak luminosity to 5x1034 cm-2s-1 with levelling
  allowing integrated of 250 fb-1 per year
    integrated over time in units of the relevant X-section
Increasing the beam brightness by reduced β* and crabbing
  reduce envelop ; emittance
  crab cavities to compensate for crossing angle
  replace inner triplet magnets to increase aperture
  modify some collimators & bending dipoles

## Slide 11: High Luminosity LHC Technical Highlights

## Slide 12: Crabbing Cavities
Increase effective overlap
RF deflector
  before and after the crossing point
RF noise
  amplitude jitter
  phase jitter
amplitude jitter
phase jitter

## Slide 13: Chinese R&D: CepC and SppC
Effort led by IHEP, Beijing*
e+e- Higgs factory (CEPC) 240 GeV, 54 km
continuation of BEPC → BEPCII → CEPC
  fits strategic needs, experience, resources
pp collider (SppC) 70 TeV, in the same tunnel
  gain sufficient time for magnet R&D and wait for technological improvements
*) Y. Wang (IHEP) IPAC'2015
http://accelconf.web.cern.ch/AccelConf/IPAC2015/talks/frygb2_talk.pdf

## Slide 14: Future Circular Collider (FCC) Study
International FCC collaboration (CERN as host lab) to study:
  pp-collider (FCC-hh) → main emphasis, defining infrastructure requirements
~16 T  100 TeV pp in 100 km
  ~100 km tunnel infrastructure in Geneva area, site specific
  e+e- collider (FCC-ee), as potential first step → start operation 2039
  HE-LHC with FCC-hh technology → start operation 2040
  p-e (FCC-he) option, IP integration, e- from ERL

## Slide 15: Future Circular Collider (FCC) Study
FCC-ee:
  c.m. energy from 45 to 183 GeV for Z, WW, H and ttbar production
  Exploration of 10 to 100 TeV energy scale via couplings with precision measurements
  ~20-50 fold improved precision on many EW quantities (equiv. to factor 5-7 in mass) (mZ, mW, mtop , sin2θweff , Rb , αQED(mz), αs(mz mW mτ), Higgs and top quark couplings)
  Machine design for highest possible luminosities at Z, WW, ZH and ttbar working points
FCC-hh:
  Highest centre of mass energy for direct production up to 20 - 30 TeV
  Huge production rates for single and multiple production of SM bosons (H,W,Z) and quarks
  Machine design for 100 TeV c.m. energy & integrated luminosity ~ 20ab-1 within 25 years
HE-LHC:
  Doubling LHC collision energy with FCC-hh 16 T magnet technology
  c.m. energy = 27 TeV ~ 14 TeV x 16 T/8.33T, target luminosity ≥ 4 x HL-LHC
  Machine design within constraints from LHC civil engineering and based on HL-LHC and FCC technologies

## Slide 16: Future Circular Collider (FCC) Site Study Example
Preliminary conclusions:
93km seems to fit the site really well, likely better than smaller ring
100km tunnel appears possible
The LHC could be used as an injector
J. Osborne & C. Cook
PRELIMINARY

## Slide 17: Future Circular Collider (FCC) Key Challenges
Energy
  Limited by the machine size and the strength of the bending dipoles
  Have to maximize the magnet strength
Luminosity
  Need to maximize the use of the beam for luminosity production
Beam power handling: The beam can damage the machine
  Quench the magnets
  Create background in the experiments
  Need a concept to deal with the beam power
Cost
  The total cost is a concern, so we have to push everything to the limit to reduce cost
  Most things will become difficult

## Slide 18: Dipole Magnet Challenge
Arc dipoles are the main cost and parameter driver
  baseline is Nb3Sn at 16T
  alternative HTS at 20T
Looking at performance offered by practical SC, considering tunnel size and basic engineering (forces, stresses, energy) the practical limit is around 20 T.
  Such a challenge is similar to a 40 T solenoid.
Field level is a challenge but many additional questions:
  aperture
  field quality
Coil sketch of a 15 T magnet with grading, E. Todesco

## Slide 19: Synchrotron Radiation
Synchrotron radiation power
100 TeV protons radiate significantly
  Total power of 5 MW (LHC 7kW)
Needs to be cooled away
  Equivalent to 30W/m per beam in the arcs
    LHC <0.2W/m, total heat load 1W/m
Current goal
  beam aperture: 2x13mm
  magnet aperture: 2x20mm
  space for shielding: 7mm
Protons loose energy
They are damped
Emittance improves with time
Typical transverse damping time 1 hour
LHC beam screen

## Slide 20: The FCC-ee Rational
Can use FCC-hh tunnel
  Tunnel cost has to be paid only once
Can operate at different energies
  90 GeV (“Tera-Z”), 160GeV (W pairs), 240GeV (Higgs via Zh)
  350GeV (top threshold, higgs productions via Zh and WW)
Limited energy reach
  But proton collider takes care of high energies
Limited beam lifetime
  due to large particle energy loss in IPs and limited energy acceptance (2%)
  need continuous top-up
Linear
Circular,
adding four experiments
Modified from original version: http://arxiv.org/pdf/1308.6176v3.pdf
F. Gianotti

## Slide 21: Linear Colliders

## Slide 22: Linear Collider Studies
International Linear Collider: ILC
superconducting technology
1.3 GHz
31.5 MV/m
ECM = 500 GeV
upgrade to 1 TeV
Compact Linear Collider: CLIC
normal conducting technology
12 GHz
100 MV/m
ECM = 3 TeV
start at 500 GeV with stepwise upgrading

## Slide 23: Superconducting RF Cavities (SRF)
High efficiency due to low Rsurface
  standing wave cavities with low peak power requirements
  but expensive cryo-cooling
Long pulse trains (long fill time)
  favourable for in-pulse feed-back
Record 59 MV/m achieved with single cell cavity at 2K (1.3 GHz)
  multi-cell in operation ~30-35 MV/m
Limitations:
  Field Emission
    due to high electric field around iris
  Quench
    surface heating from dark current, or
    magnetic field penetration at “Equator”
  Contamination
    during assembly → improve surface treatment

## Slide 24: Normal Conducting (Resistive) RF
High ohmic losses
  but use water cooling
Standing or travelling wave
Easier manufacturing
  unlike SRF, no special chemical procedures, no clean room
Short fill time tfill =  1/vG dz
  order <100 ns (~ms for SCRF)
High gradients, but only if
  high frequency
  short pulse lengths: < 1μs
  limited by RF breakdown: > 60 MV/m
Higher frequencies
  smaller structures cq. equipment
Well suited for small accelerators
  industrial and medical applications
  university
1 cm
30 GHz structure (CLIC)
11.4 GHz structure (NLC)
12 GHz structure (CLIC)

## Slide 25: CLIC Two-beam Acceleration Concept
acceleration by wakefield of drive-beam
  energy extraction and compression from high power drive beam
  only passive elements
Main parameters
  Eacc = >100 MV/m
  11.424 GHz
  230 ns pulse length
  <10-6 breakdown rate (BDR)
drive beam
main beam

## Slide 26: Drive Beam Generation
Courtesy A. Andersson

## Slide 27: Other Accelerator Studies

## Slide 28: CERN e-beam Facility for DM Searches
Implementation of an LDMX type beam
  X-band based 60m LINAC to 3 GeV in TT4-5
  Fill the SPS in 2s (bunches 5ns apart) via TT60
  Accelerate to ~10 GeV in the SPS
  Slow extraction to experiment in 10s as part of the SPS super-cycle
  Experiment(s) considered in UA2 area or bring beam back on Meyrin site using TT10

## Slide 29: ESS Neutrino Super Beam (ESSnuSB)
Doubling the ESS beam power for a second target
  linac duty cycle doubling to 8 % (RF sources, cooling)
    using new H- source
  accumulator ring (~400 m circ.) compress 2.86 ms beam pulse to few µs
    multi-turn injection, stripping H- → H+
  2nd target station with magnetic horn (350 kA)
    to deliver ~300 MeV neutrinos
Injection
Extraction
Collimation
RF

## Slide 30: Soft X-ray FEL Studies
MAX IV Soft X-ray FEL
Baseline SXL design with state-of-the-art undulator technology
  generation of short pulses (<1 fs)
  double pulses for pump-probe experiments
  strong-field single-cycle THz source
  microbunching instability
CompactLight
Impact of undulator technology on FEL performance:
  analytical computation of FEL performance parameters
  dependence on 𝜆_𝑢 & 𝐾 of undulator
Simulation studies of soft x-ray FEL
  baseline design – SASE operation
  production of attosecond light pulses
  Harmonic-lasing self-seeding (HLSS)
Large undulator strength for short period gives a huge improvement in FEL brightness.
Peak pulse energy at undulator end
Peak brilliance at ~16m along undulator length

## Slide 31: Ultrashort Light Pulse Generation
High-Harmonic Generation (HHG) sources are facing saturation
  Undulator light source is a promising way to the attosecond region
LUSIA Collaboration
  Attosecond SIngle-cycle Undulator Light
  explore novel concepts for generation of attosecond pulses with on a µJ energy scale
  coherent few-cycle light pulses down to a single-cycle by tailoring light wavefronts in an undulator

## Slide 32: Ultra-fast Electron Diffraction
X-ray FELs generate laser-like x-ray pulses
  with wavelengths from 10's nm to sub-Å region
Ultra-short electron pulse
  offer much higher elastic scattering cross sections
  an ideal tool to probe structural dynamics
Science case
  chemical reactions in water and liquid environments
  structural dynamics in biological systems
  controlling the non-equilibrium pathways toward materials’ functionality
Proposed FREIA-UED
  variable pulse lengths (0.1-10 ps),
  high electron flux (CW/1 MHz),
  excellent coherence,
  electron energy 250 keV - 2 MeV,
  collaboration with Stanford

## Slide 33
Summary and Info

## Slide 34: Summary
Several studies ongoing with complementary technologies and goals
  all studies are world-wide collaborative efforts
ILC study is ready to prepare a proposal
  Proven technology, in use for FLASH, coming up for EuXFEL
CLIC study has produced a CDR
  now focusing on the optimisation and industrialisation of the technology
FCC study is working towards a CDR in 2018
  can use the vast experience and technology from LHC
  but challenges due to high beam energy and luminosity
Let us hope that the LHC will find exciting new physics and guide our choice between the machines.

## Slide 35: Acknowledgements
With material from many colleagues
Alex Andersson, Erik Adli, Erk Jensen, Hans Braun, Andrea Palaia, Daniel Schulte, Frank Tecker, Wilfrid Farabolini, Walter Wünsch, Akira Yamamoto and Volker Ziemann
Some illustrations and photos courtesy
CERN, KEK and Symmetry Magazine