## Slide 1: Overview of the European Spallation Source (ESS)
Roger Ruber
FREIA Laboratory
Dept. of Physics and Astronomy
Uppsala University
30 October 2018

## Slide 2: Why to use neutrons?
Neutral charge
  deeply penetrating except for some isotopes
Nuclear interaction:
  cross section depending on isotope (not Z), sensitive to light elements.
Spin S = 1/2
  probing magnetism
  unstable n → p + e + νe with life time τ ~ 900s , I = I0 e- t/τ
Thermal energies result in non-relativistic velocities
  mass: n ~p; E = 293 K = 25 meV, v = 2196 m/s , λ = 1.8 Å
X-rays
Neutrons
Light
Light
X-rays
Neutrons

## Slide 3: How to produce neutrons
Nuclear Spallation
→ accelerator
Nuclear Fission
→ reactor

## Slide 4: ESS Basic Design Principles
High Power Accelerator
Ultimate energy: 2 GeV
Repetition rate: 14 Hz
Pulse length: 2.89 ms
Peak power: 125 MW
Instruments
15-22 Instruments in construction budget
(depending on scenario)
Target Station
Ultimate power: 5 MW
He-gas cooled
Rotating W-target
42 Beam ports
Ion Source
Protons
Current: 62.5 mA

## Slide 5: European Spallation Source (ESS)
1993
Proposal for a European spallation source
2003
First European design effort completed
2009
Decision that ESS will be build in Lund
2012
Design update completed
2014
Construction starts
2020
First beam on target
First neutrons
2023
Start of user program
30 years !
2025
Construction complete

## Slide 6
April 2017
Klystron Gallery
Cryo Compressor
Building
Central Utility
Building
Distribution
Substation
Primary
Substation
Target
Monolith
Exp. Hall
E01
Active
Cells
Front End
Building
High Energy
Loading Bay

## Slide 7
September 2018

## Slide 8: First 15 Neutron Science Instruments
ESS Instrument Layout (September 2017)
ESS In-Kind Partners also collaborate on sample environment, data management systems etc.
ODIN
DREAM
NMX
MIRACLES
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LOKI
VESPA
ESTIA
SKADI
+
+
C-SPEC
+
Nuclear Physics Institute
BEER
Test Beam Line
Monolith
Neutron beam extraction
Offers 42 neutron beam ports
Allows instruments to view either upper or lower moderator position

## Slide 9: The ESS Target
Target wheel
Proton beam window
Moderator and reflector plugs

## Slide 10: The ESS Accelerator
Design Drivers:
High Average Beam Power
  5 MW
High Peak Beam Power
  125 MW
High Availability
Key parameters:
2.86 ms pulses
    2 GeV
    62.5 mA peak
    14 Hz
    Protons (H+)
    Low losses
    Minimize energy use
    Flexible design for mitigation and future upgrades
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz
RF sources for HB part is the scope contingency for accelerator
First beam at 571 MeV in June 2019
5 MW capacity for 2023

## Slide 11: The ESS Accelerator
 | Length [m] | No. Cavities | β | No. Magnets | No. Steerers | No. Sections | Power [kW]
LEBT | 2.38 |  |  | 2 Solenoid | 2 x 2 | 1 | 
RFQ | 4.6 | 1 |  |  |  | 1 | 1600
MEBT | 3.83 | 3 |  | 11 Quad | 10 x 2 | 1 | 15
DTL | 38.9 | 5 |  | PM-Quads | 15 x 2 | 5 | 2200
LEBT + Spoke | 55.9 | 26 | 0.50 | 26 Quad | 26 | 13 | 330
Medium Beta | 76.7 | 36 | 0.67 | 18 Quad | 18 | 9 | 870
High Beta | 178.9 | 84 | 0.86 | 42 Quad | 42 | 21 | 1100
HEBT | 130.4 |  | (0.86) | 32 Quad | 32 | 15 | 
DogLeg | 66.2 |  |  | 12 Quad + 2D | 14 |  | 
A2T | 46.4 |  |  | 6 Quad + 8 Raster |  |  | 
 | 604.21 | 155 |  |  |  |  | 

## Slide 12: Ion Source & Low Energy Beam Transport
Beam commissioning ongoing.
First Plasma from the ESS Ion Source
M. Lindroos, TAC 14, Oct. 2016
ESS Ion Source
M. Lindroos, TAC 14, Oct. 2016
CERN Courier, May 2006

## Slide 13: Normal Conducting Linac
RF Quadrupole (RFQ)
  electric quadrupole mode with high field quality
  RF electric field concentrated near the vane tips, hence strong transverse focusing
  acceleration through longitudinal modulation pattern, hence effective array of accelerating cells
Drift Tube Linac (DTL)
  drift tube shields particle while field direction is reversed
  drift tube length adapted to particle velocity
  permanent magnet included for focusing
© CERN CDS 8303511
© CERN CDS 6808042

## Slide 14: Superconducting Linac
Double spoke resonators
  β = 0.50 (3 gaps)
  Eacc = 9 MV/m
Elliptical resonators
  β = 0.67 (6 cells) / 0.86 (5 cells)
  Eacc = 16.7 / 19.9 MV/m
Prototype cryomodule with 4 medium β 6 cell elliptical sc cavities in CEA (Saclay) test place
March 2017

## Slide 15: Beam Raster Scanning on Target
5:4 pattern
Raster system sweeping beam in 2D pattern @ target
8 colinear magnets, individually powered
Crosshatch pattern (fx/fy, ϕxy, ax, ay) within 2.86 ms pulse

## Slide 16: FREIA Laboratory: Test Facility in Uppsala
Facility for Research Instrumentation and Accelerator Development
cryogenics
- liquid helium
- liquid nitrogen
control room
- equipment controls
- data acquisition
radio-frequency (RF) power sources
3 bunkers
with test stands
horizontal cryostat
vertical cryostat
Competent and motivated staff
collaboration of physics (IFA) and engineering (Teknikum).
Funded by KAWS, Government, Uppsala Univ.
State-of-the-art Equipment

## Slide 17: FREIA Laboratory Overview of Activities
Cryo Test Stands
ESS SRF Linac
High Power RF
Controls & Data Acquisition
THz Coherent Light Source
RF = Radio Frequency
SRF = Superconducting RF
Cryo Distribution
ESS Neutrino Super-beam
HiLumi LHC
CLIC / CTF3

## Slide 18
Summary and Info

## Slide 19: Acknowledgements
With material from many colleagues
Pierre Bosland, Sebastien Bousson, Erk Jensen, Roland Garoby, Mats Lindroos, Frank Peauger, Guillaume Olry and Volker Ziemann
For details, see
  https://indico.esss.lu.se/event/528
  https://indico.esss.lu.se/event/987
Some illustrations and photos courtesy
Aarhus University, CERN, CEA, ESS, IPNO and KEK