## Slide 1: Stave 6 Local Flatness & Stave 7 Pressure Test
Shuaiyan
2018/05/29

## Slide 2: Stave 7 Defects
The defect finder finds three defects(one small) for both sides of stave 7.
L side defect plot (zoomed)
1
1
2
2
3
3
L side 5-0 psi (zoomed)

## Slide 3: Stave 7 Defects(J side)
There is one abnormal pixel causing the
maximum height to be very large(148 um)
The actual maximum height is 43 um.
J side defect plot (zoomed)
J side 5-0 psi (zoomed)
1
1
2
2

## Slide 4: Plot of Maximum Height vs Minimum X, Y defect width
Chart: Maximum Height vs Minimun X or Y width
| 10 | 13 | 23.5 | 14 | 12 | 16.5 | 16 | 10 | 16 | 17 | 10 | 12.5 | 8.5 | 19 | 15 | 17.5 | 12.5 | 13 | 27 | 10 | 17.5 | 22 | 16 | 7.5 | 15.5 | 17 | 17 | 15.5 | 16.5 | 16.5 | 12.5 | 22
 | 115 | 156 | 431 | 218 | 83 | 204 | 208 | 103 | 280 | 166 | 147 | 151 | 75 | 388 | 190 | 226 | 118 | 120 | 496 | 110 | 324 | 429 | 359 | 88 | 324 | 136 | 90 | 320 | 281 | 282 | 185 | 378
 | 54 | 60 | 55 | 43 | 31 | 15
Blue dots represent stave 7 data
Orange dots represent stave 2 & 4 data

## Slide 5: Stave 6 Local Flatness
Eliminate the points with rms larger than 15 um
For each module (98*220 points) , dividing them into 5*5 areas
Choose the medium height in each small area,drop the entire area if available points are fewer than 5 (only eliminated 24 5*5 areas for module 1)
Choose three points for generating plane, calculate the height difference

## Slide 13: Plot of Potential plane & scanned data