## Slide 1: Update on PS Longitudinal Impedance Model
B. Popovic
09/11/17

## Slide 2: PS Impedance Model Updates
Transmission line kickers
  KFA13 & KFA21 models
  Effect of vacuum chamber on impedance simulations
PS Dump
  Model of the dump currently in the machine
  Working with EN-STI on the replacement dump design to reduce its impedance*
*IWG #14 : https://indico.cern.ch/event/671318/

## Slide 3: Transmission Line Kickers
CST models built from old drawings and CATIA drawings when available
KFA13, 21, 71 & 79 all contain identical modules
  KFA13 & KFA21 are identical units
Important step would be to measure one module to confirm simulations
8C11 Ferrite
  Using APB provided definition*
Module
*https://impedance.web.cern.ch/impedance/PS.htm

## Slide 4: Effect of Vacuum Chamber
Including the chamber enlarges the structure
  More resonances at lower frequencies
  Also adds ‘chamber modes’
Single Module
Single Module, No Chamber
Mode Supported by Chamber

## Slide 5: Comparing Multi-Module Simulations
Single Module
Two Modules
KFA79 (3 Modules)
Modes Supported by Chamber Geometry
Abs(imped Z)
Abs(imped Z)
Notes: Loss mechanisms
Losses due to the ferrite itself (more modules, longer path seeing ferrites => uniform increase in impendence) (1,2,3 module simulation)
  No Chamber simulation, a broadband resonance shifted to higher frequency
2) Modes resonating in the structure itself => more modules, larger structure => resonant modes at lower frequencies ( 9 module simulation)

## Slide 6: Vacuum Chamber Supported Modes
Two Modules
E-Field Monitor
at 21.27 MHz: Side View
Appendix includes additional mode monitors

## Slide 7: Comparing KFA79 to KFA13
Inline modules produce a ‘forest’ of resonances (KFA13)
Inline modules seem to allow additional modes to build up along beam path
  I.E. Higher coupling between modules
KFA79
KFA13

## Slide 8: Comparing KFA79 (3 Modules) & KFA71 (9 Modules)
Once again ‘forest’ of modes
  Longer path length seems to result in more modes supported
KFA71 (9 Modules)
Zoomed

## Slide 9: Preliminary PS Dump Model
Installed in straight sections 47 & 48
Main problem modes are ‘Coax Cavity’-like
Simplified moveable dump
Moveable
Dump
PS
Beam Pipe
Actuator

## Slide 10: ‘Coax Cavity’-like Modes
626 MHz
811 MHz
150 MHz
Eigenmode Solver: Front View
Beam
Beam
Beam

## Slide 11: Current Replacement Design
Latest replacement design uses off the shelf cylindrical vacuum vessel
  Could be an impedance problem
Cylinder: Poor performance impedance-wise
  Excess of space: Drives resonance peaks to lower frequencies than necessary
  Supports significantly more modes than the old PS Dump
PS
Beam Pipe
Cylindrical
Vessel
To Ion Pump
Actuator

## Slide 12: Path Forward
Kickers
  Measure 8C11 Sample
    Ferrite measurement script underway
      Being benchmarked with known samples (Teflon & other ferrites)
      Need to have 8C11 samples machined
  If available, attempt to measure an individual kicker module
PS Dump
  Add realistic material definitions to the moveable dump
  New PS dump design is in progress
    Impedance reduction necessary
Passive Elements ( Bellows, transitions, etc.)
  Continuing to do a machine survey of the straight and magnet sections
  Begin modelling the most numerous elements

## Slide 13: Appendix

## Slide 14: Lower Frequency Modes: Two Module Case

## Slide 15: Two Module Case E-Field Monitors: Top View
21.27 MHz
39.22 MHz
54.66 MHz
77.35 MHz

## Slide 16: Two Module Case E-Field Monitors: Side View
21.27 MHz
39.22 MHz
54.66 MHz
77.35 MHz

## Slide 17: PS Dump Compare : Wakefield & Eigenmode :Q

## Slide 18: PS Dump Compare : Wakefield & Eigenmode : R Shunt

## Slide 19: PS Dump Compare : Wakefield & Eigenmode : RoQ