## Slide 1: Inductive Adder for FCC Injection Kicker Systems

## Slide 2
Requirements for the FCC injection Inductive Adder
Parameter | Unit | Value
Pulse flat top length | [µs] | 2.00
Flat top tolerance | [%] | ±0.50
Field rise time | [µs] | 0.425
Voltage | [kV] | 15.70
Current | [kA] | 2.50
System impedance | [Ω] | 6.25
Pulse frequency | [Hz] | 115
→ 0.350 µs of kicker magnet fill time
→ 0.075 µs remain for pulse current rise time
Low impedance
Relatively high current
Challenges of the inductive adder design:

## Slide 3
Magnetic core
Pulse capacitor
PCB
Secondary
MOSFET
switch
One layer of the Inductive Adder
Impedance matching of the stack
Layer design for fast rise times
Biasing of magnetic cores
Content

## Slide 4
Chart: Inner diameter d in m
Electric field in insulation:
Impedance of IA:
Impedance matching of the stack
Factors influencing the layer impedance:
Ratio of primary inner diameter () and stalk diameter ()
Insulation material between primary and secondary ()
Layer height ()
Inductance of primary winding ()
Outer diameter D over inner diameter d for different
stalk
inner primary winding
insulation
Examples for insulation materials:
Air
Oil
Water
Epoxy
FC-77
SF6
Vacuum
Low impedance -> small insulation gap

## Slide 5
Layer design for fast rise time
Propagation time of IA layer:
Propagation time of IA stack ( layers):
Factors influencing the rise time:
Layer height
Insulation material
Primary inductance
Output voltage, layer voltage
Switching time of switching device (SiC MOSFET)
The inductance of the secondary circuit should be low to not limit the rise time!

## Slide 6
V
C
switch
V
C
switch
I
V
C
switch
I
V
C
switch
I
4V
magnetic core
primaries
L
secondary
Biasing circuit
Remanence
Saturation
Linear
Region
Biasing of magnetic core
Biasing of the magnetic core can reduce the required core material and therefore reduce the layer height.

## Slide 7
Biasing of magnetic core
Square shaped
linear

## Slide 8
Summary
System impedance of 6.25 Ohm (2.5 kA, 15.7 kV)
Oil insulation required
Use of a biasing circuit
  reduce magnetic material
  Shorter layer height possible
  Faster rise time achievable
Capacitors
SiC MOSFETs
Insulated gate driver
22 layers
1,2m

## Slide 9
Thank you for your attention!
Questions?

## Slide 11
Small insulation gaps are difficult to manufacture.
Chart: Air
Chart: Oil
Big diameters result in high costs for the magnetic cores.
Example for insulation materials:
Air
Oil
Water
Epoxy
FC-77
SF6
Vacuum
Evaluation of Dielectricum

## Slide 12
Tolerances in stalk
Chart: Error (mm)
| 0.63379798073003035 | 0.5704181826570176 | 0.50703838458403261 | 0.44365858651101986 | 0.38027878843802099 | 0.31689899036500824 | 0.25351919229200937 | 0.19013939421899662 | 0.12675959614601162 | 6.3379798072998872E-2 | 0 | -6.3379798072998872E-2 | -0.12675959614601162 | -0.19013939421901049 | -0.25351919229200937 | -0.31689899036502212 | -0.38027878843802099 | -0.44365858651101986 | -0.50703838458403261 | -0.57041818265703148 | -0.63379798073003035
E_max (Error in ID) | 13.0716 | 12.6803 | 12.3121 | 11.9651 | 11.6374 | 11.3274 | 11.0339 | 10.7555 | 10.491 | 10.2395 | 10 | 9.7717 | 9.5538 | 9.3456 | 9.1465 | 8.9559 | 8.7733 | 8.5982 | 8.43 | 8.2686 | 8.1133
E_max (Error in OD) | 8.0479 | 8.2074 | 8.3735 | 8.5467 | 8.7273 | 8.916 | 9.1132 | 9.3195 | 9.5356 | 9.7621 | 10 | 10.25 | 10.5131 | 10.7903 | 11.0828 | 11.392 | 11.7192 | 12.0662 | 12.4347 | 12.8268 | 13.245
Z (Error in ID) | 4.304 | 4.3769 | 4.449 | 4.5203 | 4.5908 | 4.6606 | 4.7297 | 4.7982 | 4.8661 | 4.9333 | 5 | 5.0661 | 5.1317 | 5.1968 | 5.2615 | 5.3256 | 5.3893 | 5.4526 | 5.5154 | 5.5778 | 5.6399
Z (Error in OD) | 5.6338 | 5.5728 | 5.5114 | 5.4495 | 5.387 | 5.324 | 5.2604 | 5.1963 | 5.1315 | 5.0661 | 5 | 4.9333 | 4.8658 | 4.7976 | 4.7286 | 4.6589 | 4.5882 | 4.5168 | 4.4443 | 4.371 | 4.2966
can be reduced by using bigger diameters
Impedance mismatch caused by an unprecise stalk is influencing the output pulse
However, very precise production and alignment of the primary and secondary windings is necessary.
Precise manufacturing and adjustment of stalk and core is necessary!
PSpice simulations showed that the error needs to be <0.06 mm, what is a reasonable value.
Chart: 
| 0.63379798073003035 | 0.5704181826570176 | 0.50703838458403261 | 0.44365858651101986 | 0.38027878843802099 | 0.31689899036500824 | 0.25351919229200937 | 0.19013939421899662 | 0.12675959614601162 | 6.3379798072998872E-2 | 0 | -6.3379798072998872E-2 | -0.12675959614601162 | -0.19013939421901049 | -0.25351919229200937 | -0.31689899036502212 | -0.38027878843802099 | -0.44365858651101986 | -0.50703838458403261 | -0.57041818265703148 | -0.63379798073003035
E_max (Error in ID) | 13.0716 | 12.6803 | 12.3121 | 11.9651 | 11.6374 | 11.3274 | 11.0339 | 10.7555 | 10.491 | 10.2395 | 10 | 9.7717 | 9.5538 | 9.3456 | 9.1465 | 8.9559 | 8.7733 | 8.5982 | 8.43 | 8.2686 | 8.1133
E_max (Error in OD) | 8.0479 | 8.2074 | 8.3735 | 8.5467 | 8.7273 | 8.916 | 9.1132 | 9.3195 | 9.5356 | 9.7621 | 10 | 10.25 | 10.5131 | 10.7903 | 11.0828 | 11.392 | 11.7192 | 12.0662 | 12.4347 | 12.8268 | 13.245
Z (Error in ID) | 4.304 | 4.3769 | 4.449 | 4.5203 | 4.5908 | 4.6606 | 4.7297 | 4.7982 | 4.8661 | 4.9333 | 5 | 5.0661 | 5.1317 | 5.1968 | 5.2615 | 5.3256 | 5.3893 | 5.4526 | 5.5154 | 5.5778 | 5.6399
Z (Error in OD) | 5.6338 | 5.5728 | 5.5114 | 5.4495 | 5.387 | 5.324 | 5.2604 | 5.1963 | 5.1315 | 5.0661 | 5 | 4.9333 | 4.8658 | 4.7976 | 4.7286 | 4.6589 | 4.5882 | 4.5168 | 4.4443 | 4.371 | 4.2966

## Slide 13
Function generator
Oscilloscope
Power supply
Amplifier, incl. 1 Ω Shunt to measure
Test core
RC integrator to measure
Current limiting resistor
Other required parameters:
Core dimensions, weight, fill factor, no of windings
Thanks to S. Aguilera and M. Krupa
BH curve measurement test setup from BE-BI-PI