## Slide 1: Measuring the Properties of Superconductors
JUAS 2018 – Practical Work Day at CERN
  Experimental Work Divided into 3 Activities
  Activity 1: Levitation and Meissner Effect
  Activity 2: Critical Temperature Measurements and electrical Resistivity Experiment
  Activity 3: Critical Current Measurement and Critical Surface Parameterization
  Presented by March 12, 2018
  Rakesh Chandra Prajapati European Scientific Institute
Notes: QuickStarter has created an outline to help you get started on your presentation. Some slides include information here in the notes to provide additional topics for you to research.

## Slide 2: Introduction to Superconductor
Conducting Metal vs Superconductor
Property of Superconductor Below Critical Temperature
Electrical Resistance = 0
Meissner Effect
http://www.okayama-u.ac.jp/user/akimitsu/achievements/study_sc_chara_eng.html
Meissner Effect
Notes: QuickStarter has created an outline to help you get started on your presentation. Some slides include information here in the notes to provide additional topics for you to research.

## Slide 3: Type i and type ii superconductors
Type I
  Surface energy is positive
  Perfect Diamagnetism
  Superconductivity is lost above a Critical Field Hc
Type II
  Surface energy is negative
  Magnetic fields can penetrate
  Two critical fields (Hc1 and Hc2)
  Below Hc1, behaves as Type I superconductor
  Heigher critical magnetic field (Hc2)
  Superconductivity is lost above Hc2.

## Slide 4: Example of ‘Type i’ and ‘type ii’ superconductors

## Slide 5: High Temperature and low temperature superconductors
LTS material (niobium-titanium alloy)
  Liquid helium at 4.2 K
HTS material (bismuth-based, copper oxide ceramic)
  Liquid nitrogen at 77 K

## Slide 6: Critical surface of hts and lts superconductors

## Slide 7: Use of type ii superconductor for practical work

## Slide 8: Activity 1: Levitation with zero field cooling
Levitation with Zero Field Cooling
  Repulsive force while bring magnet near (Meissner Effect)
  Push the magnet hard, and the magnet is pinned to the SC surface

## Slide 9: Activity 1: Levitation with field cooling
Levitation with Field Cooling
  Magnet is on-top of YBCO without interaction
  Pour Liquid Nitrogen
  Magnet is levitated

## Slide 10: Activity 1: suspension
Started with Field Cooling
Slowly Magnet is lifted
YBCO is suspended
Suspension due to Flux pinning effect (Not Meissner Effect)

## Slide 11: Activity 2: Electrical resistance of a superconductor
Tape 1, Tape 2, Tape 3
  Copper tape
  Stainless stell tape
  BSCCO semiconductor tape

## Slide 12: Activity 2: Identify which is the superconducting tape?
Copper
Stainless Steel
S. C.
First Assumption

## Slide 13: Activity 2: ‘Tape 1’ is the superconducting tape
Therefore, Tape 1 is the Superconducting Tape
Superconductor has metallic resistive above critical temperature

## Slide 14: Activity 3: Critical Current Measurement

## Slide 15: Activity 3: Critical Current Measurement