## Slide 2
Practical Days
Vacuum Systems
V. Baglin
CERN TE-VSC, Geneva

## Slide 3: CERN accelerators complex

## Slide 4: CERN vacuum systems
  2850 ion pumps, 450 turbomolecular pumps, 325 Ti sublimation pumps,…
  6 Km of NEG coated beam pipes, 2750 pressure gauges, 40 leak detectors and 100 RGAs,1930 roughing valves and 510 gate sector valves

## Slide 5: Intersecting Storage Rings
Discovery of :
  Vacuum stability and pressure runaway
  Beam induced multipacting (electron cloud)
Developments of laboratory studies and cleaning methods

## Slide 6: Large Electron Positron Collider
Synchrotron radiation in LEP:
  From 6 to 660 keV critical energy
  Gas desorption studies
Innovative pumping system
  Antechamber with NEG pumping strip
  Water cooled and lead shielded

## Slide 7: Large Hardon Collider
Cold bore (CB) at 1.9 K which ensures leak tightness
Beam screen (BS) at 5-20 K which intercepts thermal loads and acts as a screen

## Slide 8: Vacuum, Surface and Coatings group
Design, construction, operation, maintenance and upgrade of high & ultra-high vacuum systems for Accelerators and Detectors.
Expertise and support on thin-walled vacuum chambers, windows and bellows compensation systems
Expertise in vacuum sealing and leak-tightness technology
Expertise in dynamic vacuum phenomena
Management of the industrial support contract for vacuum work in accelerators
Expertise in vacuum control systems, vacuum interlocks and monitoring tools
Coatings, surfaces treatments, surface and chemical analysis for Accelerators and Detectors. Expertise and support in the fields of:
Coatings, electroplating and surface cleaning techniques
UHV characterization and of material and surfaces
Degassing analysis and treatments

## Slide 9: Vacuum, Surface and Coatings group
Several collaborators from different countries and institutes
Design, construction, installation
and operation of the CERN vacuum systems

## Slide 10: TE-VSC organisation
Group management
+ 5 sections:
Vacuum studies and measurements
Beam vacuum operation
Design, logistics & methods
Interlock, controls & monitoring
Surface, chemistry & coatings

## Slide 11: Laboratory activities: pump down
Pump down of a vacuum system:
  start pumping
  open roughing valve
  expected pump down curve

## Slide 12: Laboratory activities: leak detection
How to locate / identify leaks in a vacuum system ?
He leak detector

## Slide 13: Laboratory activities: gas analysis
is my residual gas reasonable ?
Estimation of the partial pressure

## Slide 14: Laboratory activities: vacuum gauge
Vacuum gauges descriptions
Vacuum gauge calibration

## Slide 15: Laboratory activities: pumping speed measurement
Pumping speed measurement

## Slide 16: Design of vacuum systems
A test particle Monte-Carlo code for molecular flow
http://molflow.web.cern.ch/
R. Kersevan – M. Ady

## Slide 17: Step 1: creating geometry
CAD
Molflow+
STL format

## Slide 18: Step 2: adding physics

## Slide 19: Step 3: simulation and results
100k molecules

## Slide 20: You are welcome to join our group for the practical days !

## Slide 21
Thank you for your attention !!!