## Slide 1
LHC Upgrades and
Future Circular Colliders
http://cern.ch/fcc
FCC
PS
SPS
HL-LHC
Work supported by the European Commission under the HORIZON 2020 project EuroCirCol, grant agreement 654305
M. Benedikt
gratefully acknowledging input from HL-LHC project team, FCC coordination group global design study team and many other contributors.
Particular thanks to O. Bruning and F. Zimmermann for providing some read-to-use slides.

## Slide 2
HL-LHC motivation and goals
HL-LHC building blocks
FCC motivation and scope
  Parameters
  Design Status
  Technologies
Outline

## Slide 3
Goal of High Luminosity LHC (HL-LHC)
The main objective of HiLumi LHC Design Study is to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the
following targets:
Prepare machine for operation beyond 2025 and up to 2035
Devise beam parameters and operation scenarios for:
# enabling at total integrated luminosity of 3000 fb-1
# implying an integrated luminosity of 250 fb-1 per year,
# design oper. for m = 140 ( peak luminosity 5 1034 cm-2 s-1)
Operation with levelled luminosity! (beta*, crossing angle & crab cavity)
10x the luminosity reach of first 10 years of LHC operation!!
5 events
400
events

## Slide 4
Recap: Luminosity
colliding bunches:
with:
is determined by the magnet arrangement & powering
Lpeak >2 x 1035 cm-2s-1
n is determined by the injector chain
goal:
high bunch intensity and many bunches
small  at IP and high collision energy

## Slide 5
LHC upgrade goals: performance optimization
Luminosity recipe (round beams):
  maximize bunch intensities (1.1  2.2x1011 )
  minimize the beam emittance (3.75 2.5 μm)
minimize beam size (b* 0.55  0.15 m);
compensate for ‘F’ geometry crossing;
improve machine ‘Efficiency’
Injector complex
Upgrade LIU
New triplets
Crab Cavities
minimize number of unscheduled beam aborts

## Slide 6
LHC Limitations and HL-LHC challenges
Insertion quadrupole magnets lifetime and aperture:
 New insertion magnets and low-b with increased aperture
Geometric Reduction Factor:  SC Crab Cavities
   New technology and first time for a hadron storage ring!
Performance Optimization: Pileup density  Lumi levelling
   requires virtual luminosity >> target levelled luminosity
Beam power & losses  addt’l collimators in dispersion suppressors
Machine effciency and availability:
  # R2E  removal of all electronics from tunnel region
  # e-cloud  beam scrubbing (conditioning of surface), etc
Technical bottle necks (e.g. cryogenics)
Civil Engineering (underground)

## Slide 7
LHC technical bottleneck: Radiation damage to triplet magnets at 300 fb-1
Q2
27 MGy
MCBX3 20 MGy
Cold bore insulation
≈ 35 MGy

## Slide 8
HL-LHC technical bottleneck: Radiation damage to triplet magnets
Requires larger aperture!
New magnet technology
LHC: 70mm at 210 T/m HL@ 150mm diameter 140 T/m
LHC: 8T peak field at coils  HL> 12T field at coils (Nb3Sn)!
Need to replace existing triplet magnets with radiation hard system (shielding!) such that the new magnet coils receive a similar radiation dose @ 10 times higher integrated luminosity 3000 fb-1!  Shielding!
US-LARP MQXF magnet design
Based on Nb3Sn
technology
Tungsten blocks
Capillaries

## Slide 9
HL-LHC Challenges: Crossing Angle
Parasitic bunch encounters:
Perturbations from long-range beam-beam interaction:
Operation requires crossing angle prop. 1/√b*.
Factor 2 increase, 2 x 150 to 2 x 300 mrad)
efficient operation requires large beam separation at unwanted collision points  Separation of 10 -12 s  larger triplet apertures for HL-LHC!
Insertion Layout:
ca.130m  150m
ca.50m
Operation with ca. 2800 bunches @ 25ns spacing  approximately 30 unwanted collisions per
Interaction Region (IR).

## Slide 10
HL-LHC Upgrade Ingredients: Crab Cavities
HL-LHC
Geometric Luminosity
Reduction Factor:
effective cross section
Reduces the effect of geometrical reduction factor
Independent for each IP
Challenging space constraints:
 requires novel compact
cavity design
Crab Cavities:

## Slide 11
HL-LHC crab cavity designs
RF Dipole: Waveguide or
waveguide-coax couplers
Double ¼-wave: Coaxial couplers with
hook-type antenna
4-rod: Coaxial couplers with different antenna types
3 Advanced Design Studies with
Different Coupler concepts
Double ¼-wave installed in SPS
during last shutdown 2017/2018
Present baseline: 4 cavity/cryomod
TEST presently ongoing in SPS

## Slide 12
LHC Challenges: Beam Power
Unprecedented beam power:
potential equipment
damage in case
of failures
during
operation
In case of
failure the
beam must
never reach
sensitive
equipment!
Stored Beam power:
HL-LHC > 500 MJ / beam

## Slide 13
Collimation system upgrades
Ion physics debris: DS collimation
Cleaning: DS coll. + 11T dipoles, 2 units per beam
Low-impedance, high robustness secondary collimators
Completely new layouts Novel materials. IR1+IR5, per beam:
4 tertiary collimators 3 physics debris collimators fixed masks
40 new collimators to be produced by LS3 in
the present baseline!
S. Redaelli,
Chamonix 2016, 28-01-2016

## Slide 14
Dispersion Suppressor collimators –
11 T Nb3Sn Dipole (LS2 -2018)
MB.B8R/L
MB.B11R/L
11 T Nb3Sn

## Slide 15
Implementation & Performance Projection:
Splices fixed
Injectors upgrade
11 T dipoles
25 fb-1
3000 fb-1
300 fb-1
0.75 1034 cm-2s-1
50 ns bunch high pile up 40
1.5 1034 cm-2s-1
25 ns bunch high pile up 40
Run I
Run II
Run III
New
Low-β* quads Crab
Cavity
Phase1
Detectors
LIU
1.5 -2.2 1034 cm-2s-1
25 ns bunch very high pile up > 60
Technical limits (in experiments, too)
Cryogenic limit, Radiation &
Damage of triplet magnets
5 1034 cm-2s-1
levelled
25 ns bunch very high pile up 140
Crab
Cavity
Phase2
1000 fb-1
Energy
6.5TeV
Intensity
Upgrade

## Slide 16
The critical zones around IP1 and IP5
More than 1.2 km of LHC !!
Plus technical infrastructure
(e.g. Cryo and Powering)!!
ATLAS
New triplet Nb3Sn
required due to:
-Radiation damage
-Need for more aperture
Changing the triplet region is not enough for reaching the HL-LHC goal!
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11T Nb3Sn dipole
CMS

## Slide 17
Luminosity profile : NOMINAL HL-LHC
After LS4, proton physics days increase from standard 160 days to 200 and after LS5 to 220

## Slide 18
Very large circular hadron collider - only feasible approach to reach 100 TeV c.m. collision energy in coming decades
Access to new particles (direct production) in few-TeV to 30 TeV mass range, far beyond LHC reach
Much-increased rates for phenomena in sub-TeV mass range → much increased precision w.r.t. LHC
Energy frontier in the 21st century
Hadron collider energy reach
FCC-hh aims at O(10) higher performance (E, L) than LHC
LHC: factor ~4 in radius, factor ~2 in field  O(10) in Ecms
M. Mangano

## Slide 19
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
p-e (FCC-he) option, integration one IP, FCC-hh & ERL
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
Goal: CDR for European Strategy Update 2018/19

## Slide 20
CepC/SppC study (CAS-IHEP) 100 km (new baseline!) , e+e- collisions ~2028; pp collisions ~2042
Qinhuangdao (秦皇岛）
easy access
300 km east
from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”
100 km
50 km

## Slide 21
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – operation run 2
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
Must advance fast now to be ready for the period 2035 – 2040
Goal of phase 1: CDR by end 2018 for next update of European Strategy
CERN Circular Colliders & FCC
2040

## Slide 22
Progress on site investigations
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 23
Progress on site investigations
90 – 100 km fits geological situation well
LHC suitable as potential injector
The 97.75 km version, intersecting LHC, is now being studied in more detail
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 24
FCC 100 km intersecting version
Current baseline:
injection energy 3.3 TeV LHC
Alternative options:
Injection around 1.3 – 1.4 TeV
compatible with: SPSupgrade, LHC, FCC booster
SPSupgrade could be based on fast-cycling SC magnets, 6-7T, ~ 1T/s ramp
  SC Magnet R&D program being launched (similar to SIS 300 parameters)
Injector options:
SPS  LHC  FCC
SPS/SPSupgrade  FCC
SPS -> FCC booster  FCC
FCC-hh injector studies
Notes: See talk of Oliver on injection energy
Several options, present baseline is 3.3 GeV
Ínjection at 1.5 TeV studied as alternative, potentially compatible with SPS upgrade

## Slide 25
2 main IPs in A, G for both machines
asymmetric IR optic/geometry for ee to limit synchrotron radiation to detector
Common layouts for hh & ee
11.9 m
30 mrad
9.4 m
FCC-hh/
ee Booster
Common
RF (tt)
Common
RF (tt)
IP
IP
0.6 m
Max. separation of 3(4) rings is about 12 m:
wider tunnel or two tunnels are necessary around the IPs, for ±1.2 km.
Lepton beams must cross over through the common RF to enter the IP from inside.
Only a half of each ring is filled with bunches.
FCC-ee 1, FCC-ee 2,
FCC-ee booster (FCC-hh footprint)
FCC-hh
layout
Notes: Check with Katsunobu to have latest layout.
Check with detector people if 9 m offset is acceptable for ee detector

## Slide 26
parameter | FCC-hh |  | HE-LHC | (HL) LHC
collision energy cms [TeV] | 100 |  | 27 | 14
dipole field [T] | 16 |  | 16 | 8.3
circumference [km] | 100 |  | 27 | 27
# IP | 2 main & 2 |  | 2 & 2 | 2 & 2
beam current [A] | 0.5 |  | 1.27 | (1.12) 0.58
bunch intensity [1011] | 1 (0.2) | 1 (0.2) | 2.5 | (2.2) 1.15
bunch spacing [ns] | 25 (5) | 25 (5) | 25 (5) | 25
IP b*x,y [m] | 1.1 | 0.3 | 0.45 | (0.15) 0.55
luminosity/IP [1034 cm-2s-1] | 5 | 30 | 16 | (5) 1
peak #events/bunch crossing | 170 | 1020 (204) | 460 (92) | (135) 27
stored energy/beam [GJ] | 8.4 |  | 1.4 | (0.7) 0.36
synchrotron rad. [W/m/beam] | 30 |  | 4.1 | (0.35) 0.18
hadron collider parameters (pp)

## Slide 27
pp/p-pbar in the L-E plane

## Slide 28
phase 1: b*=1.1 m, xtot=0.01, tta=5 h, 250 fb-1 / year
phase 2: b*=0.3 m, xtot=0.03, tta=4 h, 1000 fb-1 / year
  for both phases:
  beam current 0.5 A, unchanged!
  total synchrotron radiation power ~5 MW.
radiation damping: t~1 h
luminosity evolution over 24 h
PRST-AB 18, 101002 (2015)

## Slide 29
FCC-hh MDI status
Design of interaction region
Distance from IP to first machine quadrupole L*=45 m.
Allows integrated spectrometers and compensation dipoles (or fwd solenoids)
Optics and magnet optimization for beam stay clear and collision debris.
  Magnet (triplet) lifetime should be collider lifetime (from radiation damage).
Notes: Add one slide showing optics, possibly with some smaller plots on insertions?
Detailed optimisation on optics of each insertion within overall defined boundaries.

## Slide 30
contributions: beam screen (BS) & cold bore (BS heat radiation)
Beam power & machine protection
Stored energy 8.4 GJ per beam
  Factor 25 higher than for LHC, equivalent to A380 (560 t) at nominal speed (850 km/h). Can melt 12t of copper.
  Collimation, control of beam losses and radiation effects (shielding) are of prime importance.
  Injection, beam transfer and beam dump all critical.
Damage of a beam with an energy of 2 MJ
Machine protection issues to be addressed early on!
Hydrodynamic tunneling:
beam penetrates ~300 m in Cu

## Slide 31
FCC-hh beam dilution system
1.4 km dump insertion
2.8 km collimation insertion
2.5 km dump line
Kicker
Septum
10 mrad bend
Dilution
Absorber
Fluka studies:
Bunch separation >1.8 mm
Branch separation: 4 cm
Keeps T<1500°C
2m
SC septum
Very reliable kickers, high segementation,
new methods for triggering (laser)
Huge energy to be extracted and dumped => need large dump section
Beam rigidity: 167 T.km => need long way to dilute beam ~2.5km!

## Slide 32
R&D on Superconducting Septa
Need an extraction system for safely removing the beam from the collider
hybrid system: short overall length with high robustness & availability
SuShi concept:
SC shield creates field-free region inside strong dipole field
3 candidate technologies:
NbTi/Nb/Cu multilayer sheet
HTS tape/coating
Bulk MgB2

## Slide 33
Synchrotron radiation
beam screen prototype
Photon distribution
FCC-hh beam screen prototypes
Ready for Testing 2017 in ANKA within EuroCirCol study
High synchrotron radiation load of proton beams @ 50 TeV:
~30 W/m/beam (@16 T) (LHC <0.2W/m)
5 MW total in arcs (@1.9 K!!!)
New Beam screen with ante-chamber
absorption of synchrotron radiation at 50 K to reduce cryogenic power
factor 50! reduction of cryo power
Simulation of
quench behaviour

## Slide 34
contributions: beam screen (BS) & cold bore (BS heat radiation)
Cryo power for cooling of SR heat
Overall optimisation of cryo-power, vacuum and impedance
Termperature ranges: <20, 40K-60K, 100K-120K
100MW
200MW
300MW
Multi-bunch instability growth time: 25 turns 9 turns (DQ=0.5)

## Slide 35
Main SC Magnet system
FCC (16 T) vs LHC (8.3 T)
FCC
Bore diameter: 50 mm
Dipoles:
Quads:
LHC
Bore diameter: 56 mm
Dipoles:
Quads:

## Slide 36
Nb3Sn conductor program
Nb3Sn is one of the major cost & performance factors for FCC-hh and is given highest attention
Main development goals until 2020:
Jc increase (16T, 4.2K) > 1500 A/mm2 i.e. 50% increase wrt HL-LHC wire
Reference wire diameter 1 mm
Potentials for large scale production and cost reduction
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 37
16 T dipole options and plans
Cos-theta
Blocks
Common coils
Model production 2018 – 2022,
Prototype production 2023 - 2025
Swiss contribution
via PSI
Canted
Cos-theta
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 38
HE-LHC Option
2-GeV Booster
Linac4
SPS+
HE-LHC
16-T dipole magnets
higher energy
transfer lines

## Slide 39
identical FCC-ee baseline optics for all energies
FCC-ee: 2 separate rings, LEP: single beam pipe
lepton collider parameters
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
luminosity per IP [1034 cm-2s-1] | >200 | >25 | >7 | >1.4

## Slide 40
FCC-ee
Barry Barish
13 January 2011
DAFNE
VEPP2000
combining successful ingredients of recent colliders → extremely high luminosity at high energies
LEP:
high energy
SR effects
B-factories:
KEKB & PEP-II:
high beam
currents
top-up injection
DAFNE: crab waist
Super B-factories
S-KEKB: low by*
KEKB: e+ source
HERA, LEP, RHIC:
spin
gymnastics
FCC-ee exploits lessons & recipes from past e+e- and pp colliders

## Slide 41
FCC-ee optics design
IP
Beam
Local chromaticity correction
+ crab waist sextupoles
Local chromaticity correction
+ crab waist sextupoles
Optics design for all working points achieving baseline performance
Interaction region: asymmetric optics design
Synchrotron radiation from upstream dipoles <100 keV up to 450 m from IP
Dynamic aperture & momentum acceptance requirements fulfilled at all WPs
Notes: New slide from Katsunobu on converged optics, final focus and ring optics
Sufficient dynamic aperture and momentum
Injection details missing

## Slide 42
FCC-ee MDI optimisation
MDI work focused on optimization of
l*, IR quadrupole design
Detector, compensation solenoid
SR masking and chamber layout
CERN model of
CCT IR quadrupole
BINP prototype IR quadr.
2 cm aperture, 100 T/m
Notes: New slide on MDI optimisation, L*, solenoid compensation, lumi monitoring, etc.
Slide from Mike Sullivan talk, synchrotron radiation IR, masking?
Possibly one slide on magnet design of Attilio?

## Slide 43
Efficient 2-in-1 FCC-ee arc magnets
Dipole:
twin aperture yoke
single busbars as coils
Novel arrangements allow for considerable savings in Ampere-turns and power consumption
Less units to manufacture, transport, install, align, remove,…
Quadrupole:
twin 2-in-1 design

## Slide 44
RF system requirements
 | Vtotal GV | nbunches | Ibeam mA | DE/turn GeV
hh | 0.032 |  | 500 | 
Z | 0.4/0.2 | 30000/90000 | 1450 | 0.034
W | 0.8 | 5162 | 152 | 0.33
H | 5.5 | 770 | 30 | 1.67
t | 10 | 78 | 6.6 | 7.55
“Ampere-class” machines
“high gradient” machines
x6
≈ 16 x 1 cell 400MHz,
x12
Naive scale up from an hh system
Very large range of operation parameters
Voltage and beam current ranges span more than factor > 102
No well-adapted single RF system solution satisfying requirements
Notes: New slide from Olivier
Common design for hadron and lepton low energy-high currecnt system
Synergies HL-LHC, HE LHC, FCC-hh, FCC-ee Z pole

## Slide 45
RF system R&D lines
hh
≈ 16 cells per beam
≈ 100 per beam
(+ 100 for booster ring)
Z
W
≈ 210 per beam
(+ 210 for booster ring)
W
≈ 800 per beam
(+ 800 for booster)
≈ common 2600 cells for both beams
(+ 2600 for booster)
H
t
≈ 200 per beam
(+ 200 for booster)
400 MHz single-cell cavities preferred for hh and ee-Z (few MeV/m)
Baseline Nb/Cu @4.5 K, development with synergies to HL-LHC, HE-LHC
R&D: power coupling 1 MW/cell, HOM power handling (damper, cryomodule)
400 or 800 MHz multi-cell cavities preferred for ee-ZH, ee-tt and ee-WW
Baseline options 400 MHz Nb/Cu @4.5 K, ◄▬► 800 MHz bulk Nb system @2K
R&D: High Q0 cavities, coating, long-term: Nb3Sn like components
Notes: New slide from Olivier
Common design for hadron and lepton low energy-high currecnt system
Synergies HL-LHC, HE LHC, FCC-hh, FCC-ee Z pole

## Slide 46
The HL-LHC upgrade project is in full swing and progressing towards first major installations in LS2.
The FCC study is advancing well towards the Design Report for end 2018
Clearly HL-LHC is a necessary first step in the development of technologies for future HE accelerators, in particular the FCC.
Superconductivity is the key enabling technology for LHC, HL-LHC, HE LHC and FCC.
The Nb3Sn program for HL-LHC triplets and 11 T dipoles is of prime importance towards development fo 16 T model magnets.
SC crab cavities are a major ingredient for HL-LHC and the development of high efficiency SRF systems is critical for FCC-ee.
Both HL-LHC project and FCC study show the importance of international collaboration in our field, to advance on all challenging subjects and to assure a long-term future!
In this sense we fully rely on your future contributions!
Summary