## Slide 1: Linear Colliders Lecture 4
Damping rings
NC/SC driven differences
CLIC two beam scheme
Drive Beam generation
CLIC test facility CTF3

## Slide 2: Generic Linear Collider
We have seen the different sub-systems in the previous lectures
Now let’s look at some differences in the real designs…
C.Pagani
Electron Gun Deliver stable beam current
Damping Ring Reduce transverse phase space (emittance) so smaller transverse IP size achievable
Bunch Compressor Reduce σz to eliminate hourglass effect at IP
Positron Target Use electrons to pair-produce positrons
Main Linac Accelerate beam to IP energy without spoiling DR emittance
Final Focus Demagnify and collide beams

## Slide 3: Other IP issues
Collimation:
    Beam halo will create background in detector
    Collimation section to eliminate off-energy and off-orbit particle
    Material and wakefield issues
Crossing angle:
    NC small bunch spacing requires crossing angle at IP to avoid parasitic beam-beam deflections
    Luminosity loss (≈10% when θ = σx/σz )
Crab cavities
    Introduce additional time dependent transverse kick to improve collision
Spent beam
    Large energy spread after collision
    Design for spent beam line not easy

## Slide 4: Post-Collision Line (CLIC)

## Slide 5: Bunch structure
SC allows long pulse, NC needs short pulse with smaller bunch charge
ILC
2625
0.370
970
0.156
312
20000
ILC
12
0.0005
0.37

## Slide 6: TESLA/ILC damping ring
Long pulse: 950µs * c = 285 km!!
Compress bunch train into 17 km (or less) “ring” kick individual bunches
Min. circumference by ejection/injection kicker speed (≈20 ns)
“Dog bone” ring with ≈ 400m of 1.67 T wigglers
3.2 km circular rings in the baseline ILC design
Very demanding kicker rise + fall time < 6 ns

## Slide 7: CLIC damping ring layout
167.3
Total length 421m (much smaller than ILC), beam pulse only 47m
Racetrack shape with
  96 TME arc cells (4 half cells for dispersion suppression)
  26 Damping wiggler FODO cells in the long straight sections
Slide 7

## Slide 8: Warm vs Cold RF Collider
Normal Conducting
High gradient => short linac 
High rep. rate => ground motion suppression 
Small structures => strong wakefields 
Generation of high peak RF power 
Small bunch distance 
Superconducting
long pulse => low peak power 
large structure dimensions => low WF 
very long pulse train => feedback within train 
SC structures => high efficiency 
Gradient limited <40 MV/m => longer linac  (SC material limit ~ 55 MV/m)
low rep. rate => bad GM suppression (εy dilution) 
Large number of e+ per pulse 
very large DR 

## Slide 9: CLIC scheme
Very high gradients (>100 MV/m) possible with NC accelerating structures at high RF frequencies (30 GHz → 12 GHz)
Extract required high RF power from an intense e- “drive beam”
Generate efficiently long pulse and compress it (in power + frequency)
Long RF Pulses
P0 , n0 , t0
Short RF Pulses
PA = P0 x N1
tA = t0 / N2
nA = n0 x N3
Electron beam manipulation
Power compression
Frequency multiplication
‘few’ Klystrons
Low frequency
High efficiency
Accelerating Structures
High Frequency – High field
Power stored in
electron beam
Power extracted from beam
in resonant structures

## Slide 10: CLIC two beam scheme
Transfer lines
Main Beam
Drive Beam
CLIC TUNNEL
CROSS-SECTION
High charge Drive Beam (low energy)
Low charge Main Beam (high collision energy)
=> Simple tunnel, no active elements
=> Modular, easy energy upgrade in stages
Main beam – 1 A, 156 ns
from 9 GeV to 1.5 TeV
Drive beam - 101 A, 240 ns
from 2.4 GeV to 240 MeV
5.6 m diameter

## Slide 11: CLIC – overall layout – 3 TeV
Main Beam Generation Complex
Drive Beam Generation Complex

## Slide 12: Two-beam acceleration
Counter propagation from central complex
Instead of using a single drive beam pulse for the whole main linac, several (NS = 25) short drive beam pulses are used
Each one feed a ~880 m long sector of two-beam acceleration (TBA)
pulse 2
pulse 1
main linac
decelerator sector
main beam pulse
From central complex
1
2
3
R.Corsini
Counter flow distribution allows to power different sectors of the main linac with different time bins of a single long electron drive beam pulse
The distance between the pulses is 2 Ls = 2 Lmain/NS (Lmain= single side linac length)
The initial drive beam pulse length tDB is given by twice the time of flight through one single linac
so tDB = 2 Lmain / c, 148 µs for the 3 TeV CLIC

## Slide 13: CLIC Drive Beam generation
148 μs train length – 25 x 24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
25 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 μs
Drive beam time structure - initial
Drive beam time structure - final
CLIC RF POWER SOURCE LAYOUT
Drive Beam Accelerator
efficient acceleration in fully loaded linac
Power Extraction
Drive Beam Decelerator Section (2 x 25 in total)
Combiner Ring x 3
Combiner Ring x 4
pulse compression &
frequency multiplication
pulse compression &
frequency multiplication
Delay Loop x 2
gap creation, pulse compression & frequency multiplication
RF Transverse Deflectors

## Slide 14: Lemmings Drive Beam
Alexandra Andersson

## Slide 15: Fully loaded operation
efficient power transfer from RF to the beam needed
“Standard” situation:
  small beam loading
  power at structure exit lost in load
“Efficient” situation:
high beam current
high beam loading
no power flows into load
VACC ≈ 1/2 Vunloaded

## Slide 16: Fully loaded operation
Disadvantage: any current variation changes energy gain at full loading, 1% current variation = 1% voltage variation at 20% loading, 1% current variation = 0.2% voltage variation
Requires high current stability
Stable beam successfully demonstrated in CTF3
> 95% efficiency
Beam on
~ 0 MW
Output power from accelerating structure
1.6 ms compressed RF pulse
Beam off
~ 24 MW

## Slide 17: Frequency multiplication
basic principle of drive beam generation
transform very long pulses into short pulses with higher power and higher frequency
use RF deflectors to interleave bunches
  => double power
  => double frequency

## Slide 18: Delay Loop Principle
double repetition frequency and current
parts of bunch train delayed in loop
RF deflector combines the bunches (fdefl=bunch rep. frequency)
Path length corresponds to beam pulse length

## Slide 19: RF injection in combiner ring (factor 4)
3rd
λo/4
4rd
2nd
Cring = (n + ¼) λ
injection line
septum
local
inner orbits
1st deflector
2nd deflector
1st turn
λo
RF deflector
field
combination factors up to 5 reachable in a ring
Cring has to correspond to the distance of pulses from the previous combination stage!

## Slide 20: Demonstration of frequency multiplication
Combination factor 5

## Slide 21: CTF3 preliminary phase (2001-2002)
333 ps
Streak camera images of the beam, showing the bunch combination process
t
x
83 ps
RF injection in combiner ring
A first ring combination test was performed in 2002, at low current and short pulse, in the CERN Electron-Positron Accumulator (EPA), properly modified
Combination factor 4

## Slide 22: CTF 3
CLEX
30 GHz “PETS Line”
Linac
Delay Loop – 42m
Combiner Ring – 84m
Injector
Bunch length
chicane
30 GHz test area
TL1
TL2
RF deflector
Laser
4A – 1.2µs 150 MeV
32A – 140ns 150 MeV
demonstrate remaining CLIC feasibility issues, in particular:
  Drive Beam generation (fully loaded acceleration, bunch frequency multiplication)
  CLIC accelerating structures
  CLIC power production structures (PETS)

## Slide 23: Drive beam generation achieved
combined operation of Delay Loop and Combiner Ring (factor 8 combination)
~26 A combination reached, nominal 140 ns pulse length
=> Full drive beam generation, main goal of 2009, achieved
30A
DL
CR

## Slide 24: Power extraction structure PETS
must extract efficiently >100 MW power from high current drive beam
passive microwave device in which bunches of the drive beam interact with the impedance of the periodically loaded waveguide and generate RF power
periodically corrugated structure with low impedance (big a/λ)
ON/OFF mechanism
Beam eye view
The power produced by the bunched (ω0) beam in a constant impedance structure:
P – RF power, determined by the accelerating structure needs and the module layout. I – Drive beam current L – Active length of the PETS Fb – single bunch form factor (≈ 1)
Design input parameters
PETS design

## Slide 25: Accelerating Structure Results
RF breakdowns can occur => no acceleration and deflection
Goal: 3 10-7/m breakdowns at 100 MV/m loaded gradient at 230 ns pulse length
latest prototypes (T24 and TD24) tested (SLAC and KEK)
=> TD24 reach up to 108 MV/m at nominal CLIC breakdown rate (without damping material)
Undamped T24 reaches 120MV/m
Average unloaded gradient (MV/m)
Breakdown rate (1/pulse/m)
CLIC goal
TD24
T24

## Slide 26: Simulation of RF Power Transfer
PETS
T3P models realistic, complex accelerator structures with unprecedented accuracy
Low group velocity requires simulations with 100k time steps
PETS structure
Accelerating structure
The induced fields travel along the PETS structure and build up resonantly
Arno Candel, SLAC

## Slide 27: Achieved Deceleration + RF power generation
Deceleration with 9 PETS, 20 A (end 2011)
Deceleration with 12 PETS, > 20 A (mid 2012)
Final test, 16 PETS (end 2012)
Drive beam has high current and high energy spread
Stable transport in simulations verified experimentally with 13 PETS
24 A beam decelerated by ~51%, >1.3 GW power produced!
Good agreement of power production, beam current and deceleration

## Slide 28: Achieved Two-Beam Acceleration
TD24
Drive beam OFF
Drive beam ON
Maximum probe beam acceleration measured: 31 MeV
=> Corresponding to a gradient of 145 MV/m

## Slide 29: CLIC CDRs published
Vol 1: The CLIC accelerator and site facilities (H.Schmickler)
- CLIC concept with exploration over multi-TeV energy range up to 3 TeV
- Feasibility study of CLIC parameters optimized at 3 TeV (most demanding)
- Consider also 500 GeV, and intermediate energy range
- Complete, presented in SPC in March 2011, in print: https://edms.cern.ch/document/1234244/
Vol 2: Physics and detectors at CLIC (L.Linssen)
- Physics at a multi-TeV CLIC machine can be measured with high precision, despite challenging background conditions
- External review procedure in October 2011
- Completed and printed, presented in SPC in December 2011 http://arxiv.org/pdf/1202.5940v1
Vol 3: “CLIC study summary” (S.Stapnes)
- Summary and available for the European Strategy process, including possible implementation stages for a CLIC machine as well as costing and cost-drives
- Proposing objectives and work plan of post CDR phase (2012-16)
- Completed and printed, submitted for the European Strategy Open Meeting
in September http://arxiv.org/pdf/1209.2543v1
In addition a shorter overview document as input to the European Strategy update, available at:
http://arxiv.org/pdf/1208.1402v1
2016:
CLIC Baseline update
After Higgs discovery
https://cds.cern.ch/record/2210892/

## Slide 31: Summary
Linear e+/e- Collider the only realistic approach to highest energy
Many challenges!!!
Efficient acceleration
  RF system
  High gradient
Extremely small beam sizes
  Damping ring performance is crucial
  Emittance preservation
  Alignment and stabilisation
Much interesting work left to do!!!
Much more detailed lectures at recent ILC schools http://agenda.linearcollider.org/event/6906 or http://agenda.linearcollider.org/event/7333