## Slide 1: Linear Colliders Lecture 2 Subsystems I
Particle Sources
Damping Rings
Bunch Compressor
Main Linac

## Slide 2: Reminder: Luminosity
we want high RF-beam conversion efficiency ηRF
need high RF power PRF
small normalised vertical emittance εn,y
strong focusing at IP (small βy and hence small bunch length σz)
could also allow higher beamstrahlung δBS if willing to live with the consequences (Luminosity spread and background)
Last lecture, we arrived at:

## Slide 3: Generic Linear Collider
C.Pagani
Electron Gun Deliver stable beam current
Damping Ring Reduce transverse phase space (emittance) so smaller transverse IP size achievable
Bunch Compressor Reduce σz to eliminate hourglass effect at IP
Positron Target Use electrons to pair-produce positrons
Main Linac Accelerate beam to IP energy without spoiling DR emittance
Final Focus Demagnify and collide beams
Collimation System Clean off-energy and off-orbit particles
will see the different elements in the following…

## Slide 4: e+ e- sources
we need large number of bunches of (polarized) leptons
electron sources:
  laser-driven DC photo injector
  circularly polarized photons on GaAs cathode (incompatible with RF gun)
  εn ~ 50 μm rad factor ~10 in x plane factor ~500 in y plane too large!!!
  dominated by space charge
  RF bunching system to generate bunch structure for the linac
  or laser with bunch time structure (=> even higher space charge)

## Slide 5: e+ source
basic mechanism: pair production in target material
standard method: ‘thick’ target primary e- generate photons these convert into pairs
undulator source: high energy e- produce photons in wiggler magnet thin conversion target

## Slide 6: e+ source
undulator source:
  ~0.4 rad. length ⇒ much less energy deposition in the target (5 kW compared to 20 kW) ⇒ no parallel targets needed
  smaller emittance due to less coulomb scattering (factor ~2) but still much bigger than needed!!! en ~ 10.000 μm rad !!!
  could produce polarised e+ by helical undulator
  but: need very high initial electron energy > 150 GeV !
    use primary e- beam
    consequences for the commissioning and operation
positrons are captured in accelerating structure inside solenoid and accelerated

## Slide 7: Damping rings
e- and particularly e+ from the source have a much too high ε ⇒ we have to reduce the transverse bunch size
solution: use synchrotron radiation in a damping ring (remember lecture Synchr. Rad II)
γ emission with transverse component
acceleration only in longitudinal direction
radiation
damping!!!

## Slide 8: Damping rings
for e+ we need emittance reduction by few 105
~7-8 damping times required
damping time:
final emittance
equilibrium emittance
initial emittance (~0.01 m rad for e+)
damping time
P
=
2
3
r
e
c
m
o
c
2
(
)
3
E
4
ρ
2
LEP: E ~ 90 GeV, P ~ 15000 GeV/s, τD ~ 12 ms
P - emitted radiation power
exponential damping to equilibrium emittance:

## Slide 9: Damping rings
suggests high-energy for a small ring. But
  required RF power:
  equilibrium emittance: limit E and ρ in practice
DR example:
    Take E ≈ 2 GeV
    ρ ≈ 50 m
    Pγ = 27 GeV/s [28 kV/turn]
    hence τD ≈ 150 ms - we need 7-8 τ D !!! ⇒ store time too long !!!
Increase damping and P using wiggler magnets

## Slide 10: Damping Wigglers
Insert wigglers in straight sections in the damping ring
Average power radiated per electron with wiggler straight section
Energy loss in wiggler: <B2> is the field square averaged over the wiggler length
wigglers

## Slide 11: Damping ring: emittance limits
Horizontal emittance εx defined by lattice
theoretical vertical emittance limited by
  space charge
  intra-beam scattering (IBS)
  photon emission opening angle
DR emittance in the range of existing/planned light sources
In practice, εy limited by magnet alignment errors [cross plane coupling by tilted magnets]
typical vertical alignment tolerance: Δy ≈ 30 µm ⇒ requires beam-based alignment techniques!

## Slide 12: Bunch compression
bunch length from damping ring: ~ few mm
required at IP: ~ few 100 μm or shorter
solution: introduce energy/time correlation with chicane:
long.
phase
space
N.Walker

## Slide 13: The linear bunch compressor
conservation of longitudinal emittance (σz δ = const.):
RF cavity
initial (uncorrelated) momentum spread: δu initial bunch length σz,0 compression ratio Fc= σz,0/ σz beam energy E RF induced (correlated) momentum spread: δc RF voltage VRF RF wavelength λRF = 2π / kRF longitudinal dispersion (transfer matrix element): R56
fixed by DR
compress at low energy

## Slide 14: The linear bunch compressor
chicane (dispersive section) linear part
Minimum bunch length for upright ellipse ⇒ correlation
Initial correlation
With δ2= δu2+ δc2 we get
For high compression ratio (δc≫ δu)

## Slide 15: Bunch compressor - Example
Remark: we get a large energy spread after compression
⇒ large chromatic effects in the linac
Consider a two stage compression with acceleration in between to reduce relative energy spread along the line

## Slide 16: The Main Linac
Now we got small, short bunches we ”only” have to accelerate them to collision energy
Accelerating cavities:
Ez
z
Ez
z
travelling wave structure: need phase velocity = c (disk-loaded structure)
bunch sees constant field: Ez=E0 cos(φ)
c
c
standing wave cavity:
bunch sees field: Ez =E0 sin(ωt+φ)sin(kz)
=E0 sin(kz+φ)sin(kz)
c

## Slide 17: Single bunch effects: longitudinal
Beam absorbs RF power ⇒ decreasing RF field in cavities
Single bunch beam loading: longitudinal wake field
Particles within a bunch see a decreasing field ⇒ energy gain different within a bunch

## Slide 18: Beam-loading compensation
Run off crest and use RF curvature to compensate single bunch beam-loading
Reduces the effective gradient
wakefield
RF
Total
φ = 15.5º

## Slide 19: Beam-loading compensation
Minimize momentum spread
RMS ΔE/E
<Ez>
φmin = 15.5º

## Slide 20: TW Cavity: Beam Loading
Beam absorbs RF power ⇒ gradient reduced along TW cavity for steady state
unloaded
av. loaded

## Slide 21: TW Cavity: Beam loading
Transient beam loading (multi bunch effect):
  first bunches see the full unloaded field, energy gain different
  for all LC designs, long bunch trains achieve steady state quickly, and previous results very good approximation.
  However, transient over first bunches needs to be compensated
  ‘Delayed filling’ of the structure
unloaded
av. loaded
t
V

## Slide 22: SW cavity: multi-bunch BL
With superconducting standing wave (SW) cavities:
Little losses to cavity walls
You can have afford long RF pulse with
  Many bunches
  Large time between the bunches
RF feed-back to compensate beam-loading before the next bunch arrives

## Slide 23: Linac: emittance dilution
Linac must preserve the small beam sizes, in particular in y
Possible sources for emittance dilutions are:
  Dispersive errors: (ΔE → y)
  Transverse wakefields: (z → y)
  Betatron coupling: (x, px → y)
  Jitter: (t → y)
All can increase projection of the beam size at the IP
Projection determines luminosity

## Slide 24: Linac: transverse wakefields
Bunches induce field in the cavities
Later bunches are perturbed by these fields
Bunches passing off-centre excite transverse higher order modes (HOM)
Fields can build up resonantly
Later bunches are kicked transversely
=> multi- and single-bunch beam break-up (MBBU, SBBU)
Emittance growth!!!

## Slide 25: Transverse wakefields
Effect depends on a/λ (a iris aperture) and structure design details
transverse wakefields roughly scale as W┴ ∝ f 3
less important for lower frequency: Super-Conducting (SW) cavities suffer less from wakefields
Long-range minimised by structure design
Dipole mode detuning
aN
RN
a1
R1
Long range wake of a dipole mode spread over 2 different frequencies
6 different frequencies

## Slide 26: Damping and detuning
C. Adolphsen / SLAC
  Slight random detuning between cells makes HOMs decohere quickly
  Will recohere later: need to be damped (HOM dampers)

## Slide 27: HOM damping
Each cell damped by 4 radial WGs
terminated by SiC RF loads
HOM enter WG
Long-range wake efficiently damped
Test results

## Slide 28: Single bunch wakefields
Head particle wakefields deflect tail particles
Particle perform coherent betatron oscillations
=> head resonantly drives the tail
head
tail
Tail particle
Equation of motion:
Driven Oscillator !!
More explicit:

## Slide 29: Two particle model
2 particles: charge Q/2 each, 2σz apart
Bunch at max. displacement x:
    tail receives kick θ from head
π/2 in betatron phase downstream:
    tail displacement ≈βθ
π/2 in phase further (π in total):
    -x displacement, tail kicked by –θ
    but initial kick has changed sign
=> kicks add coherently
=> tail amplitude grows along the linac
head
tail

## Slide 30: BNS damping
Counteract effective defocusing of tail by wakefield by increased focusing (Balakin, Novokhatski, and Smirnov)
Done by decreasing tail energy with respect to head
By longitudinally correlated energy spread (off-crest)
Wakefields balanced by lattice chromaticity
2 particle model:
W┴ non linear
Good compensation achievable at the price of
  lower energy gain by off-crest running
  Larger energy spread

## Slide 31: Random misalignments
BNS damping does not cure random cavity misalignment
Emittance growth:
For given Δε, it scales as
Higher frequency requires better structure alignment δYrms
Partially compensated by: higher G, lower β, lower N
~