## Slide 1: Data unpacking software
Aleksandr Mefodev
December 7 2017

## Slide 2: Unpacking structure:
TDM Unpacking
DAQ Unpacking
Calibration
HG-LG calibration
LG-ToT calibration
Amplitude reconstructions
TDM
Unpacking
Calibration
HG
HG – LG
LG - ToT
reconstructions
LY in p.e.

## Slide 3: TDM unpacking
Input file
  Daq file for one MCR in TDM mode;
Output file
  Several daq files for each FEBs;
Implemented checks
  TDM slot starts == TDM slot end
Future implementations:
  checksumL = checksumL + data;
  checksumH = checksumH + chksumL;

## Slide 4: DAQ unpacking
Input file
  List of daq files after TDM unpacking
Output file
  Root file with separate trees
Future implementations:
  Adding one more branch - global time in ns

## Slide 5: DAQ unpacking event creation procedure:
Spill header & spill time (10um & 10ms)
GTrig Header
Event data
  Event creation if was hit rising time (check TagID);
  Push hit falling time (if it exist, else push “-1”, with HitID check);
  Push hit Amplitude HG (if it exist, else push “0”, with HitID check);
  Push hit Amplitude LG (if it exist, else push “0”, with HitID check);
GTrig Trailer (Gtrig Tag Header == GTrig Tag Trailer)
Spill Trailer (Spill Tag Header == Spill Tag Trailer) & spill time

## Slide 6: Difference between versions 2 vs 3
~2 times more events

## Slide 7: Issue with HG Amplitude = 0
Possible explanation:
Events, which are in the last GTrig of each spill.
Hit ID issue

## Slide 8: Issue

## Slide 10: Calibration
Input file
  Daq file for one FEBs;
Output files
  Root file with plots & fitting for each channel;
  Txt file with gain & peaks location
Implemented checks
  Each peak sigma should be less than default
  Each distance between peaks should be in default range
Future implementations:
  Input file – list of daq files;
  Output files – Sqlite database with gain & peaks location values
  “Pedestal” search.
What will be good to have:
  Special word like “Acquisition start” with FEB’s board ID

## Slide 11: Calibration example

## Slide 12: HG-LG & LG-ToT calibrations
Input file
  List of daq files after TDM unpacking
Output files
  Root file with plots & fitting for each channel
  Txt files with fit parameters for all FEBs & channels
Cuts for fitting:
  HG & LG & ToT > 0
Future implementations:
  Output files – Sqlite database with fit parameters
  Combine with HG – p.e. calibration

## Slide 13: HG-LG example:

## Slide 14: LG-ToT example:

## Slide 15: Amplitude reconstructions
Input file
  *_all.root
Output file
  *all_reconstructed.root
New branches
  hitAmplRecon
  hitLGAmplRecon
Future implementations:
  Combine with HG – p.e. calibration
  Add LY branch in p.e.

## Slide 16: LY reconstruction with LG vs ToT data: