## Slide 1: Kickers, septa and beam transfer lines
Beam transfer devices
  Kickers
  Septa
  Protection devices
Beam transfer lines
  Distinctions between transfer lines and circular machines
  Linking machines/experiments together
  Emittance blow-up from mismatch
  Measure beam parameters (measurement lines)
Matthew Fraser, CERN (TE-ABT-BTP) based on lectures by
M.J. Barnes, W. Bartmann, J. Borburgh, B. Goddard, V. Kain and M. Meddahi

## Slide 2: Reminder: injection, septum and kicker
Septum magnet
Kicker magnet
Kickers produce fast pulses, rising their field within the particle-free gap in the circulating beam (temporal separation)
Septa compensate for the relatively low kicker strength, and approach closely the circulating beam (spatial separation)
F-quad
t
kicker field
intensity
injected
beam
‘boxcar’ stacking
Injected beam
Circulating beam
D-quad
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 3: Reminder: extraction, septum and kicker
Closed orbit bumpers
Extracted beam
t
kicker field
intensity
extracted beam
Septum magnet
Kicker magnet
F-quad
Circulating
beam
D-quad
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Kickers produce fast pulses, rising their field within the particle-free gap in the circulating beam (temporal separation)
Septa compensate for the relatively low kicker strength, and approach closely the circulating beam (spatial separation)

## Slide 4
Kickers
LHC beam dump
kickers (MKD)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 5
Magnets – design options
Type: “lumped inductance”
From generator
(e.g. PFN)
  simple magnet design
  magnet must be nearby the generator to minimise inductance
  exponential field rise-time:
  slow: rise-times ~ 1 μs
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 6
Magnets – design options
Type: “lumped inductance” or “distributed inductance” (transmission line)
From generator
(e.g. PFN)
  simple magnet design
  magnet must be nearby the generator to minimise inductance
  exponential field rise-time:
  slow: rise-times ~ 1 μs
  complicated magnet design
  impedance matching important
  field rise-time depends on propagation time of pulse through magnet:
  fast: rise-times << 1 μs
Cell 1…
Cell n - 1 …
Cell n
From generator
(e.g. PFN)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 7
Magnets – design options
Type: “lumped inductance” or “distributed inductance” (transmission line)
Other considerations:
  Machine vacuum: kicker in-vacuum or external
  Aperture: geometry of ferrite core
  Termination: matched impedance or short-circuit
From generator
(e.g. PFN)
  simple magnet design
  magnet must be nearby the generator to minimise inductance
  exponential field rise-time:
  slow: rise-times ~ 1 μs
  complicated magnet design
  impedance matching important
  field rise-time depends on propagation time of pulse through magnet:
  fast: rise-times << 1 μs
Cell 1…
Cell n - 1 …
Cell n
From generator
(e.g. PFN)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 8
Simplified kicker system schematic
Main sub-systems (“components”) of kicker system;
  RCPS = Resonant Charging Power Supply
  PFL = Pulse Forming Line (coaxial cable) or PFN = Pulse Forming Network (lumped elements)
  Fast high power switch(es)
  Transmission line(s): coaxial cable(s)
  Kicker Magnet
  Terminators (resistive)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Matched impedance example

## Slide 9
Simplified kicker system schematic
PFL/PFN charged to voltage V0 by the RCPS
Main switch is closed…
…voltage pulse of V0/2 flows through kicker
Once the pulse reaches the (matched) terminating resistor full-field has been established in the kicker magnet
Pulse length controlled between t = 0 and 2τp with dump switch
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Matched impedance example

## Slide 10
Simplified kicker system schematic
distance
Pulse forming network or line (PFL/PFN) charged to voltage V0 by the resonant charging power supply (RCPS)
  RCPS is de-coupled from the system through a diode stack
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 11
Simplified kicker system schematic
distance
Pulse forming network or line (PFL/PFN) charged to voltage V0 by the resonant charging power supply (RCPS)
  RCPS is de-coupled from the system through a diode stack
  At t = 0, main switch is closed and current starts to flow into the kicker
time,
int.
kicker
field

## Slide 12
Simplified kicker system schematic
distance
At t = τfill, the voltage pulse of magnitude V0/2 has propagated through the kicker and nominal field achieved with a current V0/2Z
  typically τp >> τfill (schematic for illustration purposes)
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 13
Simplified kicker system schematic
distance
PFN continues to discharge energy into kicker magnet and matched terminating resistor
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 14
Simplified kicker system schematic
distance
PFN continues to discharge energy into kicker magnet and matched terminating resistor
At t ≈ τp the negative pulse reflects off the open end of the circuit (dump switch) and back towards the kicker
time,
int.
kicker
field

## Slide 15
Simplified kicker system schematic
distance
PFN continues to discharge energy into matched terminating resistor
At t ≈ τp the negative pulse reflects off the open end of the circuit and back towards the kicker
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 16
Simplified kicker system schematic
distance
At t ≈ 2τp the pulse arrives at the kicker and field starts to decay
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 17
Simplified kicker system schematic
distance
time,
A kicker pulse of approximately 2τp is imparted on the beam and all energy has been emptied into the terminating resistor
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 18
Simplified kicker system schematic
distance
time,
Kicker pulse length can be changed by adjusting the relative timing of dump and main switches:
  e.g. if the dump and main switches are fired simultaneously the pulse length will be halved and energy shared on dump and terminating resistors
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 19
When the switch is fired the voltage is divided as:
Reflections
Match impedances to avoid reflections!
A simplified pulse forming circuit:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 20
When the switch is fired the voltage is divided as:
In the matched case:
Mismatches will ring in the circuit causing ripples on the pulse, or post-pulse.
Reflections
Time
Charging end of line
Load end of line
Match impedances to avoid reflections!
A simplified pulse forming circuit:
If matched:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 21
When the switch is fired the voltage is divided as:
In the matched case:
Mismatches will ring in the circuit causing ripples on the pulse, or post-pulse.
Reflections
Time
Charging end of line
Load end of line
Match impedances to avoid reflections!
A simplified pulse forming circuit:
In general
(mis-matched):
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 22
An example of reflections
Current loop measurement (L. Sermeus)
Beam-based measurement (I=200e10 ppb)
Recombination kicker KFA.20 deflects
PS booster rings 1 and 2 vertically into plane of PS at CERN
BT.KFA20 circuit schematic: operates in “virtual” short-circuit
Field and measured kick [arb. units]
Field and measured kick [arb. units]
~ few %
Beam-based kicker measurements at higher intensities, V. Forte BT + PS injection kicker meeting, CERN (15th August 2016)
PS
PSB
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 23
Magnets – transmission line
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 24
Magnets – transmission line
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
Grounded end plate
HV conductor
Return
conductor
HV
End View
Side View

## Slide 25
Magnets – transmission line
HV plate
HV conductor
Return
conductor
HV
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
Side View

## Slide 26
Magnets – transmission line
HV plate
HV conductor
Return
conductor
HV
Ferrite
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
B
beam
Side View

## Slide 27
Magnets – transmission line
Ground plate
HV conductor
Return
conductor
Ferrite
HV
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
B
beam
Side View

## Slide 28
Magnets – transmission line
HV conductor
Return
conductor
HV plate
HV
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
B
beam
Side View

## Slide 29
Magnets – transmission line
HV conductor
Return
conductor
Ferrite
HV
Ground plate
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
B
beam
Side View

## Slide 30
Magnets – transmission line
HV conductor
Return
conductor
Ferrite
HV
Ground plate
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
Side View
cell
B
beam

## Slide 31
Magnets – transmission line
Ground plate
HV conductor
Return
conductor
Ferrite
HV
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
End View
B
beam
Side View
cell

## Slide 32
Magnets – transmission line
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Ferrite C-cores are sandwiched between HV plates
  Grounded plates are interleaved to form a capacitor to ground
B
Ground plate
HV conductor
Return
conductor
Ferrite
HV
End View
and so on…
beam
Side View
cell

## Slide 33
Magnets – transmission line
Today’s fast (rise-times of < few hundred ns) kicker magnets are generally ferrite loaded transmission lines:
  Kicker magnets consists of many, relatively short, cells to approximate a broadband coaxial cable
cell
#1
#2
#(n-1)
#n
A real kicker…
Prototype for AGS injection kicker upgrade
beam
and so on…
Side View
cell

## Slide 34
Magnets – lumped inductance
Lumped inductance kicker magnets are robust and reliable, and suitable for applications where the rise-time is typically > 1 μs:
  e.g. LHC beam dump extraction and dilution kicker magnets
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 35
Magnets – lumped inductance
Lumped inductance kicker magnets are robust and reliable, and suitable for applications where the rise-time is typically > 1 μs:
  e.g. LHC beam dump extraction and dilution kicker magnets
~ 90 μs
Horizontal
dilution
Vertical
dilution
Cross-section of MKBH
(horizontal dilution magnet)
2x C-cores back-to-back
single turn coil
insulation
A damped series RLC circuit (switch closed after capacitor charged)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 36
Magnets – lumped inductance
Lumped inductance kicker magnets are robust and reliable, and suitable for applications where the rise-time is typically > 1 μs:
  e.g. LHC beam dump extraction and dilution kicker magnets
Beam dump event at 6.5 TeV on 22nd July 2016
Relative intensity [arb. Units]
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 37
Magnets – lumped inductance
Lumped inductance kicker magnets are robust and reliable, and suitable for applications where the rise-time is typically > 1 μs:
  e.g. LHC beam dump extraction and dilution kicker magnets
Generators nearby in gallery
next to LHC tunnel
MKB dilution magnets in the LHC tunnel
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 38
Magnetic parameters
B
HV conductor
Vertical aperture, Vap
Ferrite
HV
Return conductor
Horizontal
aperture, Hap
Magnetic field
Derivation: remember Ampère’s Law:
Magnet inductance
[per unit length]
Derivation: remember Faraday’s Law:
and
Dimensions Hap and Vap specified by beam parameters at kicker location
Ferrite (μr ≈ 1000) reinforces magnetic circuit and uniformity of the field in the gap
For fast rise-times the inductance must be minimised: typically the number of turns, N = 1
Kickers are often split into several magnet units, powered independently
μr
μ0
A C-core geometry,
commonly used at CERN
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 39
PFL/PFN
Pulse Forming Line (PFL)
Low-loss coaxial cable
Fast and ripple-free pulses
Attenuation (droop ~1%) becomes problematic for pulses > 3 μs
Above 50 kV SF6 pressurized PE tape cables are used
Bulky: 3 μs pulse ~ 300 m of cable
Pulse Forming Network (PFN)
Artificial coaxial cable made of lumped elements
For low droop and long pulses > 3 μs
Each cell individually adjustable: adjustment of pulse flat-top difficult and time consuming.
Reels of PFL used at the PS complex (as old as the photograph!)
SPS extraction kicker (MKE) PFN (17 cells)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 40
Power semiconductor switches
Suitable for scenarios where erratic turn-on is not allowed
For example, LHC beam dump kickers held at nominal voltage throughout operation (>10h) ready to fire and safely abort at any moment.
Hold off up to 30 kV and switch up to 18 kA
Slower switching > 1 μs (~18kA/μs)
Low maintenance
Switches
~ 340 mm
Thyratrons
Deuterium gas thyratrons are commonly used
Hold off 80 kV and switch up to 6 kA
Fast switching ~ 30 ns (~150 kA/μs)
Erratic turn-on: use with RCPS to reduce hold-off time
Thyratron
Stack of high-power semiconductor switches (GTOs)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 41
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Short Circuit
Dump Diode
int.
kicker
field
time,
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 42
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 43
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 44
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 45
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 46
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
Initial pulse reflects of the diode
time,
Boundary condition at short-circuit:
V = 0, doubling I
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 47
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Initial pulse reflects of the diode
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 48
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Diode conducts as voltage flips sign and match dump resistor absorbs energy
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 49
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Diode conducts as voltage flips sign and match dump resistor absorbs energy
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 50
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
Diode conducts as voltage flips sign and match dump resistor absorbs energy
time,
Boundary condition at short-circuit:
V = 0, doubling I
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 51
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Diode conducts as voltage flips sign and match dump resistor absorbs energy
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 52
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Diode conducts as voltage flips sign and match dump resistor absorbs energy
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 53
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
Boundary condition at short-circuit:
V = 0, doubling I
Diode conducts as voltage flips sign and match dump resistor absorbs energy
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 54
Terminated vs. short circuit
Short-circuiting the termination offers twice the kick (for a given kicker magnet):
  Fill time of kicker magnet is doubled
  Diode as dump switch provides solution for fixed pulse length
distance
Dump Diode
Short Circuit
time,
int.
kicker
field
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 55
Other topics and considerations
Ripple: cells of a transmission line kicker have a cut-off frequency that introduces dispersion in pulse:
  Cut-off frequency:
In vacuum: aperture dimensions (Hap and Vap) minimised if in vacuum:
  For given B, lower I and L can be achieved with smaller Hap and Vap
  Machine vacuum is a reliable dielectric, recovers after flashover
  Costly and time consuming to construct/maintain (cleanliness, bake-out)
Beam coupling impedance: kickers are a source of beam impedance in accelerators (wakefields and beam instabilities)
  Ferrite is shielded from beam with beam screens or serigraphy by permitting a smooth conducting path for beam induced image charges
  Beam induced heating of ferrite yoke can heat it above the Curie temp.
Measurements on AGS kicker
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 56
Septa
LHC beam dump
septa (MSD)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 57: Septa
Two main types:
  Electrostatic septa (DC)
  Magnetic septa (DC and pulsed):
    Direct drive septum
    Eddy current septum (pulsed only)
    Lambertson septum (deflection parallel to septum)
septum
Region A
Field free region
(EA = 0 and BA = 0)
unperturbed circulating beam
Challenge: low leakage field
Region B
Uniform field region
(EA ≠ 0 or BA ≠ 0)
deflected extracted beam
Challenge: field uniformity
Δx’
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 58: Electrostatic septum
Thin septum ~ 0.1 mm needed for high extraction efficiency:
  Foils typically used
  Stretched wire arrays provide thinner septa and lower effective density
Challenges include conditioning and preparation of HV surfaces, vacuum in range of 10-9 – 10-12 mbar and in-vacuum precision position alignment
E
(up to 10 MV/m
in UHV)
x
y
z
d (typically 10 to 35 mm)
V (up to 300 kV)
circulating beam
extracted
beam
septum foil
(Mo or Z-Re)
electrode
(Al, Ti, SS)
support
Grounded support
Electrode (HV)
Foil
Foil Tensioners
Bake-out lamps for UHV
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 59: Electrostatic septum
  At SPS we slow-extract 400 GeV protons using approximately 15 m of septum split into 5 separate vacuum tanks each over 3 m long:
    Alignment of the 60 - 100 μm wire array over 15 m is challenging!
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Notes: Adjustable gap width useful for:
Selective conditioning of Septum (e.g. increase gap width and increase voltage to condition feedthru’s, etc)
Permit compensation for “as built errors” in other equipment in the injection or extraction region (overkill would be to design with a big gap and voltage so as to accept any foreseeable beam size) – but the foil position has to be adjustable (and thin) to compensate for alignment errors.

## Slide 60: DC direct drive magnetic septum
magnet yoke (laminated steel)
septum
x
y
z
Cooling
Electrical connections
Circulating beam
vacuum
chamber
extracted
beam
0
B
x
x
septum
(typically 6 to 20 mm)
g
(typically
25 - 60 mm)
Continuously powered, rarely under vacuum
Multi-turn coil to reduce current needed but cooling still an issue:
  Cooling water circuits flow rate typically at 12 – 60 l/min
  Current can range from 0.5 to 4 kA and power consumption up to 100 kW!
rear
conductor
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
B

## Slide 61: Direct drive pulsed magnetic septum
septum
(typically 3 to 20 mm)
circulating
beam
rear
conductor
septum
conductor
extracted
beam
0
B
x
x
x
y
z
Beam “monitor”
Beam screen
Bake-out lamps for UHV
Septum
In vacuum, to minimise distance between circulating and extracted beam
Single-turn coil to minimise inductance, bake-out up to 200 °C (~10-9 mbar)
Pulsed by capacitor discharge (third harmonic flattens the pulse):
  Current in range 7 – 40 kA with a few ms oscillation period
  Cooling water circuits flow rate from 1 – 80 l/min
g
(typically
18 - 60 mm)
magnet yoke (laminated steel)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
B
Notes: Example: J to 300A/mm^2 peak

## Slide 62: Eddy current septum
•
I
I
magnetic
screen
return box
beam
screen
coil
0
B
x
septum
(typically 1 to 3 mm)
x
y
z
Coil removed from septum and placed behind C-core yoke:
  Coil dimension not critical
  Very thin septum blade
Magnetic field pulse induces eddy currents in septum blade
Eddy currents shield the circulating beam from magnetic field
Return box and magnetic screen reduce fringe field seen by circulating beam
In or out of vacuum, single-turn coil
Pulsed by capacitor discharge (third harmonic flattens the pulse):
  Current ~10 kA fast pulsed with ~ 50 μs oscillation period
  Cooling water circuits flow rate from 1 – 10 l/min
g
(typically
10 - 30 mm)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
B

## Slide 63: Lambertson septum
Magnetic field in gap orthogonal to previous examples of septa:
  Lambertson deflects beam orthogonal to kicker: dual plane injection/extraction
Rugged design: conductors safely hidden away from the beam
Thin steel yoke between aperture and circulating beam – however extra steel required to avoid saturation, magnetic shielding often added
x
I
I
•
Circulating
Beam
Steel yoke
Coil
Steel to avoid saturation
Thin Septum
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
B

## Slide 64: Two plane injection with Lambertson
Lambertson septum (H-kick)
Kicker magnet
(V-kick)
D-quad
Injected
beam
F-quad
F-quad
Circulating beam
D-quad
Horizontal plane
Vertical plane
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 65: Lambertson septum
  At SPS we use Lambertson septa to split the 400 GeV slow-extracted proton spill (~ seconds) to different target stations simultaneously:
    These devices are radioactive: critical that coils are located away from the septum
Field-free region
Horizontally deflected by the B-field
Continues straight: no B-field
Losses (5-10%)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Notes: Adjustable gap width useful for:
Selective conditioning of Septum (e.g. increase gap width and increase voltage to condition feedthru’s, etc)
Permit compensation for “as built errors” in other equipment in the injection or extraction region (overkill would be to design with a big gap and voltage so as to accept any foreseeable beam size) – but the foil position has to be adjustable (and thin) to compensate for alignment errors.

## Slide 66: Protection devices
When things go wrong…!
  SPS extraction septum power supply tripped during setting-up of LHC beam, 25th October 2004:
  Septum field dropped by 5% in 11 ms
  3.4 x 1013 protons at 450 GeV, i.e. 2.5 MJ of beam energy dissipated on the aperture of the transfer line
  Vacuum chamber and quadrupole magnet damaged requiring replacement
  Upgraded fast interlock system was implemented to protect against such fast failures
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 67: Protection devices
When beam energy exceeds damage limit for machine equipment one has to design for certain failure scenarios
Critical beam transfer systems have redundancy and multiple layers of protection:
  Passive protection devices form the last layer of this security
  Protection devices are designed to dilute and absorb beam energy safely
Failures associated with beam transfer equipment are typically very fast and difficult to catch, for example:
  No turn-on of kicker: injection protection
  Erratic turn-on of kicker: sweep circulating beam in the machine
  Flash-over (short-circuit) in kicker: impart the wrong kicker angle
  Transfer line magnet failure: steering beam onto aperture of downstream machine
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 68: Injection protection: e.g. LHC injection
LHC has a dedicated injection dump (TDI) to protect against fast failures on the injection kicker
Septum magnet
Kicker magnet
F-quad
Injected beam
Circulating beam
D-quad
In reality the LHC injection is dual plane: Lambertson septum kick orthogonal to kicker
TDI absorber jaws
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 69: Injection protection: e.g. LHC injection
LHC has a dedicated injection dump (TDI) to protect against fast failures on the injection kicker
  No turn-on of kicker: beam steered safely onto absorber:
Septum magnet
Kicker magnet
F-quad
Injected beam
Circulating beam
D-quad
In reality the LHC injection is dual plane: Lambertson septum kick orthogonal to kicker
TDI absorber jaws
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 70: Injection protection: e.g. LHC injection
LHC has a dedicated injection dump (TDI) to protect against fast failures on the injection kicker
  No turn-on of kicker: beam steered safely onto absorber
  Erratic turn-on of kicker: circulating beam steered safely onto absorber:
Septum magnet
Kicker magnet
F-quad
Circulating beam
D-quad
In reality the LHC injection is dual plane: Lambertson septum kick orthogonal to kicker
TDI absorber jaws
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 71: Injection protection: e.g. LHC injection
LHC has a dedicated injection dump (TDI) to protect against fast failures on the injection kicker
  No turn-on of kicker: beam steered safely onto absorber
  Erratic turn-on of kicker: circulating beam steered safely onto absorber
  Flash-over (short-circuit) in kicker: “worst-case” gives twice deflection:
Septum magnet
Kicker magnet
F-quad
Injected beam
Circulating beam
D-quad
In reality the LHC injection is dual plane: Lambertson septum kick orthogonal to kicker
TDI absorber jaws
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 72: Extraction protection: e.g. SPS extraction
SPS has a dedicated absorber (TPSG) to protect the extraction septum in case of fast failures of the extraction kicker
Septum magnet
F-quad
Extracted
beam
D-quad
Circulating beam
Kicker magnet
TPSG
absorber jaw
Closed orbit bumpers and quads
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 73: Extraction protection: e.g. SPS extraction
SPS has a dedicated absorber (TPSG) to protect the extraction septum in case of fast failures of the extraction kicker
  Erratic turn-on of kicker: asynchronous timing with particle-free gap and circulating beam swept across TPSG into transfer line:
Septum magnet
F-quad
Extracted
beam
D-quad
Kicker magnet
Closed orbit bumpers and quads
Circulating beam
TPSG
absorber jaw
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 74: Extraction protection: e.g. SPS extraction
SPS has a dedicated absorber (TPSG) to protect the extraction septum in case of fast failures of the extraction kicker
  Erratic turn-on of kicker: asynchronous timing with particle-free gap and circulating beam swept across TPSG into transfer line
  Flash-over (short-circuit) in kicker: worst-case amplitude places the extracted beam onto the absorber jaw:
Septum magnet
Kicker magnet
in short-circuit mode
F-quad
Extracted
beam
D-quad
TPSG
absorber jaw
Circulating beam
Closed orbit bumpers and quads
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 75: Extraction protection: e.g. SPS extraction
SPS has a dedicated absorber (TPSG) to protect the extraction septum in case of fast failures of the extraction kicker
TPSG and MSE (magnetic septum) installed at HIRADMAT irradiation test facility in 2012: impacted with LHC nominal intensity (288b and 1.1×1011 p/b): both devices survived!
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 76: Extraction protection: e.g. TPSG
SPS has a dedicated absorber (TPSG) to protect the extraction septum in case of fast failures of the extraction kicker
  Diluter made of graphite, 2D carbon composite, titanium alloy and nickel based alloy:
  Designed to protect downstream septum from direct impact of 450 GeV LHC ultimate beam (288 bunches at 1.7×1011 protons per bunch, 3.5 MJ)
CZ5
Ti 6Al 4V
INCO718
CfC 1.75
3100 mm
Water cooling channel
Absorber blocks
Absorber blocks inspected after impact of HIRADMAT test #6: survived and re-installed
beam
TPSG assembly without vacuum tank
Comment: small emittance (high beam brightness) can be just as much a concern as the total intensity for thermo-mechanical stresses during beam impact
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 77: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
Δμ = 60°
Δμ = 120°
Extracted beam ON nominal trajectory
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 78: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
Δμ = 60°
Δμ = 120°
Extracted beam OFF nominal trajectory
Failure of dipole here
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 79: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
  Erratic turn-on of extraction kicker: sweep
  (asynchronous with particle-free abort gap)
Δμ = 60°
Δμ = 120°
Extracted beam OFF nominal trajectory
Asynchronous turn-on: sweep
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 80: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
  Erratic turn-on of extraction kicker: sweep
  (asynchronous with particle-free abort gap)
Δμ = 60°
Δμ = 120°
Extracted beam OFF nominal trajectory
Asynchronous turn-on: sweep
sweep
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 81: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
  Erratic turn-on of extraction kicker: sweep
  (asynchronous with particle-free abort gap)
Δμ = 60°
Δμ = 120°
Extracted beam ON nominal trajectory
Asynchronous turn-on: sweep
sweep
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 82: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
  Erratic turn-on of extraction kicker: sweep
  (asynchronous with particle-free abort gap)
  Flash-over (short-circuit) in kicker:
Δμ = 60°
Δμ = 120°
Extracted beam ON nominal trajectory
Non-nominal kicker deflection
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 83: Transfer protection: e.g. SPS-to-LHC
TDI
MKE
MKI
TCDIH
SPS
TT40/60
TI 8/2
LHC
SPS to LHC transfer lines have dedicated transfer line collimators (TCDIH and V) in case of fast failures to protect LHC aperture:
  Magnet power supply trips at time t after the last extraction interlock check: beam steered onto collimator
  Current (field) error depends on circuit:
  Erratic turn-on of extraction kicker: sweep
  (asynchronous with particle-free abort gap)
  Flash-over (short-circuit) in kicker
  Momentum mismatch at extraction:
Δμ = 60°
Δμ = 120°
Extracted beam ON nominal trajectory
Beam follows dispersive trajectory
Momentum collimator
(high dispersion)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 84
Beam transfer lines
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
LHC beam dump
extraction line (TD62/68)

## Slide 85
Beam transfer lines
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
PS “switchyard”

## Slide 86
Beam transfer lines
Beam transfer lines
  Functional requirements
  Distinctions between transfer lines and circular machines
  Linking machines/experiments together
  Emittance blow-up from mismatch
  Measurement of beam parameters (measurement lines)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 87
Beam transfer lines
Transfer lines transport beams between accelerators (extraction of one to injection of the next) and on to experimental targets and beam dumps
Requirements:
  Geometric link between machines/experiment
  Match optics between machines/experiment
  Preserve emittance
  Change particles’ charge state (stripping foils)
  Measure beam parameters (measurement lines)
  Protect downstream machine/experiment
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 88: General transport
x
x
y
y
s
s
1
2
Beam transport: moving from s1 to s2 through n elements, each with transfer matrix Mi
The transfer matrix (Mi) can be expressed using the Twiss formalism:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 89: Circular Machine
Circumference = L
The solution is periodic
Periodicity condition for one turn (closed ring) imposes α1= α2, β1= β2, D1= D2
This condition uniquely determines α(s), β(s), μ(s), D(s) around the whole ring
  i.e. a single matched ellipse exists for each given location, s
One turn:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 90: Circular Machine
At a location with matched ellipse (a, b) a mismatched injected beam (a*, b*) with emittance e0, generates (via filamentation) a larger ellipse with the matched a, b, but larger emittance: e > e0
Matched ellipse determines beam shape
Turn 1
Turn 2
Turn 3
Turn n >>1
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 91: Transfer line
No periodic condition exists
The Twiss parameters are simply propagated from beginning to end of line
At any point in line, α(s) β(s) are functions of α1 and β1
One pass:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 92: Transfer line
Initial a, b are defined for a transfer line by the beam shape at the entrance
Propagation of this beam ellipse depends on the line
A transfer line optics is different for different input beams:
  Synchrotrons are often multi-purpose, accelerating different beams but extracting through a common line transfer line: optics must switch to match the input and output conditions for each beam type
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 93: Transfer line
On a single pass of a finite transfer line there is no regular motion from entrance to exit
  Periodicity is not enforced: it’s actually a design choice
  Infinite number of possible starting ellipses are transported to an infinite number of final ellipses
x
x’
x
x’
a1, b1
a*1, b*1
Transfer Line
a*2, b*2
a2, b2
Entry
Exit
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 94: Optics Matching
SPS
LHC
Regular lattice (FODO)
(elements all powered in series
with same strengths)
Final
matching
section
SPS to LHC Transfer Line (3 km)
Extraction
point
Injection
point
Initial
matching
section
Independently powered (tuneable) quadrupoles
Independently powered (tuneable) quadrupoles and (in this case) passive protection devices
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 95: Linking Machines
Beams have to be transported from extraction of one machine to injection of the next machine:
  Trajectory must be matched in all 6 geometric degrees of freedom (x,y,z,θ,Φ,ψ)
Other important constraints can include:
  Minimum bend radius, maximum quadrupole gradient, magnet aperture, cost, geology or other obstacles, etc.
An example of how geology can influence transfer line design
SPS to LHC transfer tunnel TI2 (Beam 1)
SPS to LHC transfer tunnel TI8 (Beam 2)
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 96: Linking Machines
Extraction
Transfer
Injection
a1x, b1x , a1y, b1y
ax(s), bx(s) , ay(s), by(s)
s
The Twiss parameters can be propagated when the transfer matrix M is known
a2x, b2x , a2y, b2y
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 97: Linking Machines
Linking the optics is a complicated process:
  Parameters at start of line have to be propagated to matched parameters at the end of the line (injection to another machine, fixed target etc. )
  Need to “match” 8 variables (αx, βx, Dx, D’x and αy, βy, Dy, D’y)
  Matching done with number of independently power (“matching”) quadrupoles
  Maximum β and D values are imposed by magnetic apertures
  Other constraints exist:
    Phase conditions for collimators
    Insertions for special equipment like stripping foils
    Low beam energy (β<<1) re-bunching cavities might be necessary, i.e. RF gymnastics in the transfer line
Matching with computer codes and relying on mixture of theory, experience, intuition, trial and error.
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 98: Optical Mismatch at Injection
Filamentation fills larger ellipse with same shape as matched ellipse
x
x’
Turn 0
Turn N
Time
Dispersion mismatch at injection will also cause emittance blow-up
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 99: Blow-up from betatron mismatch
Optical errors occur in transfer line and ring, such that the beam can be injected with a mismatch
Filamentation will produce an emittance increase
In normalised phase space, consider the matched beam as a circle, and the mismatched beam as an ellipse
Matched
beam (α1, β1)
a
A
Mismatched
beam (α2, β2)
b
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 100: Blow-up from betatron mismatch
The emittance after filamentation:
where
Optical errors occur in transfer line and ring, such that the beam can be injected with a mismatch
Filamentation will produce an emittance increase
In normalised phase space, consider the matched beam as a circle, and the mismatched beam as an ellipse
Mismatched
beam (α2, β2)
Matched
beam (α1, β1)
a
b
A
Aλ
A/λ
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 101: Blow-up from betatron mismatch
The emittance after filamentation:
Writing λ as a function of the matched and mismatched Twiss parameters is an exercise in geometry:
where
See appendix for derivation
Optical errors occur in transfer line and ring, such that the beam can be injected with a mismatch
Filamentation will produce an emittance increase
In normalised phase space, consider the matched beam as a circle, and the mismatched beam as an ellipse
Mismatched
beam (α2, β2)
Matched
beam (α1, β1)
a
b
A
Aλ
A/λ
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 102: Blow-up from betatron mismatch
A numerical example…
Consider b = 3a for the mismatched ellipse:
Mismatched
beam (α2, β2)
Matched
beam (α1, β1)
a
b=3a
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
See appendix for blow-up from dispersion mismatch

## Slide 103: Optics measurement with screens
A profile monitor is needed to measure the beam size
  e.g. beam screen (luminescent) provides 2D density profile of the beam
Profile fit gives transverse beam size: σ
If optics (Twiss parameters) are known, ε can be calculated from a single screen:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 104: Optics measurement with 3 screens
Assume 3 screens in a dispersion free region and that the emittance is constant along the line:
Measurements of σ at s1, s2, s3 plus knowledge of the two transfer matrices M12 and M13 allows determination of ε, α and β
s0
s1
s2
s0
s2
s1
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
beam
See appendix for derivation

## Slide 105: Summary
Depending on the injection/extraction concept we chose a dedicated combination of septa (spatial separation of fields) and kickers (temporal separation of fields)
Transfer lines present interesting challenges and differences from circular machines:
  No periodic condition mean optics is defined by transfer line element strengths and by initial beam ellipse
  Matching is subject to many constraints
  Emittance blow-up is an important consideration, and arises from several sources: mis-steering, mismatch (betatron and dispersion)
  Measurement of beam parameters is important for ensuring beams are well matched between machines and/or experiments
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 106: Summary
Depending on the injection/extraction concept we chose a dedicated combination of septa (spatial separation of fields) and kickers (temporal separation of fields)
Transfer lines present interesting challenges and differences from circular machines:
  No periodic condition mean optics is defined by transfer line element strengths and by initial beam ellipse
  Matching is subject to many constraints
  Emittance blow-up is an important consideration, and arises from several sources: mis-steering, mismatch (betatron and dispersion)
  Measurement of beam parameters is important for ensuring beams are well matched between machines and/or experiments
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Thank you for your attention

## Slide 107: Further reading and references
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Lot’s of resources presented at the recent CAS Specialised School:
Beam Injection, Extraction and Transfer, 10-19 March 2017, Erice, Italy
https://cas.web.cern.ch/schools/erice-2017

## Slide 108: Bibliography for Septa
M.J. Barnes, J. Borburgh, B. Goddard, M. Hourican, “Injection and Extraction Magnets: Septa”, CERN Accelerator School CAS 2009: Specialised Course on Magnets, Bruges, 16-25 June 2009, arXiv:1103.1062 [physics.acc-ph].
J. Borburgh, M. Crescenti, M. Hourican, T. Masson, “Design and Construction of the LEIR Extraction Septum”, IEEE Trans. on Applied Superconductivity, Vol. 16, No. 2, June 2006, pp289-292.
M.J. Barnes, B. Balhan, J. Borburgh, T. Fowler, B. Goddard, W.J.M. Weterings, A. Ueda, “Development of an Eddy Current Septum for LINAC4”, EPAC 2008.
J. Borburgh, B. Balhan, T. Fowler, M. Hourican, W.J.M. Weterings, “Septa and Distributor Developments for H- Injection into the Booster from Linac4”, EPAC 2008.
S.Bidon, D.Gerard, R.Guinand, M.Gyr, M.Sassowsky, E.Weisse, W.Weterings, A.Abramov, A.Ivanenko, E.Kolatcheva, O.Lapyguina, E.Ludmirsky, N.Mishina, P.Podlesny, A.Riabov, N.Tyurin, “Steel Septum Magnets for the LHC Beam Injection and Extraction”, Proc. of EPAC 2002, Paris.
J.M. Cravero & J.P. Royer, “The New Pulsed Power Converter for the Septum Magnet in the PS Straight Section 42”, CERN PS/PO/ Note 97-03, 1997.
J.P. Royer, “High Current with Precision Flat-Top Capacitor Discharge Power Converters for Pulsed Septum Magnets”, CERN/PS 95-13 (PO), 1995.
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 109: Bibliography for Kickers
M.J. Barnes, L. Ducimetiére, T. Fowler, V. Senaj, L. Sermeus, “Injection and extraction magnets: kicker magnets”, CERN Accelerator School CAS 2009: Specialised Course on Magnets, Bruges, 16-25 June 2009, arXiv:1103.1583 [physics.acc-ph].
D. Fiander, K.D. Metzmacher, P.D. Pearce, “Kickers and Septa at the PS complex, CERN”, Prepared for KAON PDS Magnet Design Workshop, Vancouver, Canada, 3-5 Oct 1988, pp71-79.
M.J. Barnes, G.D. Wait, I.M. Wilson, “Comparison of Field Quality in Lumped Inductance versus Transmission Line Kicker Magnets”, EPAC 1994, pp2547-2549.
G. Kotzian, M. Barnes, L. Ducimetière, B. Goddard, W. Höfle, “Emittance Growth at LHC Injection from SPS and LHC”, LHC Project Report 1116.
J. N. Weaver et al., “Design, Analysis and Measurement of Very Fast Kicker Magnets at SLAC,” Proc of 1989 PAC, Chicago, pp. 411–413.
L. Ducimetière, N. Garrel, M.J. Barnes, G.D. Wait, “The LHC Injection Kicker Magnet”, Proc. of PAC 2003, Portland, USA, pp1162-1164.
L. Ducimetière, “Advances of Transmission Line Kicker Magnets”, Proc. of 2005 PAC, Knoxville, pp235-239.
W. Zhang, J. Sandberg, J. Tuozzolo, R. Cassel, L. Ducimetière, C. Jensen, M.J. Barnes, G.D. Wait, J. Wang, “An Overview of High Voltage Dielectric Material for Travelling Wave Kicker Magnet Application”, proc. of 25th International Power Modulator Conference and High Voltage Workshop, California, June 30-July 3, 2002, pp674-678.
J. Bonthond, J.H. Dieperink, L. Ducimetikrre, U. Jansson, E. Vossenberg, “Dual Branch High Voltage Pulse Generator for the Beam Extraction of the Large Hadron Collider”, 2002 Power Modulator Symposium, Holloywood, USA, 30 June-3 July 2002, pp114-117.
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 110
Kicker Location | Beam momentum (GeV/c) | # Magnets | Gap Height [Vap] (mm) | Current (kA) | Impedance (Ω) | Rise Time (ns) | Total Deflection (mrad)
CTF3 | 0.2 | 4 | 40 | 0.056 | 50 | ~4 | 1.2
PS Inj. | 2.14 | 4 | 53 | 1.52 | 26.3 | 42 | 4.2
SPS Inj. | 13/26 | 16 | 54 to 61 | 1.47/1.96 | 16.67/12.5 | 115/200 | 3.92
SPS Ext. (MKE4) | 450 | 5 | 32 to 35 | 2.56 | 10 | 1100 | 0.48
LHC Inj. | 450 | 4 | 54 | 5.12 | 5 | 900 | 0.82
LHC Abort | 450 to 7000 | 15 | 73 | 1.3 to 18.5 | 1.5 (not T-line) | 2700 | 0.275
Example parameters for kickers at CERN
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 111
Septum Location | Beam momentum (GeV/c) | Gap Height (mm) | Max. Current (kA) | B (T) | Deflection (mrad) | Septum thickness (mm)
LEIR/AD/CTF (13 systems) | Various | 25 to 55 | 1 DC to 40 pulsed | 0.5 to 1.6 | up to 130 | 1.7 - 19.2
PS Booster (6 systems) | 1.4 | 25 to 60 | 28 pulsed | 0.1 to 0.6 | up to 80 | 1 – 15
PS complex (8 systems) | 26 | 20 to 60 | 2.5 DC to 33 pulsed | 0.2 to 1.2 | up to 55 | 3 - 11.2
SPS Ext. | 450 | 20 | 24 | 1.5 | 2.25 | 4.2 - 17.2
Example parameters for septa at CERN
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Notes: SPS Inj: LHC Ions/LHC Protons
Flux density in kicker magnet aperture typically 100mT (however 300mT for LHC Abort[Dump])

## Slide 112: Blow-up from betatron mismatch
General betatron motion:
Applying the normalisation transformation for the matched beam…
…an ellipse is obtained in normalised phase space:
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 113: Blow-up from betatron mismatch
From general ellipse properties one can write:
Mismatched
beam
Matched
Beam
a
b
Generally
where
Giving:
A
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
Aλ
A/λ
The co-ordinates of the mismatched beam can be expressed:

## Slide 114: Blow-up from betatron mismatch
We can evaluate the square of the distance of a particle from the origin as:
The new emittance is the average for all particles with positions Ai over all phases:
If we’re feeling diligent, we can substitute back for λ:
where subscript 1 refers to the matched and 2 refers to mismatched cases
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
1/2
1/2

## Slide 115: Blow-up from dispersion mismatch
Dispersion mismatch will also introduce emittance blow-up through filamentation much like optical mismatch
Introducing normalised dispersion:
Matched
beam
λDA
A
Mismatched
beam
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018
With a momentum error of the mismatch is:
Rotating the reference frame to a convenient reference (see plot):
And averaging over a distribution of particles, one can write the emittance blow-up as:

## Slide 116: Optics measurement with 3 screens
Remember how we propagate Twiss parameters from s0 to s1:
Giving us three simultaneous equations and three unknowns ε0, α0 and β0:
After a bit of algebra… we find:
✕ e
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 117: Optics measurement with 3 screens
Some (more) algebra with the above equations and we can finally express the beta function at the first screen:
And therefore also the emittance and the divergence of the beta function:
Other methods of emittance measurement:
  Extension of the above method to multiple screens: tomography
  Quad scan: same as above but use one screen and change Mquadscreen
  Direct measurements (lower intensity/energy beams):
    slit-grid or pepper-pot, laser “wire” for H- beams
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018