## Slide 1: K-modulation beta-beat measurements
Alexander Huschauer, Frank Tecker
with many thanks to the OP crew for the support!
Introduction
Measurement results
Comparison to MAD-X

## Slide 2: Introduction
Changing quadrupole gradient by ∆k
=> Tune change
=> Beta
only depends on tune measurement precision and ∆kL model-independent!
transfer function must be well known – hysteresis!
PS low-energy quadrupoles (type 401/402) are coils only
harmonic quadrupole excitation => reduce errors

## Slide 3: Quadrupole excitation
cycle with long injection flat bottom
tunes flattened
sine function added to individual quadrupoles

## Slide 4: First try
expected sine tune variation
cropped sine due to strong coupling
skew quads used to decouple the planes
good sensitivity for decoupling

## Slide 5: Uncoupled!
PR.QSKODD/EVEN 0.40 / -0.38 A
sinusoidal tune variation
excitation amplitude reduced
2 campaigns: QFN/QDN, QFW/QDW
Tunes H 6.21 / V 6.24

## Slide 6: Analysis
5-parameter fit:
Consistency checks
Average of 5 measurements
Errors fully propagated from statistical fit error
Horizontal fit results
QF
QD

## Slide 7: PR.QDW18 polarity
Amplitude of QDW18 inverted in both planes => inverted polarity!!!
17/4/17 Polarity check marked OK
Converter side OK
No intervention since 6/4/17
H
V
Fit amplitude
H

## Slide 8: Beta-beating expected from QDW18 (vs. 6.21/6.24 nom.)
MAD optics 6.21/6.24 with LE quads vs. optics with QDW18 inverted matched to the same tunes

## Slide 9: Beta-beating measured (vs. 6.21/6.24 nom.)

## Slide 10: Beta-beating measured (vs 6.21/6.24 inv.)
Now comparing to the MAD optics with QDW18 inverted

## Slide 11: Beta-beating measured (vs 6.21/6.24 inv.)

## Slide 12: Beta-beating measured (vs 6.21/6.24 inv.)
meanX=1.00089 meanY=1.0040
=> systematic errors < 1%
Fit amplitude X and Y: 0.033

## Slide 13: Conclusion
k-modulation successfully applied at the PS to measure the beta-function model-independent
Polarity inversion of PR.QDW18 found
Measured beating very close to expected one
Residual beating of ~3% in both planes seems to have distributed source
Comparison with Panos’ phase-advance method ongoing
Measurement at 6.19/6.24 to be analyzed
Interesting to measure bare machine and again with corrected polarity

## Slide 14: Spares

## Slide 15: Fit results QN

## Slide 16: Fit results QW