## Slide 1: RF Simulations
Wiebke Liebscher and Salome Schwark
Supervisor: Hermann Pommerenke
Source: Microcosm (CERN)
Notes: Topic: Radiofrequency Simulations  Cavities
Fast changing electrical field to accelerate particles
Background: Old Cavity

## Slide 2
LHC Accelerating Cavities
Source: Microcosm (CERN)
Notes: This is how it looks like in reality

## Slide 3
Source: Microcosm (CERN)
Notes: How it works (alternating field)

## Slide 4: Pill Box Cavity
Set parameters: particle velocity (and charge)
  Frequency and length of the cavity depend on these parameters
Velocity
Frequency
Length
https://www.classe.cornell.edu/public/SRF/2006/SRF060424-03/SRF060424-03.pdf; p.3
Notes: R = Shunt impedance = U0^2 / Ps (Verlorene Leistung ueber der Oberflaeche)
Shunt impedanz = Oberflaechenverluste als Widerstand in einem Schwingkreis

## Slide 5: Further Optimization
(I) Minimize losses
  Cavity as oscillating circuit
  factor: rises with descending losses
(II) Rise Efficiency
  Indicates acceleration efficiency
https://de.wikipedia.org/wiki/Schwingkreis#/media/File:Schwingkreis.svg
https://de.wikipedia.org/wiki/Parallelresonanz#/media/File:KondiSpuleWiderstandParallel.svg

## Slide 6
Notes: First modelling approach: The pill box (Keksdose )

## Slide 7
Notes: Add a beam pipe

## Slide 8
Notes: Blend edges: At edges: Strong magnetic field  Strong surface currents  Huge losses

## Slide 9
Notes: Optimized  (Losses, Frequency)

## Slide 10: E-Field
Notes: In the middle: Strongest field (for acceleration)

## Slide 11
H-Field
Notes: An electrical field always causes a corresponding magnetic field  Even though we do not need it

## Slide 12
Surface Currents
Notes: A magnetic field causes surface currents. As the material is not superconductive there is a resistance (Loss of Energy)
They heat the cavity

## Slide 13
Chart: Change of Q0 during the Optimization Process
| 1 | 2 | 3 | 4
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Q | 25541 | 25533 | 27869 | 37115
Notes: Q0: 1/Losses through surface currents; the bigger the better (Q0, a universal figure of merit characterizing the ratio of the energy stored in the cavity to the energy lost in one RF period)
1-4: Different steps of the optimization process (that we showed before)
As you can see: It gets better  The blended edges minimize the surface currents and therefore the losses

## Slide 14: Acceleration of a Particle
Notes: Electrical field in the cavity
X: Length (0 is the middle), Y the strength of the electrical field
U = E*d bzw bei E nich constant: U = integral of E d d, with Change of E during the Time: E(z) = sin(kz)* Emax(z)
The integral of the electrical field is equal to the

## Slide 15: Elliptical Cavity

## Slide 16
E Field
Surface currents

## Slide 17: Comparison
 | Pill box cavity | Elliptical cavity
Voltage U [MV] | 1 | 1
Q0 [1] | 37122 | 32309
R/Q [Ω] | 159 | 231
Surface emission [1] | 1.94 | 2.92
Magnetic quench [A/V] | 3.28 | 3.19
P [kW] | 169 | 134
Notes: Surface emission: Emax / Eacc  Emax am Rand (immer so) gegenueber dem Beschleunigungsfeld  moeglichst klein damit Feld moeglichst gross (Emax hat natuerliche Schranke)
Magnetic quench: Hmax / Eacc (Bei zu grossem Magnetfeld ist sie nicht mehr supraleitend  PUFF) Quenching: Aus Supraleitung rausfliegen  noch heisser  Snow ball effect

## Slide 18: Feeding the Cavity: The Power Coupler

## Slide 19: Thank you for listening!

## Slide 20: Sources
Belomestnykh, Sergey, and Valery Shemelin. "High-beta Cavity Design-A Tutorial." SRF International Workshop, Ithaca, New York. 2005.
https://de.wikipedia.org/wiki/Parallelresonanz#/media/File:KondiSpuleWiderstandParallel.svg
https://de.wikipedia.org/wiki/Schwingkreis#/media/File:Schwingkreis.svg
Microcosm at CERN
Used program for simulations: CST Microwave Studio

## Slide 21: Coupler
  : Not enough input
  : Too much input
!

## Slide 22: Solving Algorithm