## Slide 1
Preliminary results of the BBLR compensation experiment in LHC during MD4
S. Fartoukh, Y. Papaphilippou, A. Rossi and G. Sterbini on behalf of the BBLR team
42nd HL-LHC TCC, 7th December 2017
BBLR compensation MD team: D. Amorim, G. Arduini, H. Bartosik, R. Bruce, X. Buffat, L. Carver, G. Cattenoz, E. Effinger, S. Fartoukh, M. Fitterer, N. Fuster, M. Gasior, M. Gonzales, A. Gorzawski, G.-H. Hemelsoet, M. Hostettler, G. Iadarola, R. Jones, D. Kaltchev, K. Karastatis, S. Kostoglou, I. Lamas Garcia, T. Levens, A. Levichev, L. E. Medina, A. Mereghetti, E. Métral, D. Mirarchi, J. Olexa, S. Papadopoulou, Y. Papaphilippou, D. Pellegrini, M. Pojer, L. Poncet, A. Poyet, S. Redaelli, A. Rossi, B. Salvachua, H. Schmickler, F. Schmidt, K. Skoufaris, M. Solfaroli, G. Sterbini, R. Tomas, G. Trad, A. Valishev, D. Valuch, C. Xu, C. Zamantzas, P. Zisopoulos and all participants to the design, production and commissioning of the wire compensator prototypes (WP2, WP5, WP13 and LHC MD coordinators).
Notes: Good morning,
thank you for the opportunity to present on behalf of the team the results fo the Beam-beam long-range in LHC
1

## Slide 2
BBCW
B2, left
BBCW
B2, right
2
Aim of wire compensation in MD4
Using the IR5 wires to explore closer beam-wires distance to compensate the octupolar term of the beam-beam in IR5 (partial compensation).
Approach from S. Fartoukh et al., PRST-AB, 18, 121001 (2015)
Due to 2 dumps during the MD, we could explore only the position/currents set .
1
1
2
3

## Slide 3
3
Differences between wires in MD1* and MD4**
* The results of the MD2202 in MD1 were presented in 102nd WP2, 33rd HL-LHC TCC and 7th HL-LHC CM.
** The results of the MD2202 in MD4 were discussed in 112nd WP2.
Wire collimators jaws at 6 scoll
Max current in the wires (350/350 A in R/L wires)
b* = 40 cm
half-Xing angle = 120 mrad
1 train in B1, 3 bunches in B2
Global tune correction
Nominal octupoles.
Wire collimators jaws at 5.5 scoll
Current in the wires (340/190 A in R/L wires)
b* = 30 cm
half-Xing angle = 150 mrad
3 trains in B1, 2 bunches in B2
Orchestrated Q4/5 tune correction
Octupoles at the maximum in B1 and 0 A in B2.
Coronagraph (G. Trad).
1 July ’17 (MD1)
29 November ’17 (MD4)

## Slide 4
4
FILL6434 and FILL6435
FILL6434 dumped on an interlock of the Q4/5 in IR5 for Q-feedforward.
The 2 h at top energy were used for setup time.
FILL6435 dumped on a power supply trip (Q8, not related to the MD).
We could measure only during this fill.

## Slide 5
5
Wires positioning, BU and powering
H/V alignment (collimation team)
Power cycle (3 x ON/OFF)
Horizontal blow-up
2
1
3

## Slide 6
6
MD4 results at 340/190 A and jaw at 5.5 scoll
From elogbook
Approx +7 h of lifetime
OFF
OFF
OFF
ON
ON
ON
Positive effect of the wires visible on beam lifetime.

## Slide 7
From lifetime to effective cross-section
The previous plot is (1) not bunch-by-bunch and (2) the comparison ON/OFF compensation is fair only assuming constant luminosity.
Both limits can be overcome by considering the bunch “effective cross-section”:
Intensity loss-rate
Instantaneous luminosity
The IDEAL compensation, 2 bunches in B2
WIIRES
ON
7
WIIRES
OFF
WIIRES
ON
Notes: 7

## Slide 8
8
Result at 340/190 A and jaw at 5.5 scoll
A. Poyet
Positive effect of the wires visible on the bunch affected by the beam-beam long-range.

## Slide 9
9
Summary and next steps
Despite we could perform only ~1/3 of the planned MD program, the results of the MD4 seem to confirm and improve the observations done during MD1.
In depth analysis of the experiment is ongoing (noise reductions of our observables, sanity checks, simulations and comparison with data from scraping and coronagraph).
In 2018 two additional wires in IP1 (sub-optimal positions): test the 2 IRs compensation (42 h of MD requested*). A meeting is going to be organized (second-half March ’18) to discuss also the 2018 wire MD proposals details.
Thank you for your attention and for HL-LHC,
WP2/5/13 support!
* In 2017 we had 21 h : 10 h (MD1) + 2 h (MD3, QPS problem) + 9 h (MD4).

## Slide 10
10
BACK-UP SLIDES

## Slide 11
11
FILL6435
Beam 1, mild losses due to burn-off
Beam 2, losses dominated by blow-up

## Slide 12
12
Filling scheme
B1 was stable during the two fills.

## Slide 13
13
Result at 340/190 A and jaw at 5.5 scoll
Vertical stability
Horizontal stability
Tune stability

## Slide 14
Integration of the wire in the collimator jaws
14
The wire-beam distance has to be of the order of few mm (function of qc and s-position): LHC wires prototypes are embedded in the jaw of two operational tertiary collimators.
Max. temperature at IW=350 A: 161 oC
During the 2017, BE-BI, EN-STI and the Collimation teams performed a complete test campaign to ensure the correct functioning of the wire interlocks, the collimator motors and PUs when the wire is powered.
Courtesy of F. Carra
Top view
Side view
≈1 m
3 mm
Notes: The wire-beam distance has to be of the order of few mm.
14

## Slide 15
The BBCW position in LHC
15
The 2 BBCWs were installed in two H-collimators of B2 in IR5 (TCTPH.4R5.B2 and TCL.4L5.B2), close to the D2 separation dipoles.
Longitudinal position of the BBCW and optics used in the experiment
The ideal s-position of the BBCW is ±159 m from the IP5. The actual s-position are -150.03 and +147.94 m.
H-plane position of the BBCW
Notes: 15

## Slide 16
First results from LLRB MD
16
Result on the compensation (II)
Using dBLM signals to compute the cross-section [credit to A. Poyet, A. Gorzawski]: improved time resolution.
A constant calibration factor was adopted to rescale the BLM reading to the FBCT losses.
ON ⇾ OFF
ON ⇾ OFF
Wire
compensation
STEP 3
Notes: 16

## Slide 17
17
Analysis of the BBCW compensation
Given the constraint on the minimal beam-wire distance, it was not possible to compensate all the resonances excited by the B1.
We used the maximum current of the wires (350 A) to attack as much as possible the BBLR octupolar term.
The octupolar terms induced by the BBLR in IR5 was reduced by 75%.
Strong-beam driven resonance
BBCW driven
resonance
S. Fartoukh et al.
PRST-AB 18, 121001
Notes: 17

## Slide 18
18
Compensation studies: from LHC to HL-LHC
In the beam-beam team significant efforts are put on the wire compensation tracking studies with the two-fold aim to benchmark the LHC results and optimize the HL-LHC scenario with the wires.
For HL-LHC, preliminary results without a full optimization of the longitudinal and transverse wire position, are showing an additional gain of the order of 30 mrad for the half-crossing angle.
+ 30 mrad
Preliminary.
HL-LHC start of the levelling
Distance Beam-Wire [s, en=2.5 mm]
21
8.4
12.6
16.8
Courtesy of D. Pellegrini
Notes: 18

## Slide 19
19
PACMAN bunches and Iw modulation
The needed Iw modulation BW is of the order of 4 MHz (x10 lower than the bunch frequency).
The wavelength in vacuum of a 4 MHz EM wave is ~75 m.

## Slide 20
20
Numerical results from the RDT
We will use the RDT criterion presented and described in details in
Goal: compensate the BBLR RDTs by using 2 BBCs per IP.
Assuming
  the same Nw and dw for both BBCWs,
  that the strong beam acts as a DC wire,
  that the phase advance between BBLRs and BBLRs/BBCW is 0 or 180 deg.
the paper gives Nw and dw to compensate 4 RDTs (p1q1, q1p1, p2q2, q2p2) in closed form.
It is shown as a numerical evidence that by compensating 4 RDTs one can minimize ALL RDTs if the position of BBCW is conveniently chosen.
Using the paper’s formalism, we will show numerical results on the present LHC (2017 ATS).
Strong-beam driven RDTs
BBCW driven RDTs
Notes: 20

## Slide 21
21
IDEAL CASE: 2 BBCW for IP at sopt=+-159 m
The green boxes are the 4 RDTs used to set Nw and dw
in color code
RDT compensation map
As expected (under the mentioned assumptions) the compensation is covering many more RDTs than the 4 used to set the BBCWs (green boxes). The p+q=1 and p+q=2 could be addressed by using “local” linear magnets (Q4s and the Q4 correctors).
dipole driven
quad driven
Notes: 21

## Slide 22
22
The MD results and the RDT
Real phase advance considered
Ideal phase advance considered (b*→0)
The observed effect of the BBCW can be related to a partial compensation of the detuning terms.
Notes: 22

## Slide 23
23
IDEAL CASE: considering the phase advance.
One can quantify a posteriori the effect of the phase advance.
The compensation of the RDT does degrade. The compensation of detuning terms (Q-footprint compression) is not affected.
Real phase advance considered
Ideal phase advance considered (b*→0)
Notes: 23

## Slide 24
DA simulations with Wire in MD-like conditions I
24
Good agreement between footprints from MADX and Sixtrack.
Improvement observed but no clear identification of the optimum.
MD-like conditions: dw=8 mm. LR in IR1/5 but wire only in IR1, real aspect ratio at wire position, phase advances.
A modest gain of DA is observed for 8 mm wire-beam distance.
Optimal DA for 800 A.
With no rematch of the chromaticity (as in the MD), the gain of DA is improved.
K. Skoufaris

## Slide 25
DA simulations with Wire in MD-like conditions II
Push dw to 6 mm
Still not ideal conditions: LR in IR1/5 but wire only in IR1, aspect ratio at wire position, phase advances.
1σ (@2.5 μm) DA gained for an optimal wire current of ~400 A.
Clear improvement over all the angles.
25
0 A
400 A
K. Skoufaris