## Slide 1: CEPC Injector Linac Design
Xiaoping Li, Cai Meng, Guoxi Pei, Jingru Zhang,, Dou Wang, Chenghui Yu, Jie Gao, Shilun Pei, Yunlong Chi
Institute of High Energy Physics, CAS, Beijing
环形正负电子对撞机
Circular Electron Positron Collider

## Slide 2: Outline
Introduction
  Main parameters
  Layout of Linac
Source design
  Electron source
  Positron source
Linac design
  Electron/Positron mode
  Error study
Summary

## Slide 3: Outline
Introduction
  Main parameters
  Layout of Linac
Source design
  Electron source
  Positron source
Linac design
  Electron/Positron mode
  Error study
Summary

## Slide 4: Introduction
  Main parameters
Linac design goal
  High Availability and Reliability
    Simple structure and mature technology: S-band accelerating structure as baseline(2856.75MHz)
  Always should provide beams that can meet requirements of Booster
  Should be have potential to meet the higher requirements and updates in the future
Parameter | Symbol | Unit | Value | Potential
e- /e+ beam energy | Ee-/Ee+ | GeV | 10 | >10
Repetition rate | frep | Hz | 100 | 
e- /e+ bunch population | Ne-/Ne+ |  | >9.4×109 | >1.9×1010
 |  | nC | >1.5 | >3
Energy spread (e- /e+ ) | σE |  | <2×10-3 | 
Emittance (e- /e+ ) | εr | nm | <120 | <40
e- beam energy on Target |  | GeV | 4 | 
e- bunch charge on Target |  | nC | 10 | 

## Slide 5: Introduction
Layout of Linac
ESBS ( Electron Source and Bunching System)
  50 MeV && 11nC for positron production
ESBS
FAS
PSPAS
SAS
DR
TAS
50MeV
4GeV
1.1GeV
4GeV
10GeV
200MeV
SAS (the Second Accelerating Section)
  Positron beam to 4 GeV && 3 nC
DR (Damping Ring)
  Positron beam 1.1GeV, 60m
Positron Linac
PSPAS (Positron Source and Pre-Accelerating Section)
  Positron beam larger than 200 MeV && larger than 3 nC
FAS (the First Accelerating Section)
  Electron beam to 4 GeV && 10nC for positron production
TAS (the Third Accelerating Section)
  Positron beam to 10 GeV && 3 nC

## Slide 6: Introduction
Layout of Linac
ESBS ( Electron Source and Bunching System)
  50 MeV && 3 nC
ESBS
FAS
TAS
50MeV
4GeV
4GeV
10GeV
EBTL (Electron Bypass Transport Line)
  Electron beam @ 4 GeV && 3 nC
Electron Linac
EBTL
PSPAS
SAS
DR
1.1GeV
200MeV
FAS (the First Accelerating Section)
  Electron beam to 4 GeV && 3 nC
TAS (the Third Accelerating Section)
  Electron beam to 10 GeV && 3 nC

## Slide 7: Introduction
Layout of Linac
EBTL
ESBS
FAS
PSPAS
SAS
DR
TAS
50MeV
4GeV
1.1GeV
4GeV
10GeV
200MeV

## Slide 8: Outline
Introduction
  Main parameters
  Layout of Linac
Source design
  Electron source
  Positron source
Linac design
  Electron/Positron mode
  Error study
Summary

## Slide 9: Source design
Thermionic Triode electron gun
Sub-harmonic pre-buncher
  142.8375 MHz
  571.35 MHz
Buncher & A0
  2856.75 MHz
Emittance
  <100 mm-mrad (Norm.Rms) @11nC
Transmission
  ~90%
Electron source
Parmela

## Slide 10: Source design
Positron source
Layout of positron source
  Target (Conventional)
    tungsten@15 mm
    Beam size: 0.5 mm
  Electron Beam
    4GeV/10nC/100Hz
    Beam power 4kW
  Energy deposition
    0.784 GeV/e- @ FLUKA
    784 W  water cooling
  AMD (Adiabatic Matching Device)
    Flux Concentrator
    Length: 100mm
    Aperture: 8mm26mm
    Magnetic field: (5.5T0T) + 0.5T
Notes: .

## Slide 11: Source design
Layout of positron source
  Capture & Pre-accelerating structure
    Length:2 m
    Aperture: 25 mm
    Gradient: 22 MV/m
  Chicane
    Wasted electron separation
  Norm. RMS. Emittance
    ~2400 mm-mrad~120nm@10GeV
  Energy: >200 MeV
  Positron yield
    Ne+/Ne- > 0.5 @ [-8°,12°,235MeV, 265MeV]
Positron source

## Slide 12: Outline
Introduction
  Main parameters
  Layout of Linac
Source design
  Electron source
  Positron source
Linac design
  Electron/Positron mode
  Error study
Summary

## Slide 13: Linac design
Electron linac
Focusing device: Triplet
  1 triplet+4 Acc. Stru.1 triplet+8 Acc. Stru.
Operation mode :
  High charge mode (positron production)
    4GeV & 10 nC
    ESBS+FAS
  Low charge mode (electron injection)
    10 GeV & 3 nC
    ESBS+FAS+EBTL+TAS

## Slide 14: Linac design
Electron linac Electron injection
Low charge mode
  10 GeV with 3 nC charge
  Energy spread (rms): 0.15%
  Emittance (rms): 5 nm

## Slide 15: Linac design
Electron linac Positron production
High charge mode
  4 GeV with 10 nC charge
  Energy spread (rms): 0.6%

## Slide 16: Linac design
PSPASSAS (DR) +TAS
  SAS: 200 MeV4 GeV
  Damping Ring @ 1.1 GeV
  TAS: 4GeV10 GeV
Transverse focusing devices
  FODO structure at low energy
  Triplet at high energy
Positron linac

## Slide 17: Linac design
Positron linac
Positron linac
  10 GeV with 3 nC charge
  Energy spread (rms): 0.16%
  Emittance with DR (rms): 40(H)/24nm(V)

## Slide 18: Linac design
Whole Linac
  One-to-one correction method for both e- and e+
  Errors: Gaussian distribution, 3σ truncated
Beam orbit
  <1mm
  <0.5mm at high energy region
Misalignment errors with correction
Error description | Unit | Value
Translational error | mm | 0.1
Rotation error | mrad | 0.2
Magnetic element field error | % | 0.1
BPM uncertainty | mm | 0.1
e-
e+

## Slide 19: Linac design
4GeV Electron Linac with high charge
  Method: First orbit correction + multi-particles simulation
  Low charge
    Beam orbit can be controlled well
  High charge
    Misalignments of Acc. Tubes
    Wakefield
  In a real operation, correction is based on multi-particles orbit, so the orbit and emittance growth can be controlled better.
Misalignment errors with correction

## Slide 20: Linac design
Field errors
Simulation condition
  5000 seeds
  Accelerating structure
    phase errors and amp errors
    4 accelerating structures in one KLY
    3σ--Gaussian
Energy jitter: 0.2%
Energy spread < 0.2%
  Phase errors: 0.5 degree (rms)
  Grad. errors: 0.5% (rms)

## Slide 21: Linac design
Damping Ring
DR V1.0 | Unit | Value
Energy | GeV | 1.1
Circumference | M | 58.5
Repetition frequency | Hz | 100
Bending radius | M | 3.62
Dipole strength B0 | T | 1.01
U0 | keV | 35.8
Damping time x/y/z | ms | 12/12/6
0 | % | 0.05
0 | mm.mrad | 287.4
Nature z | mm | 7 (23ps)
inj | mm.mrad | 2500
ext x/y | mm.mrad | 704/471
inj /ext | % | 0.3/0.06
Energy acceptance by RF | % | 1.0
fRF | MHz | 650
VRF | MV | 1.8
@ D. Wang

## Slide 22: Outline
Introduction
  Main parameters
  Layout of Linac
Source design
  Electron source
  Positron source
Linac design
  Electron/Positron mode
  Error study
Summary
Notes: Next is the linac design

## Slide 23: Summary
The CEPC linac works with 100 Hz repetition, 10 GeV and one-bunch-per-pulse, which can meet the requirements of Booster;
The linac have the potential to provide positron beam and electron beam with bunch charge larger than 3nC;
One preliminary damping ring is proposed, the emittance with DR is smaller than 40 nm;
Up to now, there’s no bottleneck in linac design and further works continues.

## Slide 24
Thank you!

## Slide 25: Dynamic aperture with errors
 | DA requirement |  | DA results | 
 | H | V | H | V
10GeV (x= y =120nm) | 4x +5mm | 4y +5mm | 7.7x +5mm | 14.3y +5mm
120GeV (x=3.57nm, y= x*0.005) | 6x +3mm | 49y +3mm | 21.8x +3mm | 779y +3mm
10GeV
BSC
120GeV
w damping
With only COD corrections, DA is nearly two thirds of bare lattice
At 120GeV, radiative damping was considered.
DA requirement @ 10GeV determined by the beam stay clear region
DA requirement @ 120GeV: 1) H- quantum lifetime, 2) V- re-injection process from the collider in the on-axis injection scheme
Requirement for linac emittance: < 150nm, otherwise BSC > beam pipe