## Slide 1
Dark Matter Axion Search Experiments Using 18T HTS Magnet at CAPP/IBS in KAIST
ICHEP 2018
Byeong Hun Min
Center for Axion and Precision Physics Research
IBS
833 [5 Jul , 09:40]

## Slide 2
Outline
Axion as dark matter
Important factors for Axion search
  HTS Magnet (18T)
  Cryostat (4K)
  Cavity
  DAQ system
3. Results from our present setup
4. Factors improvement
  Dilution refrigerator (~20 mK) with 18 T magnet
  JPC : First stage amplifier
  Cancellation magnet
Our Project

## Slide 3
Axion as a Dark Matter
• Non-thermal mechanism of producing axion dark matter in the early Universe • The initial axial angle Θ determines the potential energy to be released. • The potential energy density (order of ΛQCD4) is converted into cold dark matter • Axion dark matter mass is determined by the harmonic oscillator frequency ma ≃ ΛQCD2/fa < 10-3 eV !
ΛQCD4
VEV : fa > 109GeV
Invented to solve the strong-CP problem in QCD

## Slide 4
Axionic
Dark Matter
playground
Axion Dark Matter Search
Ωa>1
NN➜NNa
Axion potential energy decays at time t~1/ma. If this is too late (too small ma) in cosmological time the dark matter can be overproduced relative to the photons
DFSZ
Warm
dark matter

## Slide 5
Axion Haloscope

## Slide 6
CAPP’s Dark Matter Axion Search Strategy
Strong magnetic field (18T)
Lower the thermal noise temperature
of first stage amplifier
High Q cavity (Q~106)

## Slide 7
18T HTS Magnet (7cm Bore)
A strong B-field and large bore
HTS magnet can be commercially
produced by SuNAM Co. Ltd.
2G HTS Superconducting Magnet
Magnetic field : 18 Tesla
Dimension: 70 mm ID / 168mm OD 200 mm uniform field (>90%) 552 mm length
Quench free design (No-Insulation winding)
Compact and easy to operate
The magnet delivery by summer 2017
Initial DM axion mass range to probe:
17 to 36 μeV
(Later we will apply multiple cavity method
to probe higher mass range search)

## Slide 8
44 double pancake coils
18 T no insulation magnet
476 mm
18 Tesla magnet
1st coil
for 25 T magnet
25 Tesla magnet
18 T was delivered in 2017.
to be delivered in 2020
non insulation type
No quench in LHe

## Slide 9
18T HTS Magnet with 4 K Cryostat
Measurement program
Related Poster : JongKuk Kim( 6 July 2018, 18:30)
Uniformity: 93%(±100 mm)
Stability: <0.05% in 2 weeks
The cavity resonance frequency is tuned by tuning rod which is controlled by stepper motor
Very high quality of our HTS magnet.

## Slide 10
Red :TM 010
Green : TM 01m
Blue : TE11m
Simulation of frequency in cavity
Related Poster : YoungJae Lee (6 July 2018, 18:30)
Red :TM 010
Dielectric rod
Conducting rod
The dielectric rod has lower frequency than conducting rod .
We use the red line (TM010 mode )for axion search.
The third factor for axion search is high Q-value cavity

## Slide 11
Cavity
● Scanning Rate vs. Length of Cavity
Scan Rate
Length of Cavity [mm]
0
100
200
300
400
500
600
max rate
length of
magnet
(467.8mm)
assuming
uniform C
Detailed
simulation
of E and B
Q(300K)=~24,000
Q(4K)=~73,000

## Slide 12
Cavity
Weak
Circulator
Coupling
Cryogenics-part
Radio frequency(RF)
Amplifier
Band pass filter(BPF)
Mixer
Local oscillator (LO)
Intermediate frequency(IF)
Amplifier
Isolator
Network
Analyzer
(NA)
Input
Output
Switch C
Spectrum
Analyzer
(SA)
Signal
Genrator
(SG)
Low noise amplifier
(LNA)
coupler
coupler
2
1
2
1
2
1
Swtich A
2
1
Switch B
Switch D
Band pass filter(BPF)
Room temperature amplifier
RF chain configuration
Signal generator
Spectrum analyzer
Network analyzer
DAQ System
Room T. amp.
It can be switched with 4 states by program (S11,S21,S22,SA)
Room temperature(RT)-part
Cryo- and room temp. DAQ system

## Slide 13
Tuning rod
Cavity cross section
Measurement of the resonant frequency in the copper cavity
We measured the resonant frequency of our cavity with dielectric tuning rod.
Temp: 4 K
B : 18 T

## Slide 14
From signal generator(f)
Noise measure
Background Noise at 4 K (under 18 T)
f = 4.227655 GHz
(Down converted IF )
T : 4 K
H : 18 T

## Slide 15
Combination of Dilution refrigerator and 18 T magnet
At present, we are going to improve our experimental setup.
the new cryostat
the new IVC for dilution unit and cavity

## Slide 16
Related Poster : JiYoung Lee
Josephson Parametric Converter (JPC : Quantum Limit Amplifier)
Inside
Outside
Flux Maps
High Frequency Mode
Low Frequency Mode
Bias current (mA)
Gain(20 dB min) | Fmin (GHz) | fmax (GHz)
High frequency | 7.72 | 8.802
Low frequency | 4.757 | 5.01
Flux maps were measured from our JPC.
JPC in hand
Delivered in May 2018
4 K exp. : HEMT amp.(2 K Noise Temp.)
Improve the 1st stage amp.
From this maps, we find the two frequency range.
Bias current (mA)
Next plan : Measure the noise temperature of JPC

## Slide 17
Cancellation Magnet Development
5 gauss
● Cancel out ~kG of stray field to a few G
● Field stability ~25ppm/hr
● Field profile test & quench test passed
Field cancel region
Delivered in Nov 2017
Cancellation Coil
The main purpose of it is cancellation of magnetic field around the JPC
Need the cancellation magnet for JPC operation in 18 T

## Slide 18
Installation of improvement factors for experiment
Dilution Refrigerator
Magnet
Cancellation magnet
JPC
Cavity
DAQ
Magnetic field : 18 T
Noise temperature : 500 mK
Q-factor : 70,000
Real time DAQ : 80% (efficiency)
(Physical temperature : 20 mK)
Our experimental setup will be installed with this condition.

## Slide 19
SQUID
JPA/JPC
CAPP18T
Projected Axion Search Goal
We will probe the axion with Dilution and JPC and so on.

## Slide 20
Summary
We use 18 T HTS solenoid magnet for Axion Haloscope research.
We measured the TM modes in the cavity at 4 K(under 18 T)
We will install the dilution refrigerator and 18 T magnet in October.
We will sure probe the dark matter Axion in the range of 17 ̴ 36 μeV.
(f : 3.7 ̴ 8.8 GHz)