## Slide 1: de Laval Micro-nozzle comparison with simple geometry nozzle CFD simulations in 2D
Przemysław Smakulski
Sławomir Pietrowicz
07-12-2017
Wrocław University of Science and Technology

## Slide 2: Specification
Dimensions for de Laval nozzle was taken from the file delivered from the CERN machine shop
In the present research has been shown the comparison between a „de Laval” nozzle and simple geometry nozzle (previos calculations given by Paolo)
Simulations were performed for nitrogen

## Slide 3: Numerical Domain: 2D simulation
Adiabatic wall
Inlet BC type: opening
Outlet BC type: opening
Rotational periodicity
Symmetry edge

## Slide 4: Numerical mesh
Mesh statistics:
Number of Nodes: 68418
Number of Elements: 33429
Hexahedra: 33429
200 mm
60 mm
Detailed view on mesh close to neuralgic part of the domain
Dcritical

## Slide 5: Boundary conditions
Case no. | Inlet |  | Outlet | 
 | Pressure* | Temperature | Pressure* | Temperature
Dcritical = 10 microns |  |  |  | 
1 | 1 bar | 20oC | 0 Pa | 20oC
2 | 3 bar | 20oC | 0 Pa | 20oC
3 | 10 bar | 20oC | 0 Pa | 20oC
Dcritical = 30 microns |  |  |  | 
4 | 10 bar | 20oC | 0 Pa | 20oC
* - absolute pressure

## Slide 6: Velocity profile Dcritical = 10 microns
Case no.1
p_INLET = 1 bar
Case no.2
p_INLET = 3 bar
Case no.3
p_INLET = 10 bar

## Slide 7: Velocity profile Dcritical = 10 microns
Case no.3
p_INLET = 10 bar

## Slide 8: Mach number close to critical cross-section Dcritical = 10 microns
Case no.1
p_INLET = 1 bar
Case no.2
p_INLET = 3 bar
Case no.3
p_INLET = 10 bar
supersonic
subsonic

## Slide 9: Comparison with the simple geometry nozzle
For the comparison reson the critical diameter of the de Laval nozzle was increased from 10 microns to 30 microns. The same value of the critical diameter (30 microns) is presented in the simple geometry nozzle.
Test was performed with similar boundary conditions.

## Slide 10: Simulations comparison: global pressure
Present simulation
D_critical = 30 microns
Previous simulation
Non

## Slide 11: Velocity Profile
De Laval
Simple Geometry
Side view

## Slide 12: Conclusions
The numerical simulation for the proposed de Laval nozzle with 10 microns critical diameter has been performed with high convergence level (under RMS factor 10-6)
De Laval construction of the nozzle provides better concentration of the beam and higher density in further distance from the nozzle outlet
Between planes C and D could be an optimal place for the placement of the 1st skimmer

## Slide 13: Complementary post-processing

## Slide 14: Profile planes position - de Laval nozzle
De Laval
14.5mm
10mm
10mm
10mm
A
B
C
D
Planes:
nozzle throat 10 mm
Comparison between those two cases

## Slide 15: Velocity Profile
p_INLET = 3 bar
Plane A
1.9 mm
1.9 mm
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 16: Velocity Profile
Plane B
8 mm
8 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 17: Velocity Profile
Plane C
14 mm
14 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 18: Velocity Profile
Plane D
18 mm
18 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 19: Density Profile
Side view
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 20: Density Profile
p_INLET = 3 bar
Plane A
2.3 mm
2.1 mm
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 21: Density Profile
Plane B
6 mm
6 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 22: Density Profile
Plane C
8 mm
8 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 30 mm

## Slide 23: Density Profile
Plane D
4.5 mm
4.5 mm
p_INLET = 3 bar
p_INLET = 10 bar
nozzle throat 10 mm

## Slide 24: Profile planes position
De Laval
Simple Geometry
14.5mm
10mm
10mm
10mm
10mm
10mm
10mm
A
B
C
D
Planes:
A
B
C
D
nozzle throat 30 mm
Comparison between de Laval nozzle and simple geometry nozzle pinlet = 10 bar

## Slide 25: Velocity Profile
De Laval
Simple Geometry
Plane A
1.7 mm
0.29 mm
nozzle throat 30 mm

## Slide 26: Velocity Profile
De Laval
Simple Geometry
Plane B
4.3 mm
4.7 mm
nozzle throat 30 mm

## Slide 27: Velocity Profile
De Laval
Simple Geometry
Plane C
7.6 mm
9 mm
nozzle throat 30 mm

## Slide 28: Velocity Profile
De Laval
Simple Geometry
Plane D
14 mm
12 mm
nozzle throat 30 mm

## Slide 29: Density Profile
De Laval
Simple Geometry
Side view
nozzle throat 30 mm

## Slide 30: Density Profile
De Laval
Simple Geometry
Plane A
1.1mm
0.025mm
nozzle throat 30 mm

## Slide 31: Density Profile
De Laval
Simple Geometry
Plane B
2.5 mm
3.2 mm
nozzle throat 30 mm

## Slide 32: Density Profile
De Laval
Simple Geometry
Plane C
8 mm
6 mm
nozzle throat 30 mm

## Slide 33: Density Profile
De Laval
Simple Geometry
Plane D
10 mm
9 mm
nozzle throat 30 mm