## Slide 1
Digesting the LIU high brightness beam: is this an issue for HL-LHC?
Asked to cover:
  Beam stability
  Electron cloud effects
  Emittance preservation
Here most of the messages and material, I still need to:
  Organize
  Compress
  Remove “technicalities”
  Acknowledge!

## Slide 2
Beam stability
[Introductory slide with overview of the work done and some references]
Main points reported in the following…

## Slide 3
Coupled bunch instabilities
CC HOMs
Growth rate (arb. un.)
Growth rate of the most critical CB mode 1 HOM, Q’ = 10, d = 100 turns
Picture illustrating
HOM optimization
Presently driven mainly by resistive-wall impedance
The beam is stabilized using the transverse damper  no problem expected for HL-LHC (there is room to increase damper gain)
Crab cavity High Order Modes (large beta) identified as additional source for CB instabilities and damper ineffective for high frequency HOM
  Impedance carefully optimized by the design team in collaboration with the impedance team

## Slide 4
Impedance-driven head-tail instabilities
Part of today’s LHC life:
  Single-bunch (head-tail) instabilities controlled by damper and a large enough tune spread (Landau damping) relying on:
    Octupole magnets in the arcs
    Beam-beam effects (when in collision)
  Octupole current required to operate reliably (i.e. also in real-life non ideal conditions) is significantly larger than expected from model
    we should keep these margins!
Main instability source is the impedance from collimators:
  Impedance reduction is part of the HL-LHC baseline
Requirement from model
BCS beams
Octupole currents at 6.5 TeV during the 2017 run
Maximum current for octupole circuits

## Slide 5
Low impedance collimators
Low impedance design confirmed experimentally by prototype installed in the LHC in 2017
Everything else - < 10 A
All other collimators - 70 A
4 primaries - 100 A
11 secondaries in IR-7 - 200 A
Impedance reduction for the collimators is part of the LHC baseline

## Slide 6
More critical at high energy due to tighter collimator gaps
Coupling between mode 0 and mode -1 is the most critical
No instability observed up to 1.9e11 p/bunch (with no margins we hand 2e11 ~1.5um in collision)
TMCI threshold can be inferred from mode-0 tune shift (instab. thresh: DQ = Qs)
Present LHC impedance
HL-LHC impedance
(after collimator impedance reduction)
Simulated opening collimators (in tests with very small number of bunches)
Transverse Mode Coupling instability (TMCI)
Instability
Instability

## Slide 7
Oct [A]
Chromaticity
6.5
5/5
13
5/5
13
10/10
13
15/15
26
15/15
52
15/15
52
10/15
52
20/15
Bunch-by bunch emittance measurements
PyECLOUD-PyHEADTAIL
simulation studies
  EC in quadrupoles (7% of the machine) alone is a key driver of instabilities at the LHC injection energy
    Simulations allowed explaining instabilities observations  large chromaticity values, relatively high octupoles current and a fully functional feedback system were needed to reach a satisfactory emittance preservation
    instability suppressed when increasing the beam energy up to 6.5 TeV due to the increased beam rigidity
(1) A. Romano et al., “Electron cloud induced instabilities in the LHC”, presentation at the Joint Ecloud-PyHEADTAIL Meeting
Electron cloud instabilities

## Slide 8
Electron cloud instabilities
  Simulation results show that the beam intensity increase foreseen by the HL-LHC has a beneficial impact on the beam stability
  Unlike LHC, the EC in quadrupoles in HL-LHC is not expected to drive the beam unstable both at injection and flattop energy after conditioning  provided that intensity dependence from build-up simulations is confirmed experimentally
    Psotential mitigation strategies have been investigated  strong stabilizing effect from large chromaticity values and mild effect from octupoles and damper

## Slide 9
Importance of controlling:
  Tunes
  Linear coupling
  Amplitude detuning
  “a4 wall”
  Linear and non-linear chromaticity
More challenging with low b* and can be impacted in non-trivial ways by beam-beam, e-cloud, etc…
More in rogelio’s talk…
Impact of optics control on transverse stability
[Add some example]

## Slide 10
Electron cloud effects
[Introductory slide with overview of the work done and some references]
Main points reported in the following…

## Slide 11
A challenge for LHC operation with 25 ns in Run 2: total load on the cryo-plants dominated by beam induced heating on arc beam screens
Much larger than expected from impedance and synchrotron radiation
Large differences observed between sectors
Several observed features compatible with e-cloud effects
Being followed-up by dedicated Task Force led by L. Tavian
LHC experience
More info can be found here
Heat load
per half cell

## Slide 12
In Run 2 configuration: small contributions from impedance and synchrotron radiation  used large available margins to cope with e-cloud
When moving to larger beam intensities (and to 7 TeV) the margin reduces strongly
Arc heat loads from impedance and synchrotron radiation
Maximum allowed by cryogenics
Margin
~7 kW
e-cloud S12
(2017)
~6 kW
Margin
~4 kW
2556b
1.1e11 p/bunch
6.5 TeV
2748b
2.2e11 p/bunch
7 TeV
e-cloud S34
(2017)
~2kW

## Slide 13
Arc heat loads – effect of bunch intensity
  Assessed with PyECLOUD simulations:
  The dependence of the heat load on the bunch intensity strongly depends on the surface properties (SEY parameter)
  The expected dependence on the bunch intensity is strongly non linear
  Full experimental validation of these curves possible only after LS2
Dipole
Quadrupole
Drift

## Slide 14
Arc heat loads: simulations for HL-LHC
  HL-LHC
  8 kW/arc (~160W/hcell)
  Present situation in the low-load sectors
  For high bunch intensity significant heat load is observed already for low SEY (from impedance, synchrotron radiation, photoelectrons in the drifts)
  Present conditioning achieved in the low-load sectors is compatible with HL-LHC
e-cloud in dipoles
e-cloud in quadrupoles
e-cloud in drifts
Impedance
Synchrotron radiation

## Slide 15
  For high bunch intensity significant heat load is observed already for low SEY (from impedance, synchrotron radiation, photoelectrons in the drifts)
  Present conditioning achieved in the low-load sectors is compatible with HL-LHC
  Expected heat load for the high-load sectors is ~10 kW/arc  not acceptable for HL-LHC
    Ongoing work to identify and suppress the source of differences among arcs is very important for HL-LHC
Arc heat loads: simulations for HL-LHC
  HL-LHC
  8 kW/arc (~160W/hcell)
  Present situation in the high-load sectors
e-cloud in dipoles
e-cloud in quadrupoles
e-cloud in drifts
Impedance
Synchrotron radiation
[Mention also importance of coatings in ITs and SAMs]

## Slide 16
8b+4e scheme
Filling pattern designed to suppress the e-cloud build-up (~30 % less bunches w.r.t. nominal)
Confirmed experimentally in the LHC in 2015 (for 1.1e11 p/bunch)
  Tests with ~1.7e11 p/bunch should be conducted in 2018
Included in the HL-LHC TDR as backup scenario in case issues with e-cloud
Average
Impedance+synch. rad
Standard 25 ns beam
Dipoles (instrumented cells in S45)
“8b+4e” beam
Dipoles (instrumented cells in S45)

## Slide 17
8b+4e scheme
Standard 25 ns trains and 8b4e trains can be combined in the same filling scheme in order to adapt the heat load to the available cooling capacity (tested in MD in 2016)
25 ns (2556b)
8b+4e (1916b)
Used in operation in the last part of the 2017 Run (to mitigate fast losses in 16L2)
8b+4e
25 ns
Measurement J. Esteban Muller

## Slide 18
Mixed filling schemes
Total heat load including e-cloud for different surface states
Heat load from impedance and synchrotron radiation
Cryogenics limit
Assumed e-cloud suppression factor with 8b+4e as observed in the worst sector (S81) in 2017
Built a simple model to optimize the “mixed scheme” to the available cooling capacity

## Slide 19
Mixed filling schemes
Built a simple model to optimize the “mixed scheme” to the available cooling capacity
Cryo limit
Cryo limit
Pure 8b+4e

## Slide 20
Failure scenario B
e-cloud scaling with intensity is found to be worse than expected
Present LHC conditioning state cannot be improved
Perf. loss with pure 25ns:
from ~25% to very bad
Perf. loss with mixed:
from ~12% to 28%
Mixed filling schemes
Built a simple model to optimize the “mixed scheme” to the available cooling capacity
Cryo limit
Cryo limit
Pure 8b+4e
Failure scenario A:
e-cloud scaling with intensity is confirmed by experiment
Present LHC conditioning state cannot be improved
Perf. loss with pure 25ns: ~25 %
Perf. loss with mixed: ~12 %

## Slide 21
Mixed filling schemes
Built a simple model to optimize the “mixed scheme” to the available cooling capacity
Cryo limit
Cryo limit
Pure 8b+4e
Pure 50 ns
Mixed 50ns/25ns
Mixed 8b+4e/25ns
Considered also 50ns/25ns mixed scheme:
Assumed ideal e-cloud suppression for 50 ns
We know from Run1 that e-cloud is suppressed with 50 ns for Ib<=1.7e11 p/bun (but at 4 TeV…)
Performance is only slightly worse than 25ns/8b+4e
Can be considered as backup for a “Failure scenario C” in which e-cloud suppression with 8b+4e is found to degrade with bunch charge

## Slide 22
Emittance preservation
[Introductory slide with overview of the work done and some references]
Main points reported in the following…

## Slide 23
  Assumptions made for HL-LHC performance estimates:
    Blow-up from Intra-Beam Scattering (IBS) is included in the model
    10% additional blow-up (0.3 mm) is assumed from end-of-injection to collisions
  These are significantly better than presently achieved in the LHC (for nominal intensity):
    Observed increase from injection to collisions ~0.8 mm
    Additional blow-up in collisions (on top of IBS) ~0.07 mm/h
  These figures are observed to be practically independent on the injected intensity/brightness
  Studies to be conducted in 2018 to better identify the sources and device possible mitigations
Emittance preservation
  To assess possible performance degradation applied LHC observed blow-up to HL-LHC cases:

## Slide 24
Emittance preservation: impact on performance
The impact of the extra blow-up on the expected performance is very small, as during a large fraction of the fill we can use b* to compensate
But with large emittances it can become tricky to ensure the required beam-beam separation…
Lim. for 6s DA

## Slide 25
Emittance preservation: backup scheme (BCMS)
Low emittance beams from the injectors (BCMS) can be used to restore the required beam-beam separation

## Slide 26
Filling schemes: standard vs BCMS
25ns_2760b_2748_2494_2572_288bpi_13inj_800ns_bs200ns
25ns_2748b_2740_2250_2376_240bpi_13inj_800ns_bs200ns
25ns_2748b_2736_2251_2375_288bpi_12inj_800ns_bs200ns
Standard (288b./inj.)
BCMS (288b./inj.)
BCMS (240b./inj.)
With 200 ns and 800 ns kicker gaps the three schemes are practically equivalent
Easier for the injectors: less time at SPS flat-bottom, less demanding for protection devices

## Slide 27
Emittance preservation in collisions
Stronger head-on beam-beam interactions (larger tune spread) will enhance the emittance growth due to coherent excitations  wen need to be careful with:
Noise from Power Converters  part of design specs for the new ones
Noise introduced by Crab Cavities
  A dedicated feedback is being designed
Noise introduced by the Transverse Damper
  Improvements are under study: use of a larger number of pickups and improved electronics
If needed, further mitigation can be obtained by introducing a small separation (~1s) at the main IPs in the first part of the fill (no impact on lumi as it is during b* leveling)
Crab Cavity noise feedback
For more info: T. Mastoridis, “Crab cavity RF noise mitigation”, HL-LHC WP2 meeting, 22 Aug 2017
For more info: X. Buffat, “Beam stability and quality in the presence of beam beam and transverse damper”, HL-LHC Annual Meeting, Madrid, 15 Nov 2017
Damper & noise
LHC
HL-LHC improved ADT
HL-LHC present ADT

## Slide 28
Thanks for your attention!

## Slide 29
DA [σ]
Luminosity []
Relaxed (6σ)
Aggressive (5σ)
Ultimate Relaxed (6σ)