## Slide 1
Towards Realistic Implementations of Large Imaging Calorimeters
AHCAL prototype with 39 layers
Precision mechanics to assemble structural components, e.g. Electron beam welding of absorber structure for excellent surface flatness and minimal deformation over large areas
Timing on a single cell level:
~3.3ns for the AHCAL in test beam mode, higher time resolution possible with faster clock setting
Integration
Small scale detector interfaces (DIF) as link between ASICS and DAQ system
Rigorous testing of all technologies at TB facilities at CERN/DESY
Gaseous Readout
GRPC based hadronic
calorimeter (SDHCAL):
binary and two bit readout
1 cm2 pad size
Key developments towards scalability to full size experiments
Improved gas flow for new 1x2 m2 GRPC plates
Automated assembly of large layers by pick and place machines
Similar technology used for a scintillator strip ECAL:
High effective granularity achieved by crossed strips in adjacent layers
Development of flat interconnections between detector modules to facilitate compact layers
SiW ECAL prototype with 15 layers
SDHCAL prototype with 48 layers
Testing of binary versus multi threshold mode of the GRPCs:
Two bit multi threshold mode improves energy resolution in SDHCAL
Successful single cell MIP calibration of the full AHCAL prototype:
Good overall detector response
Signal to Noise ratio = MPVMIPS/𝜎Noise ~50
Achievements
Signal to Noise ratio = MPVMIPS/𝜎Noise ~20 in the SiW ECAL:
Ability to trigger on and read out small signals (MIPS) demonstrated
Compact SL-board and low profile connectors as interface for slow control and readout of up to 15 chained slabs
Silicon Readout
ECAL with tungsten absorber (SiW ECAL):
Silicon pixels as active material
9x9 cm2 wafers with 5.5x5.5 mm2 cell size
Single base units (ASU‘s) validated at low energies
16 ASICs and 1024 channels per ASU
Full QA and assembly chain
Validation of up-scalability to long slabs of 8 chained modules (barrel ECAL)
AHCAL
SiW ECAL
SDHCAL
SDHCAL
The CALICE Program
Development of highly granular electromagnetic and hadronic calorimeters for particle flow reconstruction in future collider experiments. Key steps:
  Validation of the concept of high granularity with physics prototypes ✓
  Technical realization of detector systems satisfying collider constraints - Technological prototypes with fully embedded electronics tested in particle beams
  Application of CALICE expertise and technology in running experiments e.g. CMS HGCal
SiPM-on-Tile
Analogue HCAL (AHCAL):
Scintillator tiles with individual MPPC readout
3x3 cm2 segmentation
QA assurance of all modules
Sample testing of MPPC batches
Particle Flow Calorimetry
High sampling frequency and granularity in calorimeters to separate particle showers
Avoid dead material between tracker and calorimeters
➤ Calorimeters have to be inside the magnet coil
Requires the design of very compact service electronics and active layers sensitive to the MIP level
Requires precise mechanical assembly of the calorimeter structure allowing only small tolerances over large areas
Beam Tests of Technological Prototypes
Assembly of ~1 m2 prototypes with fully embedded electronics
A key element: Use of common technologies and infrastructure, such as a common ASIC family (SKIROC, SPIROC, HARDROC) to facilitate combined running.
60 GeV AHCAL Event
𝜋-
Author: Lorenz Emberger (emberger@mpp.mpg.de)
Max-Planck-Institute for Physics
Föhringer Ring 6
80805 Munich
Presenter: Kiyotomo Kawagoe (kawagoe@phys.kyushu-u.ac.jp)
Department of Physics and RCAPP
Kyushu University
744 Motooka Nishi-ku Fukuoka, 819-0395 Japan
for the CALICE Collaboration
Notes: 11