## Slide 1: Diagnostics X-ray Beamline at Diamond Light Source
Lorraine Bobb

## Slide 2: Small-scale X-ray beamline
Camera
Lens
Mirror
Scintillator
Pinhole / Interferometer
Source
Improve beam size resolution of X-ray pinhole camera:
Monochromatic  Match pinhole size to energy  Minimise PSF
Best spatial resolution
Develop X-ray interferometer which can measure smaller beam sizes (-requires monochromatic X-ray beam).
X-rays (white)
Visible light
X-rays (mono)
Monochromator
Measured beam size
+
Lattice param.
Emittance

## Slide 3: Photos of Monochromator

## Slide 4: X-ray Interferometer
[1] Pinhole interferometry with coherent hard X-rays- Wolfram Leitenberger, Horst Wendrock, Lothar Bischoff and Timm Weitkamp
Overlap @ 15 keV ≈ 0.79
Overlap @ 25 keV ≈ 0.66
Note that minimum distance for far-field is
,
however in reality which is not satisfied for all object sizes.
Example interferogram

## Slide 5: Multilayer Mono Parameters
 | Borrowed from Optics group | Incoatec
Dimensions | 300 mm x 50 mm | Approx 40mm x 100mm
D-spacing | 4.8 nm | 4 nm
Multilayers | Mo/Si with N=100 layer-pairs deposited on float glass | Tungsten/Boron Carbide (B4C) with 200 pairs
Comment | At 12 keV, it will have a Bragg angle of ~0.67 deg, giving a beam-deflection of ~23mm at 1m | 

## Slide 6
Extra Slides

## Slide 7: Principle of Operation
Camera
Lens
Mirror
Scintillator
Pinhole
Source
Synchrotron radiation is emitted from the source point.
Intermediate image is formed at the scintillator screen via a pinhole.
Image is relayed to the camera by a lens.
X-rays
Visible light

## Slide 8: Emittance Calculation
Example image from Diamond Light Source in 2010, from which the emittance can be calculated [4, 5].
X-ray pinhole cameras measure the transverse profile of the beam, from which the emittance may be calculated.

## Slide 9: Emittance Calculation
At Diamond using two pinhole cameras at different locations:
Fit a 2D Gaussian to obtain horizontal and vertical imaged sizes and respectively.
Deconvolve and scale using magnification to obtain the electron beam sizes e.g. Gaussian subtraction in quadrature:
Given the lattice parameters, solve the following matrix equation to obtain the horizontal and vertical emittances , and energy spread :

## Slide 10: Fundamental Limitations
Camera
Lens
Mirror
Scintillator
Pinhole
Source
Indirect emittance measurement
Point Spread Function (Gaussian approx.) contribution to beam size measurement [4]:
where

## Slide 11: Fundamental Limitations
Source resolution for optimised pinhole camera, given current spatial constraints at Diamond:
with
Source resolution incl. contribution from camera using a 5µm P43 screen [4]:
dominates
dominates

## Slide 12: Practical Challenges
Spatial constraints
  For sufficient source-to-screen magnification ():  X-ray path length
  Diffraction contribution to PSF from pinhole worsens with distance given a fixed aperture size : for wavelength [5].
Pinhole
Source
Scintillator screen

## Slide 13: Practical Challenges
Pinhole fabrication
  For the pinhole to be opaque to keV X-rays a high Z material is required e.g. 1mm thick Tungsten.
  Often these materials are difficult to machine.
  Especially given the high aspect ratio 10 µm (aperture): 1mm (thickness)  1:100
Environment and oxidation
  Air, nitrogen or vacuum?
  Lifetime and maintenance considerations

## Slide 14: Nov 2014: Gold Plated Tungsten Blades
50 µm
25 µm
Upstream view of Pinhole 2
Fluffy white deposits
= Aluminium Oxide
Gold “nuggets” clogging pinhole
Tungsten Oxide (blue) forms on bare Tungsten areas
400 µm

## Slide 15: Now tell us the perks!
Simple design. Simple alignment. Simple maintenance. Simple analysis. Simple…
  Quick to commission e.g. < 1 week at Diamond (2006)
  So simple, a human can learn a lot just by looking…!
Provides 2D transverse profile.
Non-invasive.
Cheap options are available.
Possible to custom build the imager to optimise for spatial resolution, turn-by-turn acquisition, dynamic range etc.
Fast image processing, thus suitable for feedback systems.

## Slide 16: Dual Purpose Diagnostic
While we have human operators, the importance of easy human interpretation shouldn’t be overlooked.
Emittance Monitoring
+
CCTV
Injection at Diamond 2015
TMBF at Diamond 2015

## Slide 17: Dual Purpose Diagnostic
Emittance Monitoring
+
CCTV
X-ray pinhole camera image
Beam sizes (2D)
Transverse profile
Beam instabilities
Skew
Beam position

## Slide 18: In Operation

## Slide 19: “Snapshot” of Current Status
Chart: Do you use X-ray pinhole cameras for emittance measurement?
| Yes (10) | No (7)
Emittance measurement | 10 | 7
π-polarisation
Diffraction
Interferometry
CRL imaging
Air (6)
Vacuum (3)
Nitrogen (1)
Parameter | Average
Aperture | 23 µm
X-ray energy | 29 keV
 | 32 %
Source-to-screen magnification | 1.6
Screen-to-camera magnification | 1.8
Parameter | Average
Aperture | 23 µm
X-ray energy | 29 keV
 | 32 %
Source-to-screen magnification | 1.6
Screen-to-camera magnification | 1.8
Chart: 
| Scintilllator
P43 | 2
CdWO4 | 4
LuAG:Ce | 1
YAG:Ce | 3

## Slide 20: Summary
Simple!  Easy to commission  Easy maintenance
Survey shows primary instrument for emittance monitoring
Fundamental limitations, given space and 30 keV X-rays etc., mean sub-micron beam size measurements are not possible.
Many practical challenges are being improved with technological advances.
Complementary general diagnostic  CCTV
Suitable for emittance feedback
Easy human interpretation

## Slide 21: References
[1] V. Popovic et al., Design and Implementation of Real-Time Multi-Sensor Vision Systems, Springer, 2017.
[2] E. S. Forster, Problemata by Aristotle, translated to English, Vol VII, 912b, 1927.
[3] E. Renner, Pinhole Photography from Historic Technique to Digital Application, Fourth Ed., Focal Press, 2009.
[4] C. Thomas et al., X-ray pinhole camera resolution and emittance measurement, Phys. Rev. ST Accel. Beams 13, 022805 (2010).
[5] P. Elleaume et al., J. Synchrotron Radiat. 2, 209 (1995).
[6] M. Madou, ``Chapter 10: Micromolding Techniques - LIGA'', Fundamentals of Microfabrication and Nanotechnology, Vol. 2, Third Ed., CRC Press, 2012, p.591-642.
[7] L.M. Bobb et al., ``Performance Evaluation of Molybdenum Blades in an X-ray Pinhole Camera'', Proc. IBIC2016, p. 796-799.

## Slide 22: Acknowledgements
Thank you for your attention.
Thanks to the Diamond Diagnostics group and to all those who participated in the survey!
Ximenes Rocha Resende | Brazilian Synchrotron Light Laboratory |  | Kuo-Tung Hsu | TPS/NSRRC
Åke Andersson | MAX IV Laboratory |  | Marcel Schuh | KARA / KIT
Volker Schlott | PSI |  | Suntao Wang | CESR/CHESS
Yongbin | SSRF/SINAP |  | Friederike Ewald | ESRF
Shiro TAKANO | SPring-8 |  | Marie Labat | SOLEIL
Rohan Dowd | Australian synchrotron |  | Gero Kube | DESY
Akash Deep Garg | RRCAT Indore INDIA |  | Ubaldo Iriso | ALBA
Oleg Meshkov | BINP |  | Jeff Corbett | SLAC