## Slide 1
AWAKE Laser Synchronization
CERN – Lancaster meeting, 11/01/2018
D. Barrientos, T. Bohl, A. Butterworth, H. Damerau, S. Döbert, W. Höfle, J. Molendijk, S. Rey, U. Wehrle, B. Woolley (CERN)
J. Moody, P. Muggli (MPP)

## Slide 2: Introduction
Proton beam
Electron beam
Laser pulse
AWAKE Synchronization and RF distribution must deliver wide range of RF signals for laser, electron and proton beams
Reference: signals (fML, frep) for laser
All signals derived from a GPS-referenced 5.9958 GHz low-jitter reference oscillator (Laurin AG)
Simultaneous arrival of beams in AWAKE
Signal | Frequency | Ratio
Laser phase locked loop, fLPLL | 5.9958 GHz | 1
Electron acceleration, fRF,e | 2.9979 GHz | fLPLL/2
2Laser mode-locker, 2fML | 176.347 MHz | fRF,e/17
Laser mode-locker, fML | 88.1735 MHz | fRF,e/34
2SPS RF system freq., 2fRF,SPS | 400.8 MHz | 2fML25/11
Common frequency, fc | 8.68 kHz | fML/10164
Pulse repetition rate, frep | 9.97 Hz | fc/870
f
t
t
f

## Slide 3: Laser synchronization
AWAKE laser synchronization to external reference designed in two stages
  88.2 MHz (fML, mode locker frequency)
  Synchronize laser pulse to 88.2 MHz from reference divider
  Standard photo diode with electronic phase discriminator
  6 GHz (fLPLL, laser PLL frequency)
  Lock laser to reference source with low jitter (design: ~30 fs)
  BOM-PS
Commercial system as locking loop controller
  Menlo system RRE-SYNCHRO Repetition Rate Stabilization

## Slide 4
Menlo
Systems
Syncronizati
on
ASOPS
Systems
CurrentSystem Layout v1.1
GPS
10MHz
RF-
Reference
5995 MHz
Menlo Laser
88MHz, 1560nm
Harmonic
lock
BOM-PD
Fundamental
lock
SYNCRO
Piezo + Tracker
feedback
PDBPF
88MHz
RF-
Distribution
Monitor
Reference
5995 MHz
88 MHz
(divider)
Fast
PD
BPF
~6 GHz
5995 MHz
(laser)
P. Dominguez, Menlo Systems

## Slide 5: Initial laser synchronization commissioning
Commissioning of harmonic lock with Menlo in 10/2016
P. Dominguez, Installation Protocol

## Slide 6: Laser synchronization status
Harmonic lock sensitive due to
  Large harmonic ratio with respect to fundamental harmonic: 68
  Small linear phase detection range of BOM-PS: ~±30°
1° error at fundamental lock may move harmonic lock beyond linear range
Decided to keep only fundamental lock for AWAKE runs
No operational experience with harmonic lock system
What can be improved?
Possible ‘Brute-force’ options:
  Introduce intermediate synchronization step?
  Re-synchronize AWAKE main divider at 88.2 MHz?

## Slide 7: Questions for discussion
Possible options to increase lock range of present BOM-PD or other optical phase detector?
Similarities/differences of CLARA and AWAKE synchronization systems?
Additional parallel synchronization observation in AWAKE?
Needs of signals in AWAKE for parallel installation?
Clarify organizational framework of J. Hendersons stays at CERN. Possible schedule for tests with AWAKE laser?