## Slide 1: Final Focus quads (QC1) FCC-ee
S. Sinyatkin
Budker Institute of Nuclear Physics
31 January 2018, CERN

## Slide 2: Outline
Magnetic design of FF quadrupole.
DA with multipole components produced by FF quads.
Closed Orbit Distortion produced by FF quads.

## Slide 3: Iron yoke twin-aperture quadrupole 2D model
Main parameters:
Max.gradient 100 T/m Length 120 cm
Aperture 4.2 cm
Clear aperture 3 cm
NbTi 1.4 x 0.8 Saddle-type coils
Permendure iron yoke
66 mm
152 mm
70 mm
Edge of quad close to IP

## Slide 4: Design of final-focus magnets for FCC ee
Superconducting coil
Stainless vacuum camber
Iron
Nitrogen screen
NbTi Superconducting cable has a rectangular shape, the size is 1.4 * 0.8 mm x mm
N=18
I = 961 A
Icritical (4.2 K; 4 T) = 2400 A
15 mm
21 mm
Notes: 4

## Slide 5: Iron yoke twin-aperture quadrupole 2D model
№ | An, T | Bn, T
1 | 0.00000 | 0.00050
2 | 0.00000 | 0.99630
3 | 0.00000 | 0.00000
4 | 0.00000 | 0.00000
5 | 0.00000 | 0.00010
6 | 0.00000 | 0.00040
7 | 0.00000 | 0.00010
8 | 0.00000 | 0.00000
9 | 0.00000 | 0.00000
10 | 0.00000 | 0.00000
11 | 0.00000 | 0.00000
12 | 0.00000 | 0.00000
13 | 0.00000 | 0.00000
14 | 0.00000 | 0.00000
66 mm
152 mm
70 mm
Edge of quad close to IP
Rharm = 10 mm
Radial shift of magnetic axis:

## Slide 6: Iron yoke twin-aperture quadrupole 3D model
188 mm
220 mm
1.2 m
80 mm
1.2 m
1.2 m
1.2 m
1 m
66 mm
80 mm
12 mm

## Slide 7: Iron yoke twin-aperture quadrupole 3D model
№ | An, T*m | Bn, T*m
1 | 0.00000 | -0.00100
2 | 0.00000 | 1.20373
3 | 0.00000 | -0.00010
4 | 0.00000 | -0.00030
5 | 0.00000 | -0.00001
6 | 0.00000 | 0.00038
7 | 0.00000 | 0.00000
8 | 0.00000 | 0.00085
9 | 0.00000 | 0.00000
10 | 0.00000 | -0.00000
Integrated field multipole components
Rharm = 10 mm
Radial shift of magnetic axis:

## Slide 8: Distribution of the multipole field components along axis 3D model
Rharm = 10 mm
QC1_1
QC1_2
B4, B6 >1*10-4
A1-11 = 0
Gradient
Normal multipole components of field
Skewl multipole components of field
Skew multipole
components of field

## Slide 9: Distribution of the multipole field components along axis 3D model
Rharm = 10 mm
Radial shift of magnetic axis:
Dipole field

## Slide 10: DA aperture with multipole components from QC1_1 magnetic model (3D model, A1,B1 excluded) Lattice: FCCee_z_213_nosol_18.seq
Nturn=200, εX=0.26nm*rad, couple= 0.36 %
MAD-X ptc_tracking
Damping is included
Nslises = 130
ds = 1 cm

## Slide 11: COD excited by QC1 misalignments Before correction
Radial shift of magnetic axis
QC1L1.1:
QC1R1.2:
m
m
σX = 0.5 mm

## Slide 12: COD excited by QC1 misalignments Before correction
Radial shift of magnetic axis
QC1L1.1:
QC1R1.2:
m
m
IP:
X= -0.22 µm
PX=-0.22 mrad
βx= 0.150 m
αx= -0.005
βy= 1.63 mm
αy= -1.52
ηx= 44 µm
η`x= -0.34 mrad

## Slide 13: COD excited by QC1 misalignments Scheme correction
Radial shift of magnetic axis
QC1L1.1:
QC1R1.2:
m
m

## Slide 14: COD excited by QC1 misalignments After correction
Steering magnets
KICK (µrad):
QC1L2.1 = -7.7
QC1R2.2 = 7.5
QC2L1.1 = 3.9
QC2R1.2 =-4.0

## Slide 15: COD excited by QC1 misalignments After correction
Radial shift of magnetic axis
QC1L1.1:
QC1R1.2:
m
m
IP:
X= 0 µm
PX=0 mrad
βx= 0.150 m
αx= 0.0
βy= 0.8 mm
αy= 0.0
ηx= -2 µm
η`x= -0.21 mrad

## Slide 16: Panofsky style quadrupole
Pros:
  Ordinary production of lenses.
  Remaining solenoidal magnetic field in QС1 area is additionally screened by iron yoke of lenses.
  No skew components of magnetic field created by lenses.
  There is small crosstalk between apertures of lenses.

## Slide 17: Panofsky style quadrupole
Cons:
  Saturation of iron yoke (nonlinearity) at large gradient.
  High order multipole components at quadrupole edges.
  No way to introduce high order multipole and skew components of magnetic field to compensate lattice nonlinearity.
  Gradient is not large and limited by iron yoke saturation and critical current.

## Slide 18: Summary
Ordinary production of lenses.
DA and Energy acceptance is about the same.
COD is corrected by additional steering coils of nearby QC1_2 and QC2_1 lenses.
Gradient is not large and limited by iron yoke saturation and critical current.

## Slide 19
Old version

## Slide 20
Old version

## Slide 21
Old version

## Slide 22
Old version