## Slide 1: FCC-ee MDI design as outcome of the first week of MDI workshop and goal of this week workshop
Workshop on the mechanical optimization of the FCC-ee MDI
January 30- February 9 2018, CERN
M. Boscolo
Thanks to all participants for inputs and discussions
my slides are based on last weeks presentations, more details there

## Slide 2: Goal
We aim at a first mechanical 3D design that can be easily changed and updated
We aim this week at discussing the assembly concept of our MDI design
example: CLIC MDI
arXiv:1202.6511
Few iterations will be probably needed
(for example after impedance budget estimation)

## Slide 3
parameter | Z | W | H (ZH) | ttbar | 
beam energy [GeV] | 45.6 | 80 | 120 | 175 | 182.5
arc cell optics | 60 / 60 | 60 / 60 | 90 / 90 | 90 / 90 | 
momentum compaction [10-5] | 1.48 | 1.48 | 0.73 | 0.73 | 
horizontal emittance [nm] | 0.27 | 0.84 | 0.63 | 1.34 | 1.46
vertical emittance [pm] | 1.0 | 1.7 | 1.3 | 2.7 | 2.9
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1 | 
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6 | 
length of interaction area [mm] | 0.42 | 0.85 | 0.9 | 2.0 | 2.1
RF frequency [MHz] | 400 | 400 | 400 | 400 | 400
tunes, half-ring (x, y, s) | (0.57, 0.61, 0.0125) | (0.562, 0.60, 0.0253) | (0.565, 0.60, 0.0179) | (0.554, 0.59, 0.0299) | (0.554, 0.59, 0.0311)
longitudinal damping time [ms] | 415 | 77 | 23 | 7.5 | 6.6
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 7.8 | 9.2
total RF voltage [GV] | 0.10 | 0.75 | 2.0 | 8.8 | 10.3
RF acceptance [%] | 1.9 | 3.5 | 2.3 | 3.5 | 3.5
energy acceptance [%] | ±1.3 | ±1.3 | ±1.7 | +2.4 / -2.8 | +2.4 / -2.8
energy spread (SR / BS) [%] | 0.038 / 0.132 | 0.066 / 0.165 | 0.099 / 0.165 | 0.144 / 0.196 | 0.150 / 0.200
bunch length (SR / BS) [mm] | 3.5 / 12.1 | 3.0 / 7.5 | 3.15 / 5.3 | 2.75 / 3.82 | 2.76 / 3.78
Piwinski angle (SR / BS) | 8.2 / 28.5 | 3.5 / 8.7 | 3.4 / 5.8 | 1.1 / 1.6 | 1.1 / 1.5
Crab sextupoles [%] | 97 | 92 | 80 | 50 | 50
bunch intensity [1011] | 1.7 | 2.3 | 1.8 | 3.2 | 3.35
number of bunches / beam | 16640 | 1300 | 328 | 40 | 33
beam current [mA] | 1390 | 147 | 29 | 6.4 | 5.4
luminosity [1034 cm-2s-1] | 230 | 34 | 8.5 | 1.9 | 1.7
beam-beam parameter (x / y) | 0.004 / 0.133 | 0.010 / 0.141 | 0.016 / 0.118 | 0.088 / 0.148 | 0.089 / 0.144
rad. Bhabha lifetime [min] | 68 | 49 | 38 | 37 | 36
allowable asymmetry [%] | ±5 | ±3 | ±3 | ±3 | ±3
required lifetime by BS [min] | 29 | 16 | 11 | 12 | 12
actual lifetime (w) by BS [min] | > 200 | 24 | 18 | 24 | 25
D. Shatilov, 19 Jan 2018

## Slide 4
parameter | Z | W | H (ZH) | ttbar | 
beam energy [GeV] | 45.6 | 80 | 120 | 175 | 182.5
arc cell optics | 60 / 60 | 60 / 60 | 90 / 90 | 90 / 90 | 
momentum compaction [10-5] | 1.48 | 1.48 | 0.73 | 0.73 | 
horizontal emittance [nm] | 0.27 | 0.84 | 0.63 | 1.34 | 1.46
vertical emittance [pm] | 1.0 | 1.7 | 1.3 | 2.7 | 2.9
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1 | 
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6 | 
length of interaction area [mm] | 0.42 | 0.85 | 0.9 | 2.0 | 2.1
RF frequency [MHz] | 400 | 400 | 400 | 400 | 400
tunes, half-ring (x, y, s) | (0.57, 0.61, 0.0125) | (0.562, 0.60, 0.0253) | (0.565, 0.60, 0.0179) | (0.554, 0.59, 0.0299) | (0.554, 0.59, 0.0311)
longitudinal damping time [ms] | 415 | 77 | 23 | 7.5 | 6.6
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 7.8 | 9.2
total RF voltage [GV] | 0.10 | 0.75 | 2.0 | 8.8 | 10.3
RF acceptance [%] | 1.9 | 3.5 | 2.3 | 3.5 | 3.5
energy acceptance [%] | ±1.3 | ±1.3 | ±1.7 | +2.4 / -2.8 | +2.4 / -2.8
energy spread (SR / BS) [%] | 0.038 / 0.132 | 0.066 / 0.165 | 0.099 / 0.165 | 0.144 / 0.196 | 0.150 / 0.200
bunch length (SR / BS) [mm] | 3.5 / 12.1 | 3.0 / 7.5 | 3.15 / 5.3 | 2.75 / 3.82 | 2.76 / 3.78
Piwinski angle (SR / BS) | 8.2 / 28.5 | 3.5 / 8.7 | 3.4 / 5.8 | 1.1 / 1.6 | 1.1 / 1.5
Crab sextupoles [%] | 97 | 92 | 80 | 50 | 50
bunch intensity [1011] | 1.7 | 2.3 | 1.8 | 3.2 | 3.35
number of bunches / beam | 16640 | 1300 | 328 | 40 | 33
beam current [mA] | 1390 | 147 | 29 | 6.4 | 5.4
luminosity [1034 cm-2s-1] | 230 | 34 | 8.5 | 1.9 | 1.7
beam-beam parameter (x / y) | 0.004 / 0.133 | 0.010 / 0.141 | 0.016 / 0.118 | 0.088 / 0.148 | 0.089 / 0.144
rad. Bhabha lifetime [min] | 68 | 49 | 38 | 37 | 36
allowable asymmetry [%] | ±5 | ±3 | ±3 | ±3 | ±3
required lifetime by BS [min] | 29 | 16 | 11 | 12 | 12
actual lifetime (w) by BS [min] | > 200 | 24 | 18 | 24 | 25
D. Shatilov, 19 Jan 2018

## Slide 5
Interaction Region Beam Pipe

## Slide 6: Interaction Region Beam Pipe
ALSO:
cryostat
bellows
flanges
dipole corrector
High order multipoles correctors
BPM
pump
HOM abs.
comp. solenoid
screening
solenoid

## Slide 7: Interaction Region Layout
not in scale
top view
x, horizontal plane

## Slide 8: Solenoid Compensation Scheme
Constraints:
  2T detector field
  L*=2.2m
  Space (i.e. only 6.6 cm distance at the tip closest to IP for QD0)
  must be inside the lumical acceptance ~140-170 mrad
  final focus quads inside the detector (low by* and large crossing angle)
  leave space for luminosity detector at small angle
  field quality at each end and all along the FF quads ≲ 10-4 for all multipoles
  emittance blow-up much smaller than 1 pm
Particles on the beam axis are not on the detector axis, so they will experience vertical dispersion, that brings vertical emittance blow-up. Due to the low nominal ey~1 pm, this effect needs to be cured. A compensating and screening solenoid scheme has been designed.
[slide from FCCWEEK17]
The 140mrad was the outcome of last year’s MDI workshop, as best solution to minimize ey blow-up (0.3 pm out pf 1 pm nominal). Last week it was pointed out by detector group that angular acceptance for the machine (including compensating solenoid) should be 100 mrad.
M. Koratzinos are K. Oide are trying to find a good trade-off between 100 mrad requirement and acceptable ey blow-up. There will be a presentation this Wed.
comment on this number from last week [slide from FCCweek17]:

## Slide 9: Solenoid Compensation Scheme
Luminosity counter
Compensating solenoid
screening
solenoid
Two solenoids are introduced in the IR:
screening solenoid that shields the detector field inside the quads (in the quad net solenoidal field=0)
compensating solenoid in front of the first quad, as close as possible, to reduce the ey blow-up (integral BL~0)
M. Koratzinos
  see talk by E. Levichev
  0.3 pm is the overall ey blow-up for 2IPs @Z with this compensation design
FF quads
[slide from FCCWEEK17]

## Slide 10: The IR 3d view with magnets
Luminosity counter
Final focus quads
screening solenoid
Compensating solenoid
0.19
z(m)
y(m)
x(m)
0.76
1
1.19
1.25
2.01
1.84
2.16
4
coordinates are from next slide
cryostat
opening angle 140 mrad (as from 2017 design)
drift chamber at z=2m with 150 mrad opening angle
  detector solenoid dimensions 3.76m( inner radius) (outer radius 3.818m) × 4m (half-length)
detector solenoid

## Slide 11: Final Focus Magnets Layout
Compensating
Solenoid
Screening
Solenoid
Defocusing
Quads
Luminometer
QC1R1_1
QC1R1_2
1 m
1.2 m
1.25 m
2.01 m
2.16 m
2.2 m
1.84 m
QC1R1_1: L= 0.7 m, K1=-75 / -75 T/m, R = 0.015 m
QC1R1_2: L= 1.4 m, K1=-173 / -166 T/m, R = 0.0175 m
[S. Sinyatkin, summary talk MDI workshop Jan.17]

## Slide 12: Latest layout
luminometer
100mrad
110mrad
140mrad
100mrad
110mrad
140mrad

## Slide 13
Length=4500 mm Inner radius = 345 mm Outer radius = 2000 mm
info from Niloufar Alipour Tehrani
IDEA design

## Slide 14: Geant-4 IR model with the shield
thanks to Anna Kolano for providing this plot

## Slide 20: IR Beam pipe design for wake field calculations
details in next talk
by A. Novokhatski
Two beam pipes are merged into one central pipe in the IR
Professional CAD design of the complicated IR geometry done, essential for
CST/HFSS numerical studies for generated and/or absorbed e.m. fields, propagating or trapped in the IR
water cooling of the beam pipe needed to avoid HOM heating in the IR chamber due to absorption of e.m. fields
HOM absorber design in progress in the central chamber, following the PEP-II experience.
[slide from FCCWEEK17]

## Slide 21: IR CAD design
complicated geometry: the area where two beam pipes merge to one single pipe
HOM Absorber

## Slide 22: 3d model of IR pipe

## Slide 28: Beam pipe
DIMENSION
Central beam pipe has 3 cm dia.
Entering and exiting beam pipe through QC1 (3cm dia.)
Pipe size increases to 4cm dia. in QC2
Size outside QC2 is 7 cm dia. (but 6 cm in plot)
HORIZONTAL MASK TIPS
+/-12 mm radius at Z= +/-2.1 m and +/-5.44 m
+/-18 mm radius at Z= +/- 8.27 m
Vert. 1cm; +/- 0.5 mm thickness
r=15mm
r=12mm
x
y
MATERIAL
Be from about +/-80 cm to accommodate LumiCal
Cu afterwards
thickness of Neg coating under study, if also in the IR, on Be chamber
5 or 10 mm Au coating in the central Be chamber proposed
(pros: useful at Z, conductivity of Be, image charge; cons: multiple scattering)?
Warm beam pipe, 2mm thickness above vacuum chamber needed for water cooling in QC1 and through the IR where 30mm dia. (if BSC elliptical, water copper tubes in the vertical plane)

## Slide 29: QC1 design
We have two designs
  BINP design: iron yoke twin aperture (superconducting, needs cooling system)
  CCT design (developed for Superb, crab-waist scheme)
More or less same space
We plan to present both design in the CDR
more details needed

## Slide 30: Iron yoke twin-aperture quadrupole 2D model
Main parameters:
Max.gradient 100 T/m Length 120 cm
Aperture 4.2 cm
Clear aperture 3 cm
NbTi 1.4 x 0.8 Saddle-type coils
Permendure iron yoke
66 mm
152 mm
70 mm
Edge of quad close to IP
BINP design

## Slide 31: Design of final-focus magnets for FCC ee
Superconducting coil
Stainless vacuum camber
Iron
Nitrogen screen
NbTi Superconducting cable has a rectangular shape, the size is 1.4 * 0.8 mm x mm
N=18
I = 961 A
Icritical (4.2 K; 4 T) = 2400 A
15 mm
21 mm
BINP design
Notes: 31

## Slide 32: Iron yoke twin-aperture quadrupole 3D model
188 mm
220 mm
1.2 m
80 mm
1.2 m
1.2 m
1.2 m
1 m
66 mm
80 mm
12 mm
BINP design

## Slide 33: Panofsky style quadrupole
Pros:
  Ordinary production of lenses.
  Remaining solenoidal magnetic field in QС1 area is additionally screened by iron yoke of lenses.
  No skew components of magnetic field created by lenses.
  There is small crosstalk between apertures of lenses.
Cons:
  Saturation of iron yoke (nonlinearity) at large gradient.
  High order multipole components at quadrupole edges.
  No way to introduce high order multipole and skew components of magnetic field to compensate lattice nonlinearity.
  Gradient is not large and limited by iron yoke saturation and critical current.
BINP design

## Slide 34: QC1 : CCT approach
An essential ingredient that simplifies the problem
CCT design

## Slide 35: Dimensions - radius
15-17mm: beam pipe
17-20mm: vacuum + superinsulation
20-22mm: inner spar
22-26mm: inner s/c cable
26-28mm: middle spar
28-32mm: outer s/c cable
32-34mm: outer spar
Water cooling
CCT design

## Slide 36: Transverse dimensions
Beam pipe
Spar (aluminium)
Vacuum
S/C wire
CCT design

## Slide 37: Dimensions, specs
The quads (QC1L1, QC2L2, QC2L3) follow the specs provided by Katsunobu
I provide the multipole files at the correct magnetic lengths and approximate strengths separately for each magnet
Katsunobu can change the strengths (linearly, as there is no iron) and combine magnets (again linearly, as there is no iron)
 | L (m) | B’ @ tt (T/m) | B’ @ Z (T/m)
QC1L1 | 1.2 | -94.4 | -96.3
QC1L2 | 1 | -92.6 | +50.3
QC1L3 | 1 | -96.7 | +9.8
QC2L1 | 1.25 | +45.8 | +6.7
QC2L2 | 1.25 | +74.0 | +3.2
CCT design

## Slide 38: Transverse dimensions
Beam pipe is 30 mm diameter
In the FF quads the first winding starts at 42mm
The inner substrate starts at 40mm
We are investigating if all the cooling needed can fit between 30 and 40mm.
In this design there is a 2mm gap between the two FF quads at 2.2m
The cable used has a cross section of 2×4=8mm2. The critical current through this cross section permits gradients in excess of 150T/m. If we do not need this capability, we can reduce the size of the cable to 2×3mm. In this way we can reduce the overall radius of each quad by 2 mm (or increase the gap between them by 4mm)
CCT design

## Slide 39
The design can have embedded correctors (x and y dipole correctors, skew quadrupole correctors, etc.)
Each corrector is very thin and comprises four extra rings that go in the outside of the main quadrupole
For excellent performance, each corrector has its compensating coil on the other aperture (powered in series)
Embedded correctors

## Slide 40: All QC1L1 correctors – A1, B1 and A2
IP
A2 corrector
A1 corrector
B1 corrector
0.5mm wire, critical current @3T is 300A, physical length ~20cm
Distance from IP (mm)
There is enough space for even five correctors, with no loss of packing factor
Three correctors installed with single wire, 0.5mm, about 20cm long, current 200A (critical current @3K is 300A).
Strength of correctors:
  A1 25mT.m (210 units)
  B1 17mT.m (145 units)
  A2 35 units

## Slide 41: Conclusions on misalignment
Internal misalignment should be better than 30um.
Beam/detector misalignment of around 1mm has a negligible effect on field quality, due to the excellent field quality of the CCT design
Ditto for 0.5mrad tilt
The values of 1mm and 0.5mrad come from optics (Katsunobu) as expected typical values
CCT design

## Slide 42: COD excited by FF quads misalignments correction scheme
Orbit errors at the FCC-ee due to the FF quadrupoles displacements (S. Sinyatkin)

## Slide 43: Heat load and cooling needs
According to E. Belli:
For the most difficult case, QC1L1
e-cloud: for SEY=1.1 ~20W/m, for SEY=1.2 ~200W/m
resistive wall: for copper, ~100W/m
direct SR heating: zero (I assume that masks will take all direct SR)
From the above, the heat load appears to be O(100)W/m
2.5 ns bunch spacing, previous parameter list
updated results in progress

## Slide 44
Example: What average effective pumping speed would be necessary for the Z-pole machine in order to have an average pressure lower than 1.0E-9 mbar?
Photon flux: F (ph/s) = 8.08E+17 · E (GeV) · I (mA) = 5.34E+22 (ph/s)
If k=2.47E+19 (mol/mbar/liter), then the gas load Q is:
Q (mbar·l/s) = F (ph/s) / k(mol/mbar/l) · h(mol/ph)
with h= photodesorption yield.
Typically a machine is considered vacuum conditioned when h < 1.0E-6 (mol/ph):
Q’ (mbar·l/s/m) = Q/ 2pr = 3.44E-8 (mbar·l/s/m) (in the arcs, r ~10 km)
Pavg (mbar) = Q’ (mbar·l/s/m) / Seff (l/s) · L(m)
Solving for for Seff, one gets: Seff (l/s) = 34.42 · L(m) (dotted line at 45 deg on previous plot)
This means that the Z-pole machine, due to its huge photon flux, would condition to Pavg<1.0E-9 only if 200 ÷ 500 l/s pumps are placed at a distance < 3 ÷ 4 m from each other;
This, in turn, would mean that in the arcs one would need 19000 ÷ 25000 pumps/beam;
Each lumped pump would in turn need pumping slots machined on the vacuum chamber: additional cost for machining, pumping plenum, flanges, cabling, etc...
IR Vacuum Concept (R. Kersevan)

## Slide 46
Remote vacuum connection
at Superkekb (Karsten Gadow)

## Slide 47: Concerns
Assembly
  Remote vacuum connection (ala Belle II)?
  Bellows between Central chamber and cryostat chambers (at least 1-2 convolutions)
  Central chamber support
  Cable and cooling pipe space for central detectors
Vibration control
Cryostat support
Magnetic forces
  Anti-solenoids have strong expulsion forces?
  Compensating solenoids have strong expulsion force near detector field edge
Overlapping Z space
  LumiCal
  Cryostat
  Remote vacuum assembly
  NEG pump
  HOM absorbers
  Shielding

## Slide 48: Summary
The IR design has been relatively stable
But now engineering concerns are coming into play
These may force a reevaluation of the IR design
We need space for bellows and vacuum connections and possibly supports
  Move the FF quads back?
  Shorten the anti-solenoid?
  Move the Lumi-Cal forward?

## Slide 49: Conclusions and next steps
3d mechanical design, assembly concept
3D simulation of the magnetic fields and magnetic forces in MDI area to optimize design.
With a design that includes BPMs, bellows, flanges, a more realistic wake field calculation will be possible.
Stabilisation issues are being addressed
Alignments Alignment and mechanical tolerances

## Slide 50: Back-up

## Slide 51: Geant4 detector modeling
modified CLIC detector model with B=2T and FCC-ee IR design

## Slide 52: End view behind LumiCal
Shielding is not shown but we should be able to fit in at least 1 cm of a high Z material (Pb, W, Ta)

## Slide 53: Features
Central beam pipe has 3 cm dia.
Entering and exiting beam pipe through Q1 (3cm dia.)
Be from about +/-80 cm to accommodate LumiCal
Pipe size increases to 4cm dia. in Q2
Size outside Q2 is currently 6 cm dia.
Mask tips +/-12 mm radius at +/-2.1 m and +/-5.44 m
Mask tips +/-18 mm radius at +/- 8.27 m
  Allows for possibility of cold bore magnets (shields quad beam pipes)
  Need to remove 43 W of SR power between Q1 and Q2 on upstream side
  Current IR design is for warm bores
Horizontal plane only
Horizontal plane only

## Slide 54: Task
FF Quads misalignments (QC1_1- QC1_3, QC2_1,QC2_2) :
  Geodesy: transverse shift of FF quads with .
  Vibrations: transverse shift of FF quads with .
IR BPM misalignments:
  Geodesy: transverse shift of BPMs with .
  Vibrations: errors of BPM readings with .
No misalignments of other elements.
Shift of FF Quads distorts CO and dispersion.
COD is corrected by IR steering magnets in the FF quadrupoles.
FCCee_z_213_nosol_18.seq
* THE MECHANICAL AND VIBRATION STUDIES OF THE FINAL FOCUS MAGNET-CRYOSTAT FOR SUPERKEKB. THPRI005 ProceedingsofIPAC2014,Dresden,Germany
Orbit errors at the FCC-ee due to the FF quadrupoles displacements
(S. Sinyatkin)

## Slide 55: Conclusion
There is no closed orbit w/o correction for 25 μm shift of Q (a small amount). After correction, the required beam parameters are restored.
The beams do not collide with 0.1 μm vibrations of FF Quads. Vertical emittance is blown up.
Feedback is required to suppress influence of the FF quads vibrations.
The beam parameters are destroyed after correction of 25 μm IR BPM misalignments. To optimize the parameters, a “golden” orbit is required.
Due to vibrations, it is impossible to use the IR BPMs for the feedback system.
It is necessary to measure Luminosity in the bandwidth 0-100 Hz. (Luminometer?)
Orbit errors at the FCC-ee due to the FF quadrupoles displacements
(S. Sinyatkin)