## Slide 1
Toward a new Treatment Planning Approach accounting for in-vivo proton range verification
Ludwig-Maximilians-Universität, München
Liheng Tian

## Slide 2: Introduction
Proton range uncertainties
CT number conversion
Anatomical changes
Patient set up
…

## Slide 3: Introduction
In-vivo proton range verification
Positron Emission Tomography (PET)
  Detection of annihilation photons from the decay of -emitters
  Takes few tens minutes to use PET scanner
  Disturbed by organ motion and washout effect
Detector
Detector
Correlator
γ
γ
Beam path

## Slide 4: Introduction
In-vivo proton range verification
Prompt Gamma (PG) Imaging
  Monitor the Prompt Gamma emitted by nuclear de-excitation of nuclei in the beam path
  Fast (within nanoseconds)
  Better PG-dose signal comfirmation
  Higher gamma production rates
  Clinical experiment shows that the retrieval precision of 2mm can be achieved
Beam path
Prompt gamma
Detector

## Slide 5: Introduction
PG emission
Dose delivery

## Slide 6: Introduction
Ideal PG & dose profile
Lateral integration of PG & dose signal
Fall-off region
c: Fall-off position
1/b : Fall-off slope

## Slide 7: Introduction
Ideal PG & dose profile
Lateral integration of PG & dose signal
Distance between PG and dose fall-off position:
dose: distal 80% dose fall off
PG : fitting function

## Slide 8: Introduction
However, the correlation between PG and dose signal is not always good
Lateral integration of PG & dose signal

## Slide 9: Introduction
Reason
  Tissue inhomogeneity (bone/air in beam path)
Dose delivery
PG emission

## Slide 10: Introduction
The PG-dose correlation of individual pencil beam (called subPB in the following) is not considered in current treatment planning system (TPS)

## Slide 11: Goal
Goal of my study:
  Optimize current TPS system, accounting for in-vivo proton range verification to enable a reliable treatment monitoring

## Slide 12: Method
Quantify and identify the degree of ‘PG-dose correlation’ for each subPBs
Criteria:
Distance between the Fall-off positions of PG & dose profile (dR)
Slope of the PG signal Fall-off region (1/b)
Fitting quality (Sum of squared errors, SSE)

## Slide 13: Method
Example:
Ideal case:

## Slide 14: Method
Example:
Large dR relates to poor correlation directly
dR
A secondary peak, relating to an air cavity, leads to high SSE value
Poor correlation case 1:

## Slide 15: Method
Example:
A shallow slope related also to an air cavity, causing the failure of fitting
Poor correlation case 2:

## Slide 16: Method
Quantify and identify the degree of ‘PG-dose correlation’ for each subPBs
Improve the initial treatment plan while maintaining the quality of plan

## Slide 17
General workflow of CERR TPS and our improved TPS:

## Slide 18: Method
Boost few subPBs which have the best PG-dose correlation
A
B
C
D

## Slide 19: Result
Dose delivery
PG-dose correlation

## Slide 20: Dose delivery

## Slide 21: Result
Dose delivery
PG-dose correlation

## Slide 22: PG-dose correlation
The color shows the PG-dose correlation and
The spot radius is linearly proportional to the proton number
Beam’s eye:

## Slide 23: Result
Quantify and identify spot-by-spot PG dose correlation automatically in a MC treatment planning process
Currently, our new approach is able to:
Provide the user with candidate subPBs which have reliable PG-dose correlation
Optimize a treatment plan which is comparable to the initial treatment plan in terms of dose distribution. Besides, few high-intensity subPBs in the new plan could provide reliable in-vivo proton range verification

## Slide 24: Future work
MC treatment plan is time-consuming, especially when more protons are needed to generate enough PG emission
Detection devices signal is different from PG emission
Combine state-of-the-art CBCT, DECT
Robustness of PG-dose correlation considering anatomical change and different uncertainties

## Slide 25: Conclusion
Though different issues are still needed to be addressed, with the results of this project, the treatment planning process in proton therapy could be improved, by integrating the PG-based in-vivo monitoring of the beam range
This novel approach could lead to a safer and more controllable proton treatment in the future

## Slide 26: Thank you!