## Slide 1: CMS High-Granularity Calorimeter (HGCAL)
TWEPP Seminar, 20 September 2018, David Barney (CERN)

## Slide 2
Today’s Tasting menu
Appetizer
Motivation for upgrading CMS endcap calorimeters
Starter
The choice of high granularity
Main Course
The CMS HGCAL design and prototyping with a side order of electronics challenges
Dessert
Measured HGCAL performance
After-seminar mints
Status and challenges ahead

## Slide 3: Appetizer Motivation for upgrading CMS endcap calorimeters for HL-LHC

## Slide 4: Luminosity provided by HL-LHC opens new doorways to physics
HL-LHC: levelled L = 5x1034cm-2s-1 and pileup 140, with potential for 50% higher L & pileup
Physics reach will include SM & Higgs, with searches for BSM including reactions initiated by Vector Boson Fusion (VBF) and including highly-boosted objects  Narrow (t) jets or merged (hadronic decays of W, Z) jets
 Ideally want to trigger on these narrow VBF & merged jets
Good jet identification and measurement: crucial for HL-LHC

## Slide 5: Existing CMS endcap calorimeters cannot cope with the expected radiation or pileup @ HL-LHC
CMS @ HL-LHC: ~1016 1 MeV neq cm-2 @ 3ab-1
in forward calorimeters, with pileup ~200 And up to 2 MGy absorbed dose
78 pileup events in 2012. Expect 140-200 @ HL-LHC

## Slide 6: CMS will replace its endcap calorimeters for HL-LHC: the High Granularity Calorimeter

## Slide 7: Starter The choice of high granularity

## Slide 8: Real need to improve jet energy resolution for the next generation of calorimeters
“Typical” jet:
~62% charged particles (mainly hadrons)
~27% photons
~10% neutral hadrons
~1% neutrinos
Multi-jet final states (outgoing quarks, gluons) Missing energy relies upon accurate jet energy measurements
Need to separate heavy bosons (W, Z, H) in hadronic decays
Jet reconstruction: weighted sum of energies in a cone  energy of original parton
Resolution: driven by calorimeter with worst resolution (HCAL)

## Slide 9: Two main approaches for improving jet energy resolution
Substantial improvement of the energy resolution of hadronic calorimeters for single hadrons: dual (or triple!) readout, e.g. DREAM
Precise reconstruction of each particle within the jet  reduction of HCAL resolution impact: particle flow algorithms and imaging calorimeters e.g. CALICE detectors for linear colliders (CLIC, ILC), CMS HGCAL
Both techniques aim at separating charged/neutral & electromagnetic/hadronic components

## Slide 10: Particle flow technique: make best use of all detectors to measure jet energies
Idea: for each individual particle in a jet, use detector with best energy/momentum resolution
Charged tracks = Tracker
e/photons = ECAL
Neutral hadrons (only 10%) = HCAL

## Slide 11: Particle flow already used in Aleph, Delphi & CMS (all have relatively low resolution HCALs)
Measurement of jets in CMS is enhanced greatly by the use of particle flow techniques
Simulation: jet energy resolution
Data: Missing energy resolution

## Slide 12: The previous generation of calorimeters could “see” showers! Can we do this again?
γ + Coul. Field →
e+ e-

## Slide 13: HGCAL has the potential to visualize individual components of showers
Simulation of 140 pileup events in CMS

## Slide 14: For best results: high granularity in 3D – separation of individual particle showers
For a Particle-Flow Calorimeter:
Granularity is more important than energy resolution
Lateral granularity should be below Molière radius in ECAL and HCAL
In particular in the ECAL: small Molière radius to provide good two-shower separation (particularly in high pileup environment)  dense absorbers and thin sensors
Sophisticated software needed!

## Slide 15: Main Course The CMS HGCAL design & prototyping

## Slide 16
A wise person once said (about the HGCAL):
“there are no show-stoppers; it is all just engineering”
Another person responded:
“HGCAL is perhaps the most challenging
engineering project ever undertaken in particle physics”

## Slide 17: Overall mechanical design of HGCAL heavily constrained by present endcap calorimeters
Present CMS endcap calorimeters
HGCAL design
Concept: remove complete endcap calo. system and replace with HGCAL

## Slide 18: Overall design of HGCAL driven by need for radiation-hard segmented sensors
Look for proven and adequately radiation-hard active materials
To build a dense e.m./hadronic calorimeter with a good energy resolution, small RM, good two-shower separation (e.m. and hadronic), with high lateral and longitudinal readout granularity
A silicon-sensor-based sampling calorimeter
(absorber materials – W, Pb, Cu, Stainless Steel)
followed by plastic scintillator tiles with direct SiPM readout for the lower radiation level region
(absorber material SS)
To realise a high-granularity calorimeter, we need: low cost/area active material(s), radiation-tolerant on-detector electronics, high-bandwidth data transmission, powerful FPGAs for off-detector electronics

## Slide 19: Granularity is driven by calibration requirements and energy resolution target
Calibration of Silicon sensors and scintillator tiles is with MIPs  need good S/N for MIPs after 3ab-1  low-capacitance Si cells  small area (0.5—1.1cm2)  Scint. cells with small area for high-efficiency light collection
Fine longitudinal sampling needed to provide good energy resolution (minimize sampling term) especially with thin active layers (e.g. 100-300mm silicon sensors)

## Slide 20: CMS HGCAL: a sampling calorimeter with unprecedented number of readout channels
Active Elements:
Hexagonal modules based on Si sensors in CE-E and high-radiation regions of CE-H
Scintillating tiles with SiPM readout in low-radiation regions of CE-H
Key Parameters:
HGCAL covers 1.5 < h < 3.0
Full system maintained at -30oC
~600m2 of silicon sensors
~500m2 of scintillators
6M Si channels, 0.5 or 1.1 cm2 cell size
  Data readout from all layers
  Trigger readout from alternate layers in CE-E and all layers in CE-H
~27000 Si modules
~110 kW per endcap
Electromagnetic calorimeter (CE-E): Si, Cu/CuW/Pb absorbers, 28 layers, 26 X0 & ~1.7l
Hadronic calorimeter (CE-H): Si & scintillator, steel absorbers, 24 layers, ~9.0l
~2m
~2.3m

## Slide 21: ~600m2 of silicon sensors (3x CMS tracker) in radiation field peaking at ~1016n/cm2
Planar p-type DC-coupled sensor pads
simplifies production technology
( consider n-type sensors for 300mm sensors in lower radiation region of HGCAL )
Hexagonal sensor geometry preferred to square
makes most efficient use of circular sensor wafer
reduces number of sensors produced & assembled into modules ( factor ~ 1.3 )
8” wafers preferable to 6”
reduces number of sensors produced & assembled into modules ( factor ~ 1.8 )
300mm, 200mm and 120mm active sensor thicknesses
match sensor thickness (and granularity) to radiation field for optimal performance
Simple, rugged module design & automated module assembly
provide high volume, high rate, reproducible module production & handling

## Slide 22: Thinner sensors: less decrease in charge collection efficiency vs fluence than thicker sensors

## Slide 23: Hexagonal silicon sensors are divided (mostly) into hexagonal cells, with some special cells
~55pF per cell
O(nA) per cell (before irradiation)
6” prototype sensor
Prototype 6” and 8” sensors made by three producers

## Slide 24: 8” silicon sensors will be hexagonal, divided with 3-fold symmetry into hexagonal cells
192 cells/sensor
432 cells/sensor
⌀ ~ 190mm
All cells have C~65pF
Coloured groupings of cells represent trigger readout units ~4.5cm2 (half the area of a single crystal in the present ECAL endcap)

## Slide 25: Silicon modules are glued assemblies, made with standardized gantry, wire-bonders etc.
Baseplate
Kapton
Silicon
PCB
Automated gantry @ UCSB used previously for CMS tracker assembly
~60 modules already made and used for test purposes.
Another ~60 being made at UCSB now

## Slide 26: HGCAL will include 27000 modules based on hexagonal silicon sensors with 0.5-1cm2 cells
Silicon sensor glued to baseplate and PCB containing front-end electronics
Wire bonding from PCB to silicon through stepped holes

## Slide 27: Silicon modules are arranged in hexagonal matrices to cover fiducial area of HGCAL
7 hexagonal modules for 2017 beam test

## Slide 28: HGCAL will also include 500m2 of scintillator tiles with on-tile SiPM readout
For first beam tests, modified CALICE AHCAL used for rear hadron calorimeter: 3x3cm2 scintillator tiles + direct SiPM readout
SiPMs already used successfully in e.g. CMS HCAL Phase 1 upgrade
Tile boards or “megatiles” limited in size by CTE of different components

## Slide 29: Automated assembly already used for CALICE prototypes: 28000 tiles on 158 boards
30 x 30 x 3 mm3 tiles, automatically wrapped and placed by “gantry” machine

## Slide 30: HGCAL Electronics: combining some of the most challenging aspects from other detector types!
Calorimeter
Pixel
Tracker
High dynamic range
Triggering capability
Radiation
Space constraints
#readout channels
Physical size
MIP sensitivity
MIP sensitivity
Low power
And full-scale production must start in ~2021!
HGCAL

## Slide 31: On-detector control/readout is a mixture of ASICs and “generic” developments
HGCAL ASICs
Phase-II “generic”
developments
Compression connectors
join the 2 PCBs
Hexaboard
Motherboard
HGCROC
Concentrators

## Slide 32: The front-end ASIC is particularly challenging in the compact & mixed-technology HGCAL
Compatibility with –ve & +ve inputs for n-on-p and p-on-n silicon and SiPMs
Low noise* (<2500e-) despite ~65pF silicon cell capacitance
  Measure MIPs (~3.5fC in 300mm silicon) with S/N > 3 for whole lifetime of HL-LHC
High dynamic range (~0.2fC  10pC, i.e. 16-bits)
   Use 130nm CMOS with 1.5V supply
  Integral linearity better than 1% over full range
Provide timing information to < 100ps for signals above tens of fC
  Need clock distribution jitter 10-15ps (same specs as for other CMS detector upgrades)
Fast shaping time (<20ns) to minimize out-of-time pileup
On-detector digitization, linearization and zero suppression
Creation of trigger sums
Buffering of data to accommodate 12.5ms L1 latency
<20mW per channel (~limited by cooling power) include Ileakage compensation
High radiation resistance (~2MGy and 1016 neq/cm2 & SEU robustness)
*want S/N ~8 at beginning of HL-LHC for 1 MIP in 120mm silicon ~ 1.5fC; upper limit from 1.5TeV photon shower producing ~6000 MIPs in a single cell

## Slide 33: HGCROC ASIC: a significant evolution from the Skiroc2 ASIC developed for CALICE
Skiroc2Skiroc2-CMS  TV1TV2  HGCROC-V1HGCROC_DV1HGCROC
AMS 350nm
Commercial 130nm CMOS
Test Vehicles
TWEPP 2016 C. de la Taille Link
TWEPP 2017 D. Thienpont Link
TWEPP 2018 C. de la Taille Link
TWEPP 2011 N. Seguin-Moreau
Link

## Slide 34: HGCROC: includes on-chip ADC, and TDCs for ToT (low power high dynamic range) & ToA (timing)
Skiroc2-CMS ASIC (2016) already had some of these features, inc. ToT & ToA
First simplified HGCAL ASIC (HGCROC-V1) in 130nm CMOS being tested now
See talk from C. de la Taille
ToT: TDC for Q > 50 fC
ADC for Q < 150 fC
ToA: TDC for Dt < 100 ps

## Slide 35: The Hexaboard front-end PCB is very challenging, partly due to the bonding holes
Stepped holes for wire-bonding to Si are not trivial to manufacture
Exploring use of embedded vias to ease the layout – but increased cost
6” hexaboard for 4xSkiroc2-CMS, 128 Si channels
FPGA for control & data aggregation
mHDMI for powering, control & data
mUSB for FPGA programming

## Slide 36: Hexaboard is evolving to final size and components, but complexity persists
8” hexaboard for 4xSkiroc2-CMS, 192 Si channels (due soon @ CERN)
8” hexaboard for 4 or 6xHGCROC, 192 or 432 Si channels. Holes will be ovals.

## Slide 37: Motherboard connects to 2-5 hexaboards & contains electrical/optical interfaces
LV & bias
Motherboard functionality:
Aggregates, formats & serializes the data (read at the L1 trigger frequency of up to 750kHz) in the data concentrator ASIC
Selects trigger sums of interest, aggregates, formats and stores these data in a 12-bunch-crossing FIFO in the trigger concentrator ASIC
Interfaces concentrators to lpGBT  VTCRX+ for data/trigger transmission
Receives and distributes fast control signals
Take input from on-detector environmental sensors and transmits outside
Distributes power to detector modules – LV & bias

## Slide 38: Motherboard connects to 2-5 hexaboards & contains electrical/optical interfaces
In TDR: Vertical space between hexaboard and motherboard ~1.6mm maximum!

## Slide 39: Preshower is a compact device, with one layer requiring ~5cm for absorber, cooling & modules
Baseplates
Silicon
Motherboard
~2.5cm
+2.5cm for cooling screen and absorber

## Slide 40: “dummy” cassette being assembled with PCBs containing only connectors and heat loads
8” hexagonal PCBs glued to silicon and baseplates  modules 3 modules connected to a single “motherboard” providing power, data concentrator and optical links

## Slide 41: Layout of motherboard puts the active elements in the lowest radiation region possible

## Slide 42: Baseline powering scheme places DC-DC converters behind CE-H, outside the cold volume
DC-DC
LDO
DC-DC need to withstand ~1014n/cm2
Can potentially replace them in LS4, LS5…
Most heat dissipation outside of cold volume
Significant copper inside cold volume



## Slide 43: Alternative is to place e.g. modified version of FEASTMP modules on the cassettes
Receiving PCB
9.4mm
FEASTMP-CLP
Hexaboard
Motherboard
~3mm
Even if TDR gap (1.6mm) is doubled…
HGCAL design
Silicon
Present versions of FEASTMP are:
too tall to fit in the gap
not sufficiently radiation tolerant (~2-3x1015n/cm2 at 2nd module from inner edge of HGCAL)

## Slide 44: Some on-detector electro/optical components in numbers
#lpGBT = #motherboards
#data concentrator ASICs = #data/control links
#trigger concentrator ASICs = #trigger links

## Slide 45: ~1 million trigger cells (TC) in HGCAL, c.f. <10000 in present CMS endcap calorimeters
On-detector 1.5msec
Off-detector 3.5msec
Time
multiplexing
TK+ CALO+ MUON
Presently exploring Serenity ATCA board for Trigger & DAQ back-end
See talk from A. Rose

## Slide 46: Putting it all together

## Slide 47: CE-E cassettes are self-supporting sandwich structures with Pb, Cu and Cu/W as absorbers
Stainless-steel clad
Pb absorber 2.1mm Stainless-steel clad
PCB motherboard
ASICs etc. PCB sensor board
Silicon
CuW baseplate
Cu cooling plate
~24 mm
Modules placed on both sides of Cu cooling plane and “closed” with steel-wrapped Pb plates

## Slide 48: Dummy cassette is installed in a cold box to study heat-transfer characteristics – works well!
@FNAL

## Slide 49: CE-H cassettes: some have all silicon (a la CE-E); some have mixture of Si and scint/SiPM
Scintillator + SiPM
Silicon

## Slide 50: Wedge-shaped “Cassettes” containing arrays of silicon modules or silicon+scintillator/SiPM
Silicon-only layer (in CE-E) showing “cassettes” and different sensor thicknesses
Mixed layer (in CE-H) with silicon at high h and scintillator+SiPM at low h

## Slide 51: Assembling CE-E: self-supporting cassettes are assembled horizontally
Cassette installation onto CE-E back flange

## Slide 52: CE-H is assembled in two steps: absorber material, followed by insertion of cassettes

## Slide 53: Final assembly steps: attach CE-E to CE-H, then rotate whole CE to vertical for lowering

## Slide 54: There are two options for removing the existing endcaps and lowering the new ones
Crawler crane (rented)
~1400 tonnes, transported in 75 trucks!
Needs large roof openings
Can move around the site
Linear winch crane (custom made)
Similar in principle to original CMS crane
Calorimeter can be rotated in this system (no need for separate rotating table)

## Slide 55: Linear winch crane can also rotate the endcaps

## Slide 56: Dessert Measured HGCAL performance

## Slide 57: Prototype silicon modules + CALICE AHCAL tested at CERN in 2017; more in 2018
Si + Pb CE-E
Si + SS front CE-H
CALICE AHCAL
Nearly 2 tonnes, 3m long
Electrons, pions, muons

## Slide 58: Beam tests in 2016 & 2017 validated basic design; good stability; MIPs seen in all parts
Mips (for calibration) seen from muons and also single particles within hadronic showers
S/N ~ 8

## Slide 59: Beam tests in 2016 & 2017 validated basic design; good comparison to simulation
Distributions from electrons and pions match those predicted by simulation (to within 5%) demonstrating accuracy and scalability
First indications that HGCAL performance is as expected from simulation
More test beam data will be taken in a few weeks @ CERN
Transverse shower shape
Electron energy resolution

## Slide 60: First 2018 beam test @ CERN featured 28-layer CE-E section
100 GeV electrons: occupancy plots for all 28 layers (last 3 layers are noisy)
MIP distribution from online DQM

## Slide 61: Silicon sensors also have good intrinsic timing resolution that does not degrade with radiation
Constant term ~20ps
~10 MIPs at 0 fb-1; ~20 MIPs at 3000 fb-1
Can look at shower evolution in 5D (energy, X, Y, Z, t)  Particle Flow

## Slide 62: HGCAL TDR was submitted in Nov. 2017 R&D continues; construction starts in 2020
CMS-TDR-17-007
Approved on 18th April 2018!

## Slide 63: A Little Extra Challenges ahead

## Slide 64: With the approval of the TDR (18th April 2018) we are entering a phase transition
Finalization of design, prototyping towards final systems (2 years)
EDR (~May/June 2020) and ESRs
  This is a much faster timescale than the original LHC-experiment construction phase
Market Surveys, orders, preproduction, qualification of final components
Production starts in <3 years !

## Slide 65: Synoptic view of HGCAL: ~5 years to finalize design, produce components, assemble, install

## Slide 66: Highly-granular calorimeters, such as HGCAL, will provide much more information than any previous calorimeter. Building and exploiting the HGCAL brings major technological challenges. An exciting time for detector and software development!

## Slide 67: backup

## Slide 68: Efficiency of detecting hadronic & em components differs from unity: non-compensation
Electromagnetic component
Non-em component (charged)
Fraction of non-em component (“h”) detected is far lower than for the em-component (“e”): e/h > 1 for most detectors. This leads to:
Non-linearities
Non-Gaussian response
Relatively poor energy resolution
em fraction is large & varies with energy & fluctuates with non-Gaussian tails

## Slide 69: Hadron showers contain electromagnetic and hadronic components
p0
p-
nuclear fragment
n
n
em component
non-em component
Electrons, photons p0  2g
 em sub-shower
Charged hadrons
Nuclear fragments, protons
Neutrons, soft gs
Breakup of nuclei
(20%)
(25%)
(15%)
(40%)
Either not detected or often too slow to be within detector time window  invisible energy
ABSORBER

## Slide 70: Particle flow resolution is clearly better than calorimeter alone
(slide shamelessly stolen from Katja Kruger from BTTB5)
Simulated ILD calorimeter/PF performance

## Slide 71: Molière radius of HGCAL is ~28mm, but high granularity  much finer details can be resolved
Shower max
Coloured rectangles: = % shower energy deposited in that layer

## Slide 72: VBF Hgg, with 720 GeV VBF jet (2 charged p + g) & 175 GeV g incident on CMS endcap; pileup 200
Showers from the two photons are visible in the layers of the electromagnetic part
DR~0.2
L2
L14
L11
L20
L23
L26
L8
L5
L17

## Slide 73: VBF Hgg, with 720 GeV VBF jet (2 charged p + g) & 175 GeV g incident on CMS endcap; pileup 200
Showers from the two pions become visible in the layers of the hadronic part
L28
L30
L31
L32
L39
L34
L40
L41
L42
L35
L36
L37
DR~0.2

## Slide 74: Regions of silicon or silicon + scintillator/SiPM governed by radiation field
Silicon in high-radiation regions
Silicon
Scintillator

## Slide 75: Full simulated reconstruction and performance of HGCAL is in its infancy
The detailed implementation of the detector geometry necessarily lags behind technical design choices. In autumn 2016, before the making of many of the important engineering decisions that are described in the TDR, the HGCAL geometry implemented in the CMS simulation and reconstruction software, CMSSW, was frozen to allow simulation work to proceed.

## Slide 76: Occupancy of cells reaches ~70% in a small high-h region, but is <20% for most of HGCAL
h = 1.57
Top num.: avg. cell occ. > 0.5 mip
Bottom: avg. trig. cell occ. > 2 mipT
avg. cell occ. > 0.5 mip
Pileup = 200, LINT=3000fb-1
avg. trig cell occ. > 2 mipT
Pileup = 200, LINT=3000fb-1
Colours = different thicknesses

## Slide 77: As an illustration, granularity and timing can mitigate the effects of pileup  5D detector!
No timing cut
VBF (H→gg) event with one photon and one VBF jet in the same quadrant,
g
VBF
jet
Cut Dt < 90ps (3s at 30ps)
Possible due to the choice of CE sampling parameters and electronics
Plots show cells with Q > 12fC (~3.5 MIPs - threshold for timing measurement) projected to the front face of the endcap calorimeter.

## Slide 78: e/g reconstructed from single 3D TPG cluster with cuts on transverse & longitudinal profiles
L1 ET > 30 GeV
Efficiency of HGCAL standalone e/g trigger algorithm >90% @ 40 GeV ET
1.7 < h < 2.9
e/g background trigger rate with ET > 30 GeV ~O(100kHz) before isolation, track matching etc.

## Slide 79: HGCAL jet trigger based on anti-kT algorithm, exploiting dense core of jets for pileup mitigation
Jet size ~ DR=0.2: good balance between pileup mitigation & minimization of energy fluctuations
L1 ET > 150 GeV
Efficiency of HGCAL standalone jet trigger algorithm >90% @ 200 GeV ET & quite insensitive to pileup
Jet background trigger rate with ET > 150 GeV ~O(10kHz) before isolation, track matching etc.

## Slide 80: G4 simulation used to predict performance of HGCAL in presence of pileup: E/m resolution
Single unconverted g in CE-E reconstructed in r<2.6cm  insensitive to pileup
H-gg, both g in HGCAL (g do not convert in TK)
Pileup 200
Stochastic term between 24-31%

## Slide 81: Jet identification greatly improved using shower-shape information from HGCAL
sVV – radial spread
Dh
QCD PU200
Zee
Zee PU200
L10% – layer in which SE >10%
Dh (electron cluster–track)
1% bkgnd @ 95% signal pT > 20 GeV
10% bkgnd @ 95% signal 10 < pT < 20 GeV
*PCA = principle component analysis

## Slide 82: Longitudinal and transverse shower shapes can also distinguish VBF jets from pileup jets
EE/FH/BH refer to names of parts of HGCAL at time of TP (2016): simulation is based on this (not very different) geometry
Pileup jets tend to start earlier in the calorimeter and be less collimated than VBF jets

## Slide 83: Traditional “cylindrical onion” hermetic particle detector, with distinct dedicated layers
Tracker: tracking and vertexing: charge identification and momentum measurements Calorimetry: energy measurements of charged and neutral particles. Separated into electromagnetic and hadronic sections
B-field: to filter particles etc.
Dedicated muon detectors

## Slide 84: ECAL also includes a 2-layer silicon-strip-based “Preshower” in its endcaps, to aid particle ID
6 x 6cm2 silicon sensor, 32 strips ~ 1cm2/strip
4 planes of 1072 sensors = 137000 channels, ~16m2 total (largest silicon-based calorimeter!)
Used mainly for p0 identification, but ID power not as good as foreseen due to upstream TK material