## Slide 1: Linear accelerator simulations for stable and sustainable operation of developing country radiotherapy linear accelerators
Marco Carlone, BC Cancer
Stewart Boogert, Royal Halloway

## Slide 2: Linac operability is an important consideration in any environment
Training on linac service personnel is difficult at BC Cancer
Communication between Medical Physicists and Linac Service technicians is challenging everywhere
We suggest that this is a critical component of any linac operation plan, especially for challenging environments

## Slide 3: Linac Physics is Complicated
Electron beam acceleration in waveguide is advanced physics.
There is a convoluted relationship between the basic physics and clinical beam properties.

## Slide 4: Teaching Linac Physics
Should relate basic physical principles to clinical parameters.
Needs a hands on component.
Jargon issues between service engineers and physicists.
Few teaching resources aimed at the radiotherapy physicist

## Slide 6
Upcoming Course Accelerator Technology (ATec)
February 28 - March 3, 2017
Led By: Dr. Marco Carlone &
Mr. Bern Norrlinger
The Accelerated Education Program
Princess Margaret Cancer Centre
Connect with Us!
Web: www.aepeducation.ca
Email: aep@rmp.uhn.ca
Twitter: @AEPcme
YouTube: AEP Education LinkedIn: Accelerated Education Program

## Slide 7: Challenges with the ATec Course
4 day length is too short for any in depth teaching.
Relating linac theory to linac service/QA problems is difficult.
Clinical linacs at PMH were not available.

## Slide 8: SIMAC Simulate Linac
Most linac physics can be modeled using simple analytical approximations
Response is consistent with a real linac response.
Meant to simulate the service mode of a clinical linac

## Slide 9: Using SIMAC
Mode selection
Linac parameter control
Clinical parameters
Linac operating values

## Slide 10: Linac Physics modules in SIMAC
Electron beam position and angle on the target
Photon transport is modelled using breamstallung yield tables (NIST) and linear attenuation in the FF and water phantom
The linac Load line is modelled using the concept of “Shunt Impedance”
Klystron saturation is modelled using an analytical (Bessel) function

## Slide 11
Teaching of beam “tuning” with SIMAC

## Slide 12
6 MeV beam on 6MV flattening filter
Pos_R = 100 mA, Ang_R = 0
7.5 MeV beam on 6MV flattening filter
4.5 MeV beam on 6MV flattening filter
Using SIMAC to teach Flatness & Symmetry as a response to beam steering and energy

## Slide 13: www.simaclinac.com

## Slide 14: Simac is freely available

## Slide 15: Work Package 5
Address the operability of a medical linac
  Address the knowledge issues around linac service by improving the SIMAC experience
    (Have good linac drivers)
  Provide automation tools to assist linac repairs by modeling include linac failures
    (Provide a driver assist mode for already good drivers)

## Slide 16: Work Package 5
Deliverable 1: Help expand the online SIMAC community by making SIMAC fully web-based.
Deliverable 2: Demonstrate the feasibility of a diagnostic data collection system.
Deliverable 3: Report on potential algorithms to implement a machine learning model to interpret fault data.

## Slide 17: Deliverable 1
SIMAC is mature and has been used
Assemble a complete set of linear accelerator physics modules
  Building a comprehensive “flight simulator” for LINACS
  Maintain code in GitHub repository to maximize community involvement

## Slide 18: Deliverable 2
Install data loggers on existing linacs and demonstrate the feasibility of collecting this data

## Slide 19: Deliverable 3
Collection of data from existing machines
Consultation on potential machine learning algorithms and implementations
Demonstration of simple predictive model of known failures

## Slide 20: Linac failure categories
Modulator/injector failure
Beam delivery error (steering)
MLC malfunctions
Power supply failures
Control system failures
Mechanical failures
Broken wires
Many others (some simple, sone not)

## Slide 21: Linac failure categories
Modulator/injector failure
Beam delivery error (steering)
MLC malfunctions
Power supply failures
Control system failures
Mechanical failures
Broken wires
Many other smaller categories
I would guess these are the majority

## Slide 22: Linac failure categories
Modulator/injector failure
Beam delivery error (steering)
MLC malfunctions
Power supply failures
Control system failures
Mechanical failures
Broken wires
Many other smaller categories
These are the most intimidating, and most difficult to teach

## Slide 23: The Art of Linac Maintenance
There is a challenging learning curve
  Service technicians are not physicists
  Distinguishing between electronics/control system problems and linac physics problems can be challenging when learning

## Slide 24: Objective with deliverable 3
To assist service technicians with diagnosis problems involving linac physics.
To reduce the “fear factor” of a large complicated machine.
It is not intended to provide a comprehensive linac fault diagnosis repair automation

## Slide 25
Deliverable 3 is more like driver assist as opposed to a driverless car.

## Slide 26: Questions/comments?