## Slide 1
STATUS of the IPHI facility (Injecteur Protons Haute Intensité)
C. Marchand CEA Paris-Saclay/IRFU/DACM

## Slide 2: Content of talk
Goals and history
IPHI layout description
RFQ conditioning and first beam (2014/2016)
Neutron production and beam diagnostic tests (2017/2018)
Present upgrades
Roadmap towards CW

## Slide 3: IPHI goals and history
Initial layout (PAC’97 Vancouver, PAC 2000 Vienna) inspired by LEDA design
  SILHI source + LEBT+ RFQ (8m, 5 MeV) + DTL (11 MeV) + MEBT (CEA/CNRS)
Actual layout (HIHBB 2004)
  Rescoping in 2002 in framework of CEA/CNRS/CERN collaboration
  IPHI limited to SILHI+LEBT+RFQ (6m, 3 MeV)+MEBT, DTL descoped
Goal: Develop R&D in France on High Intensity Proton Injector technology
  100 mA CW proton beam up to 11 MeV (352 MHz RF)
  Develop expertise for future proton accelerator projects (IFMIF, SPL, ESS, …)
  Develop compact neutrons sources to replace phased out R&D nuclear reactors
  Provide facility to test and develop novel non intercepting beam diagnostics
Notes: Rappeler ici les 3 layouts historiques (97, 2000 et 2003)

## Slide 4: Overview of IPHI installation
K1
K2
1,3MW @352MHz CW
2.8MW @352MHz pulsed
  240kW average
  10µs <Tp< 3600µs
  1Hz< Freq < 50Hz
K3
NEW (Sept 2018)
Notes: Layout 3D général, puis layout 2D général avec RF, puis layout 2D

## Slide 5: IPHI beam line components
LEBT
900kW dissipated power
300kW (100mA,3MeV)
Notes: Photos et paramètres succincts Source-LEBT-RFQ-MEBT (silde 20 Gobin+Pottin)

## Slide 6: RFQ specifications
6 sections (3 segments)
2 end plates
2 coupling plates
60 pumping ports
4 RF injections on 4th section
96 RF stub tuners
268 water cooling channels
Q1
Q2
Q3
Q4
Notes: Figure 3D avec liste specs

## Slide 7: RFQ cooling system
1
2
3
4
5
One « cold » loop: (11->30°C)
Channels 1,2 of all RFQ segments
+ Coupling plates+ end plates
Three « warm » loops (1/segment):
Channels 3,4,5 of one RFQ segment
+ Slug tuners + vacuum ports (+ RF ridges)
Notes: Boucles de refroidissement et description sommaire pompage et ridges

## Slide 8: RFQ cooling system
4
Three « warm » loops (1/segment): 25°C
Channels 4 of one RFQ segment
Minimal cooling for RFQ conditioning (2014-2016)
-> d.c. limited to < 1%
Notes: Boucles de refroidissement et description sommaire pompage et ridges

## Slide 9: Initial RFQ conditioning (2014-2015)
Frequency shift: ~ -80 kHz
Fluctuations in reflected power
Loss of 10% voltage in segment 2
Heat up on RF entries in Q2, Q3
Notes: Plot conditionnement + glitch freq + loi tension + ridge warming, inspection, repair

## Slide 10: Initial RFQ conditioning (2014-2015)
Frequency shift: ~ -80 kHz
Fluctuations in reflected power
Ridge status in Q2, Q3
after dismounting
Heavy sparking
Vaporized RF seal
Missing seal on side
Fix to solve issue
Clean ridges
Change RF seal
Add seal on side
Notes: Plot conditionnement + glitch freq + loi tension + ridge warming, inspection, repair

## Slide 11: RFQ conditioning (2016)
After replacing ridges:
Frequency shift: ~ +100 kHz
Increase of voltage in segment 2 (13%)
Can be corrected increasing segment 2 loop temperature by ~4°C
dF/dT (kHz/°C
1.2 MW peak power, 0.6% d.c. (600ms, 10 Hz)
Notes: Plot conditionnement + loi tension + dF/dT pour ratrapper 100 kHz décalage

## Slide 12: IPHI beam (low d.c.)
Transmission | Simulated | Experimental
LEBT | 70 % | 73 %
RFQ | 98 % | 93 %
First IPHI beam: spring 2016
Transmission | Simulated | Experimental
RFQ | 98 % | 96 %
Notes: Transmission initiale + profil faisceau + transmission améliorée

## Slide 13: 2017 & 2018 experimental setups
Neutron production
Be target + moderator
3He n TOF detector
nBLM detector
MCP IPM
Diagnostic tests
(prototypes for ESS)
8 m
Notes: Setup 2D pour production neutrons et tests diagnostics ESS

## Slide 14: Neutron production runs
Neutron angular anisotropy
measured by nBLM without moderator
Notes: Tests production neutrons

## Slide 15: nBLM diagnostic tests
nBLM station: fast (top) and slow nBLM
SLOW nBLM
FAST nBLM
Recoil protons (n,p) on mylar
Fast neutrons directly measured
En > 1 MeV
10 to 100 less efficient
Time response: ~10 ms
Mainly MPS
(n, α) 10B reaction on B4C
Detection of fast neutrons after moderation in polyethylene (~4cm)
10-6 < En < 100 MeV
Efficiency: few n.cm2.s-1
Time response: >200 ms
Monitoring of small bean losses
Time response of the slow nBLM detector
neutron Beam Loss Monitors
Time response of the fast nBLM detector
and beam current on target
Notes: Test diagnostics nBLM

## Slide 16: IPM diagnostic tests
MCP Hamamatsu
Goal: to measure the beam transversal profile at high energy and very low residual gas pressure with a non intrusive technique based on residual gas ionization
dX (IPM/BPM) mm
Notes: Tests diagnostics IPM

## Slide 17: Ongoing RF upgrades
SAT new K2 CW klystron
(end of june 2018)
Connect K3 pulsed klystron
(-> september 2018)
New analog LLRF (pulsed)
(->september 2018)
Notes: Uogrades RF (klys pulsé + LLRF), cooling

## Slide 18: Roadmap towards CW
Low d.c. beam run Sept. 2018 with pulsed klystron
Conditioning of RFQ to ESS d.c. (4%)
First tests for IPHI-neutrons at 7 kW end of 2018
Deliver pulsed beam for ARIES TNA
Second tests for IPHI-neutrons at 50 kW for SONATE project
Push conditioning to full CW with increased instrumentation
Preliminary SONATE layout
Notes: Planning + 3D IPHI-neutrons