## Slide 1: EDM 2018
Mike 24th January 2018

## Slide 2: 2017
2011 BNL proposal
Considerable effort by community
  Components (shielding, deflectors…)
  Instrumentation (SQUIDs, Polarimetry…)
  Lattice
  Simulations
  Systematics
  NB Lebedev’s evaluation
CERN
  Sketch possible implementation
  Components
  Examine systematics
Working assumption: it’s tough but doable

## Slide 3: Questions on basics
Systematics
  In particular radial B-field – see Christian
Simulations
  Consistent handling of KE changes in electric field?
Focusing strength
  Weak
    “required mechanical accuracies of bending plates manufacturing, assembly and installation look too tight”
  Strong (AG)
    Reduced sensitivity to effect of Br on CW/CCW splitting
    Strong focusing rules out 10-29 e.cm (?)
  Back to weak?

## Slide 7: Can you get down to order 10 aT?
See Christian… it’s not obvious

## Slide 8
In principle, no magnetic shielding will be required with continuous BPM measurement around the ring.
The finite number of detectors limits the magnetic field modes to which the system is sensitive by the Nyquist sampling theorem.
The critical parameter is the detected average radial B-field and that can be wrong only when the mode is equal to the number of the BPM locations around the ring as well as its integer multiples.

## Slide 10: Cautious prototype
Richard Talman

## Slide 11: Ambitious Prototype
Reduced energy EDM ring on COSY footprint
Spin tunes in superimposed electric and magnetic fields
IRON-FREE strip-line magnetic field
Frozen spin operation with weak vertical magnetic field
Proton EDM measurement in ring matched to COSY footprint
Low energy p-helium and p-carbon polarimetry candidates
Electron EDM measurement in ring matched to COSY footprint
Richard Talman

## Slide 14: Prototype
If we continue… a prototype of some sort would appear inevitable
To test:
  Shielding, b-field compensation
  Components
  Instrumentation
  Measurement techniques
  Systematics

## Slide 15: Option – axion search
The method uses a combination of B and E-fields to produce a resonance between the g − 2 precession frequency and the background axion field oscillation to greatly enhance the sensitivity to it.

## Slide 16: Axion search

## Slide 17: Axion search

## Slide 18: Ultra-weak focusing
Octupoles
Rolling spin
Resonant polarimetry

## Slide 19: Conclusions
Huge amount of work there in the EDM community
However important questions still to be answered
  Focusing etc.
  Is the required level of accuracy achievable?
Situation further muddied by options
  Axion search, frequency domain, ultra-weak focusing etc.
Prototype seems inevitable (if…)
  Where to be decided
  (CSR possibilities also being explored)

## Slide 20: Next steps
CP-EDM meeting 8-9 March
  Should be interesting
Thereafter re-scope for ESPP
  At this stage imagine only a sketch of possible implementation at CERN/green field