## Slide 1: Calorimeter Upgrade: Analog Electronics
D. Gascon, J. Mauricio, E. Picatoste
ICCUB//SiUB, University of Barcelona

## Slide 2: Outline
Calorimeter upgrade: analog electronics
System design
Digital building blocks
Tests
Production

## Slide 3: I. Current Analog Signal Processing
  Clipping:
  Reduce signal tail
  Reduce spill over
Front End Board
12b ADC
Detector cells
clip
12m cable
-
+
PMT
5ns 50Ω
50Ω
25ns 100Ω
100Ω
100Ω
BUFFER
Rf = 12MΩ
Cf = 4pF
100nF
22nF
INTEGRATOR
Analog Chip
  Specifications:
  Pulse shaping in 25ns
  Spill over (signal residue) < 1% after 25ns
  Integrator plateau: 4ns
  Linearity < 1%
  Rise time ~ 5 ns
  Integrator discharge:
  Clipped signal + delayed negative clipped signal
After clip
After clip
Before clip
Before clip
BiCMOS 0.8um integrated circuit 8 channels per chip

## Slide 4: I. Analog Electronics Upgrade Motivation
Front End Board
12b ADC
Detector cells
clip
12m cable
-
+
PMT
50Ω
100Ω
100Ω
BUFFER
Rf = 12MΩ
Cf = 4pF
100nF
22nF
INTEGRATOR
Analog Chip
PMT current has to be reduced to increase lifetime
  FE electronics gain has to be increased correspondingly
  BUT FE noise should not be increased in the operation!
Proposed solution:
  New ASIC
    Increased gain
    Reduced noise
    Integration / shaping
Radiation tolerance:
  Dose 100 rad per fb-1
  Radiation qualification tests
  Design techniques on ASIC
    Enclosed transistors with guard rings
Delay lines
5ns 50Ω
25ns 100Ω

## Slide 5: Outline
Calorimeter upgrade: analog electronics
System design
Digital building blocks
Tests
Production

## Slide 6: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Very difficult to integrate HQ analog delay lines
2 switched alternated paths
Switching noise
Fully differential ASAP

## Slide 7: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Clock input

## Slide 8: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Clock input
Current Amplifier output
PMT signal
PZ output
Input signal

## Slide 9: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Integrator output
Main signal
Tail
Clock input

## Slide 10: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Clock input
TH output
Main signal
Tail

## Slide 11: II. System design: channel architecture
Switched Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
Offset
Clock input
Main signal
Tail
Channel output

## Slide 12: II. ICECAL ASIC
SiGe BiCMOS 0.35um
AMS 10.5 mm2
Analog channel:
  Very difficult to integrate HQ analog delay lines
  2 switched alternated paths → no dead time between consecutive events
  Switching noise → fully differential ASAP
  Input impedance control by current feedback
    Low noise performance
FPGA
Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
Drv
x4
12b ADC
12b ADC
12b ADC
12b ADC
MEM
MEM
Phase detector charge pump
x4
Ref clock
MEM
SPI slave
MISO, MOSI, !SS, SCLK
ADC clock
Bias
25
Complete 4 analog channels
Tunable parameters
4 DLL for synchronization
2 versions with gain:
  4.5 fC/LSB
  9.0 fC/LSB
CH0
Regs+bias+DACs
DLL + Slow Ctrl
CH1
CH2
CH3

## Slide 13: Outline
Calorimeter upgrade: analog electronics
System design
Digital building blocks
Tests
Production

## Slide 14: III. Digital building blocks: DLL
LVDS Clock
CMOS Clock
Serial Reg. bus
Analog config.
Legend
Phase detector charge pump
x4
Ref clock
MEM
ADC clock
25
Vcoarse
Vcontrol
T&H clock
INT clock
5
Vcoarse
Vcontrol
Delay Lines
Clock management is internally done by the ICECAL Chip:
  Three clock phases are generated from an input reference (REF_CLK):
    Track & Hold clock phase (ΦTH). FCLK = 20 MHz.
    Integrator clock phase (ΦINT = ΦTH + ΔΦINT). FCLK = 20 MHz.
    ADC clock phase (ΦADC). FCLK = 40 MHz.

## Slide 15: III. Digital building blocks: slow and fast controls
Access to internal registers to configure the chip:
  Analog channel parameters
  DLL
  SPI Slave
Analog sub-channel reset circuit:
  FPGA needs to know the analog sub-channel source of the ADC reading Gain & Offset compensations.
  The first sub-channel is always the same for each configuration
SPI Slave
!enableSpiRefresh
MOSI
MISO
SlowCtl
FPGA
SCLK
!SS
ICECAL
SPI_Refresh
MEM
FPGA
MEM
SubCh Reset
Resynch
Ref clock
INT
Delay Line channels
Delay Line channels
Delay Line channels
Delay Line channels
TFF
TFF
···
T&H
FPGA clock
Detected
BXID_RST
ICECAL
BXID_RST_SYN
LHCb fast control

## Slide 16: Outline
Calorimeter upgrade: analog electronics
System design
Digital building blocks
Tests
Production

## Slide 17: II. ICECAL ASIC: tests results
  Spill over
  Plateau
Tests at lab and test beams:
  Linearity
  Noise

## Slide 18: II. ICECAL ASIC: radiation hardness tests
At CRC (UCL) in Louvain-la-Neuve (Belgium)
TID tests:
Use beam of 61 MeV protons
Dose up to 55 krad on 4 chips
Results:
  No SEU or SEL was detected
  No relevant variation on the chips characteristics
SEE tests:
Irradiate with heavy ions: 58Ni+18
  LET = 20.4 MeV/mg/cm2
Two chips were irradiated:
  No SEU detected
Use refresh signal
Equivalent expected limits for all channels in detector lifetime:
  1.3 SEU
  0.9 SEL

## Slide 19: Outline
Calorimeter upgrade: analog electronics
System design
Digital building blocks
Tests
Production

## Slide 20: IV. Production
Relays
IN
Open top socket
    FPGA
FEB prototype (4 data channels)
Updated mezzanine
    Motorized horizontal gantry system to move the chips from tray to the test PCB and to final tray.
    Motorized stage in the vertical direction.
    Pneumatic suction.
    Pressure sensor.
Robotic system

## Slide 21: V. Status
Production
  Standard version (v3.1): 3050 pieces
  Reduced gain (v3.2): 3050 pieces
Production test
  Mezzanine: ready
  SW:
    Test defined: rejection limits are being prepared
  Robotic setup ready in ~2 weeks
  Estimated total test time: 2-3 months

## Slide 22: Backup

## Slide 23: II. System design: Analog Electronics Specifications
PMT current has to be reduced by factor ~ 5 to increase their lifetime:
  FE electronics gain has to be increased correspondingly
  FE input equiv. noise should still be ~ 1 LSB
New ASIC:
  Increased gain
  Reduced noise
  Integration / shaping
New front end board is required:
  Low noise analog electronics
  Data transmission @ 40MHz
Energy range | 0-10 GeV/c (ECAL) Transverse energy
Calibration | 4.5 fC / 2.5 MeV / LSB
Dynamic Range | 4096-256 = 3840 : 12 bit
Noise | <≈ 1 LSB or ENC < 4 fC
Termination | 50 ± 5 Ω
Shaping | 25 ns (99% of the charge)
Baseline shift prevention | Dynamic pedestal subtraction (CDS) Pedestal is the smallest of 2 prev. Samples
Max. Peak current | 4 - 5 mA (clipped)
Spill-over residue level | ±1%
Linearity | < 1%
Crosstalk | < 0.5%
Timing | Individual (per channel)

## Slide 24: III. ICECAL pinout
Differential inputs
Differential outputs
Analog Power/Ref
Digital Power/Ref
LVDS ADC clock outs
Input clock
DLL control signals
SPI
BXID reset
Reset

## Slide 25: III. SPI refresh
D
Q
FF
D
Q
FF
D
Q
FF
P
P
P
3-V
0
1
CLK
d0
d0
PRESET
R1
R2
R3
OUT
IN
EN
SPI Slave
!enableSpiRefresh
MOSI
MISO
SlowCtl
FPGA
SCLK
!SS
ICECAL
SPI_Refresh
MEM
16-bit TMR registers:
  Each bit is stored in 3 flip-flops.
  Majority is computed.
  SEUs are automatically corrected.
    Problem: correction is done as long as SPI clock is active.
    Solution: SPI refresh signal.
SPI refresh signal:
  An auxiliary clock is provided.
  Only enabled when SPI slave is idle.
  Is optional: can be disabled by software.

## Slide 26: III. Fast control: BXID reset
Analog sub-channel reset circuit:
  An ASIC channel consists in two sub-channels.
  FPGA needs to know the analog sub-channel source of the ADC reading:
    Gain & Offset compensations.
How it works:
  FPGA generates 1-cycle width synchronous reset pulse.
  ICECAL resynchronizes this reset with its input clock.
    Metastable phases (FPGA→ASIC) are discarded.
    Debug signals:
      External pad: 32-BXID_RST_SYN
      Slow control bit (Detected)
  Integrator and T&H clocks levels are preset (clock phases remain unchanged).
  The first sub-channel is always the same for each configuration
FPGA
MEM
SubCh Reset
Resynch
Ref clock
INT
Delay Line channels
Delay Line channels
Delay Line channels
Delay Line channels
TFF
TFF
···
T&H
FPGA clock
Detected
(42) BXID_RST
ICECAL
(32) BXID_RST_SYN
LHCb fast control

## Slide 27: III. Internal delay
DLL Vcontrol out
DLL VCOARSE input generation
Proposed circuits between ICECAL and GBT-SCA
It is recommended to use a voltage divider to read the DLL VCONTROL and adapt the voltage range to the ADC input.
The input VCOARSE voltage has to be controlled by a DAC.
  Its expected value is 1.2V
  Range: from 0.5V to 2V.

## Slide 28: III. Time alignment
28
Synchronization method:
  ΦICECAL_CLK_IN: look for the most stable phase for which the sub-channel reset is performed (fixed for each PCB).
  ΦI_TH: delay between the integration time and the Track-and-Hold clocks (internal delays of the chip, optimal = 1ns).
  ΦTH: detector channel optimal integration time (particle time arrival, PM HV, signal cable length). Look for the maximum signal and minimum spill over.
  ΦADC: time at which the ADC performs the conversion (fixed for each PCB).
  ΦADC_FPGA: the ADC 12 bits of data have to be captured by the FPGA in parallel at the right phase or there will be data corruption. Use rising or falling edge of the FPGA clock (fixed for each PCB).

## Slide 29: III. Calorimeter Upgrade: ICECALv3
Tests at lab:
FPGA
Clock in
SPI
(slow control)
ICECALv3
AD9238
FILTER
ADC clock
Outputs
Inputs
FILTER
AD9238
FILTER
FILTER
USB to PC
FE PROTOTYPE
ANALOG MEZZANINE
Delay Chip
Waveform Generator
10 MHz
Trigger
12 bits
12b ADC
12b ADC
12b ADC
12b ADC
  Input impedance
  Crosstalk
Chart: frequency (Hz)

## Slide 30: III. Calorimeter Upgrade: ICECALv3
  Spill over
  Plateau
Tests at lab:
  Linearity
  Noise

## Slide 31: II. ICECAL ASIC: tests results
Check noise in different conditions:
 | Noise (LSB) | PS noise (LSB)
Laboratory | 1.4 | 1.7
Lab + cable | 1.6 | 1.8
Test beam | 12 | 2.7
Detector | < 7.1 | < 2.9
Spec: ~1 ADC count
The effects of Cockcroft-Walton HV sources and cables increase noise
Upgraded detector expected pile-up ~5 LSB
  Effect of electronics noise adds up to 5.8 LSB (vs. 5.1 LSB specified)
FEB prototype
Provisional GND

## Slide 32: II. ICECAL ASIC: tests beams
Lecroy integration
FEB
prototype
ECAL channel
PMT
Trigger (coincidence)
Measurements laptop
Beam line: T4-H8 at CERN Prevessin
Beam: e- with energy ranging from 20 to 120 GeV
Elements used:
  4x(ECAL module+PMT+12m cable)
  FEB prototype
  Lecroy integrator
  Time-to-Digital Converter (TDC)
  ICECALv3 ASIC
Main tests:
  Plateau and spill-over
  Linearity
  Noise

## Slide 33: II. ICECAL ASIC: radiation hardness tests
At CRC (UCL) in Louvain-la-Neuve (Belgium)
TID tests:
Use beam of 61 MeV protons
Different irradiation steps. Dose:
  55 krad over 3 chips
  40 krad over 1 chip
Results:
  During irradiation no SEU or SEL was detected
  No relevant variation on the chips characteristics was observed
SEE tests:
Irradiate with heavy ions: 58Ni+18
  LET = 20.4 MeV/mg/cm2
Two chips were irradiated:
  No SEU detected after a fluence of 9,5·107 part/cm2
10 kHz refresh signal (SPIREFRESH)
Equivalent expected limits for all channels in detector lifetime:
  1.3 SEU
  0.9 SEL

## Slide 34: LHCb Upgrade Electronics ICECALv3. A Full Custom design
IBias Block
Analog Ch
3-Voting FFs
DLL + SPI
Submitted: March 2014
Die Area = 10.5 mm2
3.5 mm
3.0 mm

## Slide 35: Backup: ICECALv3 architecture
Detector cells
clip
PMT
12m cable
50Ω
Front End Board
FPGA
LVDS Clock
Integrator
I
TH
Track- and-Hold
TH
Filter
Current amplifier
Multiplexer
ADC driver
PZ
ʃ
PZ
ʃ
ICECALv3 ASIC
Drv
x4
12b ADC
12b ADC
12b ADC
12b ADC
MEM
MEM
CMOS Clock
Serial Reg. bus
Phase detector charge pump
x4
Ref clock
MEM
SPI slave
MISO, MOSI, !SS, SCLK
ADC clock
Bias
25

## Slide 36
Dynamic range and version decision (I)
 | v3.1 | v3.2
Sensitility (fC/LSB) | 4.54 | 9.05
Cint | 14 | 8
Pedestal | 311 | 311
Dynamic range (LSB) | 3784 | 3784
1 LSB (MeV) | 2.5 | 5
Dynamic range (GeV) | 9.5 | 19
Noise (LSB) | 1.21 | 1.06
Noise PS (LSB) | 1.66 | 1.26
Noise (MeV) | 3 | 5.3
Noise PS (MeV) | 4.2 | 6.3
Equivalent noise from detector (LSB) | 2.1 to 2.4 | 2.1 to 2.4
Noise PS+detector noise (LSB) | 2.7 to 2.9 | 2.4 to 2.7
Noise PS+detector noise (MeV) | 6.5 to 7.2 | 8.0 to 8.6
Which ASIC version?
  ICECALv3.1.
    Lower noise
  ICECALv3.2
    Increased dynamic range
  Mixed solution? For example:
    Inner FE with ICECALv3.2
    Outer FE with ICECALv3.1

## Slide 37
Production quality control
37
Relays
IN
Open top socket
    FPGA
FEB prototype (4 data channels)
Updated mezzanine
    Motorized horizontal gantry system to move the chips from tray to the test PCB and to final tray.
    Motorized stage in the vertical direction.
    Pneumatic suction.
    Pressure sensor.
Robotic system

## Slide 38
Production quality control
    One set of parameters for all the chips
    The optimal parameter set of values is obtained from a statistically reasonable amount of chips.
    2 min < t < 5 min
Tray of accepted chips
Tray of rejected chips
Chip Test: Socket open on top
Chip to test
Tray of Chips
Tested Chip
Robot movement
Robot movement
Automated procedure

## Slide 39
Example: ASICs tested per robot run
Elements/Package | PACTA (Example) | ICECAL
Package | QFN32 | QFN64
Size | 6x6mm2 | 9x9mm2
Num Chips/Tray | 490 | 260
Num Trays | 14 | 12
Num Chips/Robot | 6860 | 3120
Num Chips per test | 4 | 1
Robot Movement + photo per test | ~176s | ~44s
Test QC Time per test | ~65s | ~300s
Test Robot+QC iteration | ~240s | ~344s
Complete Run Test | 114h~5 days | 298h~12 days
Chips Tested per day | ~1440 chips/day | ~252 chips/day