## Slide 1: slow control and acquisition

## Slide 2: The MiniDAQ environment
MiniDAQ
20 meters
of fiber
3CU
FEB

## Slide 3: Configuration of the FEB
The FEB is configured by the USB with program in python and C++ libraries
The board should be initialized , The different elements (ICECAL, FE-PGA,SEQ-PGA) are configured by the SPI, and I2C , through commands sent by the USB

## Slide 4: Test FE Data part
Test of the Data Frame received in the
Memory Management :
In fixed pattern mode (0xAA BB ..)
Random pattern mode
Test BCID is OK
easy to check from the Memory
Management panel
Data part more difficult to check
(see next slide)

## Slide 5
Bit 95
Bit 91
10
96 bits
1
3
2
4
5
7
6
8
11
9
4 bits
+
= One Channel
One Channel
Bit 0
Specific data encoding of the FEB
How we test it :
Load FE injection Ram with specif pattern
Verification with a program to retrieve a specific pattern put in the data sent by the FEB in files written by the amc40_frgwriter of the miniDAQ
Chan 0
.
.
.
Chan 7
In the FEB
In the Wide Bus frame

## Slide 6: Test I2C communication with GBT-SCA of the FE
GBT Client
FEB
By mini-HDMI to back end
By optic fiber
Read/write of some
Register of the different
Gbtx of the FEB

## Slide 7: Test SPI communication with GBT-SCA of the FE
CCP1 terminal
FEB
By mini-HDMI to back end
By optic fiber
Read/write of some
Register of SPI different
Slave (ICECAL OK),
firrmware adaptations for
Fe_pga and Tri_Seq_pga
Spi_test line command used

## Slide 8: Test SyncFrame pattern to miniDAQ
Green led synchronized
FEB
Datas
Optic fiber 7
a local command triggers 10 SyncFrames
SyncFrame = Configuration of the FEB to send the BCID under 12 bits with a fixed pattern after this.
Commutation to normal
datas with BCID under 8 bits after the 10 SyncFrames
The miniDAQ is synchronized !
But as we aren’t synchronous with a TFC cmd the miniDAQ is in Error