## Slide 1
3CU (Calorimeter Crate Controller for the Upgrade)
Production Readiness Review
Introduction
 Short reminder (TFC system, Calorimeter crate)
General description
   Main role - main part of the board - overview
  Architecture
   Global architecture - clock tree - GBT frame format - Slow Control - Delatching control - IGLOO2 FPGA - Power supplies and power tree - Rear connections - Fimware architecture
Conclusion
On behalf of the Orsay group
1

## Slide 2: PRR 3CU board
Introduction
 TFC system reminder
   Calorimeter crate reminder

## Slide 3
Introduction : TFC system reminder
3CU Boards
S-ODIN receives directly Clk from the RF-system of the LHC.
S-ODIN card distributes the Clk and the Fast Control commands to the SOL40 ant TELL40 board.
And SOL40 board distributes Clk and Fast Control command to the 3CU board.
F. Alessio Schematic
2

## Slide 4
Introduction : Calorimeter crate reminder
Calorimeter crate controller board (3CU)
Ensure signal distribution inside Front-end crate
  Clock distribution from the 3CU to all front-end board inside the same crate through 3U backplane.
  Slow control through 6U backplane
  Fast command (BxId Reset, FE Reset, …) through 3U backplane
Crate Power supply
  Reused Marathon equipment
Front-end crate with same backplanes and power supply
  3U  power supply, clock distribution, …
  6U  links between boards inside the same crate.
  New Front-end board with optical link DAQ and LLT.
  New Control Board (3CU).
  Remove TVB.
3

## Slide 5: PRR 3CU board
General description
 General description
   Global architecture
   Overview

## Slide 6
3CU : General description
3CU main role:
  Receive the GBT frame through the optical link.
  Extract the information needed by the FEBs (inside the same crate)
    40 Mhz Clock
    Time Fast Control (TFC) commands
    Experiment Control System (ECS)
Main part of the board:
  A Versatile Transceiver (VTRx), a bi-directional module composed of both optical transmitter and receiver.
  A GBTx chip that can be used to implement multipurpose high speed bidirectional optical link.
  A GBT-SCA ASIC, part of GBT chip-set to distribute the Slow Control (SC) information on the board.
  A Microsemi FPGA (IGLOO2), in charge of the processing on the 3CU.
4

## Slide 7
General description: overview
Front
Rear
6U backplane connections
3U backplane connections
GBTx
VTRx
GBT-SCA
IGLOO2
DC-DC converter
FEBs delach. Info
ECS distribution
Clock
TFC command
3CU board:
  9U / 280 mm VME board
  Thickness 2.4 mm
  Components 999 / Connections 5115
  12 layers
  Routing very tight around IGLOO2 and GBTx and SCA
5

## Slide 8
3CU Board : Global architecture
B25
AB25
B25
AB25
B77
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
GBTX
Front
Rear
Clk Ref / PLL
Phase Shift.
Clk Manager
(LVDS)
(LVDS)
(TFC cmd)
PS : 1V5
PS : 2V5 , 1V5
USB-I2C
dongle
Slave
I2C
Data
TTC cmd
Clock
SC
6

## Slide 9
3CU Board : Global architecture
B25
AB25
B25
AB25
B77
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
E-Port_SC_FEB
x (16)
GBTX
User Buses :
{I2C, //, SPI,
JTAG, 12bADC,
…} – T°
E-Port
Network
Controller
GBT-SCA
Prim. / Second.
E-Port_SCA
Slow control to FEB
Protocol used on the board
Slow Control distribution to FEB through 6U_backplane
Front
Rear
I2C
GPIO
SPI
Clk Ref / PLL
Phase Shift.
Clk Manager
…
Buffer
PS: 2V5
(SLVS)
(LVDS)
(SLVS)
(LVDS)
(TFC cmd)
PS : 1V5
PS : 2V5, 1V5
USB-I2C
dongle
Slave
I2C
Data
TTC cmd
Clock
SC
6

## Slide 10
3CU Board : Global architecture
B25
AB25
B25
AB25
B77
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
E-Port_SC_FEB
x (16)
GBTX
User Buses :
{I2C, //, SPI,
JTAG, 12bADC,
…} – T°
E-Port
Network
Controller
GBT-SCA
Prim. / Second.
E-Port_SCA
Slow control to FEB
Protocol used on the board
M2GL060
VCC Core
VCC I/O_1
VCC I/O_2
USB
Delatching
Ctrl.
Dedicated Clock IO
Clock Conditioning Circuit
LVDS
SLVS / LVDS Translator
LVDS
TFC cmd
Slow Control distribution to FEB through 6U_backplane
In_1
Out_2
Out_1
In_2
1V2
1V5
2V5
Front
Rear
TFC command
E-Port (TFC_cmd)
Buffer
PS: 3V3
TFC command
387 Max user I/Os – 10 I/O Banks
TFC cmd distribution to FEB through 3U_backplane
I2C
GPIO
SPI
Clk Ref / PLL
Phase Shift.
Clk Manager
…
Interfaces
Buffer
PS: 2V5
(SLVS)
(LVDS)
(SLVS)
(LVDS)
(LVDS)
(SLVS)
24 b
(TFC cmd)
9 b
PS : 1V5
PS : 2V5 , 1V5
{Bidirectional !}
JTAG
FlashPro
connection
90LV001
I2C
SPI
GPIO
USB-I2C
dongle
Slave
I2C
Data
TTC cmd
Clock
SC
6

## Slide 11
3CU Board : Global architecture
B25
AB25
B25
AB25
B77
Clock distribution to FEB through 3U_backplane
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
Buffer
PS: 3V3
Ref_Clk[0:7]
E-Port_SC_FEB
x (16)
GBTX
User Buses :
{I2C, //, SPI,
JTAG, 12bADC,
…} – T°
E-Port
Network
Controller
GBT-SCA
Prim. / Second.
E-Port_SCA
Slow control to FEB
Protocol used on the board
M2GL060
VCC Core
VCC I/O_1
VCC I/O_2
USB
Delatching
Ctrl.
Dedicated Clock IO
Clock Conditioning Circuit
LVDS
SLVS / LVDS Translator
LVDS
TFC cmd
Ref_Clk[3]
Slow Control distribution to FEB through 6U_backplane
LEMO
LEMO
In_Ext_Clk
Out_Ext_Clk
In_2
In_1
Out_2
Out_1
In_1
Out_2
Out_1
In_2
1V2
Front
Rear
TFC command
In_Ext_Clk
E-Port (TFC_cmd)
Buffer
PS: 3V3
TFC command
387 Max user I/Os – 10 I/O Banks
TFC cmd distribution to FEB through 3U_backplane
I2C
GPIO
SPI
Clk Ref / PLL
Phase Shift.
Clk Manager
…
Ref_Clk[2]
Interfaces
Buffer
PS: 2V5
Ref_Clk[1]
Ref_Clk[2]
Left
Right
(SLVS)
(LVDS)
(SLVS)
(SLVS)
(LVDS)
(LVDS)
(SLVS)
24 b
(TFC cmd)
9 b
Out_Ext_Clk
PS : 1V5
PS : 2V5 , 1V5
{Bidirectional !}
JTAG
FlashPro
connection
90LV001
I2C
SPI
GPIO
USB-I2C
dongle
Slave
I2C
Data
TTC cmd
Clock
SC
6
1V5
2V5

## Slide 12
3CU Board : Global architecture
B25
AB25
B25
AB25
B77
Clock distribution to FEB through 3U_backplane
Power Supply:
3V3
2V5
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
DC-DC
Converter
5V -> 1V2
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
Buffer
PS: 3V3
Ref_Clk[0:7]
E-Port_SC_FEB
x (16)
GBTX
User Buses :
{I2C, //, SPI,
JTAG, 12bADC,
…} – T°
E-Port
Network
Controller
GBT-SCA
Prim. / Second.
E-Port_SCA
Slow control to FEB
DC-DC
Converter
5V -> 1V5
Protocol used on the board
M2GL060
VCC Core
VCC I/O_1
VCC I/O_2
USB
Delatching
Ctrl.
Dedicated Clock IO
Clock Conditioning Circuit
LVDS
SLVS / LVDS Translator
LVDS
TFC cmd
Ref_Clk[3]
USB
Slow Control distribution to FEB through 6U_backplane
LEMO
LEMO
In_Ext_Clk
Out_Ext_Clk
In_2
In_1
Out_2
Out_1
In_1
Out_2
Out_1
In_2
16 FEB Delatching Ctrl line
1V2
Front
Rear
TFC command
In_Ext_Clk
E-Port (TFC_cmd)
Buffer
PS: 3V3
TFC command
387 Max user I/Os – 10 I/O Banks
TFC cmd distribution to FEB through 3U_backplane
I2C
GPIO
SPI
Clk Ref / PLL
Phase Shift.
Clk Manager
…
Ref_Clk[2]
Interfaces
Buffer
PS: 2V5
Ref_Clk[1]
Ref_Clk[2]
Left
Right
(SLVS)
(LVDS)
(SLVS)
(SLVS)
(LVDS)
(LVDS)
(SLVS)
48 b/ 80 Mhz
(TFC cmd)
9 b
Out_Ext_Clk
PS : 1V5
PS : 2V5 , 1V5
5V
{Bidirectional !}
USB Interface Mezzanine
(UM232H-B)
JTAG
FlashPro
connection
90LV001
Status Led
I2C
SPI
GPIO
USB-I2C
dongle
Slave
I2C
Data
TTC cmd
Clock
SC
6
1V5
2V5

## Slide 13: PRR 3CU board
Architecture of the board
 Clock tree
   GBT frame
   Slow control
   Delatching control
   IGLOO2 FPGA
   Power supplies and power tree
   Rear connections
   Firmware architecture

## Slide 14
3CU Board : Clock tree
XPLL / XOSC
XPLL
Clk [7:0]
3 to 1
Phase Shifter
GBTX : Clock manager
External clock source
Clk [7:0]
Clk_Slot_0
Clk_Slot_1
Clk_Slot_2
Clk_Slot_3
Clk_Slot_6
Clk_Slot_7
Clk [0]
Clk [1]
Clk [3]
Clk_Slot_11
Clk_Slot_12
Clk_Slot_13
Clk_Slot_17
Clk_Slot_14
FPGA
(SLVS)
(SLVS)
Clk to right FEBs
Clk to left FEBs
65LVDS104
1 to 4
65LVDS104
1 to 4
65LVDS104
1 to 4
65LVDS104
1 to 4
NB6L11S
1 to 2
NB6L11S
1 to 2
(LVDS)
(Lemo)
NC7SZ125
IN_Ext_Clk
DS92LV010
(LVDS)
(Unipolar)
(Lemo)
OUT_Ext_Clk
NC7SZ125
(LVDS)
(SLVS)
Clk [4]
Ext_Clk
Ext_Clk
Clock Conditioning Circuit
Global_Clk
Toward 3U Backplane for all FEB
Clock distribution on the old “Validation slot”
Clk [2]
(SLVS)
Clk to Validation
65LVDS104
1 to 4
NB6L11S
1 to 2
(LVDS)
Clk_Slot_8
Clk_Slot_9
Clk_Slot_18
Clk_Slot_19
Clk_Slot_20
Clk_Slot_5 (Validation)
Clk_Slot_4 (Validation)
Clk_Slot_15 (Validation)
Clk_Slot_16 (Validation)
0 1 2 3
4 5
6 7 8 9
11 12 13 14
15 16
17 18 19 20
3CU
  4 among 8 reference clocks on the GBTx used
Clock distribution:
  8 output reference clocks available on the GBT (SLVS).
  The 8 reference clocks are programmable both in phase, 50 ps resolution and frequency 40, 80 160 and 320.
NB6L11S (AnyLevel Input to LVDS Fanout Buffer / Translator): RMS Clock Jitter −0.5 ps, Typical
SN65LVDS104 (1:4 LVDS Clock Fanout Buffer) : already used on the CROC for the clk distribution
    Clk[0] : left FEBs on the crate through 3U backplane
    Clk[1] : right FEBs on the crate through 3U backplane
    Clk[2] : Spare (Old validation slot)
    Clk[3], Clk[4] : IGLOO2 Clock input (one should be enough ! )
7

## Slide 15
3CU Board : GBT frame
The 120-bit “GBT frame” is transmitted every 25 ns
GBT frame format:
  4 bits for the frame Header
  32 for the FEC (Forward Error Correction)
  This leaves 84 bit for data transmission
    4 bit for Slow Control information Internal Control (IC) and External Control (EC) field
    80 bit for user Data (D) transmission
    “D” and “EC” fields is not pre-assigned and can be used indistinctly for Data Acquisition (DAQ), Timing Trigger & Control (TTC) and Experiment Control (EC) application
3CU extract and process (if necessary) the TTC and EC to transmit them through backplane to the FEBs.
8

## Slide 16
3CU Board : Slow Control (SC)
GBLD
Edge-connector
I2C
PCB
Laser Diode
VTRx
TOSA
ROSA
PD +GBTIA
1 Bi-directionnal link
120b @ 40MSPS
Uplink
Down-link
E-Port
E-Port
E-Port
24 E-Port
E-Port
General Ctrl
Master
……..
Diff. Signal:
Clk, DOUT, DIN
E-Port_SC_FEB
x (16)
GBTX
User Buses :
{I2C, //, SPI,
JTAG, 12bADC,
…} – T°
E-Port
Network
Controller
GBT-SCA
Prim. / Second.
E-Port_SCA
Protocol used on the board
Slow Control distribution to FEB through 6U_backplane
I2C
GPIO
SPI
Clk Ref / PLL
Phase Shift.
Clk Manager
…
Buffer
PS: 2V5
(SLVS)
(LVDS)
(TFC cmd)
PS : 1V5
PS : 2V5 , 1V5
USB-I2C
dongle
Slave
I2C
GBT encodes SC packets in the counting room
Transmit through optical fiber SC information interlaced with the rest of the traffic (DAQ, TTC, …)
Delivers the SCA packet unmodified to the GBT-SCA
GBT-SCA provides various user-configurable interfaces capable to perform simultaneous operations
  I2C (16 independent I2C master)
  SPI (with 8 individual slave select lines )
  GPIO (32 digital IO lines)
3CU board
  Transmit the SC to the 16 FEBs inside the same crate through the 6U backplane (translator SLVS – LVDS)
  Integrate a GBT-SCA to distribute control and monitoring signals on the 3CU
9

## Slide 17
3CU Board : FEBs delatching control
Each FEBs inside the crate are protected by delatchers (2A, Current-Limited switch) of type MAX 869
  If Single Event Latchup (SEL ) occurs the MAX869 switch OFF (during few ms) the FEB and ON again
  The delatching is controlled by the 3CU one connection between each FEB and 3CU, 16 lines off the backplane)
On the 3CU
  Each delatching control line is connected to the IGLOO2 (status register)
  Status register regularly checked by the system, and if it necessary the FEB may be reloaded by ECS.
Reused the same system of the CROC board with the IGLOO2
10

## Slide 18
3CU Board : IGLOO2 FPGA
Flexible IOs structure
  Mixed voltages VCCIO_BANK (1.2, 1.5, 1.8, 2.5, 3.3V)
  Multistandard IOs
11

## Slide 19
Power supplies and power tree
5V
  Input DC-DC converter for 1V5 and 1V2
3V3
  Discret components,
2V5
  VTRx, FPGA IOs, …
1V5
  GBTx, GBT_SCA, VTRX, …
1V2
  FPGA Core
P7V unfused
P5V unfused
P3V3 unfused
P2V5 unfused
FUSE
FUSE
FUSE
DC-DC
( FEAST )
ON
DC-DC
( FEAST )
ON
P5V
P3V3
P2V5
P1V5
P1V2
ON BOARD CONNECTOR
3U BACKPLANE
Not used
3CU power supplies needed
7V, 5V, 3,3V, and 2,5V
7V must be decrease at 6V
Crate power supplies available:
12
Modification to the compatibility with the LEDTSB design
Move the 2.5V to 3.3V and use diodes to generate the 2.5V.

## Slide 20
3CU Board : rear connection with 3U and 6U Backplane
Slow control to FEB through 6U backplane (3 differentials pairs between Control slot and each FEB)
Delatching control (1point to point connection between each FEB and Control board)
Crate Id (8 bit DIP switch on 6U_backplane)
Clock distribution from Control board to all slot of the same crate (20 differentials pairs between Control slot and each FEB)
Slot ID (4 bit ….)
7V (Not used on 3CU)
3V3
NC
6U Backplane
Connected to 6U backplane
Connected to 3U backplane
3U Backplane
TFC[8:0] Timing Fast Command (3U).
B25
AB25
B25
AB25
B77
DC-DC
Converter
5V -> 1V2
Buffer
PS: 3V3
Slow control to FEB
16 FEB Delatching Ctrl line
Rear
Buffer
PS: 3V3
TFC command
Buffer
PS: 3V3
Ref_Clk[1]
Ref_Clk[2]
Left
Right
(SLVS)
(SLVS)
(LVDS)
3CU Board
3V3
5V
DC-DC
Converter
5V -> 1V5
Valid to CROC link (Old – Not used to upgrade)
3U Backplane connections
  Power supply distribution
  Clock distribution
  TFC command distribution
6U Backplane connections
  Transmit SC to all the FEBs
  Crate Id
  Delatching control line
13

## Slide 21
Firmware architecture (IGLOO 2)
We reused a lot of block implemented to the FEB
(thanks Jihane and Christophe !)
14
LP Bus_Asyn
16 bits Rd / Wr Registers
(Add 01h, 02h, 03h)
FIFO (16x1024)
(Add 05h, 06h, 07h)
Add Map
(USB)
CS
SPI Master
(SPI Cmd register)
SPI Slave
RAM Pattern
(Emulation of TFC command)
GBT_SCA
GBTX
16 bits Rd / Wr Registers
Add Map
(SPI)
CS
Optical
Link
TFC cmd to FEB Through backplane
SC
SPI
I2C
//
Extract and process TTC Cmd
receive 21bit
transmit 9 to FEB
LP Bus _2
(USB to Users // bus)
USB
Verilog inside IGLOO2










## Slide 22: PRR 3CU board
Test of the board
 Test bench
   About clock
   About MiniDAQ
   About TTC commands
   Modification before production

## Slide 23
3CU Test Bench
15
Two 3CU board prototype available
  Optical link from MiniDAQ
  External clock generator
  USB interface
  Power supply, oscilloscope , …

## Slide 24
About clock
  The 3CU board works in master Clock
    Without optical links and With GBTx configuration by dongle (I2C) from CERN
  The 3CU board works with the Clock locked on the optical fiber
  With optical links (from MiniDAQ) and with GBTx configuration by dongle (I2C) from CERN
  The test of the Clock distribution through backplane to FEB is to do.
Test status about clock and MiniDAQ
16


About MiniDAQ (Optical link between MiniDAQ and 3CU board only)
  The MiniDaq (GBT Client) read the fourth Ctrl register inside the GBT_SCA.
GBT Client
By optical link

To do

## Slide 25
Test status about TTC command
17
About MiniDAQ and TTC command
  The “Start_Run” command generate a Synch. Pulse in the frame
  Extract a Synch pulse from the frame (inside IGLOO2 FPGA)
  Transmit to FEB through backplane
MiniDAQ Ctrl Panel
3CU
By optical link
In progress

## Slide 26
Modifications and test before production
18
30 boards will be produced (including spares)
Wire modification
  Grounding of DC-DC converter (schematic mistake !)
  Add decoupling capacitor on several discret footprints
  Remove switch to command the GBTx configuration, the configuration will be from the FPGA (Triple Voting Rregister).
  Change the power supply : to move the 2.5V to 3.3V and use diodes to generate the 2.5 V. 2 Amps diode available
Standalone tests
  Extract the TTC command from a frame
  Transmit Rd/Wr from the GBTx (3CU) to GBT_SCA (3CU)
3CU board in the crate with FEB
  Transmit the Clock through backplane to all FEBs inside the same crate (At the moment the clock is present on the rear connector of the 3CU board)
  Transmit the TTC command through backplane to all FEBs inside the same crate
  Transmit Rd/Wr from the GBTx (3CU) to GBT_SCA (FEB) through backplane
In progress

## Slide 27
Conclusion
Two 3CU prototype boards available and under test
No major corrections for the final version
There are still some tests to do before production (test with FEB inside the same crate)
  The 3CU documentation is available and up to date
19

## Slide 28
Thank you

## Slide 29: SPARES

## Slide 30
Production Schedule
End of tests of prototype
Final version CAD
Final version Production
Tests of 3CU Final version
Q1
Q3
Q2
Q1
Q4
2018

## Slide 31
3CU Board : Reset tree
Push button on board reset
Schmitt-trigger
Schmitt-trigger
M2GL050
FPGA
Power On reset
N_Reset_GBT_SCA
USB
Reset Manager
USB Interface Mezzanine
(UM232H-B)
N_Reset_All_FEB_Through_3U_Backplane
Push button GBTx reset
Schmitt-trigger
N_Reset_GBTx

## Slide 32
3CU Delatching
Delatcher
Scrutinize mode
  Scrutinize the state (ON or OFF) off all board inside crate
  Storage delatching of FEB or Validation board (FEBn = OFF).
Drive mode
  Switching ON or OFF of FEB or Validation (FEBn= ON or OFF).
Same as the CROC …
3CU

## Slide 33: SLVS standard
SLVS (Scalable Low Voltage Standard)
  JEDEC standard: JESD8-13
  Differential voltage based signaling protocol.
    Voltage levels compatible with deep submicron processes.
    Typical link length runs of 30cm over PCB at 1Gbps.
    Low Power, Low EMI
  Application in data links for Flat Panel displays in mobile devices.
    Mobile Pixel Link, MPL-2 (National semi.)
SLVS specifications brief
2 mA Differential max
Line impedance: 100 Ohm
Signal: +- 200 mV
Common mode ref voltage: 0.2V
0.2V
1.2V
400mV
200mV
LVDS
SLVS