## Slide 1: ATLASpix status and development of a version for CLIC
Ivan Peric

## Slide 2
ATLASPIX is a HVCMOS large area prototype for ATLAS
Produced by AMS in 180nm HVCMOS process
Submitted as engineering run
Different substrates: standard, high resistivity
1. MuPix8 (area 1cm x 2cm)
2. ATLASPixM2 (area 3.5mm x 2cm)
3. ATLASPixSimple/ATLASPixIsoSimple (both: area 3mm x 2cm)
The chips have been implemented on 4 different substrates: 10 Ωcm (standard substrate), 50-100Ωcm, 200-400Ωcm and 0.7-2kΩcm.

## Slide 3
HVCMOS sensors are monolithic depleted active pixel sensors in standard HVCMOS technologies
Smart diode concept
Pixel electronic placed inside the collection electrode
Properties:
Monolithic
Fast signal generation and charge collection
High radiation tolerance
Cost effective production (no need for bumps)
NMOS
PMOS
P-type substrate
Depleted zone
Deep n-well
n-well
p-well
HV

## Slide 4: Reticle
…
MuPix, ATLASPIX
MuPix8
ATLASPix
Trigger readout
Triggerless readout
IsoPMOS
PMOS
C3PD
CCPD_2ndGen
CCPD_1stGen
Belle II Switcher
Main type
Simple
Simple

## Slide 5: Reticle
…
MuPix, ATLASPIX
MuPix8
ATLASPix
Trigger readout
Triggerless readout
IsoPMOS
PMOS
C3PD
CCPD_2ndGen
CCPD_1stGen
Belle II Switcher
Main type
Simple
Simple

## Slide 6: ATLASPIX simple
ATLASPIX simple with triggerless (hit driven) readout

## Slide 7: Architecture
Architecture of the chip
Pixel matrix: 24 x 400 pixels of 40µm x 130µm size.
Matrix control shift register (MSR) used to select pixels for injection, enable analogue output and hitbus (hitbus not implemented in M2) and write the pixel RAM
Hit buffers that receive pixel signals and enable priority based readout
EoC buffer to allow horizontal multiplexing
Digital control unit (DCU), PLL
Current-mode and voltage-mode DACs – they use shift register for configuration
The DAC-SR, VDAC-SR, matrix-SR and a configuration-SR form a chain
Pads
Matrix
MSR
MSR
Trigger buffers
EOC
Dcu
cdac
vdac
pads

## Slide 8
Pixel 0
Left
RO
Block
Right
RO
Block
Pixel 399
RO cell 0
RO cell 199
EoC
Left
RO
Block
Right
RO
Block
EoC
EoC
EoC
EoC
ScanIn
ScanOut
ScanOut
CU
LDPIX, LDCOL, RDCOL
Hit data
Data (1.6 Gbps)
PLL and oscillator
160MHz
Pixel 1
Hit data
ScanIn
Column 0
Column 24
Pixel 0
Pixel 399
Pixel 1
ScanOut
Pixel 199
Pixel 200
Pixel 200
Pixel 199
0
1
199
0
1
199
0
1
0
1
199
199
Pixel 201
Pixel 201
Col. control
Col. control
Row control
Bias block

## Slide 9: Pixel
Pixel contains sensor diode, charge sensitive amplifier, comparator, threshold tune DAC, RAM for tune bits (3) and disable bit and output driver
The outputs of the pixels are transmitted to the column periphery (long metal lines)
Amplifier
Sensor
Comparator
Th
BL
TDAC
Injection
Injection enable
RAM
3
4
TDAC in
TDAC write
Cinj
Bias resistance
Tout
Data transfer line
column control
Row
control
-HV
1.8V
readout cell or trigger buffer
Pixel
Offset
disable
disable
AnalogOut

## Slide 10: RO-Cell
Hit
Hit
RdScan
10 bit TS
6 bit TS
Address
x
x
LdPix
RdPix
Data
ScanIn
ScanOut
Receiver
Sync
TS
Every pixel has its RO cell at the periphery
Readout cell contains hit flag latch, timestamp memory (for leading edge time stamp and time over threshold), address generator, priority logic, bus driver

## Slide 11: EoC cell
By issuing read, the hits are transferred to EoC buffers. These EoC buffers are forming an active bus, they don’t change the data received by triggered buffer they just add the column address to the hit data. The hits are transferred from EoC buffers by RdCol signal in a priority way – the same as used for hit buffers
D-latch
Col
Add
LdCol
RdCol
PrioOut (from buffers)
Data (from buffers)
Wr
Rd
In
Data
R
S
PrioOut (not empty)

## Slide 12: DCU
Digital control unit generate the signals for the buffer readout: time stamps, Wr, trigger, RdBuf, LdBuf and RdCol. It receives and formats hit data and sends them using a fast link (1.6gbps).
Digital control unit has the inputs: RefCk (160Mhz), for debug FastCk (800MHz), SyncReset, Trigger and fast output. There are many parameter bits (e.g. for changing of time stamp speed) that are stored in the configuration shift register.
Ld pix
Ld col
Rd col
8
8b10b encoder
S
Time stamp cnt
40Mhz
Ck gen
160Mhz
200Mhz
800MHz
k
8
k
8
k
8
k
SyRes
Data Mux
PLL
Osc
40
SR
Lat
RefCk
Sin,Ck1,Ck2,Ld,Rb
SOut
TS
LdBuf, RdBuf, RdCol
PrioOut
Data
Debug
Comma
1.6gbps
40Mhz
160Mhz
200Mhz
400Mhz
800Mhz
RoSM
Global register (matrix, DACs and configuration)

## Slide 13: DCU
Digital control unit contains following blocks:
Clock generator that includes PLL and oscillator
Time stamp counter
Ld pix
Ld col
Rd col
8
8b10b encoder
S
Time stamp cnt
40Mhz
Ck gen
160Mhz
200Mhz
800MHz
k
8
k
8
k
8
k
SyRes
Data Mux
PLL
Osc
40
SR
Lat
RefCk
Sin,Ck1,Ck2,Ld,Rb
SOut
TS
LdBuf, RdBuf, RdCol
PrioOut
Data
Debug
Comma
1.6gbps
40Mhz
160Mhz
200Mhz
400Mhz
800Mhz
RoSM
Global register (matrix, DACs and configuration)

## Slide 14: DCU
Readout state machine. It receives the priority output from EoC cells (empty signal) and generate a sequence of LdBuf, RdBuf and then if EoCs are not empty, RdCol. The state machine also controls the data multiplexer and sends either the hit data, debug data or the comma words to the 8b10b encoder. The data are sent in RdCol states and in other states debug data or comma words.
Ld pix
Ld col
Rd col
8
8b10b encoder
S
Time stamp cnt
40Mhz
Ck gen
160Mhz
200Mhz
800MHz
k
8
k
8
k
8
k
SyRes
Data Mux
PLL
Osc
40
SR
Lat
RefCk
Sin,Ck1,Ck2,Ld,Rb
SOut
TS
LdBuf, RdBuf, RdCol
PrioOut
Data
Debug
Comma
1.6gbps
40Mhz
160Mhz
200Mhz
400Mhz
800Mhz
RoSM
Global register (matrix, DACs and configuration)

## Slide 15: DCU
Encoder: Custom made pipelined 8b10b encoder is used
Serializer: Novel 8to1 serializer (S) based on binary tree is used to produce bit stream. Blocks of 4 words (40 bits) are sent to the serializer
Ld pix
Ld col
Rd col
8
8b10b encoder
S
Time stamp cnt
40Mhz
Ck gen
160Mhz
200Mhz
800MHz
k
8
k
8
k
8
k
SyRes
Data Mux
PLL
Osc
40
SR
Lat
RefCk
Sin,Ck1,Ck2,Ld,Rb
SOut
TS
LdBuf, RdBuf, RdCol
PrioOut
Data
Debug
Comma
1.6gbps
40Mhz
160Mhz
200Mhz
400Mhz
800Mhz
RoSM
Global register (matrix, DACs and configuration)

## Slide 16: Readout
Hit driven, trigerless, readout (MuPix8, Simple ATLASPix)
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Address:

## Slide 17: Readout
Hit driven, trigerless, readout
Time: 0
Amplitude: 5
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Address:

## Slide 18: …
Hit driven, trigerless, readout
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Address:
Time: 0
Amplitude: 5

## Slide 19: …
Hit driven, trigerless, readout
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time: 3
Amplitude: 10
Time:
Amplitude:
Address:
Time: 0
Amplitude: 5

## Slide 20: …
Hit driven, trigerless, readout
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time: 3
Amplitude: 10
Time:
Amplitude:
Address:
Time: 0
Amplitude: 5

## Slide 21: …
Hit driven, trigerless, readout
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time: 3
Amplitude: 10
Time: 0
Amplitude: 5
Address: 1
Time:
Amplitude:

## Slide 22: …
Hit driven, trigerless, readout
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time:
Amplitude:
Time: 3
Amplitude: 10
Address: 4
Time:
Amplitude:

## Slide 23: Measurement results
Efficiency
Threshold voltage
Dominik Dannheim, Andreas Nürnberg
ATLASPix efficiency measured at CERN SpS – CLIC telescope > 99%
Spatial resolution: RMS = 12.6µm

## Slide 24: Measurement results
Figure shows the measurement performed with ATLASPixSimple at 200 Ωcm substrate
Fast readout has been used, TS period was 25ns (800mbps)
Sr-90 spectrum has been measured with ToT. (ToT has 6 bits)
The spectrum peak is 7000e. (Calibrated with x-rays)
Figure right shows signal (MPW – Sr-90) vs depletion voltage

## Slide 25: Measurement results
Result of the threshold scan for ATLASPIxSimple. Matrix has been tuned
Average threshold is ~1026e and the threshold dispersion 70e.
The noise dispersion is shown in the figure right. Average noise is 80e.
Signal to noise ratio of ATLASPIxSimple is about 80. There is enough signal. It would work also at standard substrate

## Slide 26: Measurement results
All s-curves are shown as well. Signals > 0.3V (1700e) can be detected with 99% efficiency

## Slide 27: Design for CLIC
Pixel 0
Left
RO
Block
Right
RO
Block
Pixel 399
EoC
EoC
Pixel 1
Pixel 199
Pixel 200
0
1
199
0
1
199
Pixel 201
Col. control
Pixel 0
Left
RO
Block
Right
RO
Block
Pixel 399
EoC
EoC
Pixel 1
Pixel 199
Pixel 200
0
1
199
0
1
199
Pixel 201
Col. control

## Slide 28: Design for CLIC
Left
RO
Block
Right
RO
Block
EoC
EoC
0
1
199
0
1
199
Col. control
Left
RO
Block
Right
RO
Block
EoC
EoC
0
1
199
0
1
199
Col. control
Pixel 799
Pixel 798
Pixel 0
Pixel 1
601
600
Pixel 199

## Slide 29: Layout of the CLIC pixel
22 – 25µm

## Slide 30
ATLASPIX is a HVCMOS large area prototype for ATLAS
Produced by AMS in 180nm HVCMOS process
Submitted as engineering run
Different substrates: standard, high resistivity
Features:
Pixel matrix: 24 x 400 pixels of 40µm x 130µm size
6.5 bit time over threshold
10 bit time stamp
Time stamp resolution up to 12.5ns
1.6 Gbps data transfer with 8b10b conversion
Efficiency measured in beam > 99%
SNR ~ 80
Power consumption < 200mW/cm2
Time resolution: sigma ~ 12ns (pixel to pixel variation corrected, preliminary)
Spatial resolution: 12.6µm
Design for CLIC ongoing