## Slide 1
Phu Anh Phi NGHIEM (CEA) et al.
WP2 et al. - Beam Physics studies
Results and next steps
Nov 2017- Nov 2018
EuPRAXIA Yearly Meeting
& 4th Collaboration Week
Frascati, November 19-23, 2018

## Slide 2
Rec5. SAC recommends to define a time-line for starting this down selection process that should lead to a CDR with identified solutions for the low energy case (1 GeV) and the high-energy case (5 GeV) in one year from now.
OUTLINE
1. Results obtained at each plasma stage
and selection of the schemes
2. Start-to-End simulations
Issues
Results
3. Next step
Study of errors and tolerances
Rec6. SAC recommends reinforcing the coordination with the above WP [3, 4, 5, 6, 7] and considering opening up the design space if showstoppers are identified by any of the WPs …
SAC learns from the WP2 leader that the different codes used were benchmarked one another on similar physical situations leading to compatible results. Despite this, it was pointed out a poor stability of the solutions analysed leading to a high sensitivity to the input parameters.
Rec7. SAC recommends carrying on an analysis of the stability of the solutions under investigation and including the stability parameter as an element in the down selection process; deepening the analysis of the effects associated to non-ideal conditions, such as density fluctuations in the plasma target, quality of transverse laser mode, and, ….
The analysis of the high energy 5 GeV beam is not yet finished and the general impression is that this WP is exploring a field that has not yet reached its final maturity.

## Slide 3
EuPRAXIA acceleration schemes
PPAS
5 GeV
4B
500 MeV
RFI
L
W
F
A
PWFA
PPAS
1 GeV
4A
500 MeV
RFI
LPI
LPAS
1 GeV
5 GeV
1A
LPI
5 GeV
1B
LPAS
LPAS
1 GeV
5 GeV
2A
RFI
500 MeV
LPAS
5 GeV
2B
RFI
500 MeV
LPAS
LPAS
1 GeV
5 GeV
3A
150 MeV
LPI
LPAS
5 GeV
3B
150 MeV
LPI

## Slide 4
L
W
F
A
PWFA
Restricted acceleration schemes
STRATEGIC Objective:
- Providing beam at 5 GeV meeting 'perfectly'
FEL and HEPO requirements
- Providing as well beam at 1 GeV 'usable'
for FEL and HEPO, as a 'commissioning' step
LPI
5 GeV
(1 GeV)
Scheme 1
CNR
CEA
HETL
LPAS
5 GeV
(1 GeV)
Scheme 2
RFI
500 MeV
DESY
INFN
LNF DESY
CEA
HETL
LPAS
5 GeV
(1 GeV)
Scheme 3
150 MeV
LPI
IST, LLR
LPGP, CNR
CEA
CEA LETL
CEA
HETL
PPAS
5 GeV
(1 GeV)
Scheme 4
500 MeV
RFI
LNF
LNF LNF
CEA
HETL
At Yearly meeting in Lisbone (2017)

## Slide 5
L
W
F
A
PWFA
Restricted acceleration schemes
STRATEGIC Objective:
- Providing beam at 5 GeV meeting 'perfectly'
FEL and HEPO requirements
- Providing as well beam at 1 GeV 'usable'
for FEL and HEPO, as a 'commissioning' step
LPI
5 GeV
(1 GeV)
Scheme 1
CNR
CEA
HETL
LPAS
5 GeV
(1 GeV)
Scheme 2
RFI
500 MeV
DESY
INFN
LNF DESY
CEA
HETL
LPAS
5 GeV
(1 GeV)
Scheme 3
150 MeV
LPI
IST, LLR
LPGP, CNR
CEA
CEA LETL
CEA
HETL
PPAS
5 GeV
(1 GeV)
Scheme 4
500 MeV
RFI
LNF
LNF LNF
CEA
HETL
Additionally : Scheme 2A and Hybrid schemes
PPAS
5 GeV
(1 GeV)
Scheme 5
Strathclyde, DESY
HETL
LPAS
HYBRID
At Yearly meeting in Lisbone (2017)

## Slide 6: EuPRAXIA requirements
Critical parameters of the electron beam
required at Injection or Acceleration stages

## Slide 7
Beam parameters obtained at 5 GeV
Required value
All the schemes

## Slide 8
Beam parameters obtained at 5 GeV
Required value
Schemes the closest to the requirements
Four experts
Three institutes
Three codes used:
- Warp 3D
- QFluid ~3D
- FBPIC 3D
Three injectors:
LPI 150 MeV
RFI 240 MeV
RFI 540 MeV
Close plasma,
laser parameters
Quasi linear regime
⇒
Close results
Robustness of the results !!!

## Slide 9
Beam parameters obtained at 5 GeV
Required value
Schemes selected for Start-to-End simulations
LPI 150 MeV
RFI 540 MeV
Quasi linear regime

## Slide 10
Beam parameters obtained at 1 GeV
Required value
All the schemes

## Slide 11
Beam parameters obtained at 1 GeV
Required value
Schemes the closest to the requirements

## Slide 12
Beam parameters obtained at 1 GeV
Required value
Scheme Selected for Start-to-End simulations

## Slide 13
Beam parameters obtained at 150 MeV
Required value
Scheme selected for start-to-end simulations

## Slide 14
Schemes selected for S2E simulations
Scheme 2 : RFI + LPAS (quasilinear regime)
Scheme 3: LPI (REMPI) + LPAS (quasilinear regime)
Scheme 4: RFI + PPAS (bubble regime)
LPAS
5 GeV
(1 GeV)
Scheme 2
RFI
500 MeV
HETL
LPAS
5 GeV
(1 GeV)
Scheme 3
150 MeV
LPI
LETL
HETL
PPAS
1 GeV
Scheme 4
500 MeV
RFI
LNF
HETL
Note: This is only the present snapshot. Not definitive
Other schemes and other regimes remain to be very precious alternatives !!!
They may be found to be equally or even more appropriate later on

## Slide 15
Plasma configurations used in simulations
- Plasma H, Ar, N5+, N2 impurity, …
- Longitudinal: uniform plateau
with ramps at entrance and exit
Radial: parabolic
- Longitudinal: downramp for auto injection
- Gas jet, or capillary, or cell
- Length and density:
LPAS 5 GeV: 17-28 cm, 0.1-2.5 1017 cm-3
LPAS 1 GeV: 3-7 cm, 1-5 cm-3
LPI 150 MeV: 0.6-4 mm, 7-80 1017 cm-3
Scheme ID | Realistic? | How to achieve | Imperfections | Alternative
Scheme1B P. Tomassini | No (revised) | ? more details on requirements are necessary | Described gradient at entrance too sharp | are smoother gradient and transitions acceptable for the scheme?
Scheme 2B E Svystun et al | Yes | Capillary, ramps given by fluid simuls | Low density challenging for parabolic profile, reproducibility to be tested | Gas cell also an option for parabolic profile (OFI plasma) and length smaller than 20 cm
Scheme 2B A Rossi | No | ? details on requirements are necessary | Uniformity over 50cm to be determined for a discharge | Promising option: laser created plasma
Scheme 3B T Silva et al | No | Upramp gradient too sharp; Shock for downramp gradient | Gradient fluctuations | Shock injection with a smooth gradient at entrance
Scheme 3B A Beck | No | ? beyond state-of-the-art gas jet | Gradients are linear and too sharp | Gas jets with longer, exponential ramps
Scheme 3B G Maynard | yes | Gas cell | Density controlled better than 10% | Double gas jet
Scheme 3B P Tomassini A | Yes | Gas jet far from the nozzle, smooth gradients | Pure nitrogen may induce non uniform distribution: ionization level? | Gas cell, required profile needs to be specified
Scheme 3B P Tomassini B | No (revised) | Separation of areas with “pure” gas difficult inside gas jets | Ramps need to be determined | Two-stage gas cell
Scheme 3B X Li | Yes | Low density channel may be achieved with OFI in gas capillary | Plasma uniformity needs to be specified Delta n is of the order of fluctuations, 10% | Promising option: laser created plasma
Scheme 4B A Marocchino | ? yes if uniform plasma | Depends on transverse profile, uniform ok in capillary tube with OFI | Plasma uniformity needs to be specified | -
Brigitte Cros, T. Audet
A first estimate is given:
- Realism level
- How to achieve
- Potential imperfections
- Suggestion of alternative
Interactions with WP3

## Slide 16
for 5 GeV
Laser parameters used in beam simulations
Bi-Gaussian pulse
l = 800 nm
Required laser parameters: P = 400 TW, E = 60 J, w0 = 45 mm ( a0 = 2.42, tFWHM = 141 fs)
Interactions with WP4

## Slide 17
for 1 GeV
Laser parameters used in beam simulations
(cosine squared in longitudinal
for Sch2_1 GeV_Rossi)
Required laser parameters: P = 200 TW, E = 30 J, w0 = 30 mm ( a0 = 2.57, tFWHM = 141 fs)
Bi-Gaussian pulse
l = 800 nm
Interactions with WP4

## Slide 18
for 150 MeV
Laser parameters used in beam simulations
Required laser parameters: P = 250 TW, E = 10 J, w0 = 30 mm ( a0 = 2.87, tFWHM = 38 fs)
Bi-Gaussian pulse
l = 800 nm
Interactions with WP4

## Slide 19
Start-to-End simulations
Issue: preserving emittance
when extracting the beam from the plasma and transporting it
- Parameters governing emittance growth not clear
- No solution for avoiding emittance growth in case of high charge beam
Thorough study shows that ALL the parameters governing emittance growth are:
through a drift of length
through a thin lens of strength
Recommended strategy:
1. Minimize emittance and energy spread in the acceleration part
2. Minimize the Twiss parameter in the plasma ramp
3. Minimize the integrated focusing strength in the transfer line

## Slide 20
Up- and Downramp with Linear or Exponential density profiles have been checked
Optimized length  Minimum emittance growth
1
2
Transfer line: number of quadrupoles = number of constraints
6 quadrupoles  emittance growth of only 10% at FEL entrance
Start-to-End simulations
Efficient and easy to implement

## Slide 21
Start-to-End simulations
At the entrance of user's applications,
when keeping only the "core" part where rms values are in the "plateau"

## Slide 22
Scheme 2 : RFI + LPAS (quasilinear regime)
Q = 24 pC, etr,n = 0.32 mm mrad
Scheme 3: LPI (REMPI) + LPAS (quasilinear regime)
Q = 25 pC, etr,n = 1.1 mm mrad
(actual beam distribution from LPI to LPA remaining to be done)
Scheme 4: RFI + PPAS (bubble regime)
Q = 28 pC, etr,n = 1.8 mm mrad
(g0 can be furthermore decrased)
LPAS
5 GeV
(1 GeV)
Scheme 2
RFI
500 MeV
HETL
LPAS
5 GeV
(1 GeV)
Scheme 3
150 MeV
LPI
LETL
HETL
PPAS
1 GeV
Scheme 4
500 MeV
RFI
LNF
HETL
Start-to-End simulations
At the entrance of user's applications,
when keeping only the "core" part where rms values are in the "plateau"
every other beam parameters remaining unchanged by the transfer lines
Further progress are still possible…

## Slide 23
Next step: Error and Tolerance studies
Deliverable Report in Spring 2019: "Final tolerance analysis"
Issue: very time consuming simulations
 Strategy of error studies to be defined
 Sharing of works to be coordinated
 Prerequisite: Top Level Tolerances to be defined
At this meeting!
For the moment:
- Pre-discussions on these subjects have been launched
- A preliminary list of Errors/Requirements is circulating for collecting comments

## Slide 24
Preliminary list of Errors/Requirements
Tolerance on Requirements
Power
Energy
w0
Transv. profile
Longit. profile
Focal plane position
Alignment, angle
Time shift
…
Plasma density
Plateau long. profile
Plateau trans. profile
Ramp long. profile
Input beam energy
Input beam position
Input beam angle
Input beam emittance
Input beam Twiss a, b
…
Quadrupole position
Quadrupole strength
Input beam energy
Input beam position
Input beam angle
Input beam emittance
Input beam Twiss a, b
...
Errors on Laser
Errors on Plasma
Errors on Transfer Line
Emittance
Twiss a, b
Slice emittance
Energy spread
Slice energy spread
Bunch length
Alignment, position
Alignment, angle
Energy
Charge

## Slide 25
Conclusions
Tremendous simulations and optimizations have been performed by many contributors
 Many results obtained on different injection/acceleration schemes and techniques
 First down selection performed for S2E simulations
 Issues of S2E simulations studied and solved
 Beam parameters at user's door very close to requirements
Other schemes or techniques remain very promising
Further progress still possible
Robust results (see also presentation tomorrow afternoon)
Next step: Errors and Tolerances studies